-----------------------------------
DATE:     April 13,1982

PRODUCT:  WordStar
CATEGORY: CORRECTION
Revision: All
PROBELM:  ETX/ACK & XON/XOFF protocols through CP/M LIST DEVICE
REF:      USER4, LISINP:, XON/XOFF, ETX/ACK, LST:, PRINTER

Description: 

This bug only affects printers which are sent output characters through
the standard CP/M list (LST:) device and the users wishes to implement 
the XON/OFF or ETX/ACK protocols. 

The list device driver in USER 4 includes a patchable item called LISINP:
which is necessary to provide a routine to retreive the ACK character from 
the printer.

Unfortunately this routine is never called by WordStar.  The fix is as
follows:

	A>SID WSOVLY1.OVR<CR>
	  SID VERS 1.4
	  NEXT   PC   END
	  8600  0100  BCFF
          #S739B<CR>
	  739B  FA CA<CR>
	  739C  25 .<CR>
	  #S7992<CR>
	  7992  FA CA<CR>
	  7993  25 .<CR>
          #G0<CR>
	A>SAVE 133 WSOVLY1.OVR<CR>

					EAS

             -----------------------------------
;DATE:     April 13,1982
;
;PRODUCT:  WordStar
;CATEGORY: MODIFICATION
;Revision: 3.0 only
;Subject:  SYSTEM FILE DISPLAY SUPPRESSION IN WS DIRECTORY
;
;  THIS PATCH WILL SUPPRESS DISPLAY OF ANY FILES ASSIGNED TO BE SYSTEM FILES
;  UNDER CP/M 2.XX (HAVEN'T TESTED MP/M) WITH THE COMMAND:
;	
;		STAT FN.FT $SYS
;
;		PATCH IS FOR WORDSTAR 3.00	EAS  02/03/82
;
;    THE PATCH REPRESENTS 31 BYTES OF CODE IN THE USER PATCH AREA (USER1, 
;    MORPAT:) ORGANIZED TO EXIST AT THE HIGHEST LOCATION AVAILABLE SO THAT
;    CURRENTLY EXISTING PATCHES WHICH DO NOT EXTEND PAST LOCATION 33CH WILL
;    NOT BE AFFECTED BY THE INSTALLATION OF THIS SYSTEM FILE SUPPRESSION.
;
;                             Enjoy,
;                                       Evan
;
DELENTX	EQU	2C28H	
DELENTY	EQU	2C2BH	
DTAB	EQU	2C69H	
DENTPT	EQU	36D1H	
DOSNX	EQU	2C8AH	
NDTST	EQU	2BF6H	
			
	ORG	33DH
;
MORPAT: PUSH	D	
	INX	D	
	LDAX	D	
	ANI	80H	
	POP	D	
			
	JNZ	NODISP	
	LXI	H,DTAB  
			
	JMP	DELENTY 
;
NODISP:	POP	H	
	POP 	B	
	XCHG		
	LHLD	DENTPT	
	XCHG		
	PUSH	H	
	CALL	DOSNX	
	POP	H	
	POP	D	
	JMP	NDTST	
;
	ORG	DELENTX	
;
	JMP	MORPAT	
	END
 
;DATE:     April 13,1982
;
;PRODUCT:  WordStar
;CATEGORY: MODIFICATION
;Revision: 3.0 only
;Subject:  Formmated output from printer driver
;
*************************************************
*	PRINT TO DISK WITH WORDSTAR 3.0		*
*************************************************
;
; THIS PROGRAM TAKES WHAT WORDSTAR SENDS TO THE LIST DEVICE
; TO A FILE CALLED FILEOUT.  THIS MEANS YOU CAN PRINT FILES
; DIRECTLY TO THE DISK AND THEN PRINT THEM LATER USING PIP
; OR AN EQUIVALENT.  ALSO GOOD FOR SEEING EXACTLY WHAT WORDSTAR
; DOES FOR ANY SPECIFIC PRINTER INSTALLATION.  INSTALL
; WORDSTAR FOR THE PRINTER OF YOUR CHOICE, NO PROTOCOL,
; AND CP/M "LST:" DEVICE DRIVER.  THIS PROGRAM USES
; PBGMEM, SO BE SURE TO SAVE ENOUGH PAGES TO HOLD THE
; PATCHES.
;
*************************
*	EQUATES		*
*************************
;
DEFBUF	EQU	0080H		; DEFAULT BUFFER USED FOR FILE I/O
BDOS	EQU	5		; LOCATION OF BDOS JUMP VECTOR
CLOSEF	EQU	16		; CLOSE FILE FUNCTION
DELETEF	EQU	19		; DELETE FILE FUNCTION
MAKEF	EQU	22		; MAKE FILE FUNCTION
WRITEF	EQU	21		; WRITE SEQUENTIAL
SETDMA	EQU	26		; SET DMA ADDRESS
INISUB	EQU	02A4H		; ADDRESS OF INITIALIZATION SUBR IN WS 3.0
UNISUB	EQU	02A7H		;    "    "  DEINITIALIZATION SUBR IN 3.0
PRINIT	EQU	070DH		;    "	  "  PRINTER INITIALIZATION SUBR
PRFINI	EQU	0710H		;    "    "  "       DEINITIALIZATION SUBR
MORPAT	EQU	02E0H		;    "    "  EXTRA PATCHING AREA IN ROOT
LISEND	EQU	071DH		;    "    "  LST: PRINTER DRIVER IN WS
PBGMEM	EQU	035CH		;    "    "  POINTER TO FREE MEMORY
MEM	EQU	7900H		; WHERE THE ABOVE POINTER POINTS TO INITIALLY
;
	ORG	INISUB
	JMP	INITA		; CHANGE BDOS VECTOR TO GO TO OUR ROUTINE
				; WHICH CHECKS FOR WS CHANGING DMA ADDRESS
				; SO WE CAN RESET IT AFTER WE WRITE OUR FILE
				; TO THE DISK.
;
	ORG	UNISUB
	JMP	DEINITA		; CHANGE BDOS VECTOR BACK TO WHAT IT WAS
				; ORIGINALLY.
;
	ORG	PRINIT
	JMP	INITB		; DELETE THE FILE IF IT EXISTS, AND CREATE
				; A NEW ONE.
;
	ORG	PRFINI
	JMP	DEINITB		; WRITE LAST SECTOR TO, AND CLOSE FILEOUT
;
	ORG	LISEND
	JMP	PFILE		; PRINT FILE TO DISK
;
	ORG MORPAT
INITA:	LHLD	BDOS+1		; GET BDOS VECTOR
	SHLD	CBDOS+1		; STORE IT FOR USE AFTER CHECKING FOR
				; CHANGE DMA ADDRESS
	LXI	H,TRANS		; POINT TO TRANSLATE ROUTINE
	SHLD	BDOS+1		; MAKE 6 & 7 POINT THERE SO
				; THAT WE CAN DO TRANSLATION
	RET			; AND RETURN
;
INITB:	MVI	C,DELETEF	; DELETE "FILEOUT"
	LXI	D,FILE		; IF IT EXISTS
	CALL	BDOS		; NOTE, NO ERROR CHECKING
	MVI	C,MAKEF		; CREATE THE FILE ON CURRENTLY LOGGED DRIVE
	LXI	D,FILE
	CALL	BDOS
	INR	A		; IF NO DIRECTORY SPACE
	JZ	EXIT		; RETURN TO OPERATING SYSTEM
	RET			; ELSE DONE
;
DEINITA:LHLD	CBDOS+1		; POINT TO ORIGINAL JMP ADDRESS
	SHLD	BDOS+1		; STORE IT BACK
	RET
;
DEINITB:LXI	D,DEFBUF	; POINT TO BUFFER
	MVI	C,SETDMA	; CHANGE DMA
	CALL	CBDOS
	LXI	D,FILE		; POINT TO FCB
	MVI	C,WRITEF	; WRITE IT OUT
	CALL	CBDOS
	ORA	A		; ERROR IF NON-ZERO
	JNZ	EXIT		; RETURN TO OPERATING SYSTEM
	LXI	H,DEFBUF-1	; POINT TO 80H
	SHLD	COUNT		; STORE NEW COUNT
	LHLD	NEWDMA		; GET WS'S DMA ADDRESS
	XCHG			; PUT IN DE
	MVI	C,SETDMA	; TO SET DMA AND
	CALL	CBDOS		; CHANGE IT BACK
	MVI	C,CLOSEF	; CLOSE THE FILE
	LXI	D,FILE
	CALL	CBDOS
	INR	A		; CHANGED DISKS ON US?
	JZ	EXIT		; IF SO, REBOOT
	RET			; ELSE DONE
;
TRANS:	PUSH	PSW		; SAVE ACCUMULATOR
	MOV	A,C		; GET BDOS FUNCTION NUMBER
	CPI	SETDMA		; IF SETTING DMA, WE WANT TO KNOW WHERE TO
	JZ	STODMA		;
	POP	PSW		; ELSE RESTORE ACC
CBDOS:	JMP	0000H		; AND JMP TO THE BDOS (ADDRESS PUT IN AT INITA)
;
STODMA:	XCHG			; GET NEW DMA IN HL
	SHLD	NEWDMA		; STORE IT FOR FUTURE USE
	XCHG			; RESTORE DE & HL TO ORIGINAL VALUES
	POP	PSW		; RESTORE ACCUMULATOR
	JMP	CBDOS		; AND JUMP TO BDOS
;
NEWDMA:	DW	0000H		; THIS IS WHERE WS'S DMA IS (PUT IN FROM
				; STODMA ROUTINE ABOVE
;
	ORG	PBGMEM
	DW	LEN + MEM	; STORE NEW POINTER TO END OF MEMORY AT PBGMEM
;
	ORG	MEM		; START WHERE PBGMEM ORIGINALLY POINTED TO
				; BECAUSE THERE'S NOT ENOUGH SPACE TO DO
				; ALL THIS IN MORPAT
;
; ACTUAL ROUTINE TO PRINT FILE TO DISK
;
PFILE:	LHLD	COUNT		; GET COUNT
	INX	H		; INCREMENT IT
	MOV	B,A		; SAVE CHARACTER BEING PRINTED
	MOV	A,H		; GET HI ORDER COUNT
	CPI	1		; GONE TO 100H?
	JZ	WRITIT		; YES, TIME TO WRITE A SECTOR
	SHLD	COUNT		; NO, STORE NEW COUNT
	MOV	M,B		; STORE CHARACTER
	RET			; AND RETURN
WRITIT:	PUSH	B		; SAVE LAST CHARACTER
	LXI	D,DEFBUF	; POINT TO BUFFER
	MVI	C,SETDMA	; CHANGE DMA
	CALL	CBDOS
	LXI	D,FILE		; POINT TO FCB
	MVI	C,WRITEF	; WRITE IT OUT
	CALL	CBDOS
	ORA	A		; ERROR IF NON-ZERO
	JNZ	EXIT		; RETURN TO OPERATING SYSTEM
	LXI	H,DEFBUF-1	; POINT TO 80H
	SHLD	COUNT		; STORE NEW COUNT
	LHLD	NEWDMA		; GET WS'S DMA ADDRESS
	XCHG			; PUT IN DE
	MVI	C,SETDMA	; TO SET DMA AND
	CALL	CBDOS		; CHANGE IT BACK
	POP	B		; GET LAST CHARACTER
	MOV	A,B		; INTO A
	JMP	PFILE		; AND START AGAIN
;
EXIT:	CALL	DEINITA		; RESTORE BDOS VECTOR
	JMP	0000		; AND REBOOT
;
COUNT:	DW	80H-1		; INITIALIZE TO BEGINNING - 1
FILE:	DB	0
	DB	'FILEOUT ','   '; FCB FOR OUTPUT FILE
	DB	0,0,0,0,0,0,0,0
	DB	0,0,0,0,0,0,0,0
	DB	0,0,0,0,0,0,0,0
	DW	-1		; TO MARK END
LEN	EQU	$-PFILE
END
;