Documentation	for UNSPOOL Version 3.1


		    for	CP/M 2.0 and up.

AUTHOR:
		    Gary P. Novosielski
		       Rutherford, NJ
		       (201) 935-4087
		   Evenings and	weekends.

INTRODUCTION:

	 UNSPOOL  (Ver	3.0) is	a program to send a standard
CP/M file such as a .PRN or .ASM file to the  system's	list
or  punch  device,  while  still  allowing  almost all other
system operations to take place.  The  file  is	 transferred
during periods when console is waiting for input.

SYNTAX:

	 UNSPOOL [d:]filename.ext [dev]
		 or
	 UNSPOOL dummy OFF

	 [square brackets denote optional parameters]

Where	       d:	       is  an  optional	 drive	spec
			       such as	A:  or	B:.  If	 not
			       entered,	 the current default
			       drive is	assumed.
	       filename.ext    is the name of the CP.M	file
			       to be printed/punched.
	       dev	       is  the	symbolic name of the
			       output  device  to  be  used.
			       Valid  devices  are  LST	 and
			       PUN. Note that the colon	 (:)
			       usually	 present   in  these
			       names is	NOT entered. If	 not
			       specified, the LST: device is
			       assumed.
	       OFF	       If  OFF	is specified instead
			       of   a	device	 name,	 the
			       operator	 will be offered the
			       option of cancelling  UNSPOOL
			       if it is	already	running.
	       dummy	       Because	the  word OFF is the
			       second parameter, a  filespec
			       is still	needed.	A dummy	name
			       of  "."	will  suffice  as  a
			       place holder.
Examples:
	 UNSPOOL TEST.PRN
		 will  send  the  file	TEST.PRN  from	 the


Revised	81-12-06			Page 1 of 6

_______________________________________________________________


	  Documentation	for UNSPOOL Version 3.1


current	default	drive to the current LST: device.

	 UNSPOOL A:TEST.PRN LST
		 is   exactly	equivalent   to	 the  above,
assuming drive A is the	default	drive. Note that the  device
name has no trailing colon.

	 UNSPOOL B:ZINGER.HEX PUN
		 will  send  the  file ZINGER.HEX from the B
drive to the current PUN: device regardless of	which  drive
is  currently the default. Note	that the device	is "PUN" not
"PUN:".

	 UNSPOOL . OFF
	 UNSPOOL *.* OFF
	 UNSPOOL OFF OFF
		 all cause an operator prompt: "Do you	want
to  cancel  UNSPOOL?"  A  single  "Y"  or "N" (Yes or No) is
accepted from the console as a response. Any other character
is assumed to mean "No".

	 UNSPOOL OFF
		 causes	the file "OFF.	 " to be sent to the
list device.

OPERATION:

	 Upon loading, the program checks to  see  that	 the
the  BIOS  vector  table  pointed to by	the word at location
0001H  is  valid,  i.e.	 is  a	table  of  JMP	instructions
containing at least 16 entries.	If an error is detected, the
program	 will  display	an  error message on the console and
attempt	to warm-boot CP/M.

	 If found, the BIOS vector table is copied into	 the
program	 segment  which	will remain active during unspooling
so that	subsequent application programs	running	concurrently
with UNSPOOL will still	have access to the BIOS.

	 This table is modified	to  trap  attempts  to	warm
boot  the  system,  perform direct console input, or perform
direct disk sector writes.  Direct  sector  writes  are	 not
permitted  (see	 notes)	under UNSPOOL. Warmboot	requests and
direct console input are handled as described below.

	 The address of	the old	BIOS vector table, the	BDOS
entry  address,	 and the CCP return address (from the top of
the stack on entry) are	saved in memory.

	 The  "dev"  parameter	from  the  command  line  is
checked. If not	valid, an error	message	is typed and control
returns	to the CCP.

	 If  the  "dev"	 parameter  is	the literal OFF, the
program	 executes  a  BDOS  funcion  0	(System	 Reset)	 and
terminates.


Revised	81-12-06			Page 2 of 6

_______________________________________________________________


	  Documentation	for UNSPOOL Version 3.1



	 The  file  named  in the command line is opened for
input. If not present, the command is echoed to	the  console
followed by a "?" and control returns to CCP.

	 If  the  drive	is not explicit, the current default
drive number is	recorded  internally  in  case	the  default
drive is changed while UNSPOOL is active.

	 The  current  user  number  and  IOBYTE  values are
checked	and stored internally so that if the user number  is
changed,  UNSPOOL will still be	able to	read the input file.
If the device is changed (using	STAT LST:=TTY: for  example)
unspool	 will  continue	to use the physical device in effect
at the time  the  program  was	initiated.  Any	 application
programs  will,	 however,  use	the  new  values of the	user
number and the new physical device assignments.

	 If no errors  were  detected,	the  active  program
segment	 which	monitors all calls to BDOS is relocated	into
high memory just below the CCP.	This reduces  the  available
user program area by 3 K: 4 pages for the UNSPOOL supervisor
segment,   and	8  pages  for  the  CCP	 which	is  commonly
overwritten by user program buffers. The BOOT and BDOS jumps
in low memory are modified to protect the  CCP	and  UNSPOOL
supervisor segment.

	 Control  is  then  returned  to the console. Normal
CP/M operation will then be  possible.	Characters  will  be
sent  from  the	input file to the output device	whenever the
console	is idle.

	 Whenever an application program or the	CCP requests
console	input using BDOS functions 1 or	10, or a direct	call
into the  jump	table  at  A(BOOT + 1) + 6,  the  supervisor
segment	 intercepts  these requests and	checks to see if the
console	is idle. If it is, characters are  transferred	from
the  input  file  to  the  output  device  until the console
becomes	ready, i.e. a key is actually pressed. At that	time
the  BDOS  function  or	 BIOS call is executed normally, and
control	returns	to the application program.

	 If a jump  to	BOOT  is  attempted,  this  is	also
intercepted  by	 the UNSPOOL supervisor	segment. The message
"Unspooling in progress" is displayed on the console, and no
actual	boot  takes  place.  Control  is  returned  to	 the
protected  copy	of the CCP instead. Before returning, a	disk
reset is performed and the default DMA address is  reset  to
0080H to simulate a true warm-boot as closely as possible.

	 If warmboot is	attempted using	BDOS function 0, the
program	 will prompt the operator with the option to cancel.
If the response	is "Y",	warmboot  is  performed	 using	BDOS
function 0 as requested. Otherwise the request is handled as
with normal warmboot, above.



Revised	81-12-06			Page 3 of 6

_______________________________________________________________


	  Documentation	for UNSPOOL Version 3.1


	 If  a direct BIOS call	to write a sector to disk is
attempted,  UNSPOOL  will  display  the	  message   "Invalid
operation  attempted  under  UNSPOOL.  Program aborted." The
application program will be  terminated,  but  UNSPOOL	will
continue  to run. (See Notes.) This restriction	applies	only
to direct BIOS writes. All normal file-oriented	(BDOS) reads
and writes are fully supported under UNSPOOL.

	 When the input	file is	completely transferred,	or a
1AH  end-of-file  character  is	 detected,  the	  supervisor
becomes	 inactive,  and	 passes	 on  previously	 intercepted
requests immediately, without checking console	status.	 The
sole  exception	to this	is that	direct BIOS writes are still
not permitted until the	next warmboot.
  When	the  next  warm-boot  request	is   detected,	 the
supervisor  removes  itself  from memory by executing a	true
warm-boot,  and	 informs  the  operator	 with  the   message
"UNSPOOL completed.".

NOTES:

	 While	UNSPOOL	 makes	every  effort to restore the
values of the DMA address, USER	number,	IOBYTE,	and  default
disk  drive  before  returning	control	 to  the  program, a
hardware reset may leave these	values	in  an	undetermined
state if unspooling was	actually taking	place at the time.

	 When  function	 10,  Read  Console  Buffer is used,
UNSPOOL	will transfer characters only until the	first key is
pressed. At that time, no  characters  will  be	 transferred
until  the  input  line	 is completed by pressing a carriage
return.

	 UNSPOOL requires that the List	Status	function  in
the  BIOS  was	properly  implemented at system	installation
time. UNSPOOL will not send characters to  the	LST:  device
unless	it  recieves  a	ready condition	from the List Status
routine. If the	PUN: device is	used,  no  status  check  is
provided  for by CP/M, so a not-ready condition	on the punch
may cause the system to	hang up	if PUN was specified on	 the
command	line. See the CP/M Alteration Guide for	a discussion
of the BIOS List Status	routine.

	 Although  the	console	 is polled frequently during
the unspooling of the file, some of the	diskette  operations
may take a second or two to complete, for example when a new
extent	is  opened.  Since  the	console	is not polled during
this period,  high  speed  typing  may	cause  one  or	more
characters  to be lost.	This effect will vary depending	upon
the program being run, the types of input reqests (character
or line) it uses, and the relative locations on	disk of	 the
spool file and any files in use	by the program.	As a result,
heads-down  typing  is	not  reccommended  while  UNSPOOL is
running. Some experience with UNSPOOL will  teach  the	user
when caution is	required.



Revised	81-12-06			Page 4 of 6

_______________________________________________________________


	  Documentation	for UNSPOOL Version 3.1


	 Although  it  would  be  possible to perform direct
BIOS writes  while  unspool  is	 active,  (indeed  this	 was
permitted  in  earlier	versions) this action is now trapped
and prohibited.	The reason this	was deemed necessary is	that
some existing software,	for example DU.COM, uses direct	BIOS
writes in a manner which could cause a major system crash if
allowed	under UNSPOOL.

	 The problem arises when a program  calls  the	BIOS
directly  (it is actually calling UNSPOOL's copy of the	BIOS
table) to select the drive, set	the track  and	sector,	 and
perform	 direct	 disk  I/O  without going through the normal
CP/M file handling system. This	causes	no  problem  if	 the
selecting, addressing, and I/O are all done together, but if
a console input	is done	between	the time the disk address is
set and	the call to read or write a sector, the	disk address
may  no	 longer	 be valid. This	could cause the	sector to be
written	 to  the  wrong	 disk  address,	 or  even  over	 the
directory.

	 This is true because a	request	for console input is
taken	by   UNSPOOL  as  an  opportunity  perform  its	 own
functions, which themselves include disk I/O. Although	this
problem	 could	be eliminated by insuring that console input
is not allowed to intervene between disk addressing and	disk
I/O, it	is not in the author's power to	rewrite	all existing
applications software. This better-safe-than-sorry trap	 was
therefore included.

	 Note  that direct reads are NOT trapped, since	they
do not have the	same potential for disaster, but  still	 may
be   unreliable	 for  the  same	 reasons.  It  is  therefore
recommended that software using	direct disk I/O	not  be	 run
under  UNSPOOL.	 Normal	 CP/M file-oriented (BDOS) reads and
writes always  re-select  and  re-address  the	disk  before
reading	or writing a sector, so	no similar problem exists in
the  vast  majority  of	 software which	uses the normal	CP/M
file handling system.

INSTALLATION:

	 The source file is written for	 assembly  with	 the
MAC  assembler.	 The  .HEX file	produced is LOADed to a	.COM
file and executed just as any normal program. Relocation  is
done at	execution time as described above.

	 If  the  assembly option EXPAND is set	to TRUE, tab
characters in the input	file will be expanded to spaces	with
assumed	tab stops  at  every  eighth  print  position.	This
option	should	be set to FALSE	if the printer driver or the
printer	itself can properly handle the tab character. If the
option PHYSBS is set to	TRUE,  a  backspace  character	will
cause  the  tab	 expansion  algorithm to recognize backspace
characters and decrement the column count when	a  backspace
is  encountered	in the input file. This	option should be set
to FALSE if backspace characters are ignored by	the printer.


Revised	81-12-06			Page 5 of 6

_______________________________________________________________


	  Documentation	for UNSPOOL Version 3.1


All other control codes	except carriage	return	are  assumed
to be non- printing, and are ignored by	the algorithm.

	 If tab	expansion is included, the version number in
the signon message will	be followed by "/T".

		      Gary Novosielski



















































Revised	81-12-06			Page 6 of 6

_______________________________________________________________