******************************************************************************
*          Copyright (C) 1984, 1985 - AMPRO Computers, Incorporated          *
*                                                                            *
*                                   NOTICE                                   *
*                                   ------                                   *
*                                                                            *
* Thió informatioî ió beinç madå availablå foò useró oæ AMPRÏ productó anä   *
* foò use with the program, LB-MON.COM.  No other use is authorized.         *
******************************************************************************

                             AMPRO EPROM MONITOR

                                 USER'S GUIDE



INTRODUCTION

Thió  documenô ió intendeä foò thoså whï arå familiaò witè smalì microcomputeò �
systemó  anä microprocessors®   Includeä arå descriptionó oæ eacè commanä witè �
examples¬  anä terminaì configuratioî information®   Thió monitoò ió  intendeä �
foò  primitivå  accesó  tï thå Z80Á  microprocessor¬  I/O¬  memory¬  anä  disë �
devices.


TERMINAL CONFIGURATION

Thå  AMPRÏ  EPROÍ  Monitoò  ió  designeä tï executå  witè  á  terminaì  devicå �
connecteä  tï  Seriaì Porô Á oæ thå AMPRÏ Littlå Boarä computeò  oò  aî  AMPRÏ �
Serieó 10° computeò system®   Sincå thå Monitoò initializeó alì systeí values¬ �
thå followinç seriaì terminaì parameteró musô bå preset.

                  Baud Rate:  9600
                  Bits:          8
                  Stop bits:     1
                  Parity:     none
                  Handshake:  no

Foò  detailó  oî  thå  Littlå Boarä oò Serieó  10°  computers¬  refeò  tï  thå �
appropriate user's manual.



MONITOR OPERATION

Entrù  tï thå Monitoò ió througè power-oî oò thå RESEÔ switch®   Aô  RESEÔ  oò �
power-up¬  thå Monitoò ió relocateä iî RAÍ beginninç aô 8000H®  Iæ nï bootablå �
disë  ió iî drivå A¬  thå Monitoò ió agaiî relocateä tï F000H¬  anä wilì begiî �
execution®   Iæ  onå oò morå disë driveó arå connecteä tï thå system¬  dï  noô �
inserô á bootablå disë iî drivå Á iæ yoõ wisè tï enteò thå Monitor®   However¬ �
whilå thå Monitoò prograí ió running¬ diskó caî bå reaä oò writteî á sectoò aô �
á  time®   Also¬  bootinç  thå operatinç systeí caî bå performeä froí drivå  Á �
usinç eitheò á Monitoò commanä (B© oò CTRL-Ã.
ŠEacè command¬  oò commanä witè trailinç parameters¬  musô bå terminateä witè á �
carriagå returî (RETURN)®   Iî thå followinç examples¬ thå RETURÎ keù wilì noô �
bå shown¬  thougè nothinç wilì happeî withouô enterinç RETURN®

Logicaì disë tracë anä sectoò valueó arå useä bù thå Monitoò foò disë  access® �
Physicaì tracë anä sectoò numberó arå thå actuaì tracë anä sectoò locationó oî �
aî AMPRO-formatteä disk®  

Foò  single-sideä  disks¬  logicaì  track/sectoò numberó arå thå samå  aó  thå �
physicaì track/sectoò numbers®   However¬  oî double-sideä disks¬ thå physicaì �
track/sectoò numberó arå differenô froí thå logicaì values:
48 tpi, double-sided disks (40 tracks/side): 

     Logicaì  trackó arå numbereä froí 00È througè 4FH¬  even-numbereä  trackó �
     oî  sidå  0¬  anä  odd-numbereä trackó oî sidå 1®   Physicaì  trackó  arå �
     numbereä from 00È througè 27È oî eacè side.

     Logicaì sectoró arå numbereä froí 01È througè 0AH¬  eacè side®   Physicaì �
     sectoró arå numbered froí 11È througè 1AH¬ eacè side.

96 tpi, double-sided disks (80 tracks/side):

     Logicaì trackó arå numbereä froí 00È througè 9FH¬ even-numbereä trackó oî �
     sidå  0¬  anä  odd-numbereä trackó oî sidå 1®   Physicaì trackó  arå  00È �
     througè 4FÈ oî eacè side.

     Logicaì sectoró arå numbereä froí 01È througè 05H¬  eacè side®   Physicaì �
     sectoró arå numbered froí 11È througè 15H¬ eacè side.

Tableó  A-±  througè  A-´ iî Appendiø Á lisô thå  physicaì  tracë  anä  sectoò �
locations for both single- and double-sided AMPRO-formatted disks.



MONITOR COMMANDS

Followinç arå descriptionó oæ eacè command¬  requireä parameters¬  iæ any¬ anä �
exampleó oæ eacè command®  Iî thå followinç descriptions¬ paù attentioî tï thå �
spaceó  oò  lacë oæ spaceó betweeî parameters®   Somå commoî featureó  oæ  thå �
Monitor:

     o CTRL-S is used to stop or start a console display

     o CTRL-X is used to exit a function in progress

     o All numerical parameters require hexadecimal values

     o Address parameters can contain 1 to 4 digits, while byte 
       parameters can contain 1 or 2 digits.


Tablå 1¬ whicè follows¬ listó alì oæ thå Monitoò commands®  Specifiã �
descriptions of each command follow.

Š
 
                    Table 1.  AMPRO EPROM Monitor Commands
            .                   .                                  .     
                   Command              Command Syntax
            .                   .                                  .     
               Ascii Load, Dump    A[L, D OR S][from] [until]
                  or Search
               Boot system         B
               Call subroutine     C[addr]
               Dump memory         D[from] [until]
               Exchange byte       E[from] [until] [byte] [with]
               Fill memory         F[from] [until] [hex]
                                   F[from] [until] '[ascii]
               Go anywhere         G[addr]
               Hex math            H[1st hex] [2nd hex]
               Input from port     I[port number]
               Load memory         L[addr]
               Move memory         M[from] [until] [to]
               Output to port      O[port number] [byte]
               Read disk           R[addr] [drv] [trk] [sec]
               Search for byte     S[from] [until] [byte1] [byte2]
               Command table       T
               Compare memory      V[from] [unitl] [with]
               Write disk          W[addr] [drv] [trk] [sec]
               Display stack       X
            .                   .                                  .     




ASCII Load, Dump, or Search

Syntax:   A[L, D or S][from] [until]

Permitó  loadinç  memorù witè á strinç oæ ASCIÉ characters¬  displayinç  ASCIÉ �
characteò  stringó  iî  memory¬  oò searchinç foò  á  particulaò  sequencå  oæ �
characters®   Foò thå Loaä function¬ thå [untilÝ parameteò ió optional®  Entrù �
oæ ASCIÉ characteró wilì continuå untiì á CTRL-Ø.

     AD1000 2000         Displays ASCII strings at memory locations from
                         1000H through 2000H.

     AL1000 1040         Begins storing ASCII characters from the console 
                         into memory beginning at 1000H until 1040H (64 
                         bytes).

     AS1000 1040 T       Searches for the ASCII character "T", and dis-
                         plays the address of the first occurence.





Š
BOOT the system

Syntax:   B

Witè  á  systeí  disë iî drivå A¬  typinç Â followeä bù RETURÎ wilì  booô  thå �
operating system.  Entering a CTRL-C will also start the boot operation.




CALL a subroutine

Syntax:   C[addr]

Permitó callinç á subroutinå bù enterinç Ã followeä bù aî addresó value®  Upoî �
returninç froí thå subroutine¬  thå Monitoò wilì bå iî thå commanä mode®   Foò �
example¬  tï seô á breakpoint¬ inserô thå heø codå foò á REÔ instructioî (C9H© �
aô  thå  desireä breakpoinô addresó usinç thå Ì  command®   Wheî  thå  prograí �
reacheó thå  breakpoinô address¬  prograí executioî wilì cease¬  anä returî tï �
thå Monitoò commanä mode.

     C10F0               Executes a subroutine at address 10F0H, then
                         returns to the command mode.
DUMP Memory Contents

Syntax:   D[from] [until]

Thå contentó oæ memorù beginninç aô [fromÝ througè thå [untilÝ addresó wilì bå �
displayeä  oî  thå  console®�

     D0100 01FF          Displays contents of memory from 0100H through
                         01FFH as hexadecimal values plus any printable
                         ASCII characters.


EXCHANGE byte

Syntax:   E[from] [until] [byte] [with]


Memorù  byteó  beginninç aô [fromÝ througè [untilÝ witè thå valuå [byteÝ  wilì �
becomå thå ne÷ valuå [with]®  Onlù thoså byteó matchinç [byteÝ wilì change.

     E1000 1FFF 55 AA    Stores AAH in all memory locations from 1000H
                         until 1FFFH that contain 55H.








Š
FILL Memory

Syntax:   F[from] [until] [hex]
          F[from] [until] '[ascii]

Filì memorù beginninç aô [fromÝ througè [untilÝ witè thå hexadecimaì valuå  oæ �
[hexÝ  oò  thå  ASCIÉ  character®�

     F1000 1FFF 55       Store 55H in all memory locations from 1000H
                         through 1FFFH.

     F1000 1FFF 'S       Store an ASCII S in all memory locations from
                         1000H through 1FFFH.



GO anywhere

Syntax:   G[addr]

Executås á prograí beginninç aô [addr].�

     G0100               Jump to address 0100H, and execute a program.

     GF000               Jump to the Monitor entry point (restart the
                         Monitor program).


HEX math + -

Syntax:   H[1st hex] [2nd hex]

Performó  subtractioî  anä  additioî  oæ twï onå  tï  fouò  digiô  hexadecimaì �
numbers®  Thå resultó arå displayeä aó follows.

     H1000 2000          Displays sum and difference of the two numbers:
                         1000H +/- 2000H = 3000H and F000H.

     H2000 1000          Displays sum and difference of the two numbers:
                         2000H +/- 1000H = 3000H and 1000H.



INPUT from port

Syntax:   I[port number]

Readó thå contentó oæ thå I/Ï porô aô thå [porô numberÝ address¬  anä displayó �
thå valuå oî thå console®   Botè thå hexadecimaì valuå anä binarù valuå oæ thå �
I/Ï porô arå displayed.

     I84            Input and display the byte at I/O port 84H.  Display
                    is in both hexadecimal and binary forms.
Š

LOAD Memory

Syntax:   L[addr]

Permitó changinç thå valuå oæ á bytå aô locatioî [addr]®   Tï exiô bacë tï thå �
Monitoò  commanä  mode¬  enteò á CTRL-X®   Entrù oæ ASCIÉ  characteró  withouô �
precedinç  singlå  quotå oò ouô oæ thå rangå Á - Æ foò heø  digitó  wilì  alsï �
causå aî exiô froí thå Loaä function.

     L0100               Begin entry of hex or ASCII characters at address
                         0100H.



MOVE Memory

Syntax:   M[from] [until] [to]

Moveó  thå  contentó oæ memorù beginninç aô [fromÝ througè [untilÝ  tï  á  ne÷ �
memorù locatioî beginninç aô [to]®�

     M1000 1FFF 3000     Move memory contents from 1000H through 1FFFH
                         to an area of memory beginning at 3000H (through
                         3FFFH).  



OUTPUT to Port

Syntax:   O[port number] [byte]

Writes contents of [byte] to I/O port [port number].

     O84 10              The value of 10H is written to I/O port 84H.


















Š
READ Disk Sector

Syntax:   R[addr] [drv] [trk] [sec]

Readó  onå  sectoò froí thå specifieä drive¬  track¬  anä sectoò  intï  memorù �
beginninç aô [addr]®   Driveó arå specifieä bù numberó froí ° througè ³ (drivå �
Á througè D)®  Trackó arå specifieä iî thå followinç manner:

                     48 tpi, single-sided: Tracks 0 - 27H
                     48 tpi, double-sided: Tracks 0 - 4FH
                     96 tpi, single-sided: Tracks 0 - 4FH
                     96 tpi, double-sided: Tracks 0 - 9FH

Sectoró  arå numbereä froí 01È througè 1AÈ (48tpé disks)¬  oò 01È througè  05È �
(9¶ tpé disks).

     R1000 0 1 1         Read one sector from drive A, track 01H, sector 01H,
                         into memory beginning at 1000H. 

     R100 1 4F A         Reaä onå sectoò froí drivå B¬ tracë 4FH¬ sectoò 0AÈ 
                         (10)¬ intï memorù beginninç aô 0100H.




SEARCH for Byte

Syntax:   S[from] [until] [byte1] [byte2]

Searcè  foò  á onå oò twï bytå sequencå iî memorù beginninç aô [fromÝ  througè �
[until]®  Onå oò twï byteó caî bå specified¬ anä musô bå separateä bù á space.

     S1000 1FFF E5       Searcè memorù froí  1000È througè 1FFFÈ foò anù byteó �
                         containinç  E5H¬  anä  displaù addresseó iæ  anù  arå �
                         found.

     S1000 1FFF E5 E6    Searcè memorù froí 1000È througè 1FFFÈ foò á two-bytå �
                         patterî  containinç  Eµ  anä  E¶  iî  thå   specifieä �
                         sequence.  Display addresses of those that are found.





COMMAND Table

Syntax:   T

Displays a list of Monitor commands and parameters at the console.




Š

COMPARE Memory

Syntax:   V[from] [until] [with]

Compareó  thå contentó oæ memorù beginninç aô [fromÝ througè [untilÝ witè  thå �
contentó  oæ  á  seconä  blocë oæ memorù  beginninç  aô  [with]®   Onlù  thoså �
addresseó wherå á matcè ió noô founä arå displayeä aô thå console®  Nothinç ió �
displayeä wherå á matcè occurs® 

     V1000 3FFF 4000     Compareó  thå contentó oæ memorù froí  1000È  througè �
                         3FFFÈ  witè  thå memorù contentó froí  4000È  througè �
                         7FFFH.



WRITE to Disk Sector

Syntax:   W[addr] [drv] [trk] [sec]

Writeó  onå  sectoò  tï thå specifieä drive¬  track¬  anä sectoò  froí  memorù �
beginninç aô [addr]®  Drive¬ track¬ anä sectoò parameteró arå specifieä iî thå �
samå waù aó thå REAÄ Disë Sectoò command® 

     W1000 0 1 1         Write one sector to drive A, track 1H, sector 1H,
                         from memory beginning at 1000H. 

     W100 1 4F A         Write one sector to drive B, track 4FH (79) sector 
                         0AH (10), from memory beginning at 0100H.



Display STACK

Syntax:   X

Displays the four digit hexadecimal value of the Stack Pointer.
















Š                                  Appendix A
                       Physical Track and Sector Tables

Thå followinç tableó lisô thå physicaì tracë anä sectoò organizatioî oæ AMPRO-�
formatteä  disks®   Foò  single-sideä disks¬  logicaì anä physicaì  tracë  anä �
sectoò numberinç ió identical.
 

            Table A-1.  48 tpi Single-Sided, Physical Disk Format
                 .        .                                .
                    Track               Sector
                 .        .                                . 
                     00     01  02  03  . . . 08  09  0A
                     01     01  02  03  . . . 08  09  0A
                     02     01  02  03  . . . 08  09  0A
                     .      .   .   .         .   .   .
                     .      .   .   .         .   .   .
                     25     01  02  03  . . . 08  09  0A
                     26     01  02  03  . . . 08  09  0A
                     27     01  02  03  . . . 08  09  0A
                 .        .                                .

            Table A-2.  96 tpi Single-Sided, Physical Disk Format
                     .        .                         .
                        Track            Sector
                     .        .                         . 
                         00        01  02  03  04  05 
                         01        01  02  03  04  05 
                         02        01  02  03  04  05 
                         .         .   .   .   .   .
                         .         .   .   .   .   .
                         4D        01  02  03  04  05 
                         4E        01  02  03  04  05 
                         4F        01  02  03  04  05 
                     .        .                         .

             Table A-3.  48 tpi Double-Sided Physical Disk Format
  .                                   .                                   .
                 Side 0                              Side 1
  .        .                          .        .                          .
     Track            Sector             Track            Sector           
  .        .                          .        .                          .
      00     11 12 13 . . . 18 19 1A      00     11 12 13 . . . 18 19 1A   
      01     11 12 13 . . . 18 19 1A      01     11 12 13 . . . 18 19 1A   
      02     11 12 13 . . . 18 19 1A      02     11 12 13 . . . 18 19 1A   
      .      .  .  .        .  .  .       .      .  .  .        .  .  .    
      .      .  .  .        .  .  .       .      .  .  .        .  .  .
      25     11 12 13 . . . 18 19 1A      25     11 12 13 . . . 18 19 1A   
      26     11 12 13 . . . 18 19 1A      26     11 12 13 . . . 18 19 1A   
      27     11 12 13 . . . 18 19 1A      27     11 12 13 . . . 18 19 1A   
  .        .                          .        .                          .
    Logicaì  trackó  arå  numbereä 00È througè 4FH¬  witè  eveî  numbereä �
    trackó oî sidå 0¬ anä odä numbereä trackó oî sidå 1®  Logicaì sectoró �
    arå numbereä 00È througè 0AH.
Š

  .                                                                       .
             Table A-4.  96 tpi Double-Sided Physical Disk Format
           .                          .                          .
                      Side 0                     Side 1
           .        .                 .        .                 .
              Track        Sector        Track       Sector           
           .        .                 .        .                 .
               00     11 12 13 14 15      00     11 12 13 14 15  
               01     11 12 13 14 15      01     11 12 13 14 15   
               02     11 12 13 14 15      02     11 12 13 14 15   
               .      .  .  .  .  .       .      .  .  .  .  .             
               .      .  .  .  .  .       .      .  .  .  .  .
               4D     11 12 13 14 15      4D     11 12 13 14 15   
               4E     11 12 13 14 15      4E     11 12 13 14 15
               4F     11 12 13 14 15      4F     11 12 13 14 15
           .        .                 .        .                 .
             Logicaì  trackó arå numbereä 00È througè  9FH¬  witè �
             eveî  numbereä  trackó oî sidå 0¬  anä odä  numbereä �
             trackó oî sidå 1®   Logicaì sectoró arå numbereä 00È �
             througè 05H.
           .                                                     .