THE CURSOR CHARACTER IN EDIT IS CURRENTLY AN
FF WHICH MAY NOT PRINT ON YOUR CRT. THIS CHARACTER
IS LOCATED AT 105H AND MAY BE CHANGED TO
SUIT YOUR SYSTEM. 
 
THE EDIT CURSOR BACKSPACE CHARACTER, CURRENTLY 08, IS
LOCATED AT 104H AND CAN ALSO BE CHANGED TO SUIT YOUR
REQUIREMENTS.
 
AFTER MAKING THESE CHANGES RE-BOOT AND SAVE 14 BLOCKS.
 
 
THE DELETE TO START OF LINE CHARACTER IS CONTROL/Z.
 
 
 
THE VARIOUS VERSIONS OF DEBUG
HAVE BEEN CHANGED SO THAT THE 
Z-80 INDEX REGISTERS CAN BE DISPLAYED
BY CHANGING A SINGLE BYTE IN EACH
VERSION:
 
DEBUG:57EH
LINKBUG:499H
COMBUG:53BH
HEXBUG:5B1H
 
IN EACH CASE THE BYTE IS TO
BE CHANGED FROM 6 TO 8 TO DISPLAY
THE INDEX REGISTERS. 
 
IN EACH CASE REBOOT AND SAVE 25 AFTER MAKING THE
ABOVE CHANGE.
 
THE EXIT FROM THESE PROGRAMS BACK TO CP/M IS VIA G0, 
WHICH BRANCHES TO THE WARM BOOT ENTRY AT 0. 
 

 
MAKRO:A NEW PSEUDO-OP MLAST HAS BEEN ADDED WHICH DIRECTS
THE ASSEMBLER TO SEARCH FOR A MACRO AFTER SEARCHING
THROUGH THE STANDARD OP-CODES. FOR PROGRAMS WHICH DO
NOT USE MACROS TO REDEFINE EXISTING OP-CODES THE
MLAST OP-CODE WILL SPEED THE ASSEMBLY.
THIS DISK CONTAINS THE XREF CROSS REFERENCE GENERATOR. IT
IS INVOKED AS:
 
XREF  FILESPEC     WHERE FILESPEC IS A VALID DESIGNATION
                   FOR AN EXISTING .PRN FILE, PREVIOUSLY
                   CREATED BY THE MAKRO ASSEMBLER.
 

THE OUTPUT CAN BE SENT TO YOUR PRINTER BY CONTROL-P.
 
THE DISPLAYED SYMBOL REFERENCES ARE PRECEDED BY AN =
IF THE SYMBOL IS DEFINED BY AN EQU OR SET, OR BY AN @
IF THE SYMBOL APPEARS IN THE LABEL FIELD OF THE INSTRUCTION.
THE MACRO ASSEMBLER NOW INCLUDES A CROSS REFERENCE
CAPABILITY AND SUPPORTS A SOURCE FILE "INCLUDE" OPERATION.
THE FORM OF THE INCLUDE OPERATION IS:
 
     NCLUD U:FILE
 
WHERE U IS A VALID DRIVE AND FILE IS THE NAME OF A TYPE
.ASM FILE. THE INCLUDE OPERATION MAY NOT BE NESTED, ELSE
AN "F" ERROR WILL RESULT. THE INCLUDE DIFFERS FROM THE
LINK IN THAT THE INCLUDE IS ACTED UPON IMMEDIATELY,
AS IN A "CALL", THE ORIGINAL SOURCE FILE BEING RESUMED
UPON COMPLETION OF THE INCLUSION. THE NCLUD STATEMENT IS
USED TO INTRODUCE A SUITE OF MACRO DEFINITIONS BEFORE
THEY ARE USED IN THE MAIN SOURCE FILE.
 
ON. THE NCLUD STATEMENT IS
USED TO INTRODUCE A SUITE OF MACRO DEFI