\                    MD-11 log                        14dec83tvm
S/N #00036 :    No HD boot                                      
replaced outdated chips with current revisions                  
S/N #00027 :    No HD or FL boot                                
open traces on reverse side of U75                              
S/N #00022 :    Won't read format on HD                         
pin #3 U49 shorted to pin #13 U53 on top side of PCB            
S/N #00001 :    No HD or FL boot                                
IC's U19 and U56 defective ; solder splashes on back of PCB     
S/N #00023 :    No HD or FL boot                                
IC U56 defective ; open trace on back of PCB                    
S/N #00013 :    Won't read HD format                            
IC U56 defective                                                
S/N #00003 :    No HD response at all                           
IC's U56, U19 defective                                         
S/N #00026 :    Won't boot FL or HD                             
solder splashes on back side of PCB                             
S/N #00034 :    No response at all                              
short under U38 between pin #3 U40 and pin #3 U39               
open trace from pin #20 U26 and pin #6 U2                       
S/N #00001 : won't verify HD format                             
C30 shorted                                                     
repaired 5 un-serialized boards  (mostly IC's U56 and U74)      
S/N #--- : no HD verify                                         
U56 defective                                                   
S/N #00003 : no HD verify                                       
U74 bad                                                         
S/N #00061 : no FL verify                                       
U85 defective                                                   
S/N #00106 : no FL verify                                       
U85 defective                                                   
S/N #00082 : no HD response                                     
U74 defective                                                   
S/N #00027 : no HD format                                       
U74 defective                                                   
S/N #00036 :                                                    
replaced outdated IC's with current revisions                   
S/N #00027 : no HD format                                       
U74 defective                                                   
S/N #00082 : no HD or FL boot                                   
U92 missing                                                     
S/N #00136 : printer port out    ( r.j )                        
pin #11 U8 shorted to ground                                    
S/N #00060 : no CRT response                                    
repaired numerous shorts on and around J3                       
S/N #R-2 : won't format HD                                      
Two bent pins, R28 missing, RP5 wrong type and value            
S/N #R-3 : won't format HD                                      
RP5 wrong type and value                                        
S/N #R-4 : won't format HD                                      
RP5 wrong type and value                                        
S/N #R-5 : won't format HD                                      
RP5 wrong type and value                                        
S/N #R-1 : seek error on HD                                     
seek complete line shorted low                                  
S/N #R-6 : won't format HD                                      
three bent pins, RP5 wrong type and value                       
S/N #00057 : won't boot HD                                      
several solder splashes on back of PCB                          
R/O #xxx-TM (w/o#xxxxx) s/n #xxxxx :                            
R/O #211-TM (w/o#30527) s/n #02306 : HD: data not found -->     
U94 defective                                                   
R/O #212-TM (w/o#20122) s/n #01779 : no HD verify --> updated   
R/O #213-TM (w/o#40014) s/n #02294 : no HD verify --> U94 bad   
R/O #135-TM (w/o#20122) s/n #01144 : data error on HD -->       
updated - OK                                                    
R/O #223-TM (w/o#20122) s/n #01499 : no sign-on -->             
U67 defective (RESET* line)                                     
R/O #201-TM (w/o#20119) : won't boot FL --> tests OK            
R/O #196-TM (w/o#20119) : PIP verify error --> tests OK         
R/O #214-TM (w/o#20122) s/n #02085 : data err on A: --> updated 
R/O #215-TM (w/o#20122) s/n #02079 : data not found A: -->      
updated - OK                                                    
R/O #147-TM (w/o#20122) s/n #01100 : no HD verify --> updated   
R/O #216-TM (w/o#20122) s/n #01121 : intermittent sign-on -->   
U6 - defective socket; U56 defective                            
R/O #217-TM (w/o#20122) s/n #01957 : no HD verify --> updated   
R/O #218-TM (w/o#20122) s/n #02091 : no sign-on -->             
missing slide jumper on J6; intermittently resets -->           
LOW VCC* line intermittently shorted to ground (solder splash)  
R/O #219-TM (w/o#20122) s/n #02070 : data error on HD -->       
U94 defective; U67 defective                                    
R/O #220-TM (w/o#20122) s/n #02115 : data err on B: --> U65 bad 
R/O #221-TM (w/o#20122) s/n # 01877 : no HD verify --> C29 bad  
R/O #222-TM (w/o#20122) s/n #02015 : no HD verify --> U94 bad   
R/O #224-TM (w/o#20122) s/n #02075 : no HD verify --> U94 bad   
R/O #225-TM (w/o#20124) s/n #02021 : no HD verify --> tests OK  
R/O #226-TM (w/o#20125) : intermittent sign-on -->              
FINDEX* line shorted to something -- cut and jumpered           
R/O #227-TM (w/o#20125) : won't boot FL --> U74 pin #15 bent    
R/O #228-TM (w/o#20125) : won't format --> tests OK             
R/O #229-TM (w/o#20125) : no HD verify --> U94 bad              
R/O #230-TM (w/o#20125) : no HD verify --> 10MHz XTAL bad       
R/O #231-TM (w/o#20125) s/n #02251 : no HD verify --> tests OK  
R/O #232-TM (w/o#20124) s/n #02382 : no HD verify --> tests OK  
R/O #233-TM (w/o#20125) : no HD verify --> U94 defective        
R/O #234-TM (w/o#20125) : no sign-on -->                        
DATA 5 line open between U3 and U6                              
R/O #235-TM (w/o#20125) : ram memory error --> Tests OK         
R/O #236-TM (w/o#20124) s/n #02211 : tests OK                   
R/O #237-TM (w/o#20124) s/n #02255 : tests OK                   
R/O #115-TM (w/o#20124) s/n #02339 : U94 bad                    
R/O #238-TM (w/o#20124) s/n # 02334 : no sign-on --> tests OK   
R/O #239-TM (w/o#20124) s/n #02133 : no HD verify --> U94 bad   
R/O #240-TM (w/o#20125) : no HD verify --> U94 defective        
R/O #241-TM (w/o#20124) s/n #02000 : tests OK                   
R/O #242-TM (w/o#20124) s/n #02401 : resets itself (PIP) -->    
Z80 bad; U50, U67 out of spec -- bad TTL low level              
R/O #243-TM (w/o#20124) s/n #02358 : won't verify --> U67 bad   
R/O #244-TM (w/o#20124) s/n #02200 : no HD verify --> tests OK  
R/O #245-TM (w/o#20083) : crashes during PIP (not ready) -->    
U52 defective                                                   
R/O #194-TM (w/o#20119) : error on HD --> U92 intermittent      
R/O #204-TM (w/o#20122) s/n #02055 : data not found B: -->      
U94 defective                                                   
R/O #246-TM (w/o#20122) s/n #00516 : no sign-on -->             
U8 shorted internally and destroyed 2 tantalum caps with it     
R/O #247-TM (w/o#20122) : no sign-on --> U73 stuffed backwards