EPROM


	- check a bit for monitor active flag
	  if monitor active is true 		->  long call monitor


	  else

		stuff a long return vector into location for INT2
		(absolute location 8) which initializes the NMI
		call.  This vector points to code:

			-> load the sp from 20000 - constant
				(to get a new register save area)

			-> swap register halves and push (for 68K inversion)

			-> halt


		** processor is now idle awaiting another nmi **






system call:


		INT21			; go to location 084h
		JMP	>6000		; yet to be determined
		MOVE STACK 20000H
		PUSHA
		SETINT
		HALT

	** WAITING FOR NMI **

	WHEN ONE COMES GO TO LOCATION 8 WHICH HAS A:

	RETI			;LONG RETURN FFROM INTERRUPT

	THIS LONG RETURN GOES TO CODE WHICH:

	POP A
	RETI




TRINITY SYSTEM MEMORY MAP:




FF0000 - FFFFFF			68000 MEMORY MAPPED I/O SPACE

FE0000 - FEFFFF			68451 MMU SPACE

FD0000 - FDFFFF			68000 EPROM SPACE

F00000 - FCFFFF			Z80 SLAVES

800000 - EFFFFF			80188 SLAVES
				 	
700000 - 7FFFFF			MEMORY MAPPED BIT GRAPHICS BOARD

080000 - 1FFFFF			MAXIMUM UNIX SYSTEM V SYSTEM RAM			

030000 - 07FFFF			UNIX SYSTEM RAM  (SYSTEMS WITH 512K)

000400 - 02FFFF			UNIX KERNEL

000000 - 0003FF			68000 INTERRUPT VECTORS






Z80 SLAVE MEMORY MAP:

F000 - FFFF			EMULATOR

0100 - EFFF			USER

0000 - 00FF			SYSTEM




80188 SLAVE MEMORY MAP:

FFE00 - FFFFF			EPROM

80000 - FFDFF			RESERVED FOR FUTURE EXPANSION / GRAPHICS

01600 - 7FFFF			USER RAM (512K SYSTEM)

00600 - 015FF			DOS EMULATOR

00500 - 005FF			MSDOS COMUNICATIONS AREA (ALA IBM)

00400 - 004FF			ROM COMMUNICATIONS AREA (ALA IBM)

00000 - 003FF			INTERRUPT VECTORS











6/12/84
BJG