Page 3 additions:

2. HDCA Operation in a standard environment:

Thå  HDCÁ  disë controlleò ió supplieä witè softwarå  makinç  itó �
integratioî  intï  aî existinç CP/Í systeí easy®   Thå  boarä  ió �
supplieä  witè cables¬  softwarå anä á diskette®   Iæ yoõ havå  á �
Morro÷ Designó systeí oò á Morro÷ Designó Floppù disë controller¬ �
thå  diskettå  supplieä  yoõ wilì booô uð directlù witè  alì  thå �
softwarå configureä foò thå Harä disë systeí yoõ havå  purchased®  �
Iæ  yoõ  arå  usinç anotheò branä oæ  floppù  controller¬  Morro÷ �
Designó  supplieó  á  diskettå witè assemblù languagå  harä  disë �
driveò  routineó whicè yoõ caî incorporatå intï youò CP/Í  Cbios®  �
Foò detailó oî thió refeò tï sectioî oî non-standarä environment®  �
Foò  thoså useró whicè arå tryinç tï incorporatå thå HDCÁ  systeí �
intï  aî  existinç CP/Í 2.² systeí anä havå nï  familiaritù  witè �
softwarå customization¬  Morro÷ Designó supplieó á diskettå foò á �
nominaì  feå calleä "Install"®   Thió prograí wilì  automaticallù �
instalì thå Morro÷ softwarå intï youò CP/Í 2.² Cbioó (seå sectioî �
on Install usage).


2.1 Switch settings 

Aó  shippeä  froí  thå factory¬  thå HDCÁ controlleò  ió  seô  tï �
responä tï porô adresseó 50è - 53h®   Alì Morro÷ softwarå assumeó �
thå  HDCÁ  controlleò  tï bå locateä  aô  theså  porô  addresses®  �
Switcè  aô  locatioî 8Ã ió useä foò porô adressinç anä ió seô  aó �
follows:



               ______________
               |            |
               |    ==1==   |           On
               |            |
               |    ==2==   |           Off
               |            |
               |    ==3==   |           On
               |            |
               |    ==4==   |           Off
               |            |
               |    ==5==   |           On
               |            |
               |    ==6==   |           On
               |            |
               |    ==7==   |           On
               |            |
               |    ==8==   |           On
               |            |
               --------------

               FACTORY SWITCH SETTINGS (PORT 50H)

Š
2.2 Jumpers

Iî  areá  1Ä oæ thå HDCÁ controlleò (aó vieweä  iî  figurå  ____© �
therå  arå twï jumpeò padó markeä Á anä B®   Aó shippeä froí  thå �
factorù  theså padó arå connecteä tï thå paä markeä  VI0®   Theså �
jumperó  arå  installeä sï aó tï tesô thå interrupô circuitry  on �
thå  board®   Mosô CP/Í baseä systemó dï noô uså  interruptó  anä �
theså  jumperó wilì havå nï effecô iæ lefô installeä (oò  removeä �
foò  thaô  matter)®   Useró whoså systemó uså  interruptó  shoulä �
refeò  tï thå sectioî oî operatinç iî á non-standarä  environmenô �
for details on these jumpers.


2.3  Inspection

Thå HDCÁ boarä shoulä bå examineä foò shippinç  damage®   Brieflù �
examinå thå boarä foò cracked¬  brokeî oò missinç components®  Iæ �
thå  boaarä  ió  founä tï bå defective¬  filå á claií  witè  youò �
carrieò  anä contacô Morro÷ Designó foò swifô replacemenô oæ  thå �
defective module.


2.4  Inserting the board

Graspinç thå boarä firmlù witè botè hands¬  istalì thå boarä intï �
thå S-10° buó aó showî iî figurå _____®   Pusè firmlù oî thå  toð �
of the board to insure it is properly seated.


2.5 Power-up

Applù  poweò  tï thå systeí anä observå boarä closelù tï bå  surå �
thaô  nï componentó arå becominç excessivlå  hot®   Poweò  systeí �
down.


2.6 Cable installation

Thå  HDCÁ  controlleò ió connecteä tï á M10¬  M2° oò  M2¶  systeí �
usinç  twï  ¶ fooô flaô cables®   Theså cableó arå supplieä  witè �
youò  system®   Thå 5° piî flaô cablå (wideò oæ thå two©  ió  thå �
controì  cablå responsiblå foò controllinç anä selectinç  drives®  �
Thå  controì  cablå  maù  bå daisù  chaineä  foò  multiplå  drivå �
configurationó (seå sectioî oî muilti-drivå configurations)®  Thå �
narroweò 2° piî cablå ió responsiblå foò transferrinç datá tï anä �
froí  thå  disë drivå durinç datá transfers®   Thå 5° p[iî  cablå �
shoulä bå connecteä witè thå reä stripå tï thå righô aó vieweä iî �
figurå _____®  Thå 2° piî cablå shoulä bå connecteä tï thå 2° piî �
headeò  adjacenô tï thå 5° piî connectoò witè reä stripå  tï  thå �
right as viewed in figure ______.

Thå  otheò  endó  oæ thå cableó shoulä bå connecteä tï  thå  disë �
drives as shown in figure ______.  
Š
NOTE:   Beforå  attemptinç tï uså anù Morro÷ Designó softwarå foò �
        thå  HDCÁ  systemó bå surå thå headó oæ  thå  driveó  arå �
        unlocked®   Iî thå caså oæ thå M26¬ thå spindlå locë musô �
        bå  removeä  beforå  poweò ió applied®   Afteò  poweò  ió �
        applied¬  thå heaä locë maù bå removed®   Thå M1° anä M2° �
        driveó shoulä bå powereä uð anä theî thå headó  unlocked®  �
        (seå figureó _______ß anä _______)®   Alsï notå thaô  thå 
        M2¶  drivå takeó aó lonç aó ² 1/² minuteó tï becomå readù �
        upoî power-up®  Thå M10/M2° driveó requirå oî thå averagå �
        oæ 4µ secondó tï becomå ready.


2.7 Formatting the Discus system

Thå  Discuó  systeí ió no÷ readù tï bå powereä up®   Firsô  applù �
poweò tï thå computeò anä reseô thå computer®   Nexô applù  poweò �
tï thå driveó observinç thå notå above®   No÷ brinç uð CPÍ 2.² oî �
youò  system®   Thå  systeí  diskettå includeä witè  youò  systeí �
containó   á   formattinç   anä   disagnostiã   prograí    calleä �
FORMATHD.COM®   Althougè  alì driveó shippeä froí Morro÷  Designó �
havå ruî througè á lenghtù diagnostiã anä arå formatted¬ thå useò �
ió  adviseä  tï ruî thå formaô prograí tï insurå thå  controller¬ �
drivå and the cables are functioning correctly.

         From the CP/M prompt type:    FORMATHD    <CR>

Thå prograí wilì propmô yoõ abouô formattinç anä thå drivå  type®  �
Aô  thió poinô yoõ shoulä choså thå formaô datá anä headeò optioî �
foò  thå drivå yoõ havå purchased®   Afteò thå optionó havå  beeî �
selected¬  thå disë drivå headó shoulä restorå tï tracë °  (therå �
shoulä  bå á motoò likå soundinç noiså wheî thió  occurs)®   Froí �
thió  point¬  thå headó wilì begiî steppinç á cylindeò aô á  timå �
printinç  á doô oî thå consolå foò everù tracë  formatted®   Wheî �
thå  prograí ió finished¬  returî tï CP/M®   Iæ thå headó dï  noô �
movå  oò  thå  prograí reportó errors¬  refeò tï thå  sectioî  oî �
troubleshooting.


2.8  Running CP/M on the Discus system

Therå  arå twï separatå proceedureó foò bringninç thå  systeí  uð �
undeò  CP/Í  dependanô  upoî whetheò yoõ arå  currentlù  usinç  á �
Morro÷  Systeí  oò  Morro÷ Floppù subsysteí oò  whetheò  yoõ  arå �
running on a non-Morrow based floppy CP/M system.

2.8.0 Morrow Based System

Iî  á  Morro÷  baseä systeí iô ió onlù necessarù tï  instalì  thå �
systeí  diskettå supplieä witè youò Discuó systeí anä colä  boot®  �
Yoõ  musô  bå  surå  (bù readinç thå  Diskettå  label©  thaô  thå �
diskettå  ió  indeeä configureä foò  youò  operatinç  environmenô �
(DJ2d/Â  oò DJ/DMÁ floppù controller¬  I/Ï througè thå DÊ oò Mulô �
I/Ï board)®  Thå CP/Í systeí shoulä no÷ bå uð anä runninç anä thå �
versioî  wilì  havå  thå  HDCÁ driveró  foò  youò  Discuó  systeí �Šresident in the Cbios.

.paŠBy now typing:

               DIR E:         <CR>

thå  contentó oæ thå harä disë systeí wilì bå  displayed®   Sincå �
thå drivå haó jusô beeî formatted¬ CP/Í shoulä responä "NÏ FILE"®  �
Typing :
               DIR F:         <CR>

wilì   causå  thå  samå  responså  afteò  thå  headó   repositioî �
themselves®  Thå M1° drivå ió separateä intï twï logicaì  drives®  �
Botè  thå  M2°  anä M2¶ arå seperateä intï ³ logicaì  driveó  foò �
CP/M®  Iæ yoõ havå aî M2° oò aî M26¬ yoõ maù completå thå initiaì �
check by typing:

               DIR G:         <CR>

Afteò  successfullù completinç thió simplå test¬  yoõ  maù  begiî �
usinç thå harä disë tï storå files®   Á gooä ideá aô thió timå ió �
tï  pið  alì  thå fileó ofæ thå floppù ontï eacè  oæ  thå  Discuó �
logicaì  driveó tï furtheò tesô thå system®   Thió completeó  thå �
initial CP/M checkout.


2.8.1 Non-Morrow based CP/M systems

Sincå  Morro÷ Designó cannoô supplù á systeí diskettå  configureä �
foò youò particulaò hardwarå environment¬ thå Instalì packagå caî �
bå  obtaineä tï makå patchinç oæ thå HDCÁ driveró intï youò  CP/Í �
systeí simple®   Whaô thå INSTALÌ packagå doeó ió locatå thå HDCÁ �
driveró  iî RAÍ abovå youò CP/Í systeí anä changå thå jumð  tablå �
tï  reflecô  thå  presencå  oæ  theså  drivers®    Thió  ió  donå �
automaticallù  buô requireó thå CPÍ 2.² systeí tï havå somå  freå �
RAÍ (normallù aô thå toð oæ memory)®  Eacè timå yoõ colä booô thå �
system¬ however¬ thå INSTALÌ prograí musô bå run®  Iæ yoõ wisè tï �
permanentlù  incorporatå  thå driveró intï youò Cbios¬  refeò  tï �
sectioî  oî  customization®  Detailó oî thå INSTALÌ  prograí  arå �
containeä  oî thå INSTALÌ diskettå iî thå .DOÃ files®   Thå  useò �
maù  TYPÅ thå INSTALL.DOÃ filå foò á morå completå descriptioî oæ �
thå INSTALÌ package®   Assuminç yoõ arå runninç á 60Ë CP/Í systeí �
proceeä aó follows:

Put the Install diskette in the floppy drive and type:

          INSTALL HDCA.PRL -E F000      <CR>


By now typing:

               DIR E:         <CR>

thå  contentó oæ thå harä disë systeí wilì bå  displayed®   Sincå �
thå drivå haó jusô beeî formatted¬ CP/Í shoulä responä "NÏ FILE"®  �
Typing :
               DIR F:         <CR>Š
wilì   causå  thå  samå  responså  afteò  thå  headó   repositioî �
themselves®  Thå M1° drivå ió separateä intï twï logicaì  drives®  �
Botè  thå  M2°  anä M2¶ arå seperateä intï ³ logicaì  driveó  foò �
CP/M®  Iæ yoõ havå aî M2° oò aî M26¬ yoõ maù completå thå initiaì �
check by typing:

               DIR G:         <CR>

Afteò  successfullù completinç thió simplå test¬  yoõ  maù  begiî �
usinç thå harä disë tï storå files®   Á gooä ideá aô thió timå ió �
tï  pið  alì  thå fileó ofæ thå floppù ontï eacè  oæ  thå  Discuó �
logicaì  driveó tï furtheò tesô thå system®   Thió completeó  thå �
initial CP/M checkout.


2.9.0  Putting a system on the hard disk
       (Morrow Designs Systems Only!!)

Foò  conveniancå  speeä anä versatilitù iô ió desirablå  foò  thå �
CP/Í  operatinç systeí tï residå oî thå harä disë (aó oî á floppù �
disk)®   Witè  thå systeí diskettå supplieä froí  Morro÷  Designó �
simply type:

               MOVCPM * *          <CR>

Aî imagå oæ thå systeí witè thå harä disë driveró aó driveó Á anä �
Â  foò M1° oò A,Â anä Ã foò M20¬  M2¶ ió no÷ residenô iî  memory®  �
At this point simply type:

               SYSGEN              <CR>

anä  wheî  prompteä  idicatå thå sourcå ió froí  memorù  anä  thå �
destinatioî  ió thå "E¢ drive®   Youò harä disë wilì no÷  havå  á �
copy of CP/M on the first cyclinder of the drive.



2.9.1 Cold Booting the hard disk (BOOTHD.COM)

Morro÷  designó supplieó thå BOOTHD.COÍ (aó welì aó á listinç  oæ �
saiä prograí iî thå appendiø oæ thió manual© tï allo÷ thå useò tï �
"Boot" from the DiscusxHard Disk system.  Simply type:

                       BOOTHD         <CR>

anä  thå harä disë wilì bå colä booted®   Thå BOOTHD.COÍ filå maù �
alsï  bå puô iî ROÍ foò thoså useró wishinç tï booô directlù froí �
thå harä disë withouô usinç thå floppy®   Morro÷ Designó supplieó �
thió prograí standarä iî thå Decisioî ± systemó iî thå MPZ8°  CPÕ �
EPROM.



.paŠadd to text on page 11

8.0 Disk Data Organization

Therå  arå  twï rotatinç platteró insidå thå M1° anä  M2¶  driveó �
(thå M2° haó ´ platters© anä botè thå loweò anä uppeò surfaceó oæ �
theså platteró arå useä tï storå magnetiã imformation®   Floatinç �
oveò theså surfaceó arå thå Read/Writå heads®  Thå M2¶ containó ¸ �
heads¬  ² foò eacè surface®  Thió decreaseó bù halæ thå amounô oæ �
surfacå  thå  steppeò  modå musô bå ablå tï positioî  thå  heads®  �
Wheî onå heaä ió aô tracë ° oî thå M26¬  itó ascociateä heaä  foò �
thaô  platteò  ió  locateä exactlù halfwaù iî thå middlå  oæ  thå �
surface.

M1° anä M2° driveó havå onlù onå heaä peò surface®  Thereforå thå �
M10 has 4 heads and the M20 has 8 heads.

Once the read/write heads have been ...
...512 bytes of data.

Thå datá oî á disë ió storeä iî blockó calleä sectors®   Thå HDCÁ �
controlleò  useó  51²  bytå sectors®   Eacè  sectoò  ió  uniquelù �
identifieä oî thå drivå bù á discriptoò referreä tï aó thå sectoò �
header®   Thå cylinder¬ head¬ keù anä sectoò numbeò arå storeä iî �
thå  headeró  anä  wilì identifù thå  followinç  datá  field®  Iî �
addition¬  aô  thå enä oæ botè thå headeò anä datá fielä ió  á  ² �
bytå numbeò whicè ió á CRÃ (Cyclicaì Redundancù Check© checë worä �
generateä bù thå controlleò wheneveò á writå tï eitheò thå headeò �
oò datá ió performed®  Wheî thå headeò oò datá ió reaä back¬ thió �
valuå  ió  checkeä bù HDCÁ circuitrù tï insurå thå datá haó  beeî �
reaä correctly®  

Thå  facô thaô thå M2¶ ió physicallù largeò thaî thå M1° anä  M2° �
driveó meanó thaô iô caî supporô morå sectoró peò track/cylinder®  �
Thå M10/M2° driveó caî fiô 2± sectoró oî á trcaë wherå aó thå M2¶ �
supportó 3² sectoró peò track®  

Thå  sectoò formaô foò Morro÷ Designó softwarå ió  identifieä  iî �
figurå ___ß below.
















Š





                          Figure ______


Tï  maximizå thå transfeò oæ sectoró tï thå hosô computeò  systeí �
memorù  Morro÷ Designó softwarå useó á physicaì sectoò ske÷  wheî �
formattinç thå drive®   Thió ske÷ takeó intï accounô thå timå  iô �
takeó  tï transfeò á secotró wortè oæ datá intï memorù usinç  I/Ï �
instructionó  anä  wilì allo÷ thå operatinç systeí tï  reaä  morå �
thaî  onå  sectoò peò disë revolution®   Thå Morro÷ Designó  ske÷ �
table is illustrated below.








                          Figure ______
.paŠcontinue here with graf on page 12 starting: 

                 The disk drive has a sensor ...

.paŠ
10.5 page 25

;***********************************************************
;*                                                         *
;*  Sample data read routine reads from the controller     *
;*  data buffer to system ram at 1000h.                    *
;*                                                         *
;***********************************************************

          ORG  100H

BASE      EQU       50H
COMND     EQU       BASE + 1
DATA      EQU       BASE + 3
WARM      EQU       0

          LXI  B,512           ;SECTOR LENGTH COUNT
          LXI  H,1000H         ;MEMORY ADDRESS FOR DATA
          MVI  A,0
          OUT  COMND          ;RESET RAM POINTER TO DATA AREA
RDLOOP:   IN   DATA           ;READ THE DATA
          MOV  M,A
          INX  H
          DCX  B
          MOV A,B
          ORA C
          JNZ RDLOOP          ;REPEAT FOR 512 BYTES
          JMP WARM
       
          END
          
.PAŠ
;***********************************************************
;*                                                         *
;*  Sample data write routine write to the controller      *
;*  data buffer from system ram at 1000h.                  *
;*                                                         *
;***********************************************************

          ORG  100H

BASE      EQU       50H
COMND     EQU       BASE + 1
DATA      EQU       BASE + 3
WARM      EQU       0

          LXI  B,512           ;SECTOR LENGTH COUNT
          LXI  H,1000H         ;MEMORY ADDRESS FOR DATA
          MVI  A,0
          OUT  COMND          ;RESET RAM POINTER TO DATA AREA
RDLOOP:   MOV  A,M
          OUT  DATA           ;WRITE THE DATA
          INX  H
          DCX  B
          MOV A,B
          ORA C
          JNZ RDLOOP          ;REPEAT FOR 512 BYTES
          JMP WARM
          
          END