Instructions For Installing SPOOLER on TARBELL CP/M Systems:

Your BIOS will have to be modified slightly.  One way is to
use the BIOS you are currently using, and modify it according
to the instructions in section 1 of the SPOOLER instructions.
The other way is to use one of the new BIOS's provided on the
SPOOLER disk, and make the changes required for your console
and other I/O set-up.  If your system is configured close to
our standard, then the first makes more sense, whereas if your
BIOS has been extensively modified, the second choice is better.

If you decide to use your current BIOS, be sure to read the
installation section (1) of the SPOOLER instructions.


1.  Look at the BIOS ASM file provided on the spooler disk
    to see if changes are required for your particular I/O
    set-up, and make these changes using the editor.  The
    FBIOS file is for Dual PerSci users, and the CBIOS file
    is for all others.  When you set the MSIZE, make sure
    that you have at least 1K of memory above the size you
    have specified.  For example, if you have 32K of memory,
    set the MSIZE to 31 or lower.  This allows room for the
    SPOOLER.
2.  Assemble the BIOS using the assembler.
3.  Change the MSIZE in your BOOT ASM file to be 1K lower
    than would be normal for your system, as you did with
    the BIOS file.
4.  Assemble this BOOT using the assembler.
5.  Type CPM ss * (remember the asterisk), where ss is your
    memory size minus two.  For example, if you have 32K of
    memory, the ss would be 30.
6.  Type  SAVE 32 CPMss.COM  where ss is memory size minus 2.
7.  Type  DDT CPMss.COM   where ss is memory size minus 2.
8.  Type IxBIOSxx.HEX  (x's should reflect your file name)
9.  Type  Rbias  (where bias is in the table below, and ss
                  is memory size minus 2 or MSIZE minus 1)

ss  bias    ss  bias    ss  bias    ss  bias    ss  bias
16  E080    18  D880    22  C880    26  B880    30  A880
34  9880    38  8880    42  7880    46  6880    50  5880
54  4880    58  3880    62  2880

other sizes may be interpolated from this table, or taken
from the table in the Tarbell CP/M User's Guide.

10. Type  IxBOOTxx.HEX  (fill in x's for your file name)
11. Type  R900
12. Type a control-C.
13. Type  SYSGEN
14. Press carriage-return in answer to the first question,
    A or B in answer to the second question, depending upon
    which drive you want to write the new system onto,
    then carriage return to make the transfer.
15. Do NOT press carriage return when it says to press return
    to reboot.  Instead, just reset and run to test the system.
16. Now you can test SPOOLER by following the instructions
    in Sections 2, 3, and 4 in the SPOOLER instructions.