SYSGEN


SYSGEN is the Magnum system placement utility.  It can be used to:

	1. transfer the operating system from one diskette to another
	2. transfer the operating system image from memory to diskette
	3. move or "slide" a copy of the currently running operating 
	   system from its normal place in high memory to a position
	   in memory in preparation of transfer to system tracks of diskette

The purpose of the third option is to allow programs that change attributes
of the operating system such as SETERR or any of the FLEXFORM family of
various disk formats, to be "frozen" onto the system tracks.  In this manner,
the BIOS may be customized without ever having to re-assemble.


				System Tracks

The system tracks are structured as diagrammed below.  Note that regardless
of the format of the data segment of the diskette, the system tracks are
always double density with 9 or 5 sectors of 1K (1024 bytes) per track 
for 8 and 5.25 inch disks respectively.  In either size, only the first
5 sectors are used for compatability.


 	track			sector  ( 1024 bytes/sector )
 		    1	    2	    3	    4	    5
 		+-------+-------+-------+-------+-------+
 	  0	| * |<========== bios =========>|  ccp1	| ccp  -- 0800h 2.0k
 		+-------+-------+-------+-------+-------+ bdos -- 0e00h 3.5k
 	  1	|  ccp2 |<========== bdos =========>| @	| bios -- 0f80h 3.875k
 		+-------+-------+-------+-------+-------|
 
 		* - id block 128 bytes: volume name, date, owner, reserved
 		@ - reserved 512 bytes: 

		bios - basic input output system
		ccp1 - first half (1k) of console command processor
		ccp2 - second half of console command processor
		bdos - basic disk operating system


				Setup Byte

SYSGEN has a small 4 byte patch table that must be altered as per the 
users drive configuration.  Each byte of the patch table is as follows:


	offset			bits
 		+----+----+----+----+----+----+----+----+ 
	0002	| 7    6    5    4  | 3    2    1    0 	|  setup byte for A
 		+----+----+----+----+----+----+----+----|

 		+----+----+----+----+----+----+----+----+ 
	0003	| 7    6    5    4  | 3    2    1    0 	|  setup byte for B
 		+----+----+----+----+----+----+----+----|

 		+----+----+----+----+----+----+----+----+ 
	0004	| 7    6    5    4  | 3    2    1    0 	|  setup byte for C
 		+----+----+----+----+----+----+----+----|

 		+----+----+----+----+----+----+----+----+ 
	0005	| 7    6    5    4  | 3    2    1    0 	|  setup byte for D
 		+----+----+----+----+----+----+----+----|

	bits 0-3: physical drive selection
			A - 0eh			B - 0dh
			C - 0bh			D - 07h
	bit 4: sidedness bit
			0 - single sided
			1 - double sided
	bit 5: not used
	bit 6: size select
			0 - 5.25 inch drive
			1 - 8 inch drive
	bit 7: write precompensate
			0 _ write precompensate disabled
			1 _ write precompensate enabled


	examples (values in hex)

			5b - 8 inch, double sided, drive 1 is drive B
			9e - precompensate, 5.25 inch, double sided,
			     drive 0 is drive A

	note: generally, the low order nibble, that describing the drive
	usually does not need to change.  The bits most ofter changed are
	bit 4 (sidedness) and bit 6 (size).


The patch table defaults to drives A-D being 8 inch, double sided.  The 
following shows the conversion process to make drive B 5.25 inch double sided.

> ddt sysgen.com
DDT VERS 2.2
NEXT  PC
0680 0100
-S0102				; this allows examination 
0102	5E <ret>
0103	5D <ret>
0104	5B <ret>
0105	57 <ret>
0106	CD .  <ret>		; get out of DDT's substitute mode
-S0103 <ret>
0103	5D 1d			; change the value from 5d to 1d
0104	5B .  <ret>
-^C				; ctrl C gets out of DDT

> save 8 sys8588.com		; save image to disk




							don delwood