lptout:
ul1out:	in	nspsta			;Write a character
	ani	nsptbe
	jz	uc1out			;Wait till the buffer is empty
	mvi	a,20h			;Reset the parallel output flag
	out	nspsta
	mov	a,c			;Write the character, strobe bit 7
nspout:	ori	80h
	out	nspdat
	ani	7fh
	out	nspdat
	ori	80H
	out	nspdat
	ret

uc1ist:
ur1ist:
ur2ist:	in	nspsta			;Return input buffer status
	ani	nsprbr
	rz				;Return not ready
	mvi	a,0ffh
	ret				;Return ready

lptost:		
ul1ost:	in	nspsta			;Return output buffer status
	ani	nsptbe
	rz				;Return not ready
	mvi	a,0ffh
	ret				;Return ready

	endif				;North Star I/O configuration
	page

;*************************
;Begin List Device Drivers
;*************************
;
	if	lsttyp eq 0
;*******************************
;Begin Prom Patch Driver (LDRV0)
;*******************************
;	The driver entries LSTOUT and LSTOST are defined in the CP/M
;	alternation guide (e.g.  Input parameters are in register C and
;	results are returned in register A). The LSTSET routine is used
;	for initialization code. It should execute a RET when complete.
;
;	The LSTSET routine could be placed just below the CBOOT routine.
;	This space (below CBOOT) is recyled for use as a disk buffer
;	after CBOOT is done.
;
;	These routines all point to lstskp initially so that the system
;	won't hang up, waiting for a non-existant list device to become
;	ready.
;
lstout:	jmp	lstskp		;Printer output
lstost:	jmp	lstskp		;Printer output status
lstset:	jmp	lstskp		;Printer initialization
lstskp:	ret

	endif			;End of Patch Area for List Drivers

	if	lsttyp eq 1
;*******************************************
;Begin Patch Area Driver (128 bytes) (LDRV1)
;*******************************************
;	The driver entries LSTOUT and LSTOST are defined in the CP/M
;	alternation guide (e.g.  Input parameters are in register C and
;	results are returned in register A