Z8E USER'S MANUAL













				 Copyright 1984
				       by
				  RICK SURWILO
				 23 PLMOUTH ROAD
			   STAMFORD,CONNECTICUT 06906
				 (203) 324-3809














































				TABLE OF CONTENTS

		Section 				       Page
	
	  I.  INTRODUCTION					 1

	 II.  INSTALLATION					 3
			
	III.  INVOKING Z8E AT THE CP/M COMMAND LEVEL		13
	
	 IV.  INITIALIZATION					19
	
	  V.  COMMAND INPUT					23

	 VI.  BREAKPOINTS					29

	VII.  COMMANDS:

	       A     Assemble					32
	       B     Set Breakpoint				26
	       C     Clear Breakpoint				27
	       D     Dump					28
	       E     Examine					29
	       F     Find					31
	       G     Go 					33
	       H     Display Symbol Table			34
	       I     Input File 				35
	       J     Animated Full Screen Debugging		37
	       K     Set Memory Window Address for J command	49
	       M     Move Memory				50
	       N     Output to I/O Port without Pre-read	51
	       O     Output Current Breakpoints to Console	53
	       P     Examine Flag Register			54
	       Q     Query I/O Ports				55
	       R     Register					57
	       S     Single Step				58
	       U     Save Symbol Table to Disk			60
	       V     Verify Memory				61
	       W     Write Memory Segment to Disk		62
	       X     Display Machine State			63
	       Y     Fill Memory				64
	       Z     Disassemble				65

	      APPENDIX A - Symbol File Formats			69
	      APPENDIX B - ZILOG Mnemonics			73
	      APPENDIX C - System Memory Map			91














	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo








			   Z8E - Z80 DEBUGGING MONITOR
	

	I. INTRODUCTION
		
	Z8E is a professional quality interactive debugging tool designed
	to speed the testing of Z80 assembly language programs.   Origin-
	ally written as a standalone monitor,  Z8E was used in the  deve-
	lopement  of the world's largest Touch-Tone Input/Voice  Response
	system.   Now redone to run in a CP/M or TurboDOS environment Z8E
	contains  more features in less memory than any comparable  soft-
	ware product.  Occupying less than 9K of memory, Z8E includes the
	following among its many features:

	      - Full screen animated display of the program under
		test while it is being executed by the Z80

	      - Complete Z80 inline assembler,	with labels, sym-
		bols,  expressions,  and directives,  using Zilog
		mnemonics
				
	      - Interactive  disassembly with labels and  symbols
		to  console  or disk allows the user  to  specify
		output formats and add comments 

	      - Fully  traced program execution including a  full
		screen single step command that instructs Z8E  to
		disassemble  code  and to move the cursor to  the
		next instruction to execute

	      - Up to 16 user settable breakpoints with  optional
		pass counts

	      - True  symbolic	debugging  using the  input  from
		multiple   Microsoft  MACRO-80 .PRN  and  LINK-80
		.SYM  files and Z80ASM .LST and SLRNK and  Z80ASM
		.SYM files from SLR Systems.

	      - Dynamic relocation of Z8E at load time to the top
		of   user  memory regardless of  size.	 No  user
		configuration of any kind is required.	


	You  may  want to spend some time familarizing yourself with  the
	manual and Z8E's command structure, especially the EXAMINE memory
	command, before turning to the INSTALLATION section.





					1





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo





		       This Page Intentionally Left Blank.





















































					2





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	II.  INSTALLATION

	First make a working copy of Z8E,  then place your original disk-
	ette  in  a safe place.   Make all modifications to  the  working
	copy, not the original. 

	Z8E's  (E)xamine  memory  command will be used to  change  memory
	contents.  This  command is described briefly below.  For a  more
	detailed  explanation please refer to SECTION V of  this  manual,
	COMMAND INPUT.

	Z8E requires an addressable cursor which can be patched  symboli-
	cally as follows:

	     First instruct Z8E to load itself as well as the symbol
	     file:

			A>Z8E Z8E.COM Z8E.SYM

	     The  symbol file Z8E.SYM contains the name and  address
	     of each parameter which may need to be modified.

	     Use the (E)xamine memory command to change the required
	     bytes.   You  may	enter commands in response to  Z8E's
	     asterisk  prompt.	Once you enter "E" followed  by  the 
	     symbolic  name of the address you which to change,  Z8E
	     will respond by displaying  the actual address followed
	     by  the hex and ASCII representation of the byte  being
	     examined (non-printable characters are shown as a "~").  
	     For example:

	     *E  MXYCP <cr>

	     285E   2	~   XX	 <cr>	;XX represents your input
	     285F   1B	~   XX	 <cr>	
	     2860   3D	=   XX	 <cr>	
	     2861   00	~   .		;PERIOD ENDS COMMAND
	     *	


	     IMPORTANT:
	     Always  patch using the symbolic name of the  variable;
	     the addresses shown in the example above are for demon-
	     stration only and do not necessarily reflect the actual
	     locations of the variables in memory.












					3





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	     Listed  below are the symbolic names of  the  addresses
	     which may have to be patched for your CRT. 

	     MXYCP  - Cursor addressing lead-in string.   The  first
		      byte  (the number 2 in the above example)  re-
		      presents	the  number of bytes in the  string.
		      The string may be up to 10 bytes	long.	This
		      actual  lead-in string should immediately fol-
		      low the count byte.

		      Default is the two character string:
			
			    1B (Hex), 3D (Hex)

		      ASCII ESCAPE, followed by EQUAL SIGN.
			
	     ROWB4? - Set this byte as follows:

		      NOT ZERO - Row is sent before Column
		      ZERO     - Column is sent before Row

		      Default is NOT ZERO, row sent before column.		


	     ROW    - Set  this byte to contain the value which is to  be
		      added row number before it is sent to the screen.

		      Default is 20 Hex, ASCII space.


	     COLUMN - Set  this byte to contain the value which is to  be
		      added  column  number  before  it is  sent  to  the
		      screen. Default is 20 Hex, ASCII space.


	     CASE   - This  byte  controls whether  you  prefer  entering
		      symbol  names  in  upper or lower  case.	 It  also
		      controls whether disassembly will be done in  upper
		      or   lower  case.   Patch  as follows:

		      FF - lower case  (DEFAULT)
		      00 - UPPER CASE

	     MAXLEN - This  is	the maximum length of permitted  for
		      symbol  names.   The permissable values are  6
		      and  14.	 If patched to any other value	then
		      Z8E  will use 6.	 The maximum length  of  the
		      symbol is required by Z8E in order to allocate
		      space for loading the symbol table.  If MAXLEN
		      equals  6 then Z8E reserves 8 byte per symbol,
		      6  for the name and two for the  address.   If
		      the  number  14 is used then Z8E	reserves  16
		      bytes  per symbol.   Hence MAXLEN impacts  the
		      amount of TPA available to the program since a
		      symbol  table of 16 bytes per entry  obviously


					4





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


		      takes  up  twice as much space as one  with  8
		      byte entries.

		      If,  while  reading in the symbols from  disk,
		      Z8E  encounters a symbol longer than the value
		      specified   in  MAXLEN  the  symbol  name   is
		      truncated to MAXLEN.

			    6 - Maximum Symbol Length (DEFAULT) 	
			   14 - Optional Symbol Length

	TO SAVE THE PATCHED PROGRAM:

			   *W ANYNAME.COM  (Writes the File to Disk)

	This completes the installation of Z8E.  Typing in ^C (Control C)
	in  response  to  Z8E's asterisk prompt will return  you  to  the
	operating system.







































					5





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


			     USER CODED CONSOLE I/O

	The following section provides details on a method of  optionally
	replacing  the	BDOS  calls for Console I/O which Z8E  uses  with
	physical console I/O routines or direct BIOS calls.

	To  modify  them use the symbol names listed below  and  assemble
	your  routine  at the appropriate address (via	Z8E's  (A)ssemble
	command - See Manual).


	     TTYQ:	This  routine checks the status of  the  console.
			If a character is waiting it is read;  otherwise,
			TTYQ  returns  a  zero in A to indicate  that  no
			character is waiting.
	
	     TTYI:	Read a character, waiting until one arrives.
			Return Character in A.
	
	     TTYO:	Output a character, waiting until it is sent.
			Character passed in A.


	Listed below is the code that Z8E uses to do console I/O;  use it
	as  a model.  Your routines should replace the instructions  with
	the  double  semicolons.   Be sure to save the reqisters as  show
	below.	The size of each routine must not exceed 32 bytes.






























					6





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


										
		TTYQ:	push	bc
			push	de
			push	hl
			ld	c,11	 ;;Check Console Status
			call	BDOS	 ;;BDOS returns:  A = 00  No Character
					 ;;		  A = NZ  Input Waiting
					 ;;
			and	a	 ;;Character Here?
			ld	c,6	 ;;
			ld	e,0ffh	 ;;	
			call	nz,BDOS  ;;If Character Here Read It...
					 ;;   Else Fall Thru
			pop	hl
			pop	de
			pop	bc
			and	7fh		
			ret

			org	TTYQ+32

		TTYI:	push	bc
			push	de
			push	hl
		TTYI00: ld	c,06	 ;;Unadorned Console Input
			ld	e,0ffh	 ;;Tell CP/M this is Input Request
			call	BDOS	 ;;
			and	7fh	 ;;Strip Parity
			jr	z,TTYI00 ;;Loop til Input Arrives
			pop	hl
			pop	de
			pop	bc
			ret

			org	TTYI+32


		TTYO:	push	af
			push	bc
			push	de
			push	hl
			ld	c,02	 ;;
			ld	e,a	 ;;
			call	BDOS	 ;;Console Output
			pop	hl	
			pop	de
			pop	bc
			pop	af
			ret

			org	TTYO+32






					7





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	The symbols TTYQ, TTYI, and TTYO are included in Z8E.SYM.  There-
	fore  these  routines  can be patched  symbolically  using  Z8E's
	assemble command, for example:


		*A TTYQ
		1F76	C5	TTYQ:	PUSH	BC




	Z8E  also contains a provision for user installed  initialization
	code.  As  soon as Z8E is loaded,  but before it relocates itself
	into high memory,  it makes a call to INIT.   As presently confi-
	gured INIT merely contains a RET instruction.	However the  user
	may add up to 127 bytes of initialization code.  This code may be
	used  for any purpose,	for example,  to change your SIO or  Uart
	from  interrupt driven to non-interrupt driven in the event  that
	the  Z8E  console routines were replaced.  Any code installed  at
	INIT  is executed once and is not moved to high memory	with  the
	rest of Z8E. You need not save any registers.




































					8





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


		  SUPPLYING YOUR OWN CURSOR ADDRESSING ROUTINE


	If  your computer requires a custom cursor addressing routine  it
	can be easily added by following the steps listed below:

	1.   Examine  the Z8E.SYM file that to determine the address
	     of  Z8E's standard cursor addressing routine  which  is
	     called XYCP.   Associated with name XYCP in the file is
	     its absolute address.

	2.   Using your own text editor code your routine and preface  it
	     with the following puedo-ops:

			    ASEG
			    .PHASE    XXXXH

		  Where  XXXX  represents the  absolute  hexadecimal
		  address obtained in step 1.






































					9





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo




	     Z8E will pass the row address in the B REGISTER and the
	     column  address  in the C REGISTER.  Row numbers  range
	     from 0 to 23 while column numbers range from 0 to 79.
	     Your job is to translate these two number into a cursor
	     postion on the screen of your CRT.

	     Save  all	registers including BC.  Use  the  following
	     skeleton as a guide:

				 ASEG
				 .PHASE  XXXX	     ;From  Z8E.SYM

		       YOURS:	
				 PUSH	 BC
				 PUSH	 DE
				 PUSH	 HL

				 CURSOR ADDRESSING CODE HERE

				 POP	 HL
				 POP	 DE
				 POP	 BC
				 RET

				 END	
					
	     Use  Z8E's output routine TTYO as described  above  (or
	     your  own	routine)  to output the characters  in	your
	     cursor addressing sequence. Obtain the absolute address
	     of  TTYO from the file Z8E.SYM.  Code the call  to  the
	     subroutine  using the absolute address in	hexadecimal.
	     For instance, if Z8E.SYM contains the entry:

				 2FE2	TTYO

	     then code your call statements as:

				 CALL	2FE2H

	     Z8E imposes only one restriction on the code you write.
	     In  order	to guarantee that your routine can be  relo-
	     cated  into high memory by Z8E do not load any  16  bit
	     constants	into  register pairs;  instead do two 8  bit
	     loads.   For example,  do not use the following  state-
	     ment:

				 LD	HL,1234H

	     Rather, code it like this:

				 LD	H,12H
				 LD	L,34H



				       10





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	     This  is  the only restriction other than	the  maximum
	     code  length which is placed on your code which is  128
	     bytes.

	3.   Assemble  your routine with either Macro-80 or  Z80ASM.
	     Link it with either Link-80 or SLRNK.



















































				       11





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	4.   Load Z8E.COM using Z8E:

		  A>Z8E Z8E.COM Z8E.SYM

		  *

	5.   Now overlay Z8E's cursor address code with your own:

		  *I YOURCODE.COM,XYCP

	     Z8E will load your cursor addressing routine on top its
	     own  beginning  at  the  address  associated  with  the
	     symbol XYCP.	

	6.   Save the new file using a name of your choosing:

		  *W  NEWDEBUG.COM

	7.   Exit  back  to  the  operating  system  be  entering  a
	     Control-C at the asterisk prompt.





































				       12





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo





		       This Page Intentionally Left Blank.





















































				       13





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	III.  INVOKING Z8E AT THE CP/M COMMAND LEVEL

	Upon  invokation at the CP/M command level Z8E loads at  the  low
	end  of the Transient Program Area (TPA) which begins at absolute
	address 100H.  The TPA is the area in memory where user  programs
	are executed.

	Once  loaded Z8E determines the size of the TPA by examining  the
	address  field of the jump instruction at location 5.	This  ad-
	dress  represents  both the entry point into CP/M and the end  of
	the TPA.   Z8E lowers this address by approximately 9K bytes  and
	relocates into this area by adjusting all addresses within itself
	to reflect its new location.   The jump instruction at location 5
	is similiarly modified to reflect the new size of the TPA.   Thus
	all  programs  which use this address to determine the amount  of
	available memory can run unchanged.   Z8E completes its initiali-
	zation	by storing a jump instruction to its breakpoint  handling
	software at absolute address 38 (hexadecimal).	

	Symbols which are loaded from files are stored by Z8E in a symbol
	table at the top of the TPA just below Z8E.  Z8E will dynamically
	allocate  the  storage necessary to hold all symbols loaded  from
	files; however, Z8E also allows the user to enter his own symbols
	from  the  keyboard via the (A)ssemble	command.   Z8E	does  NOT
	reserve ANY space in memory for user generated symbols.  The user
	must  explicitly  request memory space on the CP/M command  line.
	This is accomplished by entering the number of symbols for  which
	space  should be reserved as a decimal number.	 This number must
	be enclosed in parentheses and must appear as the first  argument
	on the command line as shown below:

		   A>Z8E (32)

	In  this example the user has requested space for 32 user defined
	symbols.   If  MAXLEN has be set to 6 (See INSTALLATION  Section)
	then  each symbol requires 8 bytes of  storage,  hence,  in  this
	example  Z8E will set aside 256 bytes of memory for user  defined
	symbols.

	Subsequent action is based on the format of the remainder of  the
	command line as entered by the user.  In the examples that follow
	bear  in  mind	that any of these command lines may  contain  the
	argument  requesting memory space for user symbol table  entries.
	The argument would appear immmediate after "Z8E" in every case.


	     1.    A>Z8E
			
			   Z8E resides as a standalone program in memory.



	     2.    A>Z8E  USERFILE.COM

			   USERFILE.COM is loaded at the beginning of the


				       14





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


			   TPA	and is ready to be acted on by	Z8E  com-
			   mands.



	     3.    A>Z8E  USERFILE.COM USERFILE.SYM [,bias]

			   USERFILE.SYM is read in by Z8E and all  symbol
			   names contained in the file are entered into a
			   table  which begins at the starting address of
			   Z8E (the ending address of the "new" TPA)  and  
			   extends  downward  in  memory.   The  optional
			   bias,  if  specified,  is a 16 bit value which
			   will be added to the 16 bit address associated
			   with each symbol in the file.   (In this exam-
			   ple a .SYM file is shown;  however,	since all
			   addresses  appearing in a .SYM file are  abso-
			   lute  the optional bias would probably not  be
			   used.)

			   USERFILE.COM is loaded at the start of the TPA
			   only after the .SYM file has been read and the
			   symbol  table built. 
				


	     4.    A>Z8E  USERFILE.COM	USERFILE.PRN [,bias]
			
			   As  in  the previous example  USERFILE.COM  is
			   loaded  at the beginning of the  TPA,  but  in
			   this instance a .PRN file is used to construct
			   the	symbol table.	The optional bias becomes
			   very  useful if the .LST or .PRN  file  repre-
			   sents  the  listing of a relocatable  program.
			   Relocatable programs linked using  Microsoft's
			   LINK-80 default to a load address of 103H with
			   the	three  bytes  of memory located  at  100H
			   containing  a jump to the entry point  of  the
			   program.   Therefore,  if  the user supplies a
			   bias  of 103 in the command line all  relocat-
			   able  symbols in the file will  be  associated
			   with  their actual addresses in  memory.   Any
			   bias  specified  will only be added	to  those
			   symbols  which are flagged as code relative in
			   the .PRN file. A bias will not be added to any
			   symbol  flagged  as	ABSOLUTE,   EXTERANL,  OR
			   COMMON.

			   USERFILE.COM is loaded at the start of the TPA
			   only after the .LST or .PRN file has been read
			   and the symbol table built.






				       15





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	     5.    A>Z8E USERFILE.COM USERFILE.SYM [,bias] NFILE.LST [,bias]
				
			   The true power of Z8E's symbol loading is best
			   evidenced when loading multiple symbol  tables
			   from  several files.   The first file is  gen-
			   erally  a .SYM file specifying all the  global
			   symbol names in the program to be tested.  The
			   subsequent files specified on the command line
			   are	usually .PRN or .LST files of the indivi-
			   dual  source modules that were originally  as-
			   sembled  and then linked (which  produced  the
			   .SYM file).	Although only two files (USERFILE
			   and NFILE) are shown in this example, in actu-
			   ality the number of .SYM and .PRN files speci-
			   fied  in  the command line is limited only  by
			   the	size  of Z8E's input buffer which  is  80
			   characters long.


			   USERFILE.COM  is loaded  at the start  of  the
			   TPA	only  after all .SYM and .PRN/.LST  files
			   have been read and the symbol table built.


			   Note:
			   If no bias is specified,  Z8E will use a  bias
			   of zero.


	If  more than one .LST or .PRN file is being  loaded,  then  each
	file  name can be specified with its own bias.	 The bias may  be
	entered in the form of a symbol name, hexadecimal number, decimal
	number,  or  any combinatiion of the three in an expression using
	the  + and - operators.   If the individual module has	a  global
	entry  point,  the name of which was previously loaded,  the user
	can  bias all symbols with the value associated with  this  name.
	In  this  way all symbols,  both absolute  and	relocatable,  are
	associated with their actual location in memory.

	Z8E  as  presently configured can build a symbol table	from  the
	list files produced by the following programs:

	    1. Microsoft   MACRO-80    V3.37  .PRN Files  May 8, 1980
	    2. Microsoft   MACRO-80    V3.44  .PRN Files  Dec 9, 1981
	    3. Microsoft   LINK-80     V3.44  .SYM Files  Dec 9, 1981
	    4. SLR Systems Z80ASM      V1.07  .LST Files
	    5. SLR Systems SLRNK       V1.07  .SYM Files

	Z80ASM and SLRNK may be configured for 80 or 132 column output.

	Z8E  uses the file name extension (the three characters appearing
	to the right of the period) to determine the format of the  file.
	Each  of  the above file types has a distinguishing  format.  The
	characteritics of each type are described in APPENDIX A.
		


				       16





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	During the loading process Z8E displays status and error messages
	on  the  console relating to the activity in  progress	as  shown
	below:
		
		    STATUS  MESSAGE		     DESCRIPTION

	     1. Loading: USERFILE.COM	       Z8E  is attempting to open
					       the  named  file (in  this
					       case, USERFILE.COM)


	     2.  Number of symbols loaded:     Following  the loading  of
					       all symbols from a listing
					       file  or  a .SYM file, the
					       number  of symbols  loaded
					       from the specified file is
					       displayed  as  a   decimal
					       number.


	     3.   Loaded: 100  YYYY	       Z8E displays the  starting	
		  Pages:  ZZZ		       and  ending memory addres-
					       ses  of	the  target  file
					       (the first file	specified
					       on  the CP/M command  line
					       and the one which is going
					       to be debugged).

					       "Pages:"   refers  to  the  
					       decimal	number	of  pages
					       and  is the count  of  256
					       byte  pages  in the  file.
					       This number may	be subse-
					       quently used with the CP/M
					       SAVE command once the  de-
					       bug session ends.


		  ERROR  MESSAGE			DESCRIPTION

	     1.   File not found	       The  file specified in the
					       command could not be found
					       on the specified drive.

	     2.   Symbol table not found       The   specified	file  was
					       found but did not  contain
					       a  properly formatted sym-
					       bol table.

	     3.   Invalid offset - using 0000  The  user has specified an
					       invalid offset to be added
					       to each loaded symbol. Z8E
					       will continue to load this
					       symbol  file but will  not
					       add  any bias to the  sym-


				       17





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


					       bols.  This error may have
					       occured	because the  user
					       specified an offset in the
					       form of a symbol which had
					       not    been     previously
					       loaded,	or  the user  may
					       have  specified a  numeric
					       value  which contained  an
					       illegal character.

	      4.   Syntax Error 	       The  file name was  incor-
					       rectly specified.


	After  all user files,	both symbol files and the .COM file to be
	debugged,  have been loaded Z8E displays current memory usage  as
	follows:

	     Total Symbols:    XXXX
	     Symbol Table:     XXXX - XXXX
	     Z8E relocated:    XXXX - XXXX
	     Top of memory:    XXXX	



	It  is important to note that Z8E expects the files appearing  in
	the  command  line to be appear in a specific order.   The  first
	file  name  appearing in the command line is assumed  to  be  the
	target file which is to be debugged.   It is always the last file
	to  be loaded.	All file names following the target file name are
	assumed to be symbol input files and they are loaded in the order
	in which they appear.

	The  first  file  named  in the command  line  is  always  loaded
	starting at address 100 hex.   The "I" command contains an option 
	to  allow  the file to be loaded at a  different  address.   This
	feature is not available at the CP/M command line level.

	For a discussion of the format of symbol files see APPENDIX A.


















				       18





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo





		       This Page Intentionally Left Blank.





















































				       19





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	IV. INITIALIZATION

	Once Z8E has been loaded, and has in turn loaded all files speci-
	fied on the command line,  it initializes all user registers to 0
	with the following exceptions:

	     The  user's program counter contains address  100	hex
	     which is the start of the TPA.

	     The  user's  stack pointer is set to the starting	ad-
	     dress  of Z8E (the top of the TPA) minus  two.   These
	     two  bytes  are set to zero in  accordance  with  CP/M
	     convention.   When CP/M loads a program it initializes
	     a	stack for the loaded program by pushing the address
	     of  the jump to the system warm boot routine onto	it.
	     Thus user programs (STAT.COM is an example) can choose
	     to terminate themselves  and return to CP/M by  execu-
	     ting  an RET through this address on the  stack.	Z8E
	     accomplishes  the	same objective:   the 0000  on	the
	     stack  permits the user program to return to CP/M	via
	     address  0000  which  always contains a  jump  to	the
	     system's warm boot routine.
	

	     The  user	I (interrupt) register is set to the  value
	     contained	in  the  I register when  Z8E  was  loaded.
	     Modify at your own risk.



	All  input and output by Z8E is accomplished using  buffers  con-
	tained within itself.  Z8E does not use the default DMA buffer at
	absolute  location  80 nor does it use the default  File  Control
	Block  (FCB)  at absolute location 5C.

	     Note:					
		   When  CP/M finishes loading	any  program,
		   including  Z8E,  it moves the command line
		   tail to the default DMA buffer at absolute
		   address  80 (hex) and initializes the  de-
		   fault  FCB at absolute address 5C  to  the
		   name of the first file (or first two files
		   if two or more are specified) appearing in
		   the command line.   Z8E makes use of  this
		   information	in  order to  load  the  user
		   program  and  any symbol  files.   If  the
		   program  to be tested also expects an ini-
		   tialized FCB and/or DMA buffer (as is very
		   often the case), then the user must effect
		   this  before  attempting  to  execute  the
		   program.

		   For	example,  many text editing  programs
		   are	invoked  by  typing the name  of  the
		   editor program followed by the name of the


				       20





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


		   program to edit on the CP/M command	line,
		   as in hypothetical case:

			 A>EDIT B:FYL2EDIT.BAS

		   Once the program EDIT.COM is loaded it may
		   expect  to find the default FCB to be  al-
		   ready    set   up   to   read   the	 file
		   FYL2EDIT.BAS.   EDIT.COM  may also  expect
		   the	DMA buffer to contain the  number  of
		   characters  in the command line at address
		   80,	as  well the the text of the  command
		   line starting at address 81. In this exam-
		   ple	location 80 would contain a  hexadec-
		   imal F (decimal 15) representing the  num-
		   ber	 of  characters,   and	locations  81
		   through 8F would contain the 15 characters
		   (space through S).  Similiarly,  the first
		   byte  of  the default FCB  at  address  5C
		   would  contain the number 1 (numeric equi-
		   valent  of drive B) and the next 11	bytes
		   would  contain the file name  FYL2EDIT  in
		   ASCII.   If	the name FYL2EDIT was shorter
		   than 8 characters,  then the remainder  of
		   the	file  name field in the FCB would  be
		   filled with ASCII spaces. The next 3 bytes
		   would contain the file type in  ASCII;  in
		   this  example the file type is BAS.	If no
		   file type was specified,  this field would
		   contain  3 ASCII spaces.

		   Now,  if  the  user was to debug the  EDIT
		   program using Z8E,  this initialization of
		   the	default  DMA buffer and  default  FCB
		   must  be accomplished "by hand"  prior  to 
		   attempting to debug EDIT.COM, owing to the
		   fact that CP/M has already set up these to
		   areas  with the data from the command line
		   which was typed in to load Z8E.  In short,
		   EDIT must be tricked into believing it was
		   loaded by CP/M and not by Z8E and the user
		   must  perform the initialization of	these
		   two areas.  The user may use the E command
		   (to	store both ASCII and numeric data  in
		   memory) to simulate an initialized command
		   line buffer and FCB.   Further information
		   regarding  the format of the FCB  and  DMA
		   buffer  may me found in Digital Research's
		   CP/M 2.0 INTERFACE GUIDE.








				       21





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	DEBUGGING HINT:

	It  is	not necessary to initialize the default  FCB  and/or  the
	default  (command  line)  DMA buffer every time a program  to  be
	tested is loaded (if indeed this program utilizes them).  Instead
	follow the procedure listed below (If you haven't read the  indi-
	vidual command summaries the following may make more sense later):

		  Once	you  have  loaded the program  to  test 
		  perform  the required initialization	of  the 
		  FCB's  at  5CH and 6CH and the  command  line 
		  buffer  at 80H using the E command.  Use  the 
		  ASCII string option with the E command to set 
		  the  text  portions.	Use the  numeric  input 
		  function to intialize the drive specification 
		  at address 5C and the character count at 80H. 

		  Use  the W command to write out memory start-
		  ing at address ZERO. As in:

			     *W  NEWFILE.COM  0   XXXX

		  Where XXXX is the highest address you wish to 
		  save.   Now the next time you load this  file 
		  it  will of course load at address 100H.  Use 
		  the  M  (move memory command) to move  it  to 
		  location 0000.   Your FCB and DMA buffer  are 
		  initialized.	

			      *M  100  XXXX+100  0



























				       22





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo





		       This Page Intentionally Left Blank.





















































				       23





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	V.  COMMAND INPUT

	Once  file  and  symbol table loading  has  been  completed,  Z8E
	prompts  the  operator for command input by  displaying  the  "*" 
	character.  The operator can then type any of Z8E's single letter
	commands.   Some  commands require no arguments while others  re-
	quire  between one and four. Arguments may be in any of the forms
	listed	below (except as noted in the description of the  indivi-
	dual commands): 




	     SYMBOL:	    Any  symbol previously loaded  or  previously
			    entered  via the keyboard (see A command) may
			    appear as a command argument. All symbols are
			    treated as 16 bit values.
	
									
	     HEX:	    A  16  bit	hex number may be entered  as  an
			    argument.  Only the last four characters  en-
			    tered are treated as significant input if Z8E
			    is	expecting  a 16 bit  argument.	In  those
			    instances where Z8E expects a 8 bit argument,
			    only the last two characters are significant.
			    As	such,  the user may elect to correct mis-
			    takes by either backspacing and retyping,  or
			    by	continuing to enter the number and  ensu-
			    ring  that the erroneous digit does not  ap-
			    pear  in the rightmost four (or two)  charac-
			    ters as shown in the following example:

				*E 1E21F4

				      If  a 16 bit argument  is  expected
				      Z8E  would  ignore  the  first  two
				      digits  (1 and E) and would examine
				      the  contents  of  memory  location
				      21F4.


			    If	no symbol table is present in memory then
			    hexadecimal numbers (8 or 16 bits in  length)
			    may begin with any digit 0 - F.   However, if
			    a  symbol table is in memory then all hexade-
			    cimal numbers which begin with a digit in the
			    range  A  - F are evaluated first  as  symbol
			    names.   If no corresponding name is found in
			    the symbol table then Z8E attempts to reeval-
			    uate the name as a hexadecimal  number.   For
			    example,  the  token  DEAD is a valid  symbol
			    names as well as a valid hexadecimal  number.
			    If	a symbol table is present then Z8E  first
			    searches  the  symbol table looking  for  the
			    string  DEAD.   If	no match occurs then  Z8E


				       24





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


			    treats DEAD as the hexadecimal number  0DEAD.
			    To	force  Z8E to evaluate an argument  as	a
			    hexadecimal number prefix the argument with a
			    leading zero as in 0DEAD.


	     REGISTER:	    Valid Z80 16 bit register  names are  permit-
			    ted  as arguments.	If a 16 bit register name
			    is	entered,   Z8E	uses  the  16  bit  value
			    currently contained in the specified register
			    pair  in the user's register set as an  argu-
			    ment.
	
				 *D HL 8

				      instructs  Z8E  to dump  the  first
				      eight  of  memory bytes  which  are
				      located at the address contained in
				      the user's HL register pair


			    Valid 16 bit register names:
				
				      AF - Accumulator and Flag
				      BC - BC register pair
				      DE - DE register pair
				      HL - HL register pair
				      SP - Stack Pointer
				      P  - Program Counter
				      PC - Program Counter
				      IX - IX index register
				      IY - IY index register

			    Note  that the program counter may be  speci-
			    fied in either of two ways.   The single cha-
			    racter "P" can be used to specify the program 
			    counter  provided  it does not appear  in  an
			    expression.   To include the current value of
			    the  user's program counter in an  expression
			    the mnemonic "PC" must be used.

			    If an expression used as an argument contains
			    a  register  pair as one of  its  terms,  the
			    register pair must be the first term.   Also,
			    only  one register pair may be included in an
			    expression:


				 HL+4	   valid expression

				 5+DE	   invalid expression - register
					   pair is not the first term
				
				HL+BC	   invalid   expression  - more 
					   than  one  register pair  was


				       25





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


					   specified

				 P-3	   invalid   expression   - "PC" 
					   must  be used to include  the
					   current  value of the program
					   counter in an expression	
					

			    To	 differentiate	between  the  hexadecimal
			    numbers AF,  BC,  and DE and the Z80 register
			    pairs of the same name be sure to prefix  the
			    numerical version with a leading 0.
	
			    Note  also that the Z80 prime register  names
			    are  not allowed as arguments except in the R
			    command.


	     REGISTER	    Z8E allows the user to specify the data  con-
	     INDIRECT:	    tained in the memory location pointed to by a
			    register pair as an argument.   For instance,
			    if the user's HL register pair contained 18EE
			    and the addresses 18EE and 18EF contained the
			    bytes  42 and 61 respectively,  then the com-
			    mand   *E (HL)    would examine the  contents
			    of	memory location 6142.  Note that register
			    indirect  memory references are indicated  by
			    enclosing  the register pair name  in  PAREN-
			    THESES which follows the ZILOG mnemonic meth-
			    od of signifying "the contents of".

			    The  most useful application of register  in-
			    direct  arguments  is to set  breakpoints  at
			    subroutine	return addresses.   Consider  the
			    situation  of  a program which  is	currently
			    suspended  via a breakpoint somewhere in  the
			    middle  of	a  subroutine.	 The user  is  no
			    longer  interested debugging the body of  the
			    subroutine;  he only cares about getting back
			    to the instruction that follows the CALL that
			    got  him into the subroutine.   Register  in-
			    direct format allows him to enter:

					     *B (SP)

			    This  informs Z8E to set a breakpoint at  the
			    address  pointed  to  by  the  stack  pointer
			    register.



	     DECIMAL:	    Decimal numbers in the range 0 - 65535 may be
			    entered as arguments.  All digits of the num-
			    ber  must  be in the range	0-9.   A  decimal
			    number  must be followed by a "#"  character, 


				       26





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


			    otherwise Z8E will treat it as a hex  number.
			    The  following example shows a decimal number
			    being input as part of the E command:

				 *E 512#
			
				      instructs  Z8E  to  examine  memory
				      location	512 decimal (200 hex)


	      LITERAL:	    ASCII  literals up to 78 bytes in length  are
			    permitted as arguments (Z8E's input buffer is
			    80	characters  long  less	the  opening  and
			    trailing  quote characters).   ASCII literals
			    must be enclosed in quotes.   The quote char-
			    acter  itself is the only character not  per-
			    mitted as a literal.   Commands which do  not
			    permit  the use of ARGUMENT-STRINGs (see  be-
			    low)  will still accept input in the form  of
			    quoted  strings.   In  such a case	Z8E  will
			    ignore all but the last two characters of the
			    quoted  literal,  treating the input as a  16
			    bit number.  For example if the user entered:

					    *Z 'ABCD'

			    Z8E would begin treat 'BC' as a 16 bit number
			    and begin disassembling at address at 4243.


	  ARGUMENT-	    The F (find),  E (examine memory),	N  (query
	  STRINGS:	    I/O  ports without pre-read),  Q (query   I/O
			    ports),  and  Y (fill memory) commands permit
			    the use of ARGUMENT-STRINGS, which are simply
			    combinations  of  all  valid  argument  types
			    separated by commas.  ARGUMENT-STRINGs may be
			    any  length  up to the limit of  Z8E's  input
			    buffer  which is 80  bytes	long.	ARGUMENT-
			    STRINGs  may  be terminated by either a  car-
			    riage return or the first space character not
			    appearing  in between quote characters.   The
			    following	is  an	example  of  a	15   byte
			    ARGUMENT-STRINGS  string which combines  SYM-
			    BOLS, LITERALS, HEX, and DECIMAL numbers:

			       SYMBOL,'xyZ',4F,12E4,9,21#,511#,'ABc'

			    Assuming  that SYMBOL is equal to  177H  then
			    the above ARGUMENT-STRING would evaluate to:
			
			    01 77 78 79 5A 4F 12 E4 09 15 01 FF 41 42 63

			    Again,  ARGUMENT-STRINGS  are  terminated  by
			    either  a  carriage return or  by  the  first
			    space  character  that does not appear  in	a


				       27





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


			    quoted literal string.

	Z8E permits expressions using the + and - operators.   Any  argu-
	ment type may be combined with any other type.	 The length of an
	expression  is	limited  only by the size of  the  input  buffer.
	Expressions  are  evaluated  from left to right and  the  use  of
	parentheses is not permitted.

	Z8E  indicates argument errors by printing a question mark.

	Arguments may  be  line-edited using the  standard  CP/M  control
	characters:

		       backspace:  erase the last character typed
		       control X:  erase the entire line
		       control C:  return to CP/M via warm boot

	All input is truncated to the size of Z8E's input buffer which is
	80 characters long.

	All alphabetic input to Z8E may be in uppercase or lowercase. All
	output by Z8E follows the dictates of the CASE byte as patched by
	the user (see INSTALLATION).

	In  this  manual the appearance of square brackets [ ] around  an
	argument always indicates that the argument is optional.































				       28





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo






		       This Page Intentionally Left Blank.




















































				       29





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo



	VI. BREAKPOINTS

	Breakpoints  are  those addresses in the program  under  test  at
	which  the user wishes to suspend execution and return control to
	Z8E.  The  user may set,  clear,  and display breakpoints at  any
	time,  via the appropriate command in response to Z8E's  asterisk
	prompt.   Z8E's  implementation of breakpoints does not force the
	user to tediously enter breakpoint addresses every time execution
	is resumed.  Rather,  the user may enter up to 16 breakpoint  ad-
	dresses and each breakpoint,  once set, is stored in one of Z8E's
	internal tables and remains in effect until explicitly cleared by
	the user via the Clear breakpoint command (see C command).

	Z8E also allows you to specify a pass count to be associated with
	any breakpoint that is set.   Pass counts indicate the number  of
	times  a particular instruction must be executed before Z8E  will
	regain control.

	Furthermore,  Z8E  does not modify any code in the  user  program
	until  a GO command is issued (see G command).	This permits  the
	user to examine code,  and make patches if desired,  at any point
	in the debug session.

	When  a breakpoint is reached in the user program and Z8E regains
	control,  the message:	    *BP*XXXX	  is displayed where XXXX
	represents the hexadecimal address of the breakpoint.	In  addi-
	tion,  Z8E  will display the symbolic name of this address if one
	exists	in the symbol table.  Z8E follows this with a display  of
	the  asterisk  prompt indicating it is ready  ready  for  command
	processing.

	The  message:	  *ERROR*BP*XXXX      is displayed on the console
	whenever Z8E determines that control has been regained without	a
	valid  breakpoint having been reached.	 This is generally caused
	by a user program which has gone off the deep end.   If the  user
	examines  the  current contents of the registers (via the X  com-
	mand) the current program counter will most assuredly contain  an
	address  which	had  not  previously been set  as  a  breakpoint.
	Things to look for when this situation arises include:	a program
	that blew its stack, a program that performed a 2 1/2 gainer with
	a full twist indirect through a register;  ie.	JP (HL) into  the
	great  unknown,  and  attempting to trace where wise men fear  to
	tread (BIOS and BDOS I/O routines).

	Z8E  will  allow you to single step (trace) and  set  breakpoints
	anywhere in memory.  However,  bear in mind that as you enter the
	BIOS  and BDOS netherworld your stack pointer will at some  point
	be  saved  directly in memory as CP/M switches to its  own  stack
	(your  stack  pointer is not saved on a stack  by  CP/M).   If	a
	breakpoint has been set at an instruction somewhere in BDOS or in
	the  BIOS (after this save of your stack pointer has occured) and
	this breakpoint is reached,  Z8E will itself call a BDOS  routine
	in an attempt to display the *BP*XXXX message on the console.  At
	this  point CP/M will save Z8E's stack pointer	and overlay yours


				       30





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	in memory.   When BDOS eventually restores the stack pointer  and
	executes  a  RET instruction you will not return to your  program
	and  your  stack pointer will be gone.	 These	routines  can  be
	traced, albeit with difficulty,  but you must keep an eye on what
	CP/M is doing with the stack pointer.




















































				       31





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo






		       This Page Intentionally Left Blank.




















































				       32





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	A    Assemble
	_________________________________________________________________


	The  A command permits the user to effect inline assembly of  Z80
	assembler source code,	including labels and symbols,  using  the
	full  Z80  instruction set.  In addition,  the assembler  accepts
	standard  Zilog mnemonics (APPENDIX B),  expressions using the	+
	and - operators,  as well as the following five assembler  direc-
	tives:	ORG, DEFB, DDB, EQU, and DEFW.	The format of the command
	is:

		*A  ARG1  <cr>

		  where  ARG1  represents the starting address	at  which
		  assembly will take place

		  ARG1 may be of any type


	Z8E  initially	prompts  the  user  by	first  disassembling  and
	displaying the instruction currently located at the address  spe-
	cified by ARG1.  This is done as a convenience to permit the user
	to  ensure that any patches will be assembled into memory at  the
	intended location.  Z8E then outputs a carriage return/line feed,
	displays  the address specified as ARG1,  and awaits  input.  Z8E
	will  not disassemble before every line of source code entered by
	the user, only before the first one.


	Z8E expects assembler input in the following format:


		     LABEL:  opcode  [operand1] [,operand2]


	The label field is always optional, the opcode field is mandatory
	only  if  no  label  was entered,  and	the  operand  field  must
	naturally  be  included for those Z80 instructions which  require
	one. The three fields may be separated from one another by spaces
	or tab characters.

	Z8E  does not automatically reserve space within itself for  user
	supplied symbol names. User supplied symbols, as opposed to those
	loaded	from files,  are entered from the keyboard in  the  label
	field  using the (A)ssemble command.  Symbol table space to  hold
	user  supplied	symbol names must be explicitly requested on  the
	CP/M command line as explained in the section "INVOKING Z8E at on 
        the CP/M COMMAND LEVEL".  These user supplied symbols,  once  en-
	tered,	may  be referenced in the operand field of any subsequent
	assembly  statement or in the argument field of any Z8E  command.
	These  symbols	come in handy when disassembling .COM  files  for
	which no source listing exists and also when patching code.

	The  assembler is a one pass assembler and forward references  to


				       33





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	symbols  which	do  not already appear in the  symbol  table  are
	flagged  as  errors.	However,  Z8E allows the use of  the  ORG
	directive  (see discussion below) which allows the user to  mani-
	pulate the assembler's location counter,  which helps to minimize
	the no forward reference limitation.

	Labels	may begin in any column,  but all labels must be followed
	by a colon even those appearing in an EQU statement.   Labels may
	be of any length but only the first 6 characters are significant.
	Z8E  always assigns the 16 bit value of the  assembler's  current
	location counter to the label being entered, unless the statement
	is  an EQU directive.	Labels need not be followed by an  opcode
	and this (as well as the EQU directive) provides a convenient way
	to  assign a value to a symbol name.   Merely set the  assemblers
	location counter (via the ORG directive or as ARG1 in the command
	line) to the value you wish to assign,	then type the symbol name
	followed by a carriage return.	No object code is produced and no
	user  memory areas are modified but the symbol and its associated
	value  are  entered into the user symbol table.    Z8E	does  not
	treat  duplicate symbol names as errors.   Rather,  if	the  user
	enters	a symbol name which already appears in the symbol  table,
	the  value associated with the new symbol replaces the one  asso-
	ciated with the old.  For example, if the symbol ENTRYP exists in
	the  symbol  table and is associated with the value 23DA and  the
	user assembles the following instruction:

	     41FF 0E 04       ENTRYP: LD C,4

	Z8E would replace 23DA with 41FF.

	Assembler statements which do not contain labels may begin in any
	column,  including  column one.   There is NO  need to	insert	a
	leading  space or tab before an opcode if the opcode is not  pre-
	ceded by a label.

	Operands  appearing in the operand field of the instruction to be
	assembled  may be any of the following types subject only to  the
	proviso that 16 bit values cannot appear as operand for those Z80
	instructions  which require 8 bit values.   Expressions combining
	any of the following four types (with the + and - operators)  are
	also permissable.

		       SYMBOL  (from symbol table)
		       HEX
		       LITERAL (two bytes maximum)
		       DECIMAL


	In  addition  the  dollar sign ($) may also appear in  both  the
	operand  field of any instruction in which a 16 bit  operand  is
	allowed,  and  also  in the operand field of any  relative  jump
	instruction.   The  dollar sign represents the current value  of
	the assembler's location counter, that is, the address appearing
	on the line at which the assembly is taking place.



				       34





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	The  operand field of a relative jump instruction can be  entered
	in  either of two ways.   The user may code the operand using the
	dollar sign  mentioned above as in the following examples:


		  JR  NZ,$+11	    ;jump to address PC+11 (hex)
		
		  DJNZ	$-24#	    ;jump to address PC-24 (decimal)

	The user may alternatively specify a 16 bit value in the  operand
	field  of  a relative jump instruction and let Z8E calculate  the
	relative  displacement	from the assembler's program  counter  as
	shown below:

		  JR	C,LABEL      Assuming LABEL exists, in the symbol
				     table Z8E will calculate the offset.
				     LABEL  must  be within +129 or  -126
				     bytes from the assembler's  location
				     counter  or  an assembly error  will
				     result.

		  JR	  NZ,1080    Z8E  calculates the displacement be-
				     tween the assembler's current  loca-
				     tion  counter  and the address  1080
				     (hex).


	
	Z8E indicates  error-free input by first displaying the resultant
	object	code  and  then displaying (on the next  line)	the  next
	address at which assembly will take place.

	Assembly errors are always indicated by a double pair of question
	marks which appear following the location counter.  An error flag
	is also printed and will be one of the following:

			ERROR FLAG		 MEANING

			    L	      Label starts with numeric character
					
			    O	      Invalid opcode

			    S	      Syntax error

			    T	      Symbol table full 		

			    U	      Instruction references an undefined
				      symbol name

			    V	      Value error - a 16 bit  value
				      was specified as an operand for
				      an  instruction  which  permits
				      only 8 bit numbers.		

	If  an	error occurs,  Z8E will reprompt the user with	the  same


				       35





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	location counter address.
	
	As was mentioned previously the Z8E assmebler uses standard Zilog
	mnemonics.   The  one exception to this is the EX AF,AF' instruc-
	tion.	To assemble this instruction the trailing quote character
	must be omitted.

	Z8E  supports the ORG directive which allows the user  to  change
	the value of the assembly location counter.  The operand field of
	the  ORG directive may be a 16 bit argument of any  type.   After
	setting the new assembly location counter Z8E displays the disas-
	sembled instruction at the new address.

	Z8E supports the DEFB,	DEFW,  and DDB directives which give  the
	user  the ability to assemble data constants into  memory.   DEFB
	accepts  an  8	bit operand;  the value of which in  placed  into
	memory	at the address of the assembler's current location  coun-
	ter.  DEFW allows the user to specify a 16 bit operand value, the
	low  order byte of which is placed into memory at the address  of
	the  assembler's current location counter,  while the high  order
	byte  of the operand is placed into memory at the address of  the
	assembler's current location counter plus one.	This is in accor-
	dance with the 8080/Z80 convention of storing the high order byte
	of  16 bit data toward the high end of memory.	The  DDB  (define
	double	byte) directive allows the user to specify a 16 bit value
	which,	in  contrast to the DEFW directive,  is stored in  memory
	with the high order byte toward the low end of memory.	 That is,
	a DDB directive instructs Z8E to store the most significant  byte
	of  the  16  bit operand value in memory at the  address  of  the
	assembler's  current location counter,	and the least significant
	(low  order)  byte is placed into memory at the  address  of  the
	assembler's current location counter plus one.

	The EQU directive allows the user to assign a value to a  symbol.
	An EQU directive does not generate object code.  It merely allows
	the  user  to  reference a numeric value by a  symbolic  name  in
	subsequent assembly statements or monitor commands.   It is espe-
	cially	useful	when used prior to disassembling (see Z  command)
	code  for which no symbol table exists.   The EQU  directive  re-
	quires	the user to supply a symbolic name in the label field  of
	the instruction.   If Z8E indicates errors in an EQU statement by
	printing question marks.  If an EQU statement is correctly assem-
	bled  by  Z8E,	the address of the assembler's	current  location
	counter  is  erased  since an EQU statement generates  no  object
	code.  Operands appearing in EQU statements are evaluated to a 16
	bit  value.  Z8E will display the value of this 16 bit number  as
	four hex digits in the object code field on the console.










				       36





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	B    Set Breakpoint
	_________________________________________________________________


	Breakpoints  are  those  addresses at which the  user  wishes  to
	suspend execution of the program under test.   Breakpoints may be
	set at any time in response to Z8E's asterisk prompt.  Z8E allows
	the  user to set up to 16 individual breakpoints in his  program.
	Z8E also allows the user to specify a pass count to be associated
	with any breakpoint.
	
	The command is invoked as follows:


	     *B ARG1[,pass count] [ARG2... ARGn] <cr>

		  where each argument represents the address in the  user
		  program at which a breakpoint is to be set

	Normally,  that is when no pass count is specifed,  execution  of
	the  user  program stops and control returns to the  Z8E  command
	level as soon as a breakpoint is reached. Pass counts are used to
	inform	Z8E  that execution of the user program should halt  only
	when  the  specified breakpoint is reached the	number	of  times
	times indicated by the pass count.

	Pass  counts  are specified by following the  breakpoint  address
	with a comma and then entering a pass count immediately following
	the comma.

	An existing pass count may be changed to a different value by re-
	entering the same breakpoint address,  following it with a comma,
	and then specifying the new pass count.
	
	To break on a multi-byte Z80 instruction the address specified as
	the  breakpoint  address must be that of the first  byte  of  the
	instruction.   Users who fail to observe this rule will generally
	find their programs hopping the next bus to never-never land.  If
	a patch is made at an address of a breakpoint currently in effect
	be  sure  the breakpoint address is still pointing at  the  first
	byte  of  the new instruction.	

	Multiple breakpoints may be set with the same B command by  sepa-
	rating each one with a single space.  If multiple breakpoints are
	specified  and Z8E detects an erroneous argument (a  non-existent
	symbol	for  example) a question mark will be  printed,  and  the
	command  terminates.   All valid breakpoints specified up to  the
	invalid one will be set.

	Z8E  displays  a  question mark when a attempt is made to  set	a
	seventeenth breakpoint.






				       37





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	C    Clear Breakpoint
	_________________________________________________________________


	The C command clears individual breakpoints previously set by a B
	command.  The format of the command is:


		  *C  ARG1 [ARG2...ARGn] <cr>

		       where each arg may be any valid argument type
		       which  evaluates to an address previously set
		       as a breakpoint


	Multiple  breakpoints  may  be cleared by the same C  command  by
	separating each argument with a single space.

	Z8E  displays a question mark when an attempt is made to clear	a
	non-existent breakpoint.

	To  clear  ALL	breakpoints enter:   *C *    where  the  asterisk
	indicates ALL.


































				       38





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	D    Dump
	_________________________________________________________________


	The D command allows the user to dump memory in both hexadecimal
	and ASCII to the console in user specified block sizes.
	
	The format of the command is:

		  *D  [ARG1]  [ARG2]  <cr>

		       where	ARG1 =	the starting address to dump
				
				ARG2 =	dictates    the    dump    format
					depending on its value.   If ARG2
					is  in the range 0 - 255 then  it
					is  treated  as a block size  and
					represents the number of bytes to
					be  displayed  (0 is  treated  as
					256). If ARG2 is greater than 255
					then ARG2 is treated as an ending
					address and memory will be dumped
					non-interactively to the console.

		       ARG1 and ARG2 may be of any argument type.

	If  ARG1  is omitted then the dump resumes from the  last  memory
	address  +1  as displayed via the previous invocation  of  the	D
	command.  If  no previous D command had been given then memory is
	dumped starting at address 100H.

	If  ARG2 is omitted then the most recent value of ARG2 (from  the
	last D command) is used.
	
	The  dump command displays the contents of memory in  hexadecimal
	on  the  left side of the console while the ASCII  equivalent  of
	each byte is shown on the right side.

	During	a  block by block dump (ARG2 < 256 signifies a	block  by
	block  dump)  Z8E waits for user input after each block  is  dis-
	played.   A  carriage return entered by the user causes the  next
	sequential  block to be dumped while any other	character  causes
	the command to terminate.

	For  non-interactive dumps,  starting address to ending  address,
	pressing any key terminates the dump.

	The  dump  command provides an especially easy way  of	examining
	tabular data,  for example in scanning the disk parameter headers
	in your BIOS.	That is,  by specifying the base address as  ARG1
	and  the  table  size as ARG2 the user can walk  through  memory,
	table by table.





				       39





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	E    Examine Memory
	_________________________________________________________________


	The  E	command allows the user to examine and optionally  modify
	the contents of memory.  The format of the command is:

	     *E   ARG1	<cr>

		       where  ARG1 is the address of the first byte  to 
		       examine

		       ARG1 may be any symbol type

	Upon  receipt of ARG1 Z8E will read the contents of the specified
	memory	address and display the byte in both hex and  ASCII.   At
	this  point the user has two options.  The user may specify   re-
	placement  data  to be written to memory starting at the  current
	address,  or  he  may  choose to continue  to  passively  examine
	memory.   The choice is determined by the character(s) which  are
	input after the contents of an address are displayed.

	If  the  user  wishes to modify memory starting  at  the  current
	memory address,  then an ARGUMENT-STRING may be entered following
	the  displayed	byte.	Z8E will evaluate the entire  string  and
	write  the  evaluated equivalent of the string	into  consecutive
	memory	locations starting with the current memory  address.  For
	example the user could enter the following ARGUMENT-STRING:

	     *E 45F9
	     45F9  42  B  'This is a string',0D,0A,13,4F,9,'More Text',05
			  ^						^

			  The user input apprears between the arrows  and
			  would be evaluated to the following 31 bytes: 
			
			  54 68 69 73 20 49 73 20 61 20 73 74 72 69 6E 67
			  0D 0A 13 4F 09 4D 6F 62 65 20 74 65 78 74 05	

			  These  31  bytes  would be stored  into  memory
			  locations  45F9  to 4617 and the  next  address
			  displayed on the screen would be 4618.

	     4618  23  #

	Remember  that	ARGUMENT-STRINGS may be terminated  by	either	a
	carriage  return  or by the first space character which does  not
	appear	in  a quoted literal string.  The  choice  of  terminator
	determines  the which address will be displayed next.	If a car-
	riage  return is used to terminate the ARGUMENT-STRING,  then Z8E
	will display the next sequential memory address. For example:

		  *E 1002
		  1002	45  E  12,8F,00 <cr>
		  1005	28  (


				       40





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo



	The user entered an ARGUMENT-STRING 12,8F,00 which was	evaluated
	to  3 bytes.   Since the ARGUMENT-STRING was terminated by a car-
	riage return the next address displayed was 1002+3 or 1005.

	By  terminating  the  ARGUMENT-STRING with a space the	user  can
	verify	the contents of memory just  modified.	 ARGUMENT-STRINGS
	terminated  by	a space cause Z8E to redisplay the  starting  ad-
	dress;	this  makes  the  data just  entered  availalbe  for  re-
	inspection:

		  *E 1002
		  1002	45  E  12,8F,00  <space>
		  1002	12  ~

	If the user does not want to write any data to the current memory
	address,  then the character entered should be a space character,
	up arrow (carret) character, or a carriage return.

			  CHARACTER			ACTION
		
			    space		read next sequential mem-
						ory address
			
			  up arrow		read previous memory  ad-
						dress
						
			    <cr>		read next sequential mem-
						ory address command


			   period		terminate command					

	The  user may also change the current memory address by  entering
	an  equal  sign "=" followed by a valid  argument.   The  address 
	obtained  by  evaluating this argument becomes	the  new  current
	memory address as shown below:

	     *E 1344
	     1344  89  ~  <cr>
	     1345  6F  o  <cr>
	     1346  52  R  =9F34 <cr>
	     9F34  63  c














				       41





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	 F    Find
	_________________________________________________________________


	The  find command allows the user to search memory for multi-byte
	strings in memory.  The format of the command is:

	     *F   ARG1	ARG2 <cr>

		  where  ARG1  =  the  starting address at which to begin
				  the search, it may be of any type
			
			 ARG2  =  is  an ARGUMENT-STRING representing the
				  pattern  to search for;  the	user  may
				  specify  any	combination of	arguments
				  separated by commas or spaces up to the
				  limit  of  Z8E's  command  line  buffer
				  which  is 80 bytes  long.   The  actual
				  number of bytes searched for depends on
				  how the string is ultimately evaluated.

				
	Z8E will display every address which contains data matching ARG2.
	The search continues until the end of memory is reached.

	The user may elect to cancel the search at any time by depressing
	any key on the keyboard.

	If  ARG2 is a single argument (as opposed to an argument  string)
	and  if this argument is a symbol name then Z8E will reverse  the
	order of the two bytes comprising the 16 bit operand. Most 16 bit
	values in Z80 programs are stored with the least significant byte
	at  a  given address and the most significant byte at  the  given
	address+1 (toward the high end of memory).  This is in accordance
	with the Z80 convention of storing the most significant byte of a
	16 bit argument toward the high end of memory.

	The following are examples of the FIND command:

	     *F 0 SYMBOL

	     Assuming  that the symbol "SYMBOL" is  associated  with 
	     the  hex  value 3BF then Z8E would attempt to find  all
	     address  containing  the byte pair BF and	03  in	that
	     order, with the search beginning at address 0000.	Note
	     that the order of the two bytes is reversed because the
	     symbol "SYMBOL" exists in the symbol table.   To search 
	     for  the  byte  pair 03 and BF in that order  the	user
	     should enter the argument as either a 16 bit hex number
	     (3BF) or as two 8 bit hex numbers (03,BF). 


	     *F 100 87,32#,'ABCD',0C3,symbol,'p',271F

	     Assuming  that the symbol "symbol" is  associated  with          


				       42





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	     the  hex  value 3BF then Z8E would attempt to find  all
	     starting addresses of the following 12 byte string:

		     87 20 41 42 43 44 C3 03 BF 70 27 1F


	     Notice  that Z8E would search for the two byte  pattern
	     03 BF as the value for "symbol".   If the user happened 
	     to  be  trying to find the  instruction	 JP   symbol
	     the search would fail because as mentioned above 16 bit
	     values  are  stored  low order byte  first.   The	user
	     should have entered C3 BF 03.

	     The two bytes which represent the address of symbol are
	     not  reversed as in the example above because  ARG2  is
	     specified	as an ARGUMENT-STRING as opposed to a single
	     argument.

	     Z8E would begin its search at address 100 (ARG1).






































				       43





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	G    Go 
	_________________________________________________________________


	The  G command instructs Z8E to begin or resume execution of  the
	user program.  The format of the command is:

		  *G   ARG1  <cr>

		       where	  ARG1	 =   the  address  of  the  first
					     instruction the user wishes
					     to execute.

		       ARG1 may be any argument type

	Upon  receipt of this command Z8E initializes all breakpoints  in
	the  user  program,  restores all user registers,  and	transfers
	control  to the user program under test at the address	specified
	in ARG1.   Execution within the user program will continue  until
	the  user  program reaches a breakpoint,  at which point  control
	will  return to Z8E.   This is the only way the user is  able  to
	return control to Z8E once the GO command is issued.

	Z8E breakpoint technique has been designed such that Z8E will not
	directly  initialize  a  breakpoint at the address  specified  in
	ARG1.  In  actualiity it  would be impossible to do so	since  an
	attempt  would	be made to resume execution at	this  address,	a
	breakpoint would have been set at this address, and control would
	immediately  return to the monitor without this instruction  ever
	having been executed.	 This limitation has been overcome in Z8E
	by  actually  copying the single instruction located at  ARG1  to
	Z8E's  memory,	THEN setting the breakpoint at the ARG1  address,
	and  finally executing the "moved" version of the instruction  in 
	Z8E's memory rather than in the user program. Z8E compensates for
	the  that CALL and RELATIVE JUMP instructions are affected by the
	address at which they are executed. This entire process is total-
	ly  transparent and it allows the user to debug loops by  setting
	only a single breakpoint within the range of a loop, obviates the
	need  to clear any breakpoints which are located at  the  address
	where  execution is to resume,	and even allows breakpoints at	a
	DJNZ  $   instructions!


	HINT:
	When  proceeding from a breakpoint it is simplest to use the form
	of the GO command:    *G   P <cr>    which informs Z8E to  resume
	execution  at the address specified by the user's current program
	counter.









				       44





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	H    Display Symbol Table
	_________________________________________________________________


	The  H	command allows the user to view the symbol table  on  the
	console.  The format of the command is:

		  *H   [ARG1]  <cr>

		       where ARG1 must be a symbol name


	If  ARG1  is  omitted Z8E will display the  entire  symbol  table
	starting with the first symbol in the table.   If ARG1 is present
	Z8E  will  begin the display with that symbol.	 Z8E  displays	a
	block  of  32  symbols then waits for user input.   If	the  user
	enters	a  carriage return the the next block of  32  symbols  is
	displayed.  If	the user enteres any other character the  command
	terminates.

	If  a  symbol name entered as ARG1 cannot be found in the  symbol
	table Z8E prints a question mark.



































				       45





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	I    Input file
	_________________________________________________________________


	The  I command allows the user to load files into the  TPA  after
	the debug session has started.	The format of the command is:

	     *I   ARG1[,ARG2]  <cr>

		       ARG1 is a single unambiguous file name  con-
		       forming to standard CP/M syntax rules:
		
			    - optional	drive  name followed by  a  colon
		
			    - mandatory primary file name

			    - optional	secondary file name preceded by a
			      period	

		       ARG2 is an optional load address.  If ARG2 is  not
		       specified the named file is loaded at the start of
		       the  TPA (address 100 hex).   If ARG2 is given the
		       file will be loaded at this address.  Z8E will NOT
		       relocate  individual addresses within the file  to
		       reflect the new load address.   ARG2 may be of any
		       type.

		       NOTE:  If  no arguments are entered then Z8E  will
			      redisplay the starting address,  ending ad-
			      dress,  and the number of 256 byte pages of
			      the last file loaded.


	If Z8E detects a error in the file name specification the message
	"Syntax  error"  is  printed  on  the  console  and  the  command 
	terminates.

	If  Z8E  is unable to locate the file on the specified drive  the
	message  "File  not  found" is printed on  the  console  and  the 
	command terminates.

	Z8E contains no facilties for converting .HEX (Intel Hex  format)
	object files to loadable memory image.	 All files, regardless of
	type,  are  loaded  into memory in exactly the same form as  they
	appear on disk.   To debug a .HEX file the user should first load
	the  file with the CP/M LOAD command and save the file	with  the
	CP/M  SAVE command which produces an absolute memory image  load-
	able  by Z8E.	All .COM files are of course already in  loadable
	form and no LOADing and SAVEing is required.

	If  the  file  will  not fit into the TPA,  Z8E  will  print  the
	message:

	     Out of memory - Continue?



				       46





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	If  the  user answers "Y",  Z8E will resume loading the  file  at 
	address 100 hex if ARG2 was not entered, or at the address speci-
	fied as ARG2.	If the user types any other response, the loading
	process terminates and Z8E returns to the command level. However,
	the  user may resume loading the file at a later time by  issuing
	the I command and specifying the file name "." (a single period).  
	The  user  may	choose	to specify a new  starting  load  address
	following  the period;	if ARG2 is omitted then the load  address
	defaults back to 100 hex,  the start of the TPA.  If the user has
	done  any  subsequent  disk I/O (such as loading a  new  file  of
	disassembling  to disk) in between the time loading was suspended
	and then restarted,  Z8E will treat the file name "." as a syntax 
	error.

	The  user may occasionally need to overlay a section of code in a
	program which already resides in memory with input from a file on
	disk,  for example in modifying a BIOS in preparation for MOVCPM.
	While  this  is possible with loaders which process  .HEX  object
	files,	it is not feasible with Z8E. The user can circumvent this
	limitation  by loading the file from disk into an unused  section
	of memory and then using Z8E's move command to move only the data
	needed to accomplish the overlay.



































				       47





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	J    Animated Full Screen Debugger
	________________________________________________________________

	The  J command provides the user with the ability to "see" inside 
	the  Z80  as it executes a program.   The Z8E  animated  debugger
	allows the user to view registers, memory, and instructions while
	the  Z80  is simultaneously executing code.   In  addtion  the	J
	command  provides  the	user with the  ability	to  interactively
	single-step through a program using the full screen facilities of
	the command. The format of the J command is:

		  *J   [/] [*] [ARG1] [ARG2]


		       USE  OF	THE  J	COMMAND FOR  SINGLE  STEPPING  IS
		       DESCRIBED  AT  THE  END	OF  THIS  SECTION.   THIS
		       SECTION	DESCRIBES THE NON-INTERACTIVE VERSION  OF
		       THE  J  COMMAND DURING WHICH THE USER  TURNS  OVER
		       COMPLETE  CONTROL OF THE EXECUTION OF THE  PROGRAM
		       UNDER TEST TO Z8E.

		       ARG1  is  the starting address of the display  and
		       may  be of any valid argument type.  For  example,
		       the user may specify   *J P    to resume execution
		       at the point where it had previouly been stopped.

		       The  slash and star control subroutine tracing  as
		       follows:

		       "/"  Slash  informs  Z8E not to trace any  subrou-
			    tines at all.
		
		       "*"  Asterisk informs Z8E not to trace any subrou-
			    tine  calls to addresses located in the range
			    0 to FF.  This feature is intended to  screen
			    out  calls	to location 5 (BDOS) in order  to
			    prevent  Z8E's  and  the  user's  stack  from
			    becoming hopelessly entangled.
		
		       ARG2 represents an optional timeout paramter which
		       affects	the speed at which instructions are  exe-
		       cuted.	This  number may be in the range 0 - 255,
		       with  10 (decimal) as the default if no	value  is
		       entered. A timeout value of 10 yields approximate-
		       ly  a one half second delay between the	execution
		       of sequential instructions.   A value of 0  repre-
		       sents  NO time delay and is in actuality the fast-
		       est rate a which the J command can run.

	Once  the J command commences,	Z8E takes over the Z80	and  fur-
	nishes the user with a "peephole" into the CPU.  Z8E executes one 
	instruction  at a time in the user program pausing after each one
	to dynamically update the screen display.  The J command  divides
	the screen into three areas: register map, disassembled code, and
	memory	window.   The register map displays all registers on  the


				       48





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	top  two  lines  of the screen along with the contents of  the	F
	register which is shown in mnemonic form.   Z8E also disassembles
	18  instructions based on the current PC value and displays  them
	on  the screen;  finally,  using the parameters entered in the	W
	command,  Z8E  snapshots a block of memory and displays it  as	a
	window on the screen.

	Execution of the user program continues until any non-numeric key
	on the keyboard is pressed which ends the command.   If a numeric
	key is pressed, then Z8E responds by changing the timeout parame-
	ter on the fly.  The user may use the keys 0 - 9 as a throttle to
	govern the execution speed.   Zero being the fastest;  nine being
	the slowest.

	The command also terminates whenever a user defined breakpoint is
	reached.   That  is,  if the user had set a breakpoint via the	B
	command  and this address is reached the J command ends  and  Z8E
	prompts  the user for the next command.   If the breakpoint had a
	pass  count associated with it,  the pass count must  reach  zero
	before the J command will terminate.

	USING THE J COMMAND FOR SINGLE STEPPING

	Z8E  permits  the  user to single-step through	a  program  while
	allowing  a  continuous full-screen view of the  registers,  code
	being executed,  and the contents of a block of memory as  speci-
	fied by the K command. In order to invoke the full screen single-
	step the user enters the following command:

		  *J   [/]  [*] 

			    / instructs Z8E not to trace any  subroutines
			    at all

			    *  instructs Z8E not to trace any subroutines
			    location   below   address	 100H	and    is
			    specifically  designed to allow the user  the
			    option  of	not becoming tangled in BDOS  and
			    BIOS.

			    Note  that	this version of the J command  is
			    differentiated   from   the   non-interactive
			    version  by  the  absence  of  any	 argument
			    indicating a execution address.

	This  version allows the user to execute one instruction  in  his
	program  and then regain control at the Z8E command  level.   Z8E
	will execute the instruction pointed to by the user's current PC.
	After  the instruction is executed an ARROW ( => ) points to  the
	next instruction to be executed.

	The / and * options are only valid if the next instruction to  be
	executed  is a CALL.   If the program counter is pointing at  any
	other instruction then the / and * have no effect.



				       49





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	K    Set Memory Window Parameters for Use With the J Command
	________________________________________________________________

	The  K	command sets the starting address and block size  of  the
	memory	window display during the J command.   The format of  the
	command is:

		  *K  ARG1 [,ARG2]

		  ARG1	represents  the starting address  of  the  memory
		  block.

		  ARG2 is an optional size paramter, if omitted the block
		  size defaults to the maximum.

	The  maximum  block size is 144 decimal which  is  90  hex.   The
	starting  address of the memory block can be anywhere in  memory;
	it does not have to be within the confines of the user program.







































				       50





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	M    Move Memory
	_________________________________________________________________


	The  M	command allows the user to move blocks of date	from  any
	address in memory to any other address in memory.   The format of
	the command is:

		  *M   ARG1  ARG2  ARG3 

		       where   ARG1  =	the   starting	address  of   the
					source data block	
			
			       ARG2  =	the  ending address of the source
					data block

			       ARG3  =	the   starting	address  of   the
					destination data block	


					arguments may be of any type

	Z8E automatically decides whether a head-to-head or  tail-to-tail
	move  is  required based on the three arguments  entered.   If	a
	head-to-head  move  is needed then the first byte of  the  source
	data  block  will  be written to the first byte position  of  the
	destination data block;  the second byte of the source data block
	will  be written to the second byte position of  the  destination
	data block, and so on until the ending address of the destination
	data block is reached.

	On  the other hand,  if a tail-to-tail move is necessary Z8E will
	move  the  last byte of the source data block to  the  last  byte
	position of the destination data block, followed by the second to
	last  byte  of the source data block to the second to  last  byte
	position  of  the  destination data block,  and so on  until  the
	starting address of the destination block is reached.

	A  tail to tail move would be necessary in the following  example
	to prevent the overwriting of the destination data block:

		  *M  1000 100F 1008















				       51





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	N    Output to I/O Ports Without Pre-Read
	_________________________________________________________________


	This  command allows the user to output data to an I/O port with-
	out  first reading the port (as occurs in the  Q  command).   The
	format of the command is:

			*N   [ARG1]

			       where ARG1 is the port number to which the
				     data will be written.

				     If ARG1 is omitted then Z8E uses the
				     last  port  address which	had  been
				     input by a previous N or Q command.

	Z8E will prompt the user by displaying the current port number on
	the  left hand side of the console and postioning the cursor  two
	spaces the the right.	At this point the user can enter the data
	to  be sent to the port in the form of an  ARGUMENT-STRING.   The
	ARGUMENT-STRING  allows  the user to mix various  argument  types
	such as hex data and ASCII literal strings.   Of course the  user
	can  elect to merely output single bytes if desired.   The N com-
	mand  is particularly useful when programming various  Z80  peri-
	pheral	chips such as the DMA and SIO chips which expect  initia-
	lization bytes to arrive in a stream without intervening reads.

			*N 80
			80  'T',00,12#,998

			This  ARGUMENT-STRING would be evaluated into the
			5 bytes:  54 00 0C 09 98.  These five bytes would
			be sent to port 80 via an OTIR	instruction.   No
			delay occurs between successive bytes.	

	After the data has been entered and after it has been sent to the
	I/O  port  Z8E	reprompts the user by displaying  the  same  port
	number.   This	gives the user to oppportunity to send	addtional
	data  to the same port.   However,  by not entering data the user
	can  change  the  current port address by  entering  any  of  the
	following:















				       52





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo



		CARRIAGE    The next sequential port number in	ascending
		 RETURN     order becomes the current port address.

		UP ARROW    The next sequential port number in descending
			    order becomes the current port address.

		 =ARG	    Any argument appearing immediately after  the
			    equal  sign  (no intervening spaces) is  eva-
			    luated as an 8 bit number, and if found to be
			    valid  then it becomes the new  current  port
			    address.

		PERIOD	    Terminate command


	The  user  can	also monitor an I/O port with the  N  command  by
	enclosing  the	port number on the command line  in  parentheses.
	Monitor  mode  via  the N command is identical to that of  the	Q
	command (see Q command).





































				       53





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	O    Output Current Breakpoints to Console
	_________________________________________________________________


	The  O command allows the user to view all breakpoints	currently
	in effect.  The format of the command is:

		  *O

		       no arguments are required

	If  Z8E  finds	a symbol name corresponding to the  absolute  hex
	address of a breakpoint address in the symbol table (if a  symbol
	table  exists) then the symbol name as well as the memory address
	is displayed.  If no symbol corresponding to the address is found
	only the hex address is displayed.

	If  any  pass counts are currently in effect they  are	displayed
	next to the breakpoint address with which they are associated.






































				       54





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	P    Examine/Modify PSW (Flag Register)
	_________________________________________________________________


	The  P	command  provides a convenient method  of  examining  and
	optionally  modifying  the F(lag) register in the  user  register
	set.  The format of the command is:

	     *P

		  no arguments are required on the command line

	Upon  receipt of the P command Z8E displays the mnemonics corres-
	ponding  to  the current state of the four  user-modifiable  bits
	(sign, carry, zero, parity) in Flag register:


	     MNEMONIC		 MEANING	     BIT STATUS

		P		 positive		reset
		M		  minus 		 set

		NC		 no carry		reset
		C		  carry 		 set

		PO		parity odd		reset
		PE		parity even		 set

		NZ		 not zero		reset
		Z		   zero 		 set


	Z8E  prints  the mnemonic corresponding to the current	state  of
	each  of  the  four  flag  bits.   Z8E	then  issues  a  carriage
	return/line feed and pauses for user input.   The user may modify
	any  of  the four flag bits by typing  the  appropriate  mnemonic
	followed  by  a  carriage return.   The user may  enter  multiple
	mnemonics by separating each one with a space.	

	If  no mnemonics are entered,  no flags bits are altered and  the
	command terminates.

	If an invalid flag bit mnemonic is entered Z8E prints a  question
	mark.













				       55





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	Q    Query I/O Ports
	_________________________________________________________________

	The  Q	command allows the user flexible access to I/O	ports  by
	providing  the ability to perform single byte  input,  continuous
	input (monitor mode), and single or multi-byte output following a
	pre-read of the port. The format of the command is:
	
	     *Q   [(] [ARG1] [)]

		       where ARG1 is an 8 bit port address in the range
		       0 - 255

		       ARG1 may be any symbol type,  however if a 16  bit
		       value  is  specified  only the low order  byte  is
		       significant

		       If  no  argument is given Z8E will  use	the  most
		       recent port number as entered by the user via an N
		       or Q command.

		       If  ARG1 is enclosed in parentheses Z8E will enter
		       MONITOR MODE.


	Upon  receipt  of ARG1 Z8E will read the specified I/O	port  and
	display  the byte read as both 8 bit hexadecimal value	and  it's
	ASCII equivalent.  Command options once a byte has been read from
	the I/O port are as follows:

											
	     SINGLE BYTE INPUT

		By  entering  a SPACE immediately  following  the
		displayed  contents of the I/O port the user  can
		instruct  Z8E to continue reading from	the  same
		I/O port:

			       *Q EE
			       EE   24	$  <space>
			       EE   24	$
			
		
		By  entering a CARRIAGE RETURN following the dis-
		played	contents  of the I/O port  the	user  can
		instruct   Z8E	to  read  the  next  port  number
		(ascending order):

			       *Q EE
			       EE   24	$  <cr>
			       EF   C1	A


		By  entering a caret "^" following the  displayed 
		contents  of the I/O port the user  can  instruct


				       56





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


		Z8E  to read the previous port number (descending
		order):

			       *Q EE
			       EE   24	$  ^  (up arrow entered by user)
			       ED   06	~			


		By entering an equal sign "=" followed by a valid 
		argument,  the	user can switch to reading a  new
		port address:

			       *Q EE
			       EE   24	'$'  =90
			       90   BF	'?'		


	     CONTINUOUS INPUT (MONITOR MODE)

		Z8E provides the user with the ability to monitor
		an  input  port.   Z8E will continously read  the
		selected  input port and display the contents  on
		the  screen.   Z8E displays the byte in both  hex
		and  binary.   This  feature is  useful  in  the
		testing  of I/O ports.	Depressing any key on the
		keyboard exits monitor mode.	

	     MULTI-BYTE OUTPUT

		Following  the	read of an I/O port the user  may
		elect  to  output data.  The user  may	enter  an
		ARGUMENT-STRING which will be sent to the port on
		a  byte  by byte basis with no intervening  reads
		between outputs as shown below:

			*Q 50
			50  44	'D' 23,9,'B2E',00,F723,81
				    ^			^
				    string  as entered by
				    user appears  between
				    arrows

		The  data as entered by the user in this  example
		would  first  be converted to the 9  bytes  shown
		below:
			   23 09 42 32 45 00 F7 23 81

		These  9 bytes would then be sent to port 50  one
		byte  after another without any intervening reads
		or status checks.







				       57





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	R    Examine/Modify Register Contents
	_________________________________________________________________


	The  R	command allows the user to examine and optionally  modify
	registers  and	register pairs in the  user  register  set.   The
	format of the command is:

		  *R   ARG1  <cr> or space

		       where  ARG1  is any of the 22  register	mnemonics
		       listed below:

			     A	  B    C    D	 E    H    L
			     AF   BC   DE   HL	 IX   IY   SP
			     AF'  BC'  DE'  HL'  I    R    P	PC

			    (the  program  counter may	be  specified  as
			    either P or PC)

	To  examine a register the user enters a mnemonic from the  above
	list followed by a carriage return or a space.	 Z8E will display
	the  current contents of the register on the same line.   At this
	point the user has the option of entering an argument of any type
	if  the  contents  of the register or register	pair  are  to  be
	changed.    The  replacement value may be terminated by either	a
	carriage  return or a space.  If no value is entered Z8E issues a
	carriage return/line feed and waits for the next register  mnemo-
	nic to be entered.

	If  the user specifies a 16 bit value as the new contents of an 8
	bit register only the low order byte of the value is used.

	The command terminates when a carriage return or space is entered
	when Z8E is waiting for a register mnemonic.






















				       58





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	S    Single Step
	_________________________________________________________________

				
	The S command allows the user to execute a program instruction by
	instruction.   The  S  command provides for full tracing  of  the
	user program.  The format of the command is:

	     *S   [/] [ARG1]  <cr>
		
		       where  ARG1 is the number of instructions to  exe-
		       cute in the user program,  if no argument is given
		       Z8E defaults to 1
		
		       ARG1 may be of any type

	The slash "/" allows the user control over the tracing of subrou-
	tines.	If  a slash is included before the count (if a	count  is
	entered),  or  if the slash is the only character on the  command
	line  then subroutines will not be traced.   A slash affects only
	CALL  instructions which lie within the range of  ARG1.   In  the
	most  typical  case no ARG1 is present and the single step  count
	defaults  to 1.   If the current PC,  1000 in  this  example,  is
	pointing to a call instruction then the command:

			    *S /

		  1000	CD 56 30  RASRTN: CALL	ANYSUB
		  1003	FE 04		  CP	4
		  1005	CA 17 10	  JP	Z,AHEAD


	will  cause  the  entire  subroutine ANYSUB to	be  executed  and
	control  will  return to the user at address 1003.

	If ARG1 is omitted Z8E will transfer control to the user  program
	and  one instruction,  the one pointed to by the current contents
	of the user's program counter,	will be executed.   Following the
	execution  of the instruction (or group of instructions  if  ARG2
	was  greater  than 1) Z8E regains control and automatically  dis-
	plays the current contents of all the user registers.

	The  user may optionally indicate that more than one  instruction
	is  to	be executed by entering a value greater than 1 for  ARG1.
	Z8E will transfer control to the user program and regain  control
	only  when  the specified number of instructions have  been  exe-
	cuted.	 This feature is useful in debugging small loops; in that
	the  user can set ARG1 equal to the number of instructions in the
	range of the loop.   Z8E will display the register contents after
	each  instruction of the loop is executed and return  control  to
	the user after every iteration of the loop.

	The  single  step command always causes the execution of the  in-
	struction  pointed to by the current contents of the user's  pro-
	gram counter.	This is the instruction that appears in disassem-


				       59





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	bled  form  as	part of the output of the  "X"  command  (display 
	machine  state).   Bear in mind that ARG1 is not the  address  at
	which single stepping is to begin; it is a count to the number of
	instructions  to execute.   If the user desires to single step at
	an  address other than the one contained in the program  counter,
	then  the PC register must be modified via the R  command  before
	the single step command is issued to Z8E.

	Allowing  the  convenience of entering "S" <cr>  to  execute  one 
	instruction has the side effect of not allowing the user to abort
	the  command in between the time the "S" is typed and the <cr> is 
	entered by simply omitting an argument and typing <cr>.   If  you
	change your mind and want to cancel the command, type in an inva-
	lid  argument  as ARG1.   This will cause a question mark  to  be
	displayed; however, no instruction will be executed.

	During	block  tracing (ARG1 greater than 1) the command  may  be
	terminated by hitting any key on the keyboard.

	The  S command does not relocate instructions before execution as
	does the G command (see G command).  Hence, it is not possible to
	single step through each iteration of a DJNZ $ instruction.



































				       60





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	U    Write Symbol Table to Disk
	_________________________________________________________________


	The  U command allows the user to write the current symbol  table
	to a disk file.  The format of the command is:

		
	     *U   ARG1

		       ARG1  is the name of the file to which the  symbol
		       table is to be written.

	This  command is useful to save any symbol names entered  by  the
	user  via the A command.   The entire symbol table is written  to
	disk using the format of a .SYM file (see appendix A).	The table
	can be subsequently loaded at the next invokation of Z8E.

	Note  that since the file is stored as a .SYM formatted file  the
	user should use a  file name extension that begin with the letter
	"S".   This  is due to the fact that the next time Z8E loads this 
	symbol	file it will examine the the first character of the  file
	name extension.   If the first character is an "S" the format  is 
	assumed to be .SYM and the symbol table is built accordingly; the
	appearance  of any other letter is taken to indicate a .PRN file.

	If  a file with the name ARG1 already exists on disk it  will  be
	deleted.





























				       61





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	V    Verify two memory blocks
	_________________________________________________________________


	The  V	command allows the user to compare two blocks of  memory.
	Z8E will display all differences between the two.   The format of
	the command is:

	     *V   ARG1	ARG2  ARG3

		  where  ARG1  =  the starting address of memory block 1

			 ARG2  =  the ending address of memory block 1

			 ARG3  =  the starting address of memory block 2

	Z8E compares memory block 1 to memory block 2 byte by byte.  If a
	mismatch  occurs  Z8E will display the address in each	block  at
	which  the mismatch was found,	as well as the byte contained  at
	each address.	The comparison continues until the ending address
	is reached.

	The  user may halt the command at any time by depressing any  key
	on the keyboard.

































				       62





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	W    write memory to disk
	_________________________________________________________________


	The  W command allows the user to write the contents of memory to
	a disk file. The format of the command is:

		  *W  arg1 [arg2  arg3]

		       ARG1  is the name of a file to which writing  will
		       take place.

		       ARG2 and ARG3 are the optional starting and ending
		       addresses  of the portion of memory to be  written
		       to  the disk.   If the addresses omitted then  the
		       memory  block  to  be written is  defined  by  the
		       starting  and  ending addresses of the  last  file
		       loaded.	 These	addresses can be  redisplayed  by
		       entering the I command with no arguments.


	Z8E  always  deletes any file on disk whose name is the  same  as
	ARG1.  If no file by this name exists then Z8E will automatically
	create it.

	Z8E will echo the starting memory address and continually  update
	the ending memory address as the writing to disk takes place.






























				       63





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	X    display machine state
	_________________________________________________________________


	The   X  command  displays  the  current  contents  of	all  user
	registers.  The format of the command is:

		  *X

		       no arguments are required

	Z8E  displays displays all registers,  except the I register  and
	the R register,  on two lines of the console.	In addition,  the
	instruction pointed to by the user's program counter is disassem-
	bled and displayed on the second line.	 Think of this as the "on 
        deck"  instruction:   the instruction that will be executed  upon 
	the receipt of the next G (GO) or S (SINGLE STEP) command.

	To inspect the I or R registers use the R command.






































				       64





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	Y    fill memory
	_________________________________________________________________


	The  Y command fills a user specified block of memory with a user
	specified  pattern of bytes,  the length of which is limited only
	by the length of Z8E's input buffer which is 80 bytes long:

		  *Y  ARG1  ARG2  ARG3	<cr>

		       where  ARG1  =  the  starting address of the block
				       to fill

			      ARG2  =  the ending address of the block to
				       fill

			      ARG3  =  is the data pattern to be  written
				       to  memory.   ARG3 is evaluated by
				       Z8E as type ARGUMENT-STRING  which
				       may  be of any length in the range
				       of  1 through the number of  bytes
				       remaining in the input buffer once
				       ARG1 and ARG2 have been input.


	The Y command gives the user the capability to initialize memory
	to  any  data pattern.	 The capability  of  entering  multi-byte
	strings  as the data pattern with which to fill memory allows the
	user to store repeating patterns of data in memory with a  single
	command. For example if the user entered the command:

		  *Y 1000 127C 'abcd',16,77

	Z8E  would  begin writing the 6 byte pattern  (61 62 63 64 16 77)
	entered  as ARG3 starting at address 1000.   This  pattern  would
	repeat at address 1006, 100C, 1012, etc.

	The command ends after a byte is written to the ARG2 address even
	if  this byte does not represent the last byte in the ARG3 block.
	In the above example the command would end when a byte is written
	to address 127C even if that byte is not 77.
















				       65





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	Z    disassemble command
	_________________________________________________________________


	The  Z	command allows the user to disassemble a block	of  data.
	Z8E  performs  disassembly,  which is the translation  of  binary
	memory data into source code format,  using the full Z80 instruc-
	tion set and Zilog mnemonics.	The resultant source code may  be
	directed  to the console or to the console and a disk file simul-
	taneously.  Z8E also allows the user to disassemble interactively
	when ARG2 is equal to 1. The format of the command is:

		  *Z  ARG1 [ARG2 ARG3]	<cr>

		       where   ARG1  =	 the start address at which disa-
					 ssembly is to begin

			       ARG2  =	 is  optional and represents  the
					 upper	limit of the  disassembly
					 process (see details below)

			       ARG3  =	 is  an optional file name speci-
					 fication for disassembly to disk	

		       ARG1 may be of any argument type.

		       ARG2  is  treated in one of two ways depending  on
		       its  value:

			 1) If	ARG2 evaluates to a number between 1  and
			    255  (decimal) Z8E will disassemble in "block 
                            mode" and ARG2 becomes a count of the  number 
			    of instructions per block to disassemble.  As
			    will  be  explained below,	Z8E pauses  after
			    each  block  is disassembled and  allows  the
			    user to continue or to terminate the command.

			    If ARG2 is omitted altogether a default block
			    size of 1 is used.	
			
			    Whenever ARG2 equals 1,  either explicitly or
			    by default,  Z8E allows interactive disassem-
			    bly which allows the user to choose the  out-
			    put  format of the data.   Interactive disas-
			    sembly is discussed below.

			 2) If	ARG2 evaluates to a number  greater  than
			    255  it  is assumed to be an ending  address.
			    In	this case disassembly will  proceed  from
			    starting  address  (ARG1) to  ending  address
			    (ARG2) and no user intervention is required.

		       ARG3,  if present,  is assumed to be the name of a
		       disk  file into which the disassembled output will
		       be written.   Z8E searches the specified disk  for


				       66





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


		       the  named file.   If the file is found,  then all
		       disassembled output will be written to  it,  over-
		       writing any data that existed there.   If the file
		       does  not exist the file will be created using the
		       name specified in ARG3.	

		       NOTE:  If  ARG3 is present ARG2 must be explicitly
		       specified, otherwise Z8E will mistakenly treat the
		       file name as ARG2.

	Z8E outputs to the console using the following format:

	     ADDRESS	  OBJECT CODE	   LABEL:   OPCODE    OPERAND


	Z8E writes to disk using the following formart:
					
					   LABEL:   OPCODE    OPERAND

	Z8E  disassembles  memory block by block in  the  user	specified
	block  size.   After  each  block is output Z8E pauses	for  user
	input.	 A carriage return input by the user terminates the  com-
	mand,  while  any  other  character causes the next block  to  be
	disassembled (unless interactive mode is in effect).  Perhaps the
	most convenient way to disassemble is to specify a count of  one,
	either explicity or by omitting ARG2, and to use the space bar as
	an  on/off switch.   Holding down the space bar produces  output,
	releasing  the	space  bar ends output.

	Z8E's  disassembler is especially powerful when used in  conjunc-
	tion  with the symbol facility.   By building a symbol table with
	both  .PRN and .SYM files,  and/or creating user  defined  symbol
	names  via  the  A command,  the user can virtually  recreate  an
	assembler output listing (minus the comments) with Z8E	inserting
	labels and symbolic operands wherever possible.

	If  Z8E cannot match  an operand in the disassembled  instruction
	to  a corresponding symbol in the symbol table,  or if no  symbol
	table exists, Z8E uses the hexadecimal value.

	If multiple symbols in the symbol table are equal to the same  16
	bit  value  or address,  Z8E disassembles using the first  symbol
	name  encountered  in  the search of the symbol  table	which  is
	equated to the 16 bit operand specified in the instruction  being
	disassembled.  This   will unavoidably produce an occasional mis-
	named  operand when more than one symbol name is equated  to  the
	same  16  bit value.

	Z8E  does not substitute symbol names in those	Z80  instructions
	which reference 8 bit immediate data (ie.  LD  A,24H).	Eight bit
	immediate  data  is disassembled as a quoted ASCII  character  if
	it's absolute value is in the range 20 hex to 7E hex;  otherwise,
	it is disassembled as a hex byte.

	Output by Z8E to a disk file is instantly assemblable by most any


				       67





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	assembler which accepts Zilog mnemonics without any modifications
	other than adding an END statement at the end of the file.

	When  disassembling a block of memory (starting address to ending
	address)  the  disassembly process may be halted at any  time  by
	depressing any key on the keyboard.

	Interactive  disassembly allows the user to specify the format of
	the source code produced by disassembly on a line by line  basis.
	Interactive  mode,  which  is always in effect whenever  ARG2  is
	equal to 1,  causes Z8E to pause after each instruction is disas-
	sembled.   This  pause for input permits the user to enter one of
	the following commands to choose the desired output format:


	    CHARACTER		 OUTPUT FORMAT	       EXAMPLE

	
		A		  ASCII DEFB	      DEFB   'Q'

		B		   HEX DEFB	      DEFB   23H

		C		     CODE	      EX     DE,HL

		D		   HEX DEFW	      DEFW   02FCH  or	
						      DEFW   LABEL

		;		  add COMMENT	      ;This is a Comment

	     carriage		(terminate command)
	      return
	
	     any other		 PROCEED TO THE
	     character		NEXT INSTRUCTION


	     ASCII DEFB:
	     The  contents of memory at the current disassembly  ad-
	     dress is converted to a quoted ASCII character.  Values
	     less  than hexadecimal 20 (ASCII space) or greater than
	     hexadecimal  7E  (ASCII tilde) cannot  be	disassembled
	     into this format.	

	     HEX DEFB:
	     The 8 bit contents of memory at the current disassembly
	     address are converted to a hex byte.

	     CODE:
	     This  is the normal default for  disassembly.   As  Z8E
	     moves  on	to a new address it will always display  the
	     contents  of memory as a Z80 instruction.	 The "C"  is 
	     only  needed to redisplay the contents of memory as  an
	     instruction had one of the other characters (A,  B,  or
	     D) already have been entered.



				       68





	Z8E - Z80 DEBUG MONITOR 			     Rick Surwilo


	     HEX DEFW:
	     The contents of the two bytes of memory starting at the
	     loaction of the current disassembly address are  output
	     as  a  define  word directive.   The  byte  pointed  to
	     directly by the current disassembly address becomes the
	     low order byte of the operand.  The byte at disassembly
	     address plus one becomes the high order byte.

	     NOTE:
		    If	Z8E had just disassembled  a  multi-
		    byte  Z80  instruction and the user  en-
		    tered any of the characters listed above
		    (A,  B, C, or D) only the first byte, or
		    first  two for "D",  of the  instruction 
		    would  be  converted  to  the  requested
		    format.   The  remaining  bytes  of  the
		    instruction  would be treated as  a  new
		    Z80  instruction once the user proceeded
		    to the next disassembly address.

	     ADDING COMMENTS
	     Z8E  allows  the  user to add one comment per  line  of
	     disassembled code.  If MAXLEN is set to 6 then comments
	     may be up to 29 characters in length.  If MAXLEN is set
	     to  14  then  comments may be up to  16  characters  in
	     length.


	If  during  disassembly,  Z8E  encounters data	which  cannot  be
	disassembled  into  a valid Z80 instruction it will  display  the
	data as DEFB's.


























				       69





				   APPENDIX A









	FILE FORMAT FOR SYMBOL TABLES

	Z8E  is  currently set up to be able to read any of  the  listing
	files  which appear below:

	    1. Microsoft   MACRO-80    V3.37  .PRN Files  May 8, 1980
	    2. Microsoft   MACRO-80    V3.44  .PRN Files  Dec 9, 1981
	    3. Microsoft   LINK-80     V3.44  .SYM Files  Dec 9, 1981
	    4. SLR Systems Z80ASM      V1.07  .LST Files
	    5. SLR Systems SLRNK       V1.07  .SYM Files

	The unique characteristics of each are:

	    MACRO-80 V3.37

	    Z8E  searches  for	the 8 byte string "Symbols:"  in  the 
	    file.   Once this string is found,	Z8E expects an	ASCII
	    carriage  return character and an ASCII line feed charac-
	    ter  to be the  next two bytes in the file.   The  symbol
	    table listing should begin in the next character position
	    in the file.

	    Each  line	of  the symbol table  listing  contains  four
	    symbol names and an associated address.

	    If	the character following the symbol's hex value is  an
	    apostophe,	the  symbol is considered to be program rela-
	    tive.  If  the user specified a bias in the command  line
	    the bias will be added to the symbol's value.

	    If	the character following the symbol's hex value is  an
	    "I"  (meaning  that the symbol is globally defined)  then 
	    the  character following the "I" is  examined.   If  this 
	    character is an apostrophe it is considered to be program
	    relative  and  the	bias,  if specified is added  to  the
	    value.

	    If	the character following the hex symbol value  or  the
	    "I" is any character besides an apostrophe, the symbol is 
	    considered absolute and the bias will not be added.

	    The  file should be terminated with the CP/M  end-of-file
	    character (control Z which is equivalent to a hex 1A).

	    If	the string "Symbols" is never found,  Z8E prints  the 
	    message:  Symbol Table not Found




				       70





				   APPENDIX A


	    MACRO-80  V3.44

	    Z8E  searches  for	the 8 byte string "Symbols:"  in  the 
	    file.   Once this string is found,	Z8E expects an	ASCII
	    carriage  return character and an ASCII line feed charac-
	    ter  to be the  next two bytes in the file.   The  symbol
	    table listing should begin in the next character position
	    in the file.

	    In	this  release of MACRO-80 the format  of  the  symbol
	    table is completely opposite of V3.37.   That is, the hex
	    value appears before the symbol name.  In addition, these
	    hex value/symbol name combination appear three per line.

	    The  character  appearing after the hex value  is  inter-
	    preted as described for version 3.37.

	    If	the string "Symbols" is never found,  Z8E prints  the 
	    message:  Symbol Table not Found

	
	    LINK-80  V3.44

	    LINK-80  can  optionally produce a link map  (.SYM	file)
	    which  lists  all  globally defined symbols if  the  user
	    specifies  the  "Y" option the  L80  command  line.   Z8E 
	    treats  all symbols names loaded from a LINK-80 .SYM file
	    as absolute (non-relocatable)  addresses.	Nevertheless,
	    if	the user specifies a bias,  it will be added to every
	    symbol value read in from the .SYM file.

	    Z8E  expects  the first symbol value in a  .SYM  file  to
	    begin  in  the  first byte position in  the  file.	 Each
	    symbol value consists of four hexadecimal bytes in	ASCII
	    followed  by a tab character.   Immediately after the tab
	    character is the symbol name which may be between one and
	    six alphanumeric characters in length.   The symbol  name
	    is	followed  by a tab and the sequence  repeats.	Every
	    fourth  symbol value/symbol name pair should be  followed
	    by a carriage return and line feed.

	    The  file should be terminated with the CP/M  end-of-file
	    character (control Z which is equivalent to a hex 1A).


	    Z80ASM

	    Z80ASM  may  be configured to produce either  80  or  132
	    column output.

	    Z8E searches for the 8 byte string "Symbol Table:" in the 
	    file.   This  string need not be at the beginning of  the
	    file;  Z8E will scan the entire file looking for it. Once
	    this  string  is found,  Z8E expects  an  ASCII  carriage
	    return  character and an ASCII line feed character to  be


				       71





				   APPENDIX A


	    the  next two bytes in the file.   The symbol table list-
	    ing  should  begin in the next character position in  the
	    file.

	    In	a Z80ASM .LST file the hex value appears  before  the
	    symbol  name.  Hex value/symbol name combinations  appear
	    three per line.  Z80ASM symbol names may contain up to 16
	    characters.  Z8E will accept the first 14 characters of a
	    symbol name if MAXLEN is set to 14 or the first 6 charac-
	    ters if MAXLEN is set to 6. 

	    If the string "Symbol Table:" is never found,  Z8E prints 
	    the message:

			     Symbol Table Not Found

	    SLRNK

	    SLRNK  can	optionally  produce a link  map  (.SYM	File)
	    similar  to the one produced by Link-80.  Z8E treats  all
	    symbols  loaded from a SLRNK .SYM file as  absolute  sym-
	    bols.  However, as in the case of Link-80 .SYM files, Z8E
	    will  add  a  relocation bias to each symbol  if  one  is
	    specified.

	    Each  symbol value in a SLRNK .SYM file consists of  four
	    hexadecimal  bytes	followed by a space followed  by  the
	    symbol  name.   The symbol name is followed by two	ASCII
	    tab characters.

	    Use SLRNK's /M option to produce a link map.


	NOTE:

	    While reading in a MACRO-80 .PRN file,  or a Z80ASM  .LST
	    file,  Z8E is capable of reading an entire assembly list-
	    ing  file  looking for the "Symbols:" string  or  "Symbol 
	    Table:" string.  These strings need not be located at the 
            beginning  of  the file.   However,  the loading  of  the 
            symbol  table  will  be speeded up  considerably  if  the 
            symbol  table  is  the only data in the  file.   This  is 
            accomplished quite easily in both MACRO-80 by turning off 
            the  listing  during an assembly through the use  of  the 
            .XLIST directive.  The listing can then be turned back on 
            just prior to the END directive via a .LIST directive  to 
            ensure that the symbol table is written to disk.

            If  you  are using Z80ASM use the /S option  to  instruct 
            Z80ASM to produce a symbol file.



        Z8E  is able to process symbol tables which occupy multiple pages 
        in any of the file types mentioned above.  Headings which precede 


                                       72





                                   APPENDIX A


        each page are automatically ignored by Z8E. 






























































                      APPENDIX B - ZILOG MNEMONICS       


                                
                                
          0049                  NN     EQU   49H       ;8 BIT OPERAND
          123F                  NNNN   EQU   123FH     ;16 BIT   OPERAND
          0036                  INDEX  EQU   36H       ;INDEX REGISTER INDEX

          010B    8E                   ADC   A,(HL)
          010C    DD 8E 36             ADC   A,(IX+INDEX)
          010F    FD 8E 36             ADC   A,(IY+INDEX)
          0112    8F                   ADC   A,A
          0113    88                   ADC   A,B
          0114    89                   ADC   A,C
          0115    8A                   ADC   A,D
          0116    8B                   ADC   A,E
          0117    8C                   ADC   A,H
          0118    8D                   ADC   A,L
          0119    CE 49                ADC   A,NN
          011B    ED 4A                ADC   HL,BC
          011D    ED 5A                ADC   HL,DE
          011F    ED 6A                ADC   HL,HL
          0121    ED 7A                ADC   HL,SP
                                
                                
          0123    86                   ADD   A,(HL)
          0124    DD 86 36             ADD   A,(IX+INDEX)
          0127    FD 86 36             ADD   A,(IY+INDEX)
          012A    87                   ADD   A,A
          012B    80                   ADD   A,B
          012C    81                   ADD   A,C
          012D    82                   ADD   A,D
          012E    83                   ADD   A,E
          012F    84                   ADD   A,H
          0130    85                   ADD   A,L
          0131    C6 49                ADD   A,NN
          0133    09                   ADD   HL,BC
          0134    19                   ADD   HL,DE
          0135    29                   ADD   HL,HL
          0136    39                   ADD   HL,SP
          0137    DD 09                ADD   IX,BC
          0139    DD 19                ADD   IX,DE
          013B    DD 29                ADD   IX,IX
          013D    DD 39                ADD   IX,SP
          013F    FD 09                ADD   IY,BC
          0141    FD 19                ADD   IY,DE
          0143    FD 29                ADD   IY,IY
          0145    FD 39                ADD   IY,SP
                                

          0147    A6                   AND   (HL)
          0148    DD A6 36             AND   (IX+INDEX)
          014B    FD A6 36             AND   (IY+INDEX)
          014E    A7                   AND   A
          014F    A0                   AND   B
          0150    A1                   AND   C
          0151    A2                   AND   D


                                       74





                      APPENDIX B - ZILOG MNEMONICS       


          0152    A3                   AND   E
          0153    A4                   AND   H
          0154    A5                   AND   L
          0155    E6 49                AND   NN
                                
                                
          0157    CB 46                BIT   0,(HL)
          0159    DD CB 36 46          BIT   0,(IX+INDEX)
          015D    FD CB 36 46          BIT   0,(IY+INDEX)
          0161    CB 47                BIT   0,A
          0163    CB 40                BIT   0,B
          0165    CB 41                BIT   0,C
          0167    CB 42                BIT   0,D
          0169    CB 43                BIT   0,E
          016B    CB 44                BIT   0,H
          016D    CB 45                BIT   0,L
                                
                                
          016F    CB 4E                BIT   1,(HL)
          0171    DD CB 36 4E          BIT   1,(IX+INDEX)
          0175    FD CB 36 4E          BIT   1,(IY+INDEX)
          0179    CB 4F                BIT   1,A
          017B    CB 48                BIT   1,B
          017D    CB 49                BIT   1,C
          017F    CB 4A                BIT   1,D
          0181    CB 4B                BIT   1,E
          0183    CB 4C                BIT   1,H
          0185    CB 4D                BIT   1,L
                                
                                
          0187    CB 56                BIT   2,(HL)
          0189    DD CB 36 56          BIT   2,(IX+INDEX)
          018D    FD CB 36 56          BIT   2,(IY+INDEX)
          0191    CB 57                BIT   2,A
          0193    CB 50                BIT   2,B
          0195    CB 51                BIT   2,C
          0197    CB 52                BIT   2,D
          0199    CB 53                BIT   2,E
          019B    CB 54                BIT   2,H
          019D    CB 55                BIT   2,L
                                
                                
          019F    CB 5E                BIT   3,(HL)
          01A1    DD CB 36 5E          BIT   3,(IX+INDEX)
          01A5    FD CB 36 5E          BIT   3,(IY+INDEX)
          01A9    CB 5F                BIT   3,A
          01AB    CB 58                BIT   3,B
          01AD    CB 59                BIT   3,C
          01AF    CB 5A                BIT   3,D
          01B1    CB 5B                BIT   3,E
          01B3    CB 5C                BIT   3,H
          01B5    CB 5D                BIT   3,L
                                
                                
          01B7    CB 66                BIT   4,(HL)


                                       75





                      APPENDIX B - ZILOG MNEMONICS       


          01B9    DD CB 36 66          BIT   4,(IX+INDEX)
          01BD    FD CB 36 66          BIT   4,(IY+INDEX)
          01C1    CB 67                BIT   4,A
          01C3    CB 60                BIT   4,B
          01C5    CB 61                BIT   4,C
          01C7    CB 62                BIT   4,D
          01C9    CB 63                BIT   4,E
          01CB    CB 64                BIT   4,H
          01CD    CB 65                BIT   4,L
                                
                                
          01CF    CB 6E                BIT   5,(HL)
          01D1    DD CB 36 6E          BIT   5,(IX+INDEX)
          01D5    FD CB 36 6E          BIT   5,(IY+INDEX)
          01D9    CB 6F                BIT   5,A
          01DB    CB 68                BIT   5,B
          01DD    CB 69                BIT   5,C
          01DF    CB 6A                BIT   5,D
          01E1    CB 6B                BIT   5,E
          01E3    CB 6C                BIT   5,H
          01E5    CB 6D                BIT   5,L
                                
                                
          01E7    CB 76                BIT   6,(HL)
          01E9    DD CB 36 76          BIT   6,(IX+INDEX)
          01ED    FD CB 36 76          BIT   6,(IY+INDEX)
          01F1    CB 77                BIT   6,A
          01F3    CB 70                BIT   6,B
          01F5    CB 71                BIT   6,C
          01F7    CB 72                BIT   6,D
          01F9    CB 73                BIT   6,E
          01FB    CB 74                BIT   6,H
          01FD    CB 75                BIT   6,L
                                
                                
          01FF    CB 7E                BIT   7,(HL)
          0201    DD CB 36 7E          BIT   7,(IX+INDEX)
          0205    FD CB 36 7E          BIT   7,(IY+INDEX)
          0209    CB 7F                BIT   7,A
          020B    CB 78                BIT   7,B
          020D    CB 79                BIT   7,C
          020F    CB 7A                BIT   7,D
          0211    CB 7B                BIT   7,E
          0213    CB 7C                BIT   7,H
          0215    CB 7D                BIT   7,L
                                
                                
          0217    DC 123F              CALL   C,NNNN
          021A    FC 123F              CALL   M,NNNN
          021D    D4 123F              CALL   NC,NNNN
          0220    CD 123F              CALL   NNNN
          0223    C4 123F              CALL   NZ,NNNN
          0226    F4 123F              CALL   P,NNNN
          0229    EC 123F              CALL   PE,NNNN
          022C    E4 123F              CALL   PO,NNNN


                                       76





                      APPENDIX B - ZILOG MNEMONICS       


          022F    CC 123F              CALL   Z,NNNN
                                
                                
          0232    3F                   CCF
                                
                                
          0233    BE                   CP   (HL)
          0234    DD BE 36             CP   (IX+INDEX)
          0237    FD BE 36             CP   (IY+INDEX)
          023A    BF                   CP   A
          023B    B8                   CP   B
          023C    B9                   CP   C
          023D    BA                   CP   D
          023E    BB                   CP   E
          023F    BC                   CP   H
          0240    BD                   CP   L
          0241    FE 49                CP   NN
                                
                                
          0243    ED A9                CPD
          0245    ED B9                CPDR
          0247    ED A1                CPI
          0249    ED B1                CPIR
                                
                                
          024B    2F                   CPL
                                
                                
          024C    27                   DAA
                                
                                
          024D    35                   DEC   (HL)
          024E    DD 35 36             DEC   (IX+INDEX)
          0251    FD 35 36             DEC   (IY+INDEX)
          0254    3D                   DEC   A
          0255    05                   DEC   B
          0256    0B                   DEC   BC
          0257    0D                   DEC   C
          0258    15                   DEC   D
          0259    1B                   DEC   DE
          025A    1D                   DEC   E
          025B    25                   DEC   H
          025C    2B                   DEC   HL
          025D    DD 2B                DEC   IX
          025F    FD 2B                DEC   IY
          0261    2D                   DEC   L
          0262    3B                   DEC   SP
                                
                                
          0263    F3                   DI
                                
                                
          0264    10 04                DJNZ   $+6
                                
                                


                                       77





                      APPENDIX B - ZILOG MNEMONICS       


          0266    FB                   EI
                                
                                
          0267    E3                   EX   (SP),HL
          0268    DD E3                EX   (SP),IX
          026A    FD E3                EX   (SP),IY
          026C    08                   EX   AF,AF'          
          026D    EB                   EX   DE,HL
          026E    D9                   EXX
                                
                                
          026F    76                   HALT
                                
                                
          0270    ED 46                IM   0
          0272    ED 56                IM   1
          0274    ED 5E                IM   2
                                
                                
          0276    ED 78                IN   A,(C)
          0278    DB 49                IN   A,(NN)
          027A    ED 40                IN   B,(C)
          027C    ED 48                IN   C,(C)
          027E    ED 50                IN   D,(C)
          0280    ED 58                IN   E,(C)
          0284    ED 60                IN   H,(C)
          0286    ED 68                IN   L,(C)
                                
                                
          0288    34                   INC   (HL)
          0289    DD 34 36             INC   (IX+INDEX)
          028C    FD 34 36             INC   (IY+INDEX)
          028F    3C                   INC   A
          0290    04                   INC   B
          0291    03                   INC   BC
          0292    0C                   INC   C
          0293    14                   INC   D
          0294    13                   INC   DE
          0295    1C                   INC   E
          0296    24                   INC   H
          0297    23                   INC   HL
          0298    DD 23                INC   IX
          029A    FD 23                INC   IY
          029C    2C                   INC   L
          029D    33                   INC   SP
                                
                                
          029E    ED AA                IND
          02A0    ED BA                INDR
          02A2    ED A2                INI
          02A4    ED B2                INIR


          02A6    E9                   JP   (HL)
          02A7    DD E9                JP   (IX)


                                       78





                      APPENDIX B - ZILOG MNEMONICS       


          02A9    FD E9                JP   (IY)
          02AB    DA 123F              JP   C,NNNN
          02AE    FA 123F              JP   M,NNNN
          02B1    D2 123F              JP   NC,NNNN
          02B4    C3 123F              JP   NNNN
          02B7    C2 123F              JP   NZ,NNNN
          02BA    F2 123F              JP   P,NNNN
          02BD    EA 123F              JP   PE,NNNN
          02C0    E2 123F              JP   PO,NNNN
          02C3    CA 123F              JP   Z,NNNN
                                
                                
          02C6    38 04                JR   C,$+6
          02C8    18 04                JR   $+6
          02CA    30 04                JR   NC,$+6
          02CC    20 04                JR   NZ,$+6
          02CE    28 04                JR   Z,$+6
                                
                                
          02D0    02                   LD   (BC),A
          02D1    12                   LD   (DE),A
          02D2    77                   LD   (HL),A
          02D3    70                   LD   (HL),B
          02D4    71                   LD   (HL),C
          02D5    72                   LD   (HL),D
          02D6    73                   LD   (HL),E
          02D7    74                   LD   (HL),H
          02D8    75                   LD   (HL),L
          02D9    36 49                LD   (HL),NN
                                
                                
          02DB    DD 77 36             LD   (IX+INDEX),A
          02DE    DD 70 36             LD   (IX+INDEX),B
          02E1    DD 71 36             LD   (IX+INDEX),C
          02E4    DD 72 36             LD   (IX+INDEX),D
          02E7    DD 73 36             LD   (IX+INDEX),E
          02EA    DD 74 36             LD   (IX+INDEX),H
          02ED    DD 75 36             LD   (IX+INDEX),L
          02F0    DD 36 36 49          LD   (IX+INDEX),NN
                                
                                
          02F4    FD 77 36             LD   (IY+INDEX),A
          02F7    FD 70 36             LD   (IY+INDEX),B
          02FA    FD 71 36             LD   (IY+INDEX),C
          02FD    FD 72 36             LD   (IY+INDEX),D
          0300    FD 73 36             LD   (IY+INDEX),E
          0303    FD 74 36             LD   (IY+INDEX),H
          0306    FD 75 36             LD   (IY+INDEX),L
          0309    FD 36 36 49          LD   (IY+INDEX),NN
                                
                                
          030D    32 123F              LD   (NNNN),A
          0310    ED 43 123F           LD   (NNNN),BC
          0314    ED 53 123F           LD   (NNNN),DE
          0318    22 123F              LD   (NNNN),HL


                                       79





                      APPENDIX B - ZILOG MNEMONICS       


          031B    DD 22 123F           LD   (NNNN),IX
          031F    FD 22 123F           LD   (NNNN),IY
          0323    ED 73 123F           LD   (NNNN),SP
                                
                                
          0327    0A                   LD   A,(BC)
          0328    1A                   LD   A,(DE)
          0329    7E                   LD   A,(HL)
          032A    DD 7E 36             LD   A,(IX+INDEX)
          032D    FD 7E 36             LD   A,(IY+INDEX)
          0330    3A 123F              LD   A,(NNNN)
          0333    7F                   LD   A,A
          0334    78                   LD   A,B
          0335    79                   LD   A,C
          0336    7A                   LD   A,D
          0337    7B                   LD   A,E
          0338    7C                   LD   A,H
          0339    ED 57                LD   A,I
          033B    7D                   LD   A,L
          033C    3E 49                LD   A,NN
          033E    ED 5F                LD   A,R
                                
                                
          0340    46                   LD   B,(HL)
          0341    DD 46 36             LD   B,(IX+INDEX)
          0344    FD 46 36             LD   B,(IY+INDEX)
          0347    47                   LD   B,A
          0348    40                   LD   B,B
          0349    41                   LD   B,C
          034A    42                   LD   B,D
          034B    43                   LD   B,E
          034C    44                   LD   B,H
          034D    45                   LD   B,L
          034E    06 49                LD   B,NN
                                
                                
          0350    ED 4B 123F           LD   BC,(NNNN)
          0354    01 123F              LD   BC,NNNN
                                
                                
          0357    4E                   LD   C,(HL)
          0358    DD 4E 36             LD   C,(IX+INDEX)
          035B    FD 4E 36             LD   C,(IY+INDEX)
          035E    4F                   LD   C,A
          035F    48                   LD   C,B
          0360    49                   LD   C,C
          0361    4A                   LD   C,D
          0362    4B                   LD   C,E
          0363    4C                   LD   C,H
          0364    4D                   LD   C,L
          0365    0E 49                LD   C,NN
                                


          0367    56                   LD   D,(HL)


                                       80





                      APPENDIX B - ZILOG MNEMONICS       


          0368    DD 56 36             LD   D,(IX+INDEX)
          036B    FD 56 36             LD   D,(IY+INDEX)
          036E    57                   LD   D,A
          036F    50                   LD   D,B
          0370    51                   LD   D,C
          0371    52                   LD   D,D
          0372    53                   LD   D,E
          0373    54                   LD   D,H
          0374    55                   LD   D,L
          0375    16 49                LD   D,NN
                                
                                
          0377    ED 5B 123F           LD   DE,(NNNN)
          037B    11 123F              LD   DE,NNNN
                                
                                
          037E    5E                   LD   E,(HL)
          037F    DD 5E 36             LD   E,(IX+INDEX)
          0382    FD 5E 36             LD   E,(IY+INDEX)
          0385    5F                   LD   E,A
          0386    58                   LD   E,B
          0387    59                   LD   E,C
          0388    5A                   LD   E,D
          0389    5B                   LD   E,E
          038A    5C                   LD   E,H
          038B    5D                   LD   E,L
          038C    1E 49                LD   E,NN
                                
                                
          038E    66                   LD   H,(HL)
          038F    DD 66 36             LD   H,(IX+INDEX)
          0392    FD 66 36             LD   H,(IY+INDEX)
          0395    67                   LD   H,A
          0396    60                   LD   H,B
          0397    61                   LD   H,C
          0398    62                   LD   H,D
          0399    63                   LD   H,E
          039A    64                   LD   H,H
          039B    65                   LD   H,L
          039C    26 49                LD   H,NN
                                
                                
          039E    2A 123F              LD   HL,(NNNN)
          03A1    21 123F              LD   HL,NNNN
                                
                                
          03A4    ED 47                LD   I,A
                                
                                
          03A6    DD 2A 123F           LD   IX,(NNNN)
          03AA    DD 21 123F           LD   IX,NNNN
                                
                                
          03AE    FD 2A 123F           LD   IY,(NNNN)
          03B2    FD 21 123F           LD   IY,NNNN


                                       81





                      APPENDIX B - ZILOG MNEMONICS       





          03B6    6E                   LD   L,(HL)
          03B7    DD 6E 36             LD   L,(IX+INDEX)
          03BA    FD 6E 36             LD   L,(IY+INDEX)
          03BD    6F                   LD   L,A
          03BE    68                   LD   L,B
          03BF    69                   LD   L,C
          03C0    6A                   LD   L,D
          03C1    6B                   LD   L,E
          03C2    6C                   LD   L,H
          03C3    6D                   LD   L,L
          03C4    2E 49                LD   L,NN
                                
                                
          03C6    ED 4F                LD   R,A
                                
                                
          03C8    ED 7B 123F           LD   SP,(NNNN)
          03CC    F9                   LD   SP,HL
          03CD    DD F9                LD   SP,IX
          03CF    FD F9                LD   SP,IY
          03D1    31 123F              LD   SP,NNNN
                                
                                
          03D4    ED A8                LDD
          03D6    ED B8                LDDR
          03D8    ED A0                LDI
          03DA    ED B0                LDIR
                                
                                
          03DC    ED 44                NEG
                                
                                
          03DE    00                   NOP
                                
                                
          03DF    B6                   OR   (HL)
          03E0    DD B6 36             OR   (IX+INDEX)
          03E3    FD B6 36             OR   (IY+INDEX)
          03E6    B7                   OR   A
          03E7    B0                   OR   B
          03E8    B1                   OR   C
          03E9    B2                   OR   D
          03EA    B3                   OR   E
          03EB    B4                   OR   H
          03EC    B5                   OR   L
          03ED    F6 49                OR   NN
                                
                                
          03EF    ED BB                OTDR
          03F1    ED B3                OTIR
                                
                                


                                       82





                      APPENDIX B - ZILOG MNEMONICS       


          03F3    ED 79                OUT   (C),A
          03F5    ED 41                OUT   (C),B



          03F7    ED 49                OUT   (C),C
          03F9    ED 51                OUT   (C),D
          03FB    ED 59                OUT   (C),E
          03FD    ED 61                OUT   (C),H
          03FF    ED 69                OUT   (C),L
          0401    D3 49                OUT   (NN),A
                                
                                
          0403    ED AB                OUTD
          0405    ED A3                OUTI
                                
                                
          0407    F1                   POP   AF
          0408    C1                   POP   BC
          0409    D1                   POP   DE
          040A    E1                   POP   HL
          040B    DD E1                POP   IX
          040D    FD E1                POP   IY
                                
                                
          040F    F5                   PUSH   AF
          0410    C5                   PUSH   BC
          0411    D5                   PUSH   DE
          0412    E5                   PUSH   HL
          0413    DD E5                PUSH   IX
          0415    FD E5                PUSH   IY
                                
                                
          0417    CB 86                RES   0,(HL)
          0419    DD CB 36 86          RES   0,(IX+INDEX)
          041D    FD CB 36 86          RES   0,(IY+INDEX)
          0421    CB 87                RES   0,A
          0423    CB 80                RES   0,B
          0425    CB 81                RES   0,C
          0427    CB 82                RES   0,D
          0429    CB 83                RES   0,E
          042B    CB 84                RES   0,H
          042D    CB 85                RES   0,L
                                
                                
          042F    CB 8E                RES   1,(HL)
          0431    DD CB 36 8E          RES   1,(IX+INDEX)
          0435    FD CB 36 8E          RES   1,(IY+INDEX)
          0439    CB 8F                RES   1,A
          043B    CB 88                RES   1,B
          043D    CB 89                RES   1,C
          043F    CB 8A                RES   1,D
          0441    CB 8B                RES   1,E
          0443    CB 8C                RES   1,H
          0445    CB 8D                RES   1,L


                                       83





                      APPENDIX B - ZILOG MNEMONICS       


                                
                                
          0447    CB 96                RES   2,(HL)
          0449    DD CB 36 96          RES   2,(IX+INDEX)
          044D    FD CB 36 96          RES   2,(IY+INDEX)
          0451    CB 97                RES   2,A
          0453    CB 90                RES   2,B
          0455    CB 91                RES   2,C
          0457    CB 92                RES   2,D
          0459    CB 93                RES   2,E
          045B    CB 94                RES   2,H
          045D    CB 95                RES   2,L
                                
                                
          045F    CB 9E                RES   3,(HL)
          0461    DD CB 36 9E          RES   3,(IX+INDEX)
          0465    FD CB 36 9E          RES   3,(IY+INDEX)
          0469    CB 9F                RES   3,A
          046B    CB 98                RES   3,B
          046D    CB 99                RES   3,C
          046F    CB 9A                RES   3,D
          0471    CB 9B                RES   3,E
          0473    CB 9C                RES   3,H
          0475    CB 9D                RES   3,L
                                
                                
          0477    CB A6                RES   4,(HL)
          0479    DD CB 36 A6          RES   4,(IX+INDEX)
          047D    FD CB 36 A6          RES   4,(IY+INDEX)
          0481    CB A7                RES   4,A
          0483    CB A0                RES   4,B
          0485    CB A1                RES   4,C
          0487    CB A2                RES   4,D
          0489    CB A3                RES   4,E
          048B    CB A4                RES   4,H
          048D    CB A5                RES   4,L
                                
                                
          048F    CB AE                RES   5,(HL)
          0491    DD CB 36 AE          RES   5,(IX+INDEX)
          0495    FD CB 36 AE          RES   5,(IY+INDEX)
          0499    CB AF                RES   5,A
          049B    CB A8                RES   5,B
          049D    CB A9                RES   5,C
          049F    CB AA                RES   5,D
          04A1    CB AB                RES   5,E
          04A3    CB AC                RES   5,H
          04A5    CB AD                RES   5,L
                                
                                
          04A7    CB B6                RES   6,(HL)
          04A9    DD CB 36 B6          RES   6,(IX+INDEX)
          04AD    FD CB 36 B6          RES   6,(IY+INDEX)
          04B1    CB B7                RES   6,A
          04B3    CB B0                RES   6,B


                                       84





                      APPENDIX B - ZILOG MNEMONICS       


          04B5    CB B1                RES   6,C
          04B7    CB B2                RES   6,D
          04B9    CB B3                RES   6,E
          04BB    CB B4                RES   6,H
          04BD    CB B5                RES   6,L
                                
                                

          04BF    CB BE                RES   7,(HL)
          04C1    DD CB 36 BE          RES   7,(IX+INDEX)
          04C5    FD CB 36 BE          RES   7,(IY+INDEX)
          04C9    CB BF                RES   7,A
          04CB    CB B8                RES   7,B
          04CD    CB B9                RES   7,C
          04CF    CB BA                RES   7,D
          04D1    CB BB                RES   7,E
          04D3    CB BC                RES   7,H
          04D5    CB BD                RES   7,L 
                                
                                
          04D7    C9                   RET
          04D8    D8                   RET   C
          04D9    F8                   RET   M
          04DA    D0                   RET   NC
          04DB    C0                   RET   NZ
          04DC    F0                   RET   P
          04DD    E8                   RET   PE
          04DE    E0                   RET   PO
          04DF    C8                   RET   Z
                                
                                
          04E0    ED 4D                RETI
          04E2    ED 45                RETN
                                
                                
          04E4    CB 16                RL   (HL)
          04E6    DD CB 36 16          RL   (IX+INDEX)
          04EA    FD CB 36 16          RL   (IY+INDEX)
          04EE    CB 17                RL   A
          04F0    CB 10                RL   B
          04F2    CB 11                RL   C
          04F4    CB 12                RL   D
          04F6    CB 13                RL   E
          04F8    CB 14                RL   H
          04FA    CB 15                RL   L
                                
                                
          04FC    17                   RLA
                                
                                
          04FD    CB 06                RLC   (HL)
          04FF    DD CB 36 06          RLC   (IX+INDEX)
          0503    FD CB 36 06          RLC   (IY+INDEX)
          0507    CB 07                RLC   A
          0509    CB 00                RLC   B


                                       85





                      APPENDIX B - ZILOG MNEMONICS       


          050B    CB 01                RLC   C
          050D    CB 02                RLC   D
          050F    CB 03                RLC   E
          0511    CB 04                RLC   H
          0513    CB 05                RLC   L
                                
                                
          0515    07                   RLCA
                                

          0516    ED 6F                RLD
                                
                                
          0518    CB 1E                RR   (HL)
          051A    DD CB 36 1E          RR   (IX+INDEX)
          051E    FD CB 36 1E          RR   (IY+INDEX)
          0522    CB 1F                RR   A
          0524    CB 18                RR   B
          0526    CB 19                RR   C
          0528    CB 1A                RR   D
          052A    CB 1B                RR   E
          052C    CB 1C                RR   H
          052E    CB 1D                RR   L
                                
                                
          0530    1F                   RRA
                                
                                
          0531    CB 0E                RRC   (HL)
          0533    DD CB 36 0E          RRC   (IX+INDEX)
          0537    FD CB 36 0E          RRC   (IY+INDEX)
          053B    CB 0F                RRC   A
          053D    CB 08                RRC   B
          053F    CB 09                RRC   C
          0541    CB 0A                RRC   D
          0543    CB 0B                RRC   E
          0545    CB 0C                RRC   H
          0547    CB 0D                RRC   L
                                
                                
          0549    0F                   RRCA
                                
                                
          054A    ED 67                RRD
                                
                                
          054C    C7                   RST   0
          054D    CF                   RST   08H
          054E    D7                   RST   10H
          054F    DF                   RST   18H
          0550    E7                   RST   20H
          0551    EF                   RST   28H
          0552    F7                   RST   30H
          0553    FF                   RST   38H
                                


                                       86





                      APPENDIX B - ZILOG MNEMONICS       


                                
          0554    9E                   SBC   A,(HL)
          0555    DD 9E 36             SBC   A,(IX+INDEX)
          0558    FD 9E 36             SBC   A,(IY+INDEX)
          055B    9F                   SBC   A,A
          055C    98                   SBC   A,B
          055D    99                   SBC   A,C
          055E    9A                   SBC   A,D
          055F    9B                   SBC   A,E
          0560    9C                   SBC   A,H
          0561    9D                   SBC   A,L
          0562    DE 49                SBC   A,NN
          0564    ED 42                SBC   HL,BC
          0566    ED 52                SBC   HL,DE
          0568    ED 62                SBC   HL,HL
          056A    ED 72                SBC   HL,SP
                                
                                
          056C    37                   SCF
                                
                                
          056D    CB C6                SET   0,(HL)
          056F    DD CB 36 C6          SET   0,(IX+INDEX)
          0573    FD CB 36 C6          SET   0,(IY+INDEX)
          0577    CB C7                SET   0,A
          0579    CB C0                SET   0,B
          057B    CB C1                SET   0,C
          057D    CB C2                SET   0,D
          057F    CB C3                SET   0,E
          0581    CB C4                SET   0,H
          0583    CB C5                SET   0,L
                                
                                
          0585    CB CE                SET   1,(HL)
          0587    DD CB 36 CE          SET   1,(IX+INDEX)
          058B    FD CB 36 CE          SET   1,(IY+INDEX)
          058F    CB CF                SET   1,A
          0591    CB C8                SET   1,B
          0593    CB C9                SET   1,C
          0595    CB CA                SET   1,D
          0597    CB CB                SET   1,E
          0599    CB CC                SET   1,H
          059B    CB CD                SET   1,L
                                
                                
          059D    CB D6                SET   2,(HL)
          059F    DD CB 36 D6          SET   2,(IX+INDEX)
          05A3    FD CB 36 D6          SET   2,(IY+INDEX)
          05A7    CB D7                SET   2,A
          05A9    CB D0                SET   2,B
          05AB    CB D1                SET   2,C
          05AD    CB D2                SET   2,D
          05AF    CB D3                SET   2,E
          05B1    CB D4                SET   2,H
          05B3    CB D5                SET   2,L


                                       87





                      APPENDIX B - ZILOG MNEMONICS       


                                
                                
          05B5    CB DE                SET   3,(HL)
          05B7    DD CB 36 DE          SET   3,(IX+INDEX)
          05BB    FD CB 36 DE          SET   3,(IY+INDEX)
          05BF    CB DF                SET   3,A
          05C1    CB D8                SET   3,B
          05C3    CB D9                SET   3,C
          05C5    CB DA                SET   3,D
          05C7    CB DB                SET   3,E
          05C9    CB DC                SET   3,H
          05CB    CB DD                SET   3,L
                                
                                
          05CD    CB E6                SET   4,(HL)
          05CF    DD CB 36 E6          SET   4,(IX+INDEX)
          05D3    FD CB 36 E6          SET   4,(IY+INDEX)
          05D7    CB E7                SET   4,A
          05D9    CB E0                SET   4,B
          05DB    CB E1                SET   4,C
          05DD    CB E2                SET   4,D
          05DF    CB E3                SET   4,E
          05E1    CB E4                SET   4,H
          05E3    CB E5                SET   4,L
                                
                                
          05E5    CB EE                SET   5,(HL)
          05E7    DD CB 36 EE          SET   5,(IX+INDEX)
          05EB    FD CB 36 EE          SET   5,(IY+INDEX)
          05EF    CB EF                SET   5,A
          05F1    CB E8                SET   5,B
          05F3    CB E9                SET   5,C
          05F5    CB EA                SET   5,D
          05F7    CB EB                SET   5,E
          05F9    CB EC                SET   5,H
          05FB    CB ED                SET   5,L
                                
                                
          05FD    CB F6                SET   6,(HL)
          05FF    DD CB 36 F6          SET   6,(IX+INDEX)
          0603    FD CB 36 F6          SET   6,(IY+INDEX)
          0607    CB F7                SET   6,A
          0609    CB F0                SET   6,B
          060B    CB F1                SET   6,C
          060D    CB F2                SET   6,D
          060F    CB F3                SET   6,E
          0611    CB F4                SET   6,H
          0613    CB F5                SET   6,L
                                
                                
          0615    CB FE                SET   7,(HL)
          0617    DD CB 36 FE          SET   7,(IX+INDEX)
          061B    FD CB 36 FE          SET   7,(IY+INDEX)
          061F    CB FF                SET   7,A
          0621    CB F8                SET   7,B


                                       88





                      APPENDIX B - ZILOG MNEMONICS       


          0623    CB F9                SET   7,C
          0625    CB FA                SET   7,D
          0627    CB FB                SET   7,E
          0629    CB FC                SET   7,H
          062B    CB FD                SET   7,L
                                
                                
          062D    CB 26                SLA   (HL)
          062F    DD CB 36 26          SLA   (IX+INDEX)
          0633    FD CB 36 26          SLA   (IY+INDEX)
          0637    CB 27                SLA   A
          0639    CB 20                SLA   B
          063B    CB 21                SLA   C
          063D    CB 22                SLA   D
          063F    CB 23                SLA   E
          0641    CB 24                SLA   H
          0643    CB 25                SLA   L
                                
                                
          0645    CB 2E                SRA   (HL)
          0647    DD CB 36 2E          SRA   (IX+INDEX)
          064B    FD CB 36 2E          SRA   (IY+INDEX)
          064F    CB 2F                SRA   A
          0651    CB 28                SRA   B
          0653    CB 29                SRA   C
          0655    CB 2A                SRA   D
          0657    CB 2B                SRA   E
          0659    CB 2C                SRA   H
          065B    CB 2D                SRA   L
                                
                                
          065D    CB 3E                SRL   (HL)
          065F    DD CB 36 3E          SRL   (IX+INDEX)
          0663    FD CB 36 3E          SRL   (IY+INDEX)
          0667    CB 3F                SRL   A
          0669    CB 38                SRL   B
          066B    CB 39                SRL   C
          066D    CB 3A                SRL   D
          066F    CB 3B                SRL   E
          0671    CB 3C                SRL   H
          0673    CB 3D                SRL   L
                                
                                
          0675    96                   SUB   (HL)
          0676    DD 96 36             SUB   (IX+INDEX)
          0679    FD 96 36             SUB   (IY+INDEX)
          067C    97                   SUB   A
          067D    90                   SUB   B
          067E    91                   SUB   C
          067F    92                   SUB   D
          0680    93                   SUB   E
          0681    94                   SUB   H
          0682    95                   SUB   L                           
          0683    D6 49                SUB   NN
                                


                                       89





                      APPENDIX B - ZILOG MNEMONICS       


                                
          0685    AE                   XOR   (HL)
          0686    DD AE 36             XOR   (IX+INDEX)
          0689    FD AE 36             XOR   (IY+INDEX)
          068C    AF                   XOR   A
          068D    A8                   XOR   B
          068E    A9                   XOR   C
          068F    AA                   XOR   D
          0690    AB                   XOR   E
          0691    AC                   XOR   H
          0692    AD                   XOR   L
          0693    EE 49                XOR   NN













































                                       90





                      APPENDIX B - ZILOG MNEMONICS       

































































                      APPENDIX B - ZILOG MNEMONICS       




                         APPENDIX C - SYSTEM MEMORY MAP

                       ||||||||||||||||||||||||||||||||||||     FFFF
                       ||                                ||
                       ||                                ||
                       ||      CP/M (BDOS and BIOS)      ||
                       ||                                ||
                       ||                                ||
                       ||||||||||||||||||||||||||||||||||||
                       ||                                ||
                       ||    Z8E (Approx 8.75 BYTES)     ||
                       ||                                ||
                       ||||||||||||||||||||||||||||||||||||
                       ||                                ||
                       ||     OPTIONAL SYMBOL TABLE      ||
                       ||                                ||
                       ||||||||||||||||||||||||||||||||||||
                       ||                                ||
                       ||                                ||
                       ||                                ||               
                       ||                                ||
                       ||                                ||
                       ||                                ||
                       ||              TPA               ||
                       ||                                ||
                       ||                                ||
                       ||                                ||
                       ||                                ||
                       ||                                ||
                       ||                                ||
                       ||                                ||
                       ||||||||||||||||||||||||||||||||||||  --- 0100
                       ||                                ||
                       ||      PAGE ZERO  RESERVED       || 
                       ||                                || 
                       ||||||||||||||||||||||||||||||||||||  ___ 0000



















                                       92





                      APPENDIX B - ZILOG MNEMONICS       


                            COMMAND SUMMARY REFERENCE

        CMD         Description                      Arguments

         A        Inline  Assembly             StartAddr 
         B        Set Breakpoint               Addr1[,Pass Count]  [Addr2..AddrN]
         C        Clear Breakpoint             Addr1               [Addr2..AddrN]
         D        Dump Memory                  [StartAddr]         [End/Count] 
         E        Examine Memory               StartAddr
         F        Find                         StartAddr           MatchData
         G        Go                           ExecutionAddr
         H        Display Symbol Table         [FirstSymbol]
         I        Input File                   FileName            [,Load Address]
         J        Full Screen/Animated Debug   [/] [*] [Addr]      [Timeout]
         K        Set Memory Window            StartAddr           [Size]
         M        Move Memory                  SourceStart    SourceEnd    DestStart
         N        Output to Port NO Pre-Read   [(] PortAddr [)]
         O        Output Current Breakpoints
         P        Exam/Modify PSW (Flag Reg)
         Q        Query I/O Port               [(] PortAddr [)]
         R        Examine/Modify Registers     RegSpecifier
         S        Single-Step                  [/]  [Count]
         U        Write Symbol Table To Disk   FileName    
         V        Verify Memory                SourceStart     SourceEnd   DestStart
         W        Write to Disk                FileName        [StartAddr] [EndAddr] 
         X        Examine Machine State
         Y        Fill Memory                  FromAddr        ToAddr       Data
         Z        Disassemble                  StartAddr       End/Count    FileName




        []        Denotes Optional Argument
        [/]       Do Not Trace Subroutine
        [*]       Do Not Trace BDOS Call  
        [(] [)]   I/O Port Monitor Mode





                       Z8E   Copyright (c) 1984  AERO-SOFT















                                       93