All serial test are done at 8 bit word length , 2 stop bits, no parity check
at 19,000 baud rate unless otherwise stated.

The memory in the system must be enabled for extended addressing.
There must be ram chips in sockets 5D, and 6D.

The CP/M system must be 56K or bigger.

*******************************************************************************
All RS-232 jumpers set for data communications equipment.

	A   B   C   D   E   F   G
	*   *   *   *---*   *---*
	|   |
	*   *   *   *---*   *---*
	H   I   J   K   L   M   N
*******************************************************************************
		SWITCH SETTINGS FOR THE NON-TEST BOARD

Switch 2D:			EXTENDED ADDRESSING
		off   on
	        ________
	       |        |
	       | ==     | 1 - A23    set to 00h
	       | ==     | 2 - A22
	       | ==     | 3 - A21
	       | ==     | 4 - A20
	       | ==     | 5 - A19
	       | ==     | 6 - A18
	       | ==     | 7 - A17
	       | ==     | 8 - A16
	       |________|

Switch  7B:			PORT SELECT
		off   on
	        ________
	       |     == | 1 - PHANTOM ENABLE
	       |     == | 2 - A7 \
	       | ==     | 3 - A6  \
	       | ==     | 4 - A5   > PORT ADDRESS  set to 60h
	       |     == | 5 - A4  /
	       |     == | 6 - A3 /
	       |     == | 7 - RAM 0 WRITE ENABLE
	       |     == | 8 - RAM 1 WRITE ENABLE
	       |________|

Switch 10B:			MEMORY ADDRESS
		off   on
		________
	       |        |
	       |     == | 1 - EXTENDED ADDRESS DISABLE
	       | ==     | 2 - RAM DISABLED ON RESET
	       |     == | 3 - A15 \
	       |     == | 4 - A14  \  4k UPPER ADDRESS SELECT
	       |     == | 5 - A13  /   set to 00h
	       |     == | 6 - A12 /
	       | ==     | 7 - POWER ON JUMP ENABLE
	       | ==     | 8 - POWER ON JUMP CHIP SELECT
	       |________|

J4:			ADDRESS ENABLE FOR INTERRUPTS
	A  B  C

        *--*  *		DISABLED

*******************************************************************************
		SWITCH SETTINGS FOR THE TEST BOARD

Switch 2D:			EXTENDED ADDRESSING
		off   on
	        ________
	       |        |
	       |     == | 1 - A23      set to 0Fh
	       |     == | 2 - A22
	       |     == | 3 - A21
	       |     == | 4 - A20
	       | ==     | 5 - A19
	       | ==     | 6 - A18
	       | ==     | 7 - A17
	       | ==     | 8 - A16
	       |________|

Switch  7B:			PORT SELECT
		off   on
	        ________
	       |     == | 1 - PHANTOM ENABLE
	       |     == | 2 - A7 \
	       | ==     | 3 - A6  \
	       |     == | 4 - A5   > PORT ADDRESS set to 48h
	       |     == | 5 - A4  /  
	       | ==     | 6 - A3 /
	       |     == | 7 - RAM 0 WRITE ENABLE
	       |     == | 8 - RAM 1 WRITE ENABLE
	       |________|

Switch 10B:			MEMORY ADDRESS
		off   on
		________
	       |        |
	       | ==     | 1 - EXTENDED ADDRESS DISABLE
	       | ==     | 2 - RAM DISABLED ON RESET
	       | ==     | 3 - A15 \
	       | ==     | 4 - A14  \  4k UPPER ADDRESS SELECT
	       |     == | 5 - A13  /   set to #C000h
	       |     == | 6 - A12 /
	       | ==     | 7 - POWER ON JUMP ENABLE
	       | ==     | 8 - POWER ON JUMP CHIP SELECT
	       |________|


J4:			ADDRESS ENABLE FOR INTERRUPTS
	A  B  C

        *  *--* 	ENABLED

	 
	
B: is jumpered to *pint













		WHAT THIS TEST DOES

SERIAL PORTS -

	1. 	Tests to make sure that all the registers on each port
	   will initialize.
	2.	Tests transmit with a walk test.
	3.	Tests receive with a walk test.
	4.	Tests transmit and receive at 5,6,7,8 bits word length.
	5	Tests transmit and receive at 110,300,600,1200,2400,
	  4800,9600,19200  baud rates only.
	6.	Tests to make sure the port will overflow if a character is
	  sent before the last character is read.
	7.	Tests to make sure parity works correctly.
	8.	Tests all control bits RTS, CTS, DTR, DSR, RCD.


PARALLEL PORTS-

	1.	Tests input port with walk test.
	2.	Tests both output ports with walk tests.
	3. 	Tests for tri-state.
	4.	Tests restore bit.


CLOCK-

	1.	Tests to make sure that the clock can be loaded.
	2.	Tests for accurate timing of the clock against another clock.

MEMORY-

	1.	Tests extended addressing.
	2.	Tests bank select.
	3	Tests all data lines.
	4.	Tests all address lines.

INTERRUPTS-

	1. 	Tests for all 8 interrupts in the correct priority.
	    	     (As in most advanced interrupt systems if there
		     is a problem with the interrupts any response 
		     may occur, from system crashes to garbled printout.
		     If any of these things occur after the heading for
		     the interrupt test then the following test should 
		     help to find the cause. )

	2.	A loop test exists for troubleshooting interrupts.
	  To use this test the jumper at j4 must be placed over
	  pins A & B, on the test board.  Do not change this jumper
	  with the computer running as this may cause the system to 
	  crash.














*******************************************************************************

	When the test is started, and evey time the menu appears
    the serial ports on both boards are initialized.  if any errors
    occur the test cannot be run.

	The errors that occur are -

		1.	Baud rate won't initialize
				(divisor latch reg on A.C.E. chip)
		2.	Line control reg. won't initialize
				(line control reg on A.C.E. chip)
		3.	Modem control reg. won't initialize
				(modem control reg on A.C.E. chip)

	These errors must be repaired before the test will continue.