.mt 4
.mb 4
                RESOURCE

        A disassembler for 8080 programs
        by Ward Christensen

        CP/M U.G. 1/80

Suggestions?  Call me evenings at (312) 849-6279
                ----------------
RESOURCE commands are inconsistent at best. - RESOURCE is a 
kludge based on years of disassembler experience and hacking, 
and was never "planned" - just coded sitting at a tube, and
modified over 2 years before being contributed to the CP/M UG.

For example, to kill a symbol: k.label   but to kill a 
control value: caddr,k and to kill a comment: ;addr,
but RESOURCE does the job like no other I have seen.
                ----------------
N-O-T-E: Pardon the editorial, but I feel hardware without
good software is useless to 99% of us.  Most good software
has to be paid for.  I strongly support the legitimate purchase
of licensed software.  I do not regularly use any programs
which I have not purchased.  (Yes, I do occasionally "try"
one, but then buy it if I plan on using it).  I have been
asked by software businesses NOT to distribute RESOURCE -
because of its ability to produce good .asm source quickly.
But there are so many disassemblers out, why not a good, 
conversational one?   Please use it in the spirit in which it 
was contributed: to enlarge your understanding of the micro-
computer world around you, and to allow you to customize 
programs which you legitimately own, for your own use.

        "Semper non rippus offus"
----
NOTE: any command taking a hex address (Dnnnn, etc)
may take a value in the form .label but arithmetic
may not be performed.  (i.e. d.start is ok, but d.start+8 not)
                ----------------
        Overall structure of RESOURCE:  It is a .COM file,
which runs at 100H.  It goes thru 1700 or so, then the stack.
At 1800 is a 512 entry table for control commands.  Each is
3 bytes long, and controls the format of the re-sourced list,
i.e. is it DB, DS, DW, instructions, etc.
        At 1E00 is the start of the symbol table.  It has no
defined length as such.  If it is not used, it occupies only
2 bytes.
        If you want to re-source something which is in memory,
such as a PROM, a program previously loaded in high memory,
"CP/M itself", or whatever, you can just do so.
        However, typically you want to disassemble a program
which runs at 100H, which is where RESOURCE runs.   Bob
Van Valzah would have solved that by making RESOURCE 
relocatable and moving itself up under BDOS.  I wasn't that
industrious.
        Instead, RESOURCE uses the concept of an "invisible"
OFFSET.  After all, what do you care where it is as long
as it LOOKS like it's at 100h?
        So, you set an offset.  O2F00 sets it to 2F00 Hex.ŠReading a .COM file (RFOO.COM) causes it to come into 3000 on.
If you say D100 or L100 it dumps or lists what LOOKS like your
program.  Internally, RESOURCE is adding the offset to the
D and L addresses.
        What should you set the offset to?  Well, that depends
upon how many symbols you will use.  O1F00 will load the
program at 2000, thus allowing only 1E00-1FFF for symbols,
i.e. 512 bytes or about 50-60 labels.  If you didn't leave
enough space, then used B to build a default symbol table,
the table could run into and clobber your .com file!  (easy
recovery, however: just change the offset to being higher,
and read in the .COM file again)  Each entry takes 3 bytes
+ the symbol length, and if you like 7 byte labels like I
do, that means 10 bytes/label.  An offset of 2F00 should
be adequate.
        If you want to put comments into the disassembled
program, you will have to designate an area to Use for the
comments.  The U command (e.g. U4000) specifies what area
is to be used.
        Before issuing the O (offset) command, do:
        L5 7
which will show the JMP to BDOS, which is the highest memory
yoõ maù use® (Notå thaô iæ yoõ have¬ foò example¬ aî emptù �
4K memorù boarä iî higè memory¬ yoõ caî Uså THAÔ foò comments).
        Let's take an example:  You have an 8K file, FOO.COM
which you want to disassemble.  It will have about 300 labels.
300 x 10 is 3000, or call it 4K (what's a K unless you're
tight).  The symbol table starts at 1E00.  4K more is 2E00.
Let's load the .COM at 2E00, so since it normally starts
at 100H, the offset is 2D00.  O2D00 is the command.
We then RFOO.COM to read it in.  It says 4E00 2100, which
means it came into actual memory to 4E00, but 2100 if we
are talking with respect to loading at 100.
        Thus we could set our comments table up after
the .COM program - say at 5000:  U5000
        The ? command shows the memory utilization for
control, symbol, and comments entries.  (No, I never put
in anything to keep track of the .COM - you'll just have
to do that yourself).
        If you ever want to dump real memory, you'll have
to reset the offset to 0: O0  but then set it back.
If you are not sure what it is, typing O will tell the
current offset.

        Hoo, boy!  Hope this kludge of documentation
is enough to get you going - hmmm, better give you
some of the gotcha's I've discovered...

                ---- WATCH FOR ----

*       Symbols overflowing into the .COM.
        (Use ? command to see how full symbol table is)

*       Control entries overflowing into .SYM (altho I
        can't believe anyone will have a program with
        more than 512 control entries!!!)

*       Comments overflowing into BDOS (ug!!)Š
*       Using an offset which is not in free memory
        and overlaying BDOS or whatever.

*       The B(uild) command gobbling up too much when building
        a DB:  "B" will take a DB 'GOBBELDY GOOK' followed
        by LXI H,FOO and take the LXI as a '!' (21H) so
        you'll have to manually stick a new "I" control
        entry in at the address of the LXI.  You might
        also delete the incorrect "I" entry which RESOURCE
        stuck in (typically at the second byte of the LXI)

*       Trying to dump real memory without setting the
        offset back to 0.  (then forgetting to set it back
        to its proper value)

*       Forgetting how big the .COM file you are disassembling
        was.

*       Using RESOURCE to rip off software (yes, I know, you
        heard that before, but only 3 in 100 needed to be 
        told, and 2 in 100 needs to be told again, and 1 in
        100 doesn't give a rat's fuzzy behind anyway!!)

*       Forgetting to take checkpoints when disassembling
        large files.  You may even want to rotate the names
        under which things are saved:

        STEMP1.SYM
        STEMP1.CTL
        STEMP1.DOC

*       Missing a label:  Suppose you have a control entry
        for a DW, resulting in:
        
        DFLT:           ;172C
                DW      100H

        but somewhere in the program, the following exists:

                LDA      172DH

        Even if you did a B and have a label L172D, it won't
        show up since it's in the middle of a DW.  Instead,
        do this:

        K.l172d         kill the old label
        e172d,.dflt+1   put in the new label as a displacement
                        off the beginning.

*       improperly disassembling DW's (see previous item).
        You might be tempted to make DFLT a DB so that

        DFLT:           ;172C
                DB      0
        L172D:          ;172D
                DB      1
Š        Note that while this disassembles and reassembles
        properly, it is not "as correct" as the technique
        used in the previous item.

*       Having the "B" command overlay your "E" control entry.
        What?  Well, "B"uild is pretty dumb.  If he finds 8
        DB type characters in a row, he fires off a DB from
        then on until he runs out of those characters.  Suppose
        your program was 200 long (ended at 3FF), and you
        had zeroed (aha!  Nice DB candidates) memory there
        (there meaning at your offset address + whatever).

        Then you QB100,400 and viola!!  RESOURCE overlaid
        your "E" control with a "B".  
                ----------------

        RESOURCE is relatively complete.  (well, actually,
        the phrase "rampant featureitis" has been "mentioned").
        ...But there's always another day, and another K...

                SO... Here's my "wish list"

        ..it might save you telling me YOU think such-and-such
        would be nice...

*       Targets of LHLD, SHLD should automatically be flagged
        as type DW in the control table.  Ditto LDA and STA
        as DB or as second half of DW.  Ditto targets of LXI
        as DB (?).

*               E5C,.FCB
        followed by
                E6C,.FCB+
        should automatically calculate the appropriate
        displacement, and put it in the symbol table.

*       The comments facility should be enhanced to allow
        total SUBSTITUTION of entire line(s) of the code,
        i.e. at address such-and-such, replace the next 3
        bytes with the following arbitrary line.  This
        would help those "how do I explain what was being
        done" cases such as:    LXI     H,BUFFER AND 0FF00H

*       Add the ability to, in one instruction, rename
        a default (LXXXX) label to a meaningful name.

                ----------------
RESOURCE types an "*" prompt when it is loaded.  You may
then enter any of the following commands.  Each command
is a single letter followed by operands.  Commas are shown
as the delimiter, but a space will also work.

                ----------------
                ----------------
;       Put comments into the program.
        (must execute 'u' command first, to assign area
        for comments to be placed)
Š        ;addr,comment   enter a comment
        ;addr           lists existing comment
        ;               lists entire comments table
        ;addr,          deletes existing comment

        note that '\' is treated as a new line, i.e.
        \test\ will be formatted:

        ;
        ;TEST
        ;
                ----------------
Attempt to find DB's while listing the program.
-       This command works just like 'L', but attempts
        to find DB's of 8 chars or longer.

        (see 'L' command for operand formats)
                ----------------
Build default sym tbl (LXXXX) labels for each
-       2 byte operand encountered.  Note 'B' is
        identical to 'L' except labels are built.

        (see 'L' command for operand formats)
                ----------------
Control table usage:
-       c               dump ctl tbl
        cnnnn           dump from starting
        cnnnn,x         define format from nnnn
                        to next entry.  values of x:

                        B = DB (attempts ASCII
                                printable, 0DH, 0AH, 0)
                        W = DW (attempts label)
                        S = DW to next ctl entry
                        I = instructions
                        K = kill this ctl entry
                        E = end of disassembly

        NOTE every control entry causes a "control break"
        (NO, RESOURCE was NOT written in RPG) which means
        a new line will be started.  Thus if you have a
        string in memory which disassembles as:

        DB      'Invalid operand',0DH
        DB      0AH

        You might want to change it putting the 0DH,0AH
        together on the second line - just enter a "B"
        control entry for the address of the 0DH.

        The same technique could be used to make

        DB      'TYPESAVEDIR ERA REN '

        appear as

        DB      'TYPE'
        DB      'SAVE'Š        DB      'DIR '
        DB      'ERA '
        DB      'REN '

                ----------------
dump:
-       dxxxx           Dumps 80H from xxxx on
        daaaa,bbbb      Dumps from aaaa thru bbbb
        d,bbbb          Continues, thru bbbb
        d               Continues, 80H more

        NOTE 80H is the default dump length.  If you have
        a larger display, you can change the default via:

        d=nn            nn is the HEX new default.

        For example, a 24 line tube could display 100H:

        d=100           or..
        d=100,200       Defaults to 100, dumps 200-2ff

                ----------------
enter symbol:
-       ennnn,.symbol   symbol may be of any length,
                        and contain any char A-Z or 0-9,
                        or "+" or "-".  This allows:
                        E5D,.FCB+1.  Note the "+" is not
                        checked, i.e. E5D,.FCB+2 would be
                        wrong (assuming FCB is at 5C) but
                        would be allowed to be entered.

        Note if you enter two symbols for the same address,
        whichever one is first alphabetically will show up
        on the disassembled listing.  If you have a label
        which has the wrong address, you need not explicitly
        kill the old one before entering the new.  A label
        which is spelled exactly the same as an existing one
        will replace the existing one even if the addresses
        are different.
                ----------------
Find occurrence of address or label.  Note this function
-       runs until interrupted (press any key).
        fnnnn,ssss      find address nnnn in memory.  Start
                        the search at ssss.  Runs forever.
                        Press any key to stop.
        f               continue previous find command
        fnnnn           find nnnn starting at address you last
                        stopped at in the f command
                ----------------
kill symbol from table
-       k.symbol
                ----------------
.paŠlist (disassemble).  This command is used to list the
-       file, or to list it to disk after enabling
        the .ASM file save via 'SFILENAME.ASM' command

        l               lists 10 lines from prev pc
        lssss,eeee      lists from ssss to eeee
        l,eeee          lists from current pc to eeee
        lssss           lists 10 lines at ssss

        Note that if you have a control 'e' entry, then the
        list will stop when that address is found.  This allows
        you to 'lstart,ffff'. 

        The 10 line default may be changed via:

        L=nn            where nn is a HEX line count, e.g.
        L=14            set to 20 lines/screen

        You can change the default and list, e.g.

        L=9,100         Dflt to 9 lines, list at 100.

        NOTE: when using L to list the .ASM program to disk,
        you should either list the entire program at once
        using: Lssss,eeee or, you can list small pieces
        at a time.  As long as you list again without
        specifying a starting address, (L or L,nnnn) then
        the output file will continue uninterrupted.

        You may do dump commands, and others, without
        affecting what is being written to disk.
                ----------------
offset for disassembly
-       o               print current offset
        onnnn           establish new offset

        (note that the offset is always added to any 
        address specified in an a, b, d, or l command.
        to dump real memory, the offset must be reset to
        0 (O0) before the dump.)
                ----------------
prolog generation - this routine generates an
-       ORG instruction, and equates for any label
        outside of a given low-hi address pair.
        (the start and end addresses of your program).
        e.g. if disassembling from 100 to 3ff, it will
        generate 'fcb equ 5ch' if FCB is in the symbol
        table.  In typical use, you would 'sfilename.asm'
        then use the P command to write the prolog, then
        the L command to write the program itself.

        Pstart addr,end addr
.pa        Šquiet command: any command which is preceeded by a q
-       will be done 'quietly'.  For example, to save
        a .asm program, you could just do:

        ql100,3ff       or      ql100,ffff if you have
        set the 'e' control in the control table.

        Another use is to build a default symbol table
        by taking a pass thru the program: QB100,xxxx
                ----------------
read .com, .ctl, .sym, or .doc file
-       rfilename.com   reads in at offset+100h
        rfilename.ctl   loads the ctl table
        rfilename.sym   loads the sym file
        rfilename.doc   loads the comments table (note
                        'u' command must have been issued)
                ----------------
save .asm, .ctl, .sym, or .doc file
-       sfilename.asm   use 'l' command to write, z to end
        sfilename.CTL   saves the CTL table
        stablename.sym  saves the sym file
        sfilename.doc   saves the comments table
                ----------------
use area of memory for comments table
-       unnnn           such as ud000 if you had an
                        open board at 0d000h
                ----------------
purge sym tbl and CTL tbl
        x
        -
                ----------------
close .asm file (note that a preferred way to close the
        .asm file is to have specified a control entry
        for the end address (e.g. c1ff,e))
        z
        -
--------------------------------------------
--------------------------------------------
Here is a sample of the RESOURCE usage.

Given:  a COM file (lets say test.com) which runs at 100
        (as any good COM file should), and goes thru 2FF.

lines preceded by ---> are typed by you.

---> RESOURCE
---> o2200      set the offset to 2200, which means the
                program will read into 2200 + 100 = 2300.

---> rtest.com  reads the com file into memory. system says:
                2500 0300 which is the actual hi load addr,
                (2500) and the original hi load addr (300)

                REMEMBER this address (300) because you might
                want to put a "E" (end of assembly) control
                entry there.
.paŠ<<<<note>>>> that all 'L' (disassembly list) and 'D' (dump)
        commands work with the offset added.  Thus, you
        should learn to forget that the disassembler is
        in memory, and think of it as if your program were
        actually at 100.  D100 will dump your program.
        
        also note:  if the program being "RESOURCEd" will
        have a fairly large symbol table, then you will
        have to set the offset higher: o2f00 or some such.
        (the ? command will show symbol table usage: if your
        symbol table is nearing the .com file, then just
        set a new offset (higher) and re-load the .com)

        if you want to dump r-e-a-l memory, you would have
        to reset the offset to 0: o0  (but don't forget to
        reset it to 1f00 before continuing with your program.)

If you are disassembling something which is in memory at
its correct address (such as looking at ccp) then don't
set the offset.  It defaults to 0 when dis is first loaded.

--->    l100    list your program - lists "about" 10 lines.

--->    d100    do a dump of your program.

NOTE that typically here are the steps to disassembling
        a program which has just been read into memory:

Use the dump command to find the ASCII DB areas.

Note that the 'a' command may be used to automatically
find the db's, but you must then check them to insure
that they don't extend too far.  All printable characters,
0dh, 0ah, and 00h are considered candidates for ASCII db's.

At least 8 characters in a row must be found to make sure
that long sequences of mov instructions won't be taken
as db's.

Use the cnnnn,k command to kill erronious entries put
in the control table by the a command, but then immediately
put in the right address, such as via cnnnn,i
.paŠIf you wanted to scan the program for ASCII db's yourself,
use the 'c' (control) command to set the beginning and
        end of ASCII areas.  For example, a program
        which starts out:
0100            jmp     start
0103            db      'copyright .....'
0117    start   .....

would show up in the dump as:

0100  c3170144 4f50xxxx  xxxxxxxx xxxxxxxx  *...copyr ight....*
0110  xxxxxxxx xxxxxxxx  xxxxxxxx xxxxxxxx  *xxxxxxxx ........*


Thus you would want to instruct the disassembler to switch
to db mode at 103, and back to instruction mode at 117, thus:
        c103,b
        c117,i

Continue doing this, bracketing every ASCII db which is in
the middle of instructions, by a b control instruction
and an i control instruction.  Note that multiple db's in
a row need not have separate cnnnn,b instructions, but that
these do cause a 'line break', i.e. if you have a table
of ASCII commands, for example:

02e5    db      'load'
02e9    db      'save'

the disassembler would disassemble these as:
02e4    db      'loadsave'

you could put in an additional control entry: c2e9,b, which
would cause the disassembler to generate:

02e4    db      'load'
02e8    db      'save'

This is much more readable and realistic.

Note that before generating each byte of a db, a symbol
table lookup is done to determine if there is a label
at that location, and if so, a new line is started.

Thus if 'loadlit' and 'savelit' were in the symbol table,
as the labels on the 'load' and 'save' above, no separate
'b' control instruction would be required as the label
would cause the break.

<<<<NOTE>>>> that at this time the automatic label checking
is n-o-t done for ds instructions.  Make sure that each
ds instruction references only up to the next label.  This
means that multiple ds's in a row must each be explicitly
entered into the control table.  Presence of a label is
not sufficient.
                        ----
.paŠSteps, continued:

After building the control entries with cnnnn,b and cnnnn,i
put in a control entry cnnnn,e which defines the address of
the end of your program.  The l command will then automatically
stop there, and in addition, if you are in 'save xxx.asm'
mode, the output .asm file will be closed.  If you do
mot define a control 'e' entry, then you will have to use
the break facility to stop the l command (don't use control-c
as that will re-boot cp/m).  If you were writing an .asm
file, you would have to user the z command to close the
file.

Next, you would list your program to determine how it looks.
when you recognize a routine by it's function, insert a label.

For example, if you saw that location 7ef was a character
out routine (type) then enter a label into the symbol table:
        E7EF,.TYPE

NOTE that all symbols start with a '.', so as to be dis-
tinguished from hex data.

NOTE that if you want the disassembler to make default labels
for you, use b (for build labels) instead of l (for list
program).  The b commands causes lnnnn default labels to
be inserted in the symbol table for every 2 byte operand
encountered (LXI, SHLD, JMP, etc).  It will undoubtedly
make some you don't want, such as L0000.  You will have to:

        K.L0000         kill label L0000 from the table.

When you encounter data reference instructions, try
to determine what type of area the instruction points to.
Typically,, LXI instructions may point to a work area
which should be defined as a DS, or to an ASCII string,
in which case we will have already made it a 'b' control
instruction.  Operands of LHLD and SHLD instructions
should be made DW instructions.  For example if you
encounter LHLD 0534H, then issue a control instruction:

        C534,W

NOTE that whatever mode you are last in will remain in
effect.  Therefore if 534,w is the last entry in the
control table, all data from there on will be taken to be
DW's.
.paŠSuppose that you determine that address 7cf is a 128 byte
buffer for disk I/O.  You want it to disassemble to:

DKBUF           ;07CF
        DS      80H

You do this as follows:

        C7CF,S          to start the DS
        C84F,B          to define it's end, and
        E7CF,.DKBUF     to put the symbol in the table.

Continue, iteratively using the 'l' command and the 'c'
and 'e' commands until you have the listing in a nice
format.  You will then probably want to save the control
symbol and comments tables.  Or, you could have been 
saving them at checkpoint times (so if you make a 
major mistake you could go back to a previous one).

To save a control file:
        sfilename.CTL   (any filename, may include a: or b:)

To save a symbol file:
        sfilename.sym

To save a comments file:  
        sfilename.doc   (not ".com" of course)

NOTE that the filetypes must be used as shown, but
that any legal filename (or disk:filename such as b:xxxx.CTL)
may be used.

You could now control-c to return to CP/M, and come back
later to resume your disassembly:

        RESOURCE
        o2200
        rtemp.com
        rtemp.sym
        rtemp.ctl
        uxxxx           (such as u4000)
        rtemp.doc

This will take you back exactly where you left off.

If you want to save a .asm file out to disk, do the following:

Make sure that there is a control entry defining the end
of the program (such as c200,e) or else you will have to 
specify the ending address and manually type a z command to 
close the file. 

        sfilename.asm

A message will indicate that the file is opened.  Any
subsequent a, b, or l command will have whatever is listed
written to disk.  Encountering a 'e' control, or typing a z
command will then close the .asm file.  The listing mayŠbe interrupted, and continued.  Since the l command types
only 10 lines, use laddr,ffff to list thru the end of the
assembly.

If this is the 'final' save of the .asm file, you will
probably want to put an 'org' at the beginning of the
output file, as well as generate equ instructions for
any references outside of the program.  For example, a
typical cp/m program will have references to:
        bdos    at 5
        fcb     at 5ch
        tbuff   at 80h

The 'p' (for prologue) command generates the org, then
scans the symbol table and generates equates:
        BDOS    EQU     05H
        FCB     EQU     05CH    (etc.)


If you have an "e" control entry in your file, you can
list as follows:  laddr,ffff - the listing will continue
until the "e" control entry is found


Additional commands:

If you entered a label in the symbol table but now want
to get rid of it:
 
       k.symbol

NOTE: to rename a symbol, such as when you had a system-
assigned lnnnn label but now want to make it meaningful:

        k.l0334
        e334,.type

You could even:

        e.l0334,.type
        k.l0334

--but that takes more typing.



Here are some more commands:

?               prints statistics on symbol and control table
                usage, etc.

c               prints the entire control table

cnnnn           prints the control table starting
                at address nnnn

ds              dumps the symbol table.  Interrupt it
                by typing any key.Š
ds.symbol       starts dumping at the specified symbol,
                or the nearest symbol.  thus "ds.f" starts
                the dump at the first label starting
                with the letter 'f'.

Have fun, and let me know of any problems or
        suggested improvements
        ------------------------

                RESOURCE
        "Quick" command summary

Any address may be replaced by .symbol i.e. D.START

;addr,comment           Enter a comment
;addr                   Lists existing comment
;                       Lists entire comments table
;addr,                  Deletes existing comment
A(see "L" for operands) Attempt to find DB's
B(see "L" for operands) Build default sym tbl (Lxxxx)
C                       Dump ctl tbl
Cnnnn                   Dump ctl starting at nnnn
Cnnnn,x                 Define format from nnnn (B,E,I,S,W)
Dxxxx                   Dumps 80H from xxxx on
Daaaa,bbbb              Dumps from aaaa thru bbbb
D,bbbb                  Dump thru bbbb
D                       Dump 80H more
D=nn                    nn= Hex dump size default.
Ds                      Dumps the symbol table.
Ds.symbol               Sym dump starting at .symbol
Ennnn,.symbol           Enter symbol into table
Fnnnn,ssss              Find address nnnn starting at ssss
F                       Continue previous find command
Fnnnn                   Find nnnn
K.symbol                Kill symbol from symbol table
L                       Lists 10 lines from prev pc
Lssss,eeee              Lists from ssss to eeee
L,eeee                  Lists from current pc to eeee
Lssss                   Lists 10 lines at ssss
L=nn                    nn is hex list default # of lines
O                       Print current offset
Onnnn                   Establish new offset
Pstart addr,end addr    Generate program prolog
Q                       Before any command suppresses
                        console output: QB100,200
Rfilename.COM           Reads in at offset+100h
Rfilename.CTL           Loads the ctl table
Rfilename.SYM           Loads the sym file
Rfilename.DOC           Loads the comments table (note
Sfilename.ASM           Save .ASM file.  Write w/L, Z to end
Sfilename.CTL           Saves the CTL table
Sfilename.SYM           Saves the sym file
Sfilename.DOS           Saves the comments table
Unnnn                   Use nnnn for comments table
X                       Purge all symbols and control
Z                       Write eof to .ASM file (
?                       Prints statistics (sym, ctl, comments)