ANADISK - The Ultimate Diskette Utility




			 Charles P. Guzis
			       SYDEX
		       153 North Murphy Ave.
		       Sunnyvale, CA  94086
			  (408) 739-4866


			 September 1, 1988
			   Version 1.32


	    Copyright 1987, 1988, All Rights Reserved.
		     Charles P. Guzis / SYDEX


      THIS IS NOT FREE SOFTWARE and may not  be	 sold  without
      the  author's  express written permission.   If you have
      paid a "public domain" vendor for this program, rest as-
      sured that not one bit of what you paid ever  gets  back
      to  the  author.	  If  you  use this program,  YOU MUST
      REGISTER.	 Neither SYDEX nor Mr. Guzis will answer tech-
      nical support inquiries from unregistered users.

      To register,  send $15.00 with your name,	 company  name
      (if any) and address to -

			       SYDEX
		       153 North Murphy Ave.
			Sunnyvale, CA  94086

      Upon receipt of your registration fee,  you will be sent
      the most current version of ANADISK and its accompanying
      documentation.

      ANADISK and this document are  protected	by  copyright.
      The receipt or possession of this document does not con-
      vey   any	 rights	 beyond	 those	enumerated  herein  to
      reproduce or distribute its contents.    If  ANADISK  or
      this  document are copied,  a fee may be charged for the
      service of copying only, and not for ANADISK itself.  If
      such a charge is made,  it must be clearly identified as
      a service charge only by the vendor.










			 Table of Contents


   INTRODUCTION.................................................1

   ANADISK IN BRIEF.............................................1

   ANADISK OPERATION............................................1
    Menus.......................................................2
    The Main Menu...............................................2
     SCAN Operation.............................................3
      Searching for Data........................................5
     SECTOR EDIT Operation......................................6
     FILE EDIT Operation........................................8
     REPAIR Operation...........................................9
     COPY Operation............................................10
     DUMP Operation............................................11
    Accessing External Drives..................................11
    Notes on Media Types.......................................12


































				 i







 INTRODUCTION

 This document is comprised of major excerpts of the full  ANADISK
 reference  material.	 If you wish to get a copy of the complete
 documentation for  ANADISK  -	you  guessed  it  -  you  have	to
 REGISTER.  See the preceding page for information on registering.


 ANADISK IN BRIEF

 ANADISK is a general-purpose utility package to analyze, inspect,
 edit, repair and copy diskettes.  It is intended for IBM Personal
 Computer-compatible  machines	and  makes  extensive  use  of the
 hardware facilities of this series of machines.  ANADISK does not
 support the "hard" disk, just diskettes.

 ANADISK contains  support  for,  but  is  not	limited	 to,  DOS-
 compatible diskettes.	 Almost any diskette that can successfully
 be read  by  the  hardware  contained	in  your  machine  can	be
 processed by ANADISK.

 Menus,	 windows  and  use  of	color  where available are part of
 ANADISK's implementation and make it easy to use, even by the in-
 experienced.


 ANADISK OPERATION

 As distributed,  ANADISK consists of this  file  (usually  called
 READ.ME or ANADISK.DOC) and the file ANADISK.EXE.  To begin using
 ANADISK, just place the ANADISK.EXE file where it can be executed
 as a program and enter -

	   ANADISK

 at the DOS prompt.

 If you have a monochrome display adapter, ANADISK's displays will
 be  light  on	a dark background with occasional reverse video or
 highlighting.

 If you have a monochrome monitor connected to	a  color  graphics
 adapter,  or  you find that you would rather have a light-on-dark
 display rather than a color display,  simply invoke ANADISK  with
 the following line -

	   ANADISK M

 All displays will be light on a dark background.




			      Page 1







 If  all goes well,  you'll get what a friend calls the "elevator"
 display - a graphic ANADISK floats down to  the  bottom  of  your
 screen,  and the registration information appears.  After a short
 pause, the main menu appears.

 During the operation of ANADISK,  there are two keys whose  func-
 tion does not change:

      ESCape  exits from whatever ANADISK is currently doing.	If
      ANADISK is at the Main Menu,  ESCape exits to DOS.    Other-
      wise,  ESCape  takes ANADISK back one menu or display.	In
      general, ESCape takes ANADISK  back to whatever it was doing
      before the current operation.

      F1 gets a help display if one is available.   Beginning with
      version 1.31, a help display is available everywhere ANADISK
      requests keyboard input.	 This help is "context sensitive";
      that is, it relates directly to the current state of ANADISK
      execution.   For example,	 pressing F1 at the main menu will
      display  a  short	 explanation  of  the choices shown on the
      menu.   Pressing any other key will then bring you  back	to
      the main menu.


 Menus

 Menus are used to select ANADISK's operating modes.   The current
 choice for an item is indicated by displaying that item in a  in-
 verse video field;  the current position within the menu is indi-
 cated by blinking that item.	To select a different choice,  use
 the right- and left-arrow cursor keys.	 To go to the next line in
 the  menu,  use  the  up-  or	down-arrow cursor keys.	  When all
 choices have been made,  press the ENTER  key	and  ANADISK  will
 progress to the next menu.  To exit to DOS, press the ESCape key.


 The Main Menu

 ANADISK's  main  menu  selects  what function is to be performed.
 The following operations are available:

      SCAN - reads every sector on a diskette, indicates the find-
	   ings,  and optionally pauses	 for  examination.    This
	   function  can  be  used to determine the type of a dis-
	   kette, or just to determine its basic readability.	In
	   addition,  SCAN is used to search for a data pattern on
	   a diskette.






			      Page 2








      EDIT SECTORS - allows editing of the  data  on  a	 diskette,
	   sector by sector.   Many other operations are possible;
	   the diskette under examination need not be a	 DOS  dis-
	   kette.  SECTOR mode is often used to repair data errors
	   or to change the structure of data not normally  acces-
	   sible with the normal DOS utilities.

      EDIT  FILES  -  edits data contained in a DOS file on a dis-
	   kette.   Because a file structure is essential to  this
	   mode, it may be used only with DOS diskettes.  The dis-
	   play and operation is similar to that of EDIT SECTORS.

      REPAIR  -	 reconciles the File Allocation Tables,	 moves bad
	   sectors and scans the diskette for readability.  REPAIR
	   can be used to salvage a diskette containing unreadable
	   files.   Again,  because the REPAIR function requires a
	   DOS	file structure,	 it may be used only with DOS dis-
	   kettes.

      COPY - copies one diskette to another, regardless of format.
	   While not intended  as  a  method  for  defeating  copy
	   protection schemes,	the COPY function will make a true
	   copy of just about any diskette,  regardless of format.
	   This	 operation also verifies the integrity of the copy
	   by performing a read-after-write check of each sector.

      DUMP - copies a range of cylinders to a file.  This function
	   allows "off-line" processing of data read by  the  SCAN
	   operation.

 Where	the  integrity or format of a diskette is unknown,  a SCAN
 operation should first be performed.  If data errors are reported
 during the progress of a SCAN,	 it is best to	attempt	 a  repair
 first by using the SECTOR or FILE Edit modes.	REPAIR mode can be
 used as a "last resort" for correcting DOS diskettes, or to iden-
 tify a particular file containing erroneous data.

 After	the  operating	mode has been selected from the main menu,
 depressing the ENTER key will cause  one of several sub-menus	to
 appear.      Each sub-menu contains specifications for parameters
 pertaining to the operating mode selected.


 SCAN Operation

 The SCAN mode sub-menu displays the following options;






			      Page 3







      DISKETTE UNIT - Selects which diskette unit will be scanned.
	   Normally, these appear as A: through D:.   However,	if
	   physical unit access has been specified (see "Accessing
	   Other  Drives"),  the diskette unit choices will appear
	   as 0: through 3:.

      PRINTER OUTPUT - If selected,  causes a log to be printed on
	   device  LPT1:  during  the SCAN operation.	Otherwise,
	   results of the scan are only displayed and not printed.

      PAUSE AFTER ANOMALIES -  If  selected,  ANADISK  will  pause
	   after an anomalous condition or error occurs.    Press-
	   ing any key will cause execution to resume.

      SHOW DETAIL MAP AFTER ANOMALIES - If selected,  a map of the
	   track will be displayed showing cylinder, head and sec-
	   tor	addresses as they occur on the track.	Errors and
	   deleted data marks are also noted.	Pressing  any  key
	   will cause SCAN operation to resume.

      SEARCH  FOR A DATA PATTERN - If selected,	 allows specifica-
	   tion of a hexadecimal or ASCII  data	 value	up  to	20
	   bytes in length.   In addition, a hexadecimal selection
	   mask may also  be  specified;  '1'  bits  in  the  mask
	   specify  positions that are to be considered during the
	   search; '0' bits are "don't cares".

	   For more information on this mode,  see "Searching  for
	   Data", below.

 SCAN  mode first attempts to determine the characteristics of the
 diskette drive and controller.	 As  the  characteristics  of  the
 equipment  found are determined,  they are reported in either the
 left (General Information) or right (Detailed	Information)  win-
 dows.	An attempt is made to determine the following:

	   1.	 If the diskette contains any readable information.

	   2.	 The  data rate (250Kbps,  300Kbps or 500Kbps) used
		to record the information, if applicable.  This is
		reported in terms of the drive type and the  terms
		"high" or "low" density.

	   3.	 The  track density or spacing of the diskette ver-
		sus the normal	recording  track  density  of  the
		drive (48 or 96 tracks per inch).  If the diskette
		appears to be blank,  this is reported and ANADISK
		exits to the main menu.

	   4.	 If the diskette contains 512 byte sectors,  sector
		0,  side 0,  cylinder 0 is read and examined for a
		DOS boot sector.  If one is found, the information

			      Page 4







		is saved and used in operations involving DOS file
		structure.   Additionally,  a "pop-up" window  ap-
		pears,	showing the information read from the boot
		sector.	  Pressing any key causes this	window	to
		disappear.

		If no valid boot sector data can be found, a check
		is  made for a File Allocation Table (FAT) present
		on the first track of the diskette.    If  one	is
		found,	the  diskette  is assumed to be a DOS dis-
		kette,	and analysis is conducted based on the FAT
		identification byte located.   Note that either of
		the two FATs may be  intact  (something	 that  DOS
		will not look for).

	   5.	 If  a	DOS diskette is detected,  all FAT clusters
		are checked for correct range,	and if both copies
		of  the	 FAT can be read,  the two copies are com-
		pared  for  consistency.     Any  differences  are
		reported  and  may  be	repaired  by  means of the
		REPAIR mode or the SECTOR edit mode.

		If a DOS diskette cannot be identified, a check is
		made for a few other common diskette  types,  such
		as CP/M-86 system diskettes.

		Regardless  of	the  type of diskette,	the entire
		diskette is scanned for structure and readability,
		reporting changes in the overall  format  of  each
		track as well as any errors detected.


 Searching for Data

 A  SCAN  mode	option	allows	a  diskette  to	 be searched for a
 specified data value.	 If this option is selected  on	 the  SCAN
 sub-menu, another menu will appear with the following choices:

      SEARCH KEY MODE specifies whether the search key will be en-
	   tered in ASCII or hexadecimal.   In either case,  up to
	   20 bytes of data may be entered.

      SEARCH QUALIFICATION specifies how much 'leeway'  should  be
	   given  in  the search.   if NONE is selected,  the data
	   value will be located exactly as it is entered.  IGNORE
	   CASE will cause upper- and lower-case ASCII letters	to
	   be considered as being equivalent.  SPECIFY MASK allows
	   specification  of a hexadecimal mask value.	 This mask
	   value contains '1' bits in those positions of the  data
	   value  to be considered in the search.  '0' bits denote
	   "don't care" positions.


			      Page 5







 When either the search data value or mask is being entered, Alt-X
 (the Alt and 'X" keys depressed simultaneously),  will cause  the
 current  position  to	be  regarded as a "don't care".   That is,
 Alt-X specifies a "wild card" which will not be considered in the
 search.   The first byte of the search data value must not  be	 a
 "don't care".

 After	the  search  data  value and the qualifying mask have been
 specified,  a normal track-by-track scan is performed of the dis-
 kette.	  When a match is found with the specified value,  a "pop-
 up" window gives the location and, if applicable,  the file where
 the match occurred.  ANADISK then pauses until one of the follow-
 ing keys has been pressed:

      C	    to continue and find the next occurrence of the value.

      S	    to skip the remainder of the track and continue search-
	   ing with the next track.

      E	    to	enter  SECTOR  EDIT mode with the sector containing
	   the data.   When an exit from SECTOR EDIT mode is made,
	   the "pop up" window reappears.

      ESCape to exit SCAN mode and return to the main menu.

 The search for a match on a specified data value continues to the
 end of the diskette.


 SECTOR EDIT Operation

 The  SECTOR  Edit  mode allows diskette data to be altered or in-
 spected on a sector address basis,  as contrasted with	 the  FILE
 edit  mode,  which  allows editing of data within a specified DOS
 file.

 The SECTOR EDIT sub-menu selects the diskette unit to be used.

 Like SCAN mode,  SECTOR Edit mode begins operation by determining
 the diskette type and drive characteristics.  After this is done,
 a prompt is displayed to select the track and side containing the
 sector(s) to be inspected or modified.

 The right- and left-cursor keys are used to select the track, the
 up- and down-cursor keys are used to select the head or side con-
 taining the sector.   The "ruler" line shows this position change
 correspondingly.     When the ENTER key is pressed,  the track is
 read for analysis and a track map is displayed.

 The desired sector is selected from the displayed  track  map	by
 use of the up- and down-cursor keys. When the sector to be edited
 is highlighted,  the ENTER key is pressed to display the data for

			      Page 6







 that sector.	Note that the sectors are listed in the	 order	in
 which they occur on the track,	 but that the selection is done in
 strictly numerical order.

 The sector data is displayed in hexadecimal  and  ASCII  formats;
 the  current  position	 within	 the sector data is indicated by a
 highlighted, inverse video block.   Sector data may be changed by
 simply entering new data at the current position or by making use
 of  one of the predefined function keys.   If the sector data has
 been changed,	but not re-written to the disk,	 the  word  "SAVE"
 will  appear  in  the	editing menu window as a reminder that the
 data displayed does not yet reflect the actual data on the disk.

 The function keys are as follows:

      F1    Help key, brings up a help display for editing.

      F2    Re-reads the current sector and display its data.

      F3    Writes the currently displayed data back  to  the  dis-
	   kette.

      F4    Toggles the deleted data mark indicator.   If set,	the
	   data in the buffer will be written (when  F3	 is  used)
	   back	 to  the  diskette  with a Deleted Data Mark.	If
	   clear, no deleted data mark will be set.

      F5    Shifts all the currently displayed data  left  one	bit
	   from	 the  current  position	 to the end of the sector.
	   High-order bits shifted out of the current position are
	   discarded;  zeroes are shifted into the low-order  bits
	   of the last byte of the sector.

      F6    Shifts  all	 the currently displayed data right one bit
	   from the current position to the  end  of  the  sector.
	   High-order  zeroes  are  shifted into the current posi-
	   tion, with low order bits being discarded from the last
	   byte of the sector.

      F7    Takes the ones' complement (logical NOT)  of  the  cur-
	   rently  displayed data from the current position to the
	   end of the sector.

      F8    Fills the remainder of the currently  displayed  sector
	   with the value of the byte at the current position.

      F9    Reads the next sector of the current track; if the last
	   sector  has	just been read,	 "wraps" back to the first
	   sector on the track.




			      Page 7







      F10   Changes  the  display  mode	  and	data   entry   from
	   hexadecimal	to  ASCII  or  vice-versa.   When in ASCII
	   entry mode,	all printable characters (value of a space
	   or above) can be entered.

      Shift-F2	 Performs  a  "diagnostic  read"  of the track.   A
	   diagnostic read involves reading the data field of  the
	   first  sector  and continues with all fields until 8192
	   bytes have been read.    ID fields,	gap bytes and CRCs
	   are read indiscriminately; no attempt to re-synchronize
	   the	data  separator is made after the first sector has
	   been read.	This function allows viewing of	 raw  data
	   and	may be used to determine the value of a data field
	   whose address ID field has been corrupted.

      Shift-F3	 Performs a read of every  sector  on  the  current
	   track and side;  the data is accumulated.  The track is
	   then re-formatted and the data rewritten to the  track.
	   Before the formatting occurs,  you will be asked to ap-
	   prove the formatting - if ESCape is pressed, the opera-
	   tion will not be performed.	 This function may be used
	   to transfer just one track from one diskette to another
	   by swapping the source and destination after the prompt
	   appears, but before a response is given.

      Shift-F9	 Reads the previous sector on the track; if already
	   at the beginning of the track, "wraps" to the last sec-
	   tor on the track.

      Shift-F10	 Reads the next side; equivalent to exiting back to
	   the main display and advancing to the next side.

      ESCape - Backs up to the previous display.

 In  case  of sector data errors,  ANADISK will attempt to present
 all data recoverable from the diskette.   Some of  the	 functions
 just described are intended to assist in recovering data that has
 become	 corrupted.   The Shift Right,	Left and NOT functions are
 especially useful in this respect.

 If a sector shows up as "missing" or "added" on the track map, it
 cannot be read,  nor  will  it	 be  written.	 If  any  data	is
 recoverable when a sector is read however,  the sector can be re-
 written and the error condition generally will disappear.


 FILE EDIT Operation

 FILE Edit mode is similar to the SECTOR Edit mode  of	operation,
 with  the  exception that DOS file structure is used as the basis
 for organizing information, rather than the physical organization
 of sectors on the diskette.

			      Page 8








 The opening display for FILE Edit mode presents a  list  of  file
 names contained in the root directory of the diskette.	  The cur-
 sor up- and down-arrow keys are used to select	 the  file  to	be
 edited;  the  file  name  display may be "paged"  by means of the
 Page Up (PgUp) or Page Down (PgDn) cursor keys.

 To examine the files in a particular subdirectory,  position  the
 cursor bar to the subdirectory name and press ENTER.	To go back
 to the parent directory of a subdirectory,  position to the  ".."
 entry and press ENTER.	  To begin editing a file, position to the
 file name and press ENTER.

 The  editing  display	is  almost identical to that of the SECTOR
 Edit mode, with the following exceptions:

      F9    Reads the next sector in the file, rather than the next
	   sector on the track.

      Shift-F9	 Reads the previous sector in the file, rather than
	   the previous sector on the track.

      Shift-F10	 Does not operate in this mode.

 Note that the file name and offset from the beginning of the file
 appear in the editing menu window, along with a "SAVE" indication
 if data has been altered.


 REPAIR Operation

 REPAIR mode can be considered to be two functions.   The first is
 a rudimentary DOS diskette check and verify mode; the second is a
 bad  sector  remapping mode.  The bad sector remapping operations
 should be viewed as a "last resort" type of repair as the overall
 structure of the diskette is affected.

 REPAIR mode performs the following tasks:

      1.    Checks for the presence and agreement of two  File	Al-
	   location tables on the diskette.   If a disagreement is
	   found,  or one table is absent,  a new copy of the  FAT
	   may optionally be rewritten to the diskette.

      2.    Scans the entire diskette for unreadable data.   If any
	   is found,  the file containing the bad data is located,
	   the	cluster	 (a  grouping  of sectors used by DOS as a
	   "unit" of diskette space) is reassigned to a  different
	   area	 of  the  diskette and the data (or as much of the
	   data that can be read) is written to the newly assigned
	   cluster.   The original cluster containing the data	is
	   marked as unavailable for future allocation.

			      Page 9








 The  object of REPAIR mode is to produce a readable DOS diskette.
 Missing data or data in error still must  be  corrected  manually
 but  the  structure  and size of files will be correct.   The DOS
 utility CHKDSK can  be useful when checking  the  structural  in-
 tegrity  of  a	 diskette and should be used after REPAIR mode has
 been run for a "second opinion".


 COPY Operation

 COPY mode allows the contents of one diskette	to  be	copied	to
 another,  regardless  of  format or DOS orientation.	While COPY
 mode will successfully produce copies of  many	 "copy  protected"
 diskettes,  the intent of its function is to enable one to copy a
 diskette which is not copyable using the DOS DISKCOPY function.

 A two-drive machine is not necessary for this function;  that is,
 the source and target drives may be the same unit.  If one of the
 drives	 is a high-capacity (PC-AT type) drive and normal 40 track
 diskettes are being copied,  the high-capacity	 drive	should	be
 designated  as	 the source drive and the normal-capacity drive as
 the destination to ensure an accurate, readable copy.

 The COPY sub-menu requests specification of the source	 and  des-
 tination  drives.    When ENTER is depressed,	the COPY operation
 begins by reading the source diskette.

 If the type of the source drive and diskette  is  not	compatible
 with the type of the destination drive,  an error message will be
 issued and ANADISK will exit COPY mode.   For	instance,  a  1.2M
 byte  high-density  diskette  in  a  high-density drive cannot be
 copied to a 360K byte normal-density drive.

 A scan of the diskette is performed as the copy proceeds;  errors
 are  noted  in	 exactly the same manner and format as in the SCAN
 mode.	 Sectors containing data errors are copied  with  the  er-
 roneous  data written as read.	  Each track is read back after it
 is written for verification.	The copy process completes when no
 more data can be found on the source diskette.

 If the destination and source drives have been selected to be the
 same  unit,  ANADISK  will  prompt  for  disk	changes as needed.
 ANADISK attempts to read as much data as is possible into  memory
 from  the  source diskette before writing to the destination dis-
 kette.	  With a 640K system under DOS 3.3,  about 46 double-sided
 tracks can be copied before a disk change is necessary.






			      Page 10








 DUMP Operation

 The  DUMP operation specifies that data read during a SCAN opera-
 tion be written to a file.   Either the entire disk or a part	of
 it can be written to the specified file.

 The DUMP operation first requests specification of the drive con-
 taining  the diskette to be scanned.	A prompt is then displayed
 for the name of the file  to  contain	the  data  read	 from  the
 scanned diskette.   If the ESCape key is pressed at this time, an
 exit is made to the main menu.	  Otherwise,  the  named  file	is
 created  and  prompts	are displayed for the cylinder range to be
 written to the file.  If the starting cylinder is specified to be
 greater than the ending cylinder,  no data will be written to the
 file.	 Otherwise, a series of records of the following form will
 be written:

      1 Byte	 The actual (physical) cylinder number.
      1 Byte	 The actual head (or side) number; either 0 or 1.
      1 Byte	 The cylinder number as read.
      1 Byte	 The head or side number as read.
      1 Byte	 The sector number as read.
      1 Byte	 The length code as read.  Thus, a length code of 1
		implies a sector length of 256 bytes; a code of 2,
		512 bytes; 3, 1024 bytes, and so on...
      2 Bytes	 The length of the data read.	This  a	 an  Intel-
		style binary word;  that is, the least significant
		byte of the number precedes the	 most  significant
		byte.  Thus, a length of 512 bytes (200 hex) would
		appear	as 00 02.   If this quantity is zero,  the
		sector data could not be read.

      Then follows the sector data.

 All sectors  occurring	 on  a	side  will  be	grouped	 together;
 however,  they	 will appear in the same order as they occurred on
 the diskette.	Therefore,  if an 8 sector-per-track diskette were
 scanned which had a physical interleave of 2:1, the sectors would
 appear in the order 1,5,2,6,3,7,4,8.


 Accessing External Drives

 In  its  normal  operating  mode,  ANADISK uses BIOS interrupt 11
 (hex) to determine the number of diskette drives attached to  the
 computer.    The  ROM BIOS gets this information from the mother-
 board DIP switches (on PC's and XT's), or from the CMOS RAM writ-
 ten by the SETUP program (on AT's).   If a  drive  has  been  in-
 stalled  which	 is  not  indicated  by	 either of these settings,



			      Page 11







 ANADISK will need to be told about the total number  of  diskette
 drives	 that are actually installed.	This is done by specifying
 the number of drives on the ANADISK command line.  For example,

		ANADISK 4

 indicates a four-drive system is present.   ANADISK will refer to
 these drives as 0:, 1:, 2: and 3:.


 Notes on Media Types

 ANADISK  contains  code  to recognize single density (FM encoded)
 diskettes if the host diskette controller supports that facility.
 The notation "FM",  rather than "MFM" will appear in the  GENERAL
 INFORMATION window.   All operations (read, write and format) are
 supported.

 Additional code has been incorporated in Version 1.31 to  provide
 support  for ATARI ST 3.5" diskettes.   Strictly speaking,  these
 are not DOS diskettes,	 but their structure is close  enough  for
 them to be treated as such.

 High-density  modes  (1.2Mbyte 5.25" and 1.44Mbyte 3.5") are sup-
 ported only on AT-class computers and Personal System/2 models 50
 and above.


















 Some  of  the	terms  used  in	 this  document	 are   proprietary
 trademarks of one or more of the following:

      International  Business Machines - IBM,  PS/2,  Personal
      System/2, PC AT.	Microsoft - MS-DOS




			      Page 12







			  SYDEX SHAREWARE

      CON->FORMAT - Concurrent	"background"  diskette  formatter.
      Features	 "pop-up"  operation  and  "hot  key"  activation.
      You've got to see it to believe.   Supports all current  DOS
      formats. $15.00 ($50.00 site) registration fee.

      22DISK - Transfer files,	format, examine and erase files on
      "foreign" CP/M diskettes on your PC.   Includes tips on sup-
      porting  8"  and  5.25" single-density diskettes.   Contains
      definitions for over 200 different formats.   $15.00 ($40.00
      site) registration fee.

      22NICE  -	 A  CP/M 2.2 emulation package.	  Supports the NEC
      V-series chips or performs emulation by  software	 for  both
      the  8080	 and Z80 processors.   Includes terminal emulation
      and diskette handling for common	CP/M  systems.	  Includes
      22DISK.  $30.00 ($75.00 site) registration fee.

      ANADISK  -  The compleat diskette utility.   Nothing like it
      anywhere else;  scan,  edit,  repair and copy just about any
      kind of diskette.	 $15.00 ($50.00 site)  registration fee.

      TELEDISK - Turn any diskette into a compressed data file and
      vice-versa.  Allows you to send and receive entire diskettes
      via modem.  Even works with some "copy-protected" diskettes.
      $20.00 ($65.00 site) registration fee.

      COPYQM - Cheap diskette duplicator.  Format, copy and verify
      multiple	diskettes  from	 a single master.   Implements "no
      keyboard" interaction mode and drive "round  robin"  servic-
      ing.    Supports	all standard DOS formats.   $15.00 ($50.00
      site) registration fee.

      FORMATQM - Mass diskette formatter - format a  box  of  dis-
      kettes at a single sitting.  Implements "no keyboard" inter-
      action mode and drive "round robin" servicing.  Supports all
      standard	DOS  formats.	 $10.00 ($40.00 site) registration
      fee.

			  RETAIL SOFTWARE

      SIM-CGA  4.2  -  Color  Graphics	 Adapter   simulation	on
      monochrome (Hercules-compatible) graphics-equipped machines.
      Available	 from better software retailers and distributed by
      CSS, ABCO and American Software Distributors.

      SIM-EMS - Simulate Lotus/Intel/Microsoft Expanded Memory	on
      PC-AT  class  machines.	Conforms to EMS 4.0 specification.
      Distributed by CSS and ABCO.



			      Page 13