PLEASE DO NOT DOCUMENT THE CONTENTS OF THIS FILE FOR YOUR
CUSTOMERS OR END USERS.  INCLUDED ARE DATA RELATED TO DOS
IMPLEMENTATIONS INCLUDING A VERSION DEPENDENT SYSTEM CALL
(GET_DPB) WHICH OEM'S MAY USE WHEN WRITING FORMAT.


        The following notation is used below:

        [item]      item is optional.
        item*       item is repeated 0 or more times.
        item+       item is repeated 1 or more times.
        {item1 | item2}
                    item1 is present or item 2 is present  but
                    not both.
        <object>    indicates a syntactic variable.


UNDOCUMENTED COMMAND.COM FEATURES


COMMAND invokation

COMMAND [[<drive>:]<path>] [<cttydev>] [/D] [/P] [/C <string>]

        /P  If  present  COMMAND  will be permanent, otherwise
            this is a transient command.

        /D  If present COMMAND  will  not prompt  for DATE and
            TIME when it comes up.

        d:  Specifies  device  where  command  will  look  for
            COMMAND.COM current default drive if absent.

        <Path>  Specifies  a  directory  on  device  d:   root
            directory if absent.

        <cttydev> Name of the CTTY device.  \DEV\CON if absent
            and  command  is permanent.  The \DEV\ may be left
            off if AVAILDEV is TRUE (see sysinit doc).

        /C <string> If present /C must  be  the  last  switch.
            This  causes  COMMAND to try to execute the string
            as if the user had typed it at the standard input.
            COMMAND  executes  this  single command string and
            then exits.  If the /P switch  is  present  it  is
            ignored  (can't  have  a single command, permanent
            COMMAND).  NOTE: ALL of the text  on  the  command
            line  after  the  /C is just passed on.  It is not
            processed for more arguments, this is why /C  must
            be last.


GET_DPB UNDOCUMENTED SYSTEM CALL.  THIS CALL MAY BE USED
TO GET A POINTER TO THE PHYSICAL LOCATION OF THE DISK DEVICE
DRIVER.  CONSULT THE DBP STRUCTURE DOCUMENTED IN DOSSYM.ASM


+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
|     C  A  V  E  A  T     P  R  O  G  R  A  M  M  E  R     |
|                                                           |

    Name:   *   GET_DPB      - get pointer to drive  parameter
                block

    Assembler usage:
            MOV     AH,GET_DPB
            INT     21h
        ; DS:BX has address of drive parameter block

    Description:
            Return pointer to default drive parameter block.

    Error returns:
            None.

    Assembler usage:
            MOV     DL,DrvNUM
            MOV     AH,32H
            INT     21h
        ; DS:BX has address of drive parameter block

    Description:
            Return pointer  to drive parameter block for drive
        designated in DL (0=Default, A=1, B=2 ...)

    Error returns:
        AL = FF
                The drive given in DL is invalid.
|                                                           |
|     C  A  V  E  A  T     P  R  O  G  R  A  M  M  E  R     |
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+




                DIFFERENCES AND NEW ADDITIONS
                  TO THE INT 24H HARD ERROR
                   HANDLER(s) FOR MSDOS 2.0


1.) Additional Constraints:

        Under previous versions it was not  explicitly  stated
    that an  INT  24H  handler  must preserve the ES register.
    It is now required that  INT  24H  handlers  preserve  ES.

        When it is  desired  to  ignore  an  error,  the  same
    registers must  be  preserved  as  when  it  is desired to
    retry the operation (SS,SP,DS,BX,CX,DX).

        It was not clearly stated in  the  past,  but  it  was
    true, that  only  system  calls 1-12 can be made by an INT
    24H handler.  Making any  other  calls  will  destroy  the
    DOS stack  and  thus  its  ability  to  retry or ignore an
    error.

        INT 24H Handlers  should  always  return  to  the  DOS
    on a  retry,  ignore,  or abort.  Failure to return to the
    DOS will leave the DOS in an unstable state  until  a  non
    1-12 function call is made.

2.) Additional features:

        Character device  errors  are  now  handled by the INT
    24H mechanism.   Previously  only  Disk  I/O  errors  were
    handled by  the  INT  24H handler.  Additional information
    is now passed to the INT 24H handler  in  the  BP  and  SI
    registers (which need not be preserved).

        BP:SI is  a  DWORD  pointer  to  the  Device Header of
    the device causing the error.  Information can  be  gotten
    from this  header  as  to  whether  the  device is a block
    or character device, and if  the  device  is  a  character
    device the  name  of the device can also be obtained.  The
    DEVICE-DRIVERS document for 2.0  contains  the  definition
    of this header format.

    NOTE:  AL  (drive number for Disk errors) is indeterminate
        on character device errors.  Bit 7  of  AH  is  always
        1 for  character  device  errors, previously bit 7 was
        1 only in the case of a bad memory image of  the  FAT.

LIST OF INT 24H ERROR CODES PASSED IN DI

    0 Write Protect violation
    1 Unknown Unit              NEW
    2 Drive not ready
    3 Unknown command           NEW
    4 CRC error
    5 Bad Drive Request Structure length   NEW
    6 Seek error
    7 Unknown media             NEW
    8 Sector not found

    9 Printer out of paper      NEW
    A Write Fault
    B Read Fault                NEW
    C General Failure

As mentioned above BP:SI points to the device header:

BP:SI->
           +--------------------------------------+
           | DWORD Pointer to next device         |
           |  (-1 if last device)                 |
           +--------------------------------------+
           | WORD Attributes                      |
           |  Bit 15 = 1 if char device 0 if blk  |
           |  if bit 15 is 1                      |
           |      Bit 0 = 1 if Current sti device |
           |      Bit 1 = 1 if Current sto output |
           |      Bit 2 = 1 if Current NUL device |
           |      Bit 3 = 1 if Current CLOCK dev  |
           |  Bit 14 is the IOCTL bit (see below) |
           |  Bit 13 is the NON IBM FORMAT bit    |
           +--------------------------------------+
           | WORD Pointer to Device strategy      |
           |      entry point                     |
           +--------------------------------------+
           | WORD Pointer to Device interrupt     |
           |      entry point                     |
           +--------------------------------------+
           | 8-BYTE character device name field   |
           | Character devices set a device name  |
           | For block devices the first byte is  |
           | The number of units                  |
           +--------------------------------------+

    To tell if the error  occured  on  a  block  or  character
device you  must  look  at bit 15 in the attribute field (WORD
at BP:SI+4).

    If the name of the character device  is  desired  look  at
the eight bytes starting at BP:SI+10.



ANSI CURSOR CONTROL ESCAPE SEQUENCES


As defined for the IBM PC.

Notes:

1.  The default value is used when no explicit value is given
    or a value of zero is given.

2.  Pn  -  Numeric  parameter.   A decimal  number  specified
    with ASCII digits.

3.  Ps - Selective parameter.     Any decimal number  that  is
    is  used  to  select a subfunction.  Multiple subfunctions
    may  be  selected  by  separating  the   parameters   with
    semi-colons.


C U R S O R   F U N C T I O N S

CUP - Cursor Postion

      ESC [ Pl ; Pc H

HVP - Horizontal & Vertical Postion

      ESC [ Pl ; Pc f

   CUP  and  HVP  move the cursor to the position specified by
the parameters.  The first parameter specifies the line number
and  the  second  parameter  specifies the column number.  The
default value is one.  When no parameters are given the cursor
is moved to the home postion.

CUU - Cursor Up

      ESC [ Pn A

   Moves the cursor up one line without changing columns.  The
value of Pn determines the number of lines moved.  The default
value for Pn is one.  This sequence is ignored if  the  cursor
is already on the top line.

CUD - Cursor Down

      ESC [ Pn B

   Moves the cursor down one line  without  changing  columns.
The  value  of  Pn  determines the number of lines moved.  The
default value for Pn is one.  This sequence is ignored if  the
cursor is already on the bottom line.

CUF - Cursor Forward

      ESC [ Pn C

   Moves the cursor forword one column without changing lines.
The  value  of Pn determines the number of columns moved.  The
default value for Pn is one.  This sequence is ignored if  the
cursor is  already in the rightmost column.

      ESC [ Pn D

Moves the cursor back one column without changing lines.  The
value of Pn determines the number of columns moved.  The default
value for Pn is one.  This sequence is ignored if the cursor
is already in the leftmost column.

DSR  - Device Status Report

       ESC [ 6 n

The  console  driver  will output a CPR sequence on receipt of
DSR.

CPR - Cursor Position Report (from console driver to system)

       ESC [ Pn ; Pn R

   The  CPR  sequence  reports  current  cursor  position  via
standard  input.   The  first  parameter specifies the current
line and the second parameter specifies the current column.

SCP - Save Cursor Postion

       ESC [ s

   The current cursor position is saved.  This cursor position
can be restored with the RCP sequence.

RCP - Restore cursor position

       ESC [ u

   Restores  the  cursor position to the value it had when the
console driver received the SCP sequence.

E R A S I N G

ED - Erase Display

     ESC [ 2 J

Erases  all  of  the  screen  and  the cursor goes to the home
position.

EL - Erase Line

     ESC [ K

   Erases from  the cursor to the end of the line and includes
the cursor position.




M O D E S   O F   O P E R A T I O N

SGR - Set Graphics Rendition

      ESC [ Ps ; ... ; Ps m

Invokes  the  graphic rendition specified by the parameter(s).
All  following  characters  are  rendered  according  to   the
parameter(s) until the next occurence of SGR.

Parameter     Parameter Function

   0            All Attributes Off
   1            Bold On
   4            Underscore On           (monochrome displays
                                        only)
   5            Blink On
   7            Reverse Video On
   8            Concealed On            (ISO 6429 standard)
  30            Black foreground        (ISO 6429 standard)
  31            Red foreground          (ISO 6429 standard)
  32            Green foreground        (ISO 6429 standard)
  33            Yellow foreground       (ISO 6429 standard)
  34            Blue foreground         (ISO 6429 standard)
  35            Magenta foreground      (ISO 6429 standard)
  36            Cyan foreground         (ISO 6429 standard)
  37            White foregound         (ISO 6429 standard)
  40            Black background        (ISO 6429 standard)
  41            Red background          (ISO 6429 standard)
  42            Green background        (ISO 6429 standard)
  43            Yellow background       (ISO 6429 standard)
  44            Blue background         (ISO 6429 standard)
  45            Magenta background      (ISO 6429 standard)
  46            Cyan background         (ISO 6429 standard)
  47            White backgound         (ISO 6429 standard)

SM  - Set Mode          (IBM/MICROSOFT Private)

      ESC [ = Ps h
or    ESC [ = h
or    ESC [ = 0 h
or    ESC [ ? 7 h


Invokes the screen width or type specified by the parameter.

Parameter     Parameter Function

   0            40 x 25 black and white
   1            40 x 25 color
   2            80 x 25 black and white
   3            80 x 25 color

   4            320 x 200 color
   5            320 x 200 black and white
   6            640 x 200 black and white
   7            wrap at end of line


RM - Reset Mode

      ESC [ = Ps l
or    ESC [ = l
or    ESC [ = 0 l
or    ESC [ ? 7 l


   Parameters are the  same  as  SM  (Set  Mode)  except  that
parameter 7 will reset wrap at end of line mode.



K E Y B O A R D   R E - A S S I G N M E N T

Although not part of the ANSI 3.64-1979 or ISO  6429  standard
the  IBM  PC  keyboard  re-assignment was done in a compatible
way.

The control sequence is:

     ESC [ Pn ; Pn ; ... Pn p
or   ESC [ "string" ; p
or   ESC [ Pn ; "string" ; Pn ; Pn ; "string" ; Pn p
or   any other combination of strings and decimal numbers

The  final  code in the control sequence ("p") is one reserved
for private use the by ANSI 3.64-1979 standard.

The first ASCII code in the  control  sequence  defines  which
code  is  being  mapped.   The  remaining  numbers  define the
sequence  of  ASCII  codes  generated   when   this   key   is
intercepted.

To  every  rule  there is an exception, however!  If the first
code in the sequence is zero (NUL) then the first  and  second
code make up an extended ASCII re-definition.

Here are some examples:

1.  Reassign the Q and q key to the A and a key (and the other
    way as well):

    ESC [ 6 5 ; 8 1 p               A becomes Q
    ESC [ 9 7 ; 1 1 3 p             a becomes q
    ESC [ 8 1 ; 6 5 p               Q becomes A
    ESC [ 1 1 3 ; 9 7 p             q becomes a

2.  Reassign  the  F10  key  to to a dir command followed by a
    carriage return:

    ESC [ 0 ; 6 8 ; " d i r " ; 1 3 p

    The 0;68 is the extended ASCII code for the F10  key.   13
    decimal is a carriage return



CONFIG.SYS CONFIGURATION FILE

               Configuration files in MSDOS 2.0


In many cases, there are installation-specific  configurations
of  the  DOS  that  are need to be set up at boot time.  It is
considered a poor design for a user/OEM to have to re-build MS-DOS
include  special  drivers or to include a particular number of
device drivers.  The configuration file allows a  user/OEM  to
configure his system without extra work.

The  configuration  file  is  simply  an  ASCII  file that has
certain commands for the boot task.  The boot  process  is  as
follows:

    Disk  boot  sector  is read.  This contains enough code to
    read the DOS and the initial BIOS.

    This DOS and initial BIOS are read.

    A long jump to the BIOSINIT routine is made.  A variety of
    BIOS initializations are done.

    A  long  jump to the SYSINIT routine in the SYSINIT module
    is  made.   This  module  (supplied  by  MICROSOFT)   will
    initialize   the  DOS  and  read  the  configuration  file
    CONFIG.SYS, if it exists, to  perform  device  instalation
    and various other user settable things.  Its final task is
    to  EXEC  the  command  interpreter,  which  finishes  the
    bootstrap process.

The  following  are  a  list of commands for the configuration
file CONFIG.SYS:

    BUFFERS = <number>
        This is the number of additional sector buffers to add
        to the system list.  The  effect  of  several  BUFFERS
        commands is to allocate a series of buffers.

    FILES = <number>
        This is the number of open files that the XENIX system
        calls can access.

    DEVICE = <filename>
        This installs the device driver in <filename> into the
        system list.

    BREAK = <ON or OFF>
        If ON is specified (the default is OFF), a  check  for
        ^C  at  the  console input will be made every time the
        system is called.  ON improves the  ability  to  abort
        programs over previous versions of the DOS.

    SHELL = <filename>
        This begins execution of the shell (top-level  command
        processor) from <filename>.

A typical configuration file might look like this:

BUFFERS = 10
FILES = 10
DEVICE = \bin\network.sys
BREAK = ON
SHELL = a:\bin\command.com a:\bin /p

   The default value for BUFFERS is OEM specific in  that  the
OEM can specify the number in the BIOS.  A typical value is 2,
the minimal value is one.  The  default  value  for  FILES  is
usually  8  (as above it may be set by OEM BIOS) , so "FILES =
10" actually allocates only 2 new file channels.  If a  number
less  than  or  equal  to  five  is  specified, the command is
ignored.  BREAK defaults to OFF.


INCOMPATIBILITIES BETWEEN MSDOS 1.25 AND MSDOS 2.0- 2.X



Areas where 2.0 is not compatible with  previous  versions  of
the DOS.

+ Direct calls to the BIOS
        Any program which jumped directly to the BIOS  by  way
        of the jump table at 40:0 will no longer work.

+ FAT pointer calls
        Programs which used system calls 27 and 28  to  get  a
        pointer  to  the FAT will no longer work.  Because the
        FAT is now cached with other disk resources, there  is
        no  fixed  location  in memory to pass the address of.
        The calls still exist,  however,  and  have  the  same
        format.  THEY CAN ONLY BE USED TO GET THE FAT ID BYTE.
        On return ES:BX points to a FAT ID BYTE for the Drive.
        Doing  anything  except  READing  this  ONE  byte will
        probably crash the system.  In order  to  get  at  the
        FAT,  programs  will  first call DSKRESET (call 13) to
        flush out any dirty buffers, and then  make  a  GETDPB
        call  (call  31 or 50) to find out which sector on the
        disk the FAT starts at, how big it is,  and  how  many
        copies of  it there are.  Then INT 25H and INT 26H can
        be used to transfer the FAT in and out of the programs
        memory space.

+ INT 25H and INT 26H
        In order for the  above  to  work,  and  in  order  to
        maintain  some  order  in  the  world of multi-surface
        disks, it is required that INT 25H  and  26H  use  the
        MSDOS sector mapping rather than some rather arbitrary
        head-cylinder-sector mapping.

The following subroutine will read the fat into  the  area  of
memory specified by DS:BX.  DL contains the drive number, DL=0
means read the fat from the default drive, DL=1 indicates read
from drive A:, and so on.

getfat:
        push    bx              ; save pointer to fat area
        push    ds
        mov     ah,50           ; request the dpb
        int     21h
        mov     cx,[bx+15]      ; get fat sector count
        mov     dx,[bx+6]       ; first sector of fat
        pop     ds              ; restore fat area pointer
        pop     bx
        mov     al,dl           ; is it the default drive?
        or      al,al
        jnz     driveok         ; if not, load fat

        mov     ah,19h          ; ask for default drive
        int     21h             ; get the default drive
        inc     al              ; map a=0 to a=1
driveok:
        dec     al              ; map a=1 to a=0
        int     25h             ; read the fat into DS:BX
        pop     ax              ; clean up the stack
        ret