SOME NOTES ON THE INSIDES OF CP/M (V1.4)

     THIS FILE CONTAINS SECRET INFORMATION- IT SHOULD BE ERASED
BEFORE READING IT.  THIS INFORMATION WAS OBTAINED BY EITHER POKING AROUND
IN CP/M OR FROM EXAMINATION OF CLASSIFIED DOCUMENTS ( FBI & CIA BEWARE).
ALL LOCATIONS ARE GIVEN IN HEX (AN ARBITRARY BASE SHOULD HAVE BEEN USED
TO PROTECT THE INNOCENT ) AND THEY REFER TO A 16K CP/M VERSION OF CP/M
VERSION 1.4 ON A STANDARD 8 INCH SINGLE DENSITY IBM FORMATTED DISC.

	I.  "AUTO LOAD" FEATURE

     CP/M 1.4 HAS THE ABILITY TO AUTOMATICALLY EXECUTE A PRE-SELECTED
COMMAND AT THE END OF A COLD OR WARM BOOT STARTUP.  THIS FEATURE
IS NORMALLY USED TO COME UP WITH A SIGN-ON MESSAGE OR TO LOAD A SPECIFIC
PROGRAM (SUCH AS BASIC). IT COULD ALSO BE USED AS A DIRTY TRICK BY MAKING
IT LOAD A DISC FORMATTER OR ERASING PROGRAM.
     THE BASIC IDEA IS VERY SIMPLE.  ON COLD BOOT, THE  GOCPM   ROUTINE
(LOOK AT A COPY OF THE BIOS) JUMPS INTO CP/M AT THE START OF  CCP  
(AT 2900H).  THIS ENTRY POINT FORCES A 'LOG-ON' OF DRIVE  'A' AND
AN EXECUTION OF ANY SINGLE LINE COMMAND THAT IS IN THE LINE INPUT BUFFER.
THE STANDARD VERSIONS OF CP/M HAVE THIS INPUT BUFFER SET TO THE EMPTY
STATE, SO THE STANDARD PROMPT IS DISPLAYED (A>) AFTER LOG-ON.  SOME OF
THE RELEVANT CODE IS SHOWN BELOW:

2900H:	CCPBASE:	JMP START  ;USUAL GOCPM ENTRY
			JMP START/CLEAR   ;ALTERNATE ENTRY TO CLEAR
;					   BUFFER FIRST
			DB  7FH    ;MAXIMUM INPUT BUFFER SIZE
	BUFLEN:		DB  00	   ;BUFFER CHARACTER COUNTER
			DS  16	   ;SPACE FOR 16 LETTERS
			DB  "COPYRIGHT ..."  ;COPYRIGHT NOTICE (CAN
;					     ; BE WRITTEN OVER)

	FOR EXAMPLE:
     TO MAKE THE COLD AND WARM BOOT UP SEQUENCES LOAD BASIC FROM
DRIVE B, YOU NEED ONLY PATCH THE ABOVE CODE TO READ:
	
	BUFLEN:		DB  7   ;COMMAND LENGTH
			DB "B:BASIC" ;7 LETTER COMMAND TO LOAD
;					FILE: BASIC.COM.
			DB 00H,0DH   ;COMMAND TERMINATORS 

YOU CAN EASILY DO THIS WITH  SYSGEN  AND  DDT.  IF YOU ONLY WANT THE
COMMAND TO EXECUTE ON A COLD START AND NOT ON A WARM BOOT (AS CAUSED
BY A CONTROL-C), YOU MUST ALSO MODIFY YOUR  BIOS  SO THAT IT JUMPS
TO CCPBASE ON A COLD-START-- BUT CCPBASE+3 ON A WARM START.  THIS
ENTRY POINT CLEARS THE LINE BUFFER BEFORE ENTERING THE COMMAND
PROCESSOR.

	II.  CP/M SERIAL NUMBERS

     I WAS GOING TO GIVE THIS INFORMATION IN CYPHER--BUT THE TRAPDOOR
CODE IS TOO COMPLICATED.  THUS I WILL GIVE YOU A HINT:  THE SERIAL
NUMBERS OCCURE IN TWO IDENTICAL BLOCKS OF 6 BYTES OF CODE IN CP/M
(IN BOTH THE CCP AND BDOS).  THESE SAME TWO BLOCKS OCCURE IN THE
RELOCATED IMAGE OF CP/M CONTAINED IN THE PROGRAM: MOVCPM.COM
(THE CP/M RELOCATOR).  IF YOU CAN'T FIND THEM KNOWING THIS, YOU
DON'T DESERVE TO KNOW ABOUT THEM.

	III.  TABLEIZED CONTROL DATA FOR CP/M

     THE AUTHORS OF CP/M 1.4 DECIDED TO MAKE IT EASIER FOR  OEM'S
TO PERSONALIZE CP/M (FOR VARIOUS TYPES OF HARDWARE) BY PUTTING
A NUMBER OF PIECES OF CONTROL DATA IN TABLES OR SINGLE ROUTINES.
THE BULK OF THESE ARE CONTAINED IN BDOS.  THESE INCLUDE THE SECTOR
INTERLACE TABLE AND PROCESSING ROUTINE, THE SYSTEM ERROR ROUTINE
ADDRESS TABLE, AND THE DISC SIZE SPECIFICATION BYTES.
THIS IS SHOWN BELOW:

3100H:		DS 6   ;SERIAL # DATA.
3106H:	BDOS:	JMP  ENTRY  ; THIS IS WHERE YOU ENTER WHEN YOU
	;		      CALL THE VARIOUS CP/M FUNCTIONS
	;		      THRU A CALL TO ADDRESS 05H.
	; --- TRANSFER TABLE FOR DISC ERRORS
3109H:		DW  PERSUB ;PERMANENT DISC ERROR ROUTINE
		DW  SELSUB ;SELECT ERROR ROUTINE
		DW  ROERR  ;RO (READ ONLY) ERROR ROUTINE
	;
	; --- ROUTINE TO TRANSLATE LOGICAL TO PHYSICAL SECTOR #
	;     BY TABLE LOOKUP.  ENTER WITH REQUESTED LOGICAL SECTOR
	;     # IN (C), EXIT WITH PHYSICAL SECTOR # IN (C).
	;
310FH:	TRANS:	LXI H,TABLE	;POINT TO TABLE
		MVI B,0
		DAD B
		MOV C,M		;CONVERT
		JMP SELSEC
		NOP
	;  TRANSLATION TABLE
311AH:	TABLE:	DB 01H,07H,0DH,13H,19H,05H,0BH,11H
		DB 17H,03H,09H,0FH,15H,02H,08H,0EH
		DB 14H,1AH,06H,0CH,12H,18H,04H,0AH,10H,16H
	;--- 6 EXTRA BYTES
		DB 00H,00H,00H,00H,00H,00H
	;
	; --- DISC SIZE PARAMETER BLOCK
	;
313AH:	SECSIZ:	DB 26  ;NUMBER OF SECTORS/TRACK
	DIRMAX: DB 63  ;MAX. NUMBER OF DIRECTORY ENTRYS
	BLKSHF: DB 3   ;2^3=8=NUMBER OF SECTORS/BLOCK
	BLKMSK: DB 7   ;2^BLKSHF-1
	MAXBLK: DB 242 ;# OF ALLOCATED BLOCKS ON DISC
	DIRALL: DB 0C0H; FIRST BYTE OF ALLOCATION MAP TO RESERVE
	;		 TWO BLOCKS FOR DIRECTORY.
	OPTRKS: DB 2   ;NUMBER OF TRACKS USED TO SAVE BOOT AND
	;		OPERATION SYSTEM.
	;------------------------------------------------------
	NOTE: IF YOU TRY CHANGING THE DISC LAYOUT BY ALTERING THE
ABOVE TABLE, YOU MAY HAVE TO MAKE THE PATCH SHOWN BELOW.  THIS PATCH
ACTUALLY FIXES A BUG IN CP/M 1.4 WHICH YOU WOULD NOT SEE UNTIL YOU
TRIED TO CONFIGURE IT FOR A DIFFERENT DISC LAYOUT (THEY FORGOT TO MAKE
ONE ROUTINE USE THE TABLE DATA FOR THE DISC LAYOUT).

	3972:	CALL	33F4H	;USE ROUTINE THAT DOES IT RIGHT
		NOP
		NOP		;PATCH OUT UNUSED CODE
		NOP
	3978:	MOV	A,C	;GET BLOCK # POSITION
	3979:	LXI	H,3DF8H	


	IV.  ALLOCATION MAP AND DIRECTORY CHECKSUM TABLE

     WHEN YOU DO A WARM BOOT OR SELECT A NEW DRIVE FOR THE FIRST TIME
SINCE THE LAST WARM BOOT, THERE IS A NOTICABLE DELAY WHILE CP/M DOES
SOMETHING ON THE DISC (BEFORE IT ISSUES THE PROMPT).  THIS DELAY
IS CAUSED BY 3 BASIC OPERATIONS BEING DONE BY CP/M:
	
	1.  RE-BOOTING IN CP/M FROM THE DISC.
	2.  CONSTRUCTING AN ALLOCATION MAP FOR THE DISC (BY
	    READING THE DIRECTORY).
	3.  CHECKSUMMING THE DIRECTORY.

CP/M 1.4 MAINTAINS SEPARATE ALLOCATION MAPS (31 BYTES EACH) AND
CHECKSUM TABLES (16 BYTES EACH) FOR EACH OF THE FOUR POSSIBLE
DISC DRIVES.  
	WHAT IS AN ALLOCATION MAP I HERE YOU ASK?  IT IS ESSENTIALLY
A DIRECTORY OF ALL OF THE USED (ALLOCATED) AND UNUSED 1K BLOCKS ON THE
GIVEN DISC.  CP/M USES THIS TABLE TO FIND OUT WHICH BLOCKS ARE AVAILABLE
WHEN YOU TRY TO SAVE A NEW FILE ON THE DISC.  IT CONSTRUCTS THIS TABLE
BY LOOKING AT THE ALL OF THE ALLOCATION BYTES IN THE VARIOUS FILE CONTROL
BLOCKS SAVED IN THE DISC DIRECTORY.  THIS IS DONE THE FIRST TIME YOU
SELECT A NEW DRIVE (I CALL THIS A LOGON OPERATION).  IT DOES NOT DO THIS
EACH TIME YOU SELECT THE DRIVE (TO SAVE TIME), BUT ONLY THE FIRST TIME
AFTER EACH WARM OR COLD BOOT (OR BDOS RESET).  THUS THERE IS A POSSIBILITY
OF YOU REALLY MAKING A BAD MISTAKE IF YOU SWITCH DISCETTES ON A DRIVE
THAT HAS ALREADY BEEN LOGGED IN BECAUSE THE ALLOCATION MAP NO LONGER
IS CORRECT FOR THIS DRIVE.  FOR INSTANCE, IF YOU TRIED TO SAVE A FILE
ON THIS DRIVE, IT MIGHT (AND PROBABLY WOULD) USE A 1K BLOCK THAT WAS
AVAILABLE ON THE PREVIOUS DISCETTE- BUT NOT SO ON THE PRESENT ONE (THUS
OVERWRITING PART OF ANOTHER FILE).  THIS ERROR COULD ACTUALLY OCCURE
UNDER CP/M 1.3.  TO FIX THIS IN CP/M 1.4, THE AUTHORS CREATED CHECKSUM
TABLES WHICH PROVIDE A 1 BYTE CHECKSUM FOR EACH OF THE SECTORS OF THE
DIRECTORY- FOR EACH OF THE FOUR DRIVES.  THE INTERNAL MACHINERY OF CP/M
1.4 TESTS THESE CHECKSUMS EACH TIME A SECTOR OF THE DIRECTORY IS ACCESSED
AND WILL SET THE DRIVE TO READ-ONLY STATUS IF THE CHECKSUMS CHANGE 
UNEXPECTEDLY.
     THE ALLOCATION MAPS CAN BE FOUND (IN A 16K CP/M 1.4) STARTING AT:

		3CFA, 3D1A, 3D3A, AND 3D5A

THE FORMAT IS TO USE ONE BIT FOR THE ALLOCATION OF EACH 1K BLOCK OF
THE DISC THAT IS ACCESSABLE FOR FILE OPERATIONS (TRACKS: 2-76).
THE BLOCK IS ALLOCATED (IN USE) IF ITS CORRESPONDING MAPPING BIT IS
A ONE AND AVAILABLE FOR USE IF IT IS A ZERO.  A NEW DISC (OR AN EMPTY
ONE) HAS ONLY TWO BLOCKS ALLOCATED ( 0,1) .  THIS PREVENTS THE
DIRECTORY (THE FIRST TWO BLOCKS) FROM BEING OVERLAYED.  SUCH A DISC
WOULD HAVE AN ALLOCATION MAP LIKE:

		3CFA:	DB 0C0H	;ALLOCATE TWO BLOCKS FOR DIRECTORY
			DB 00
			DB 00
			.  .
			.  .
			.  .
			DB 00

NOTE: BDOS FUNCTION CODE # 27 IS USED TO ACCESS THIS MAP AND SOME
PROGRAMS IN THE CP/M USER GROUP DISCS (SUCH AS DUMP.COM ON DISC 24)
WILL GIVE A NICE PRINT OUT OF IT ON THE CONSOLE.

	V.  A PATCH TO FIX THE R/O ERROR SEQUENCE IN CP/M 1.4

     CP/M 1.4 HAS THE ANNOYING HABIT OF AUTOMATICALLY MAKING A PREVIOUSLY
LOGGED ON DISC DRIVE READ ONLY (R/O) IF YOU SWITCH DISCS IN THAT DRIVE 
(WITHOUT LOGGING ON THE DRIVE AGAIN).  THIS CAN BE PARTICULARLY ANNOYING
IF YOU ONLY HAVE A SINGLE DRIVE.  THIS IS NOT REALLY A BUG IN CP/M.  THIS
IS A WAY OF AVOIDING A POSSIBLY DISASTEROUS CONDITION (AS DESCRIBED ABOVE).
HOWEVER, I DO NOT COMPLETELY AGREE WITH THEIR WAY OF HANDLING THIS ERROR
CONDITION.  I THINK THAT IN MOST SITUATIONS, A BETTER CHOICE IS TO 
AUTOMATICALLY RE-LOGON THE NEW DISCETTE WHEN THE ERROR IS DETECTED (BEFORE
ANY DISC WRITE OPERATIONS).  THE PATCH SHOWN BELOW IMPLEMENTS THIS CHOICE.
WARNING: IF ANY DISC FILES ARE STILL OPEN WHEN THE DISCS ARE SWITCHED YOU
CAN STILL GET INTO TROUBLE- SO WATCH OUT!!

	OLD CODE			NEW CODE

	34C6:	CALL	34AE		CALL	34AE
		RAR			RAR
		JNC	34D5		JNC	34D5
		LXI	H,34D5	   --   JMP	35E0	;LOGON DRIVE
		PUSH	H		PUSH	H
		LHLD	310D		LHLD	310D
		PCHL			PCHL
	34D5:	RET			RET

	VI.  THE ET BYTE (FIRST BYTE OF THE FCB)

     THE FIRST BYTE OF A FCB (WHEN USED FOR DISC FILE OPERATIONS)
IS USUALLY SPECIFIED IN THE CP/M MANUALS AS A ZERO.  HOWEVER IT IS
ACTUALLY USED BY CP/M TO PERFORM AUTOMATIC DRIVE SELECTS DURING
FILE ACCESS.  IT SPECIFIES WHICH DRIVE THE SPECIFIED FILE IS ON:

	ET BYTE=0	FILE ON CURRENTLY SELECTED DRIVE
		1	FILE IS ON DRIVE A
		2	FILE IS ON DRIVE B
		3	FILE IS ON DRIVE C
		4	FILE IS ON DRIVE D

THIS PARTICULARLY USEFUL WHEN USING   DDT.   THIS IS BECAUSE
THE INPUT OPERATION IN DDT WILL NOT ACCEPT THE USUAL CP/M SYNTAX:

	-IB:FILE.HEX		(IT DOESN'T LIKE THE   B:  PART)

HOWEVER YOU CAN NOW DO THE SAME THING BY FIRST USING THE INPUT
COMMAND AND THEN SETTING THE ET BYTE OF THE FCB (AT 05CH) WITH
THE DDT SET COMMAND:

	-IFILE.HEX
	-S5C
	005C 00 02
	005D 46 .
	-

	VII.  RE-ENTRY POINTS TO CP/M AND DDT

     OCCASIONALLY I FIND IT USEFUL (WHEN POKING AROUND IN MEMORY)
TO BE ABLE TO RE-ENTER CP/M OR DDT (WHEN LOADED) WITHOUT DOING A
WARM BOOT (JUMP 00H) .  AFTER LOOKING AROUND IN CP/M 1.4 AND  DDT
I FOUND SOME POINTS THAT SEEM TO WORK OK.  I FOUND THEM BY LOOKING
AT HOW THE PROGRAMS GET INITIALIZED AND WHERE THEY RESET THE STACK
POINTER.

	16K CP/M 1.4 RE-ENTRY POINT: 3037H

		3037:	LXI	SP,3085
			LDA	30C9	;GET DRIVE #
			CALL	29B8	;LOG IN THIS DRIVE #
			JMP	2C71	;PRINT PROMPT, START CP/M.

NOTE:  WHEN DDT IS LOADED, CP/M OVERLAYS PART OF THIS CODE AND
PUTS A  RST 00  AT  3037H.

	RE-ENTRY POINTS FOR DDT

     I FOUND TWO POINTS THAT SEEM TO WORK OK IN  DDT.  HOWEVER, SINCE
DDT SITS AT A MEMORY LOCATION THAT IS DEPENDENT ON YOUR CP/M SIZE, I
WILL HAVE TO GIVE THE LOCATIONS ON A RELATIVE BASIS.  IN YOU SYSTEM,
LOAD  DDT  AND DISASSEMBLE THE JUMP AT LOCATION  05H:

		A>DDT
		DDT VER 1.4
		-L5
		0005  JMP 2100       --- CALL THIS JUMP ADDRESS : ADDX

THE ADDRESS REFERENCED BY THE JUMP AT  0005H WILL BE USED AS THE BASIS
FOR THE TWO RE-ENTRY POINTS:

		ADDX+06FEH
		ADDX+06D2H

---------------------------------------------------------------------
					BY  BRUCE KENDALL