TRINITY SPECIFICATIONS - To be announced at 84 NCC (July 9-12)
----------------------


For delivery AUG 1 ...
------------------
CPU       -    MC68000 (with MC68451 MMU) running at up to 10 MHz

MEMORY    -    512 KB (expandible to 2 MB)

STORAGE   -    16 or 34 MB hard disks (expandible to 4 drives)
               optional 5 MB 'REMOVABLE' hard disk (Fall 84)
               400 KB 5.25" floppy (expandible to 4 drives)
               optional 1.2 MB 8" floppy (up to 4 drives)

I/O       -    4 RS-232C serial ports (expandible to 8)
               1 Centronix compatible parallel port

Op/Sys    -    UNIX SYSTEM V derived with UNISOFT enhancements

Price     -    Complete 4-user system for under $9000.
		(less terminals!)

For delivery SEP 15 ...
-------------------
SLAVES    -    80188 MS/DOS-compatible slaves with 128 KB of
               on board 'DUAL-PORT' RAM (optional 512 KB)

=================================================================

FEATURES
--------

* Powerful 3-point DMA architecture  (I/O, Hard, and Floppy disk) 
  allows  superior  4-user performance,   unheard of  in  systems
  retailing below the $10,000. barrier.

* Combines 3 industry standards ... MC68000, UNIX (SYSTEM V), and 
  the IEEE-696 bus ... assures  tremendous applications  software 
  availability, and hardware flexibility.

* With MS/DOS compatible slaves, even more inexpensive commercial 
  software extensions  can be made available to  UNIX.  An  ideal 
  combination for 3rd-party program development, VAR's and OEM's.



Kevin:

The features section is really good!! Like the way you blended in
the 3 points into 3 points!!

bjg -6/20/84-