MCALL-C: A Communications Protocol 
               for Personal Computers


       Copyright (C) 1980 by Tim J. Pugh, Jr.




In  the protocol description which follows,  I  will 
identify alternative approaches that were considered 
in  arriving  at the present  protocol.  But  before 
getting into the protocol itself I would like to try 
to  clear  up  a  misunderstanding  that  may  exist 
concerning telecommunications protocols. The type of 
protocol which I am describing has no bearing on the 
information content of the data.   The protocol acts 
simply  as  an envelope or container of  data.   The 
data   is   inserted  into  the  envelope   at   the 
originating  (transmitting)  end  and  automatically 
removed at the receiving end.  Thus, by the time the 
data is placed on disk, it looks exactly the same as 
it did on the disk of the originator.

Perhaps the first question to answer is "why have  a 
protocol?".   The principal reason for having one is 
to insure,  as far as possible, that no data is lost 
or  garbled  in the transmission.   One can,  and  I 
often do,  transmit and/or receive data files with a 
large Time Sharing Computer (TSC).   These TSCs' are 
typically very uncooperative beasts which output the 
data  to you in "their own good  time",  usually  as 
fast  as  it can be sent.   They are  not  concerned 
whether you had noise on the line or whether you had 
time to write the last record to disk.   That's your 
problem.  Thus, if you have a system which pays rapt 
attention to the incoming data and if the weather is 
good  and  you have a high quality modem,  then  you 
have  an  excellent chance of receiving  error  free 
data.

However,  one cannot depend on all the above  stated 
conditions  being met,  especially when two personal 
computers  are  involved.    Such  a  transfer  will 
frequently  be  "long distance".    Each  additional 
TELCO  switching  center  involved  in  the   "call" 
reduces the signal to noise ratio and often there is 
line "echo" distortion present.  Thus, reliable data 
transfer becomes questionable without an intervening 
mechanism.   An  appropriate communications protocol 
supplies this mechanism.


         SERIAL VERSUS BLOCKED DATA FORMAT


The simplest way to transfer a file is the way it is 
done  with a TSC.   The file is  simply  transferred 
serially  to  completion.   It  is assumed  the  the 
receiving file has already been created and that the 
TSC is capable of recording the data at the  maximum 
BAUD  rate;  e.g.,  300 BAUD.   Such an approach can 
also  be  used for transfers  between  two  Personal 
Computers  (PCs') provided the operation is properly 
coordinated and synchronized.   However,  it is much 
preferable   to  have  the  two  computers  do   the 
necessary synchronization and coordination since  it 
is  then both more convenient for the users and less 
error  prone.   We  have  thus  posited  a  protocol 
whereby  the  file is automatically  opened  at  the 
Transmitting  (TX) end and created at the  receiving 
(RX) end and might look something like this:

          -->     @SOH <filename><typ>
          <--     @ACK
          -->     <file data>

The  directed arrows indicate the direction of  data 
transfer  where "-->" indicates data from the TX  to 
the  RX.   The  "@"  signifies ASCII and  thus  @SOH 
indicates   the  ASCII  Start  Of   Header   control 
character.    Similarly,   "@ACK"   signifies  ASCII 
ACKnowledge.   Assuming  that the  originating  (TX) 
operator  has  previously specified the name of  the 
file to be transferred;  i.e.,  <filename><type> and 
further   assuming  that  communications  has   been 
established  between  the  two  parties,   then  the 
transfer is initiated by the TX end issuing an  @SOH 
followed  by  the  name  of  the  file.    Since  an 
indeterminate  amount of time is required for the RX 
system  to  create  the  corresponding   file,   and 
ACKnowledgment  is required before the data transfer 
can begin.   Why an indeterminate amount of time  to 
open a file?  Partly because there is such a variety 
of  floppy disks and controllers capable of  running 
under   CP/M  (both  8"  and  5  1/4").    Since   a 
"handshake" character, @ACK, was required to signify 
"file  created  OK";  why not include the option  of 
sending @NAK (Negative AcKnowledge) to signify  some 
problem  in opening the file?   Lets further  assume 
that  if @NAK is received by the TX end,  the  "@SOH 
<filename><typ>" will be repeated.

Since  we have provided for retransmission (reTX) of 
the Header Record,  the next question is how can  we 
discontinue the retransmission, assuming the problem 
persists  over  several reTXs'.   This introduces  a 
third control character,  @CAN (ASCII CANcel).  Thus 
our "handshake" in response to the Header Record can 
take one of three forms.   This situation is handled 
nicely by the BACKUS-NAUR notation which follows:

          <ack.form> ::= @ACK | @NAK | @CAN

Which  states that the acknowledge form  is  defined 
equal to either @ACK or @NAK or @CAN.

We   next  look  at  the  <file  data>.    The  most 
conventional method for "recording" received data is 
to first buffer it in memory and subsequently  write 
it  to  disk.   This allows the RX system to  handle 
high BAUD rates, e.g., 1200 BAUD, without data loss.  
However,  if  large files  are  transferred,  buffer 
overflow  might result.   Thus,  it is desirable  to 
allow   the  buffer  to  be  "dumped"  to  disk   at 
appropriate  times.    A  simple  solution  to  this 
problem  is  to  break the <file  data>  into  small 
blocks followed by an <ack.form>.  Thus, if the data 
is  broken  into equal blocks of 128 characters  the 
protocol would look something like this:

          -->     @SOH <filename><typ>
          <--     @ACK
          -->     <data.blk>
          <--     @ACK
          -->     <data.blk>
          <--     @ACK
          ...
          ...
          -->     <data.blk>
          <--     @ACK

The  @ACK  following each <data.blk>  tells  the  TX 
system  that the buffer write operation is  complete 
and   the  next  block  can  be  sent.    The  above 
considerations argues strongly for a BLOCKED  rather 
than a SERIAL data format for our protocol.  


           DATA INTEGRITY CONSIDERATIONS


The blocked protocol specified thus far provides for 
error recovery (reTX) in the the <filename><typ> was 
garbled;  e.g., noise caused a given character to be 
converted  to  a character which is not  legal  when 
specifying  file names.   It also provided time  for 
data  blocks to be transferred from memory to  disk.  
However,  no  provision has been made to insure that 
data integrity is maintained.

The  most commonly employed techniques for  handling 
this  problem is to use either a  Cyclic  Redundancy 
Check (CRC) or a Checksum.   The CRC usually employs 
a polynomial equation for its realization.  The term 
checksum,  as  used here,  simply means a sum of all 
the  characters in a given data block.   Since  each 
character  in  the ASCII set can be  represented  by 
seven data bits,  this simply means the  accumulated 
total obtained by adding each character, in turn, to 
the  previous  partial  sum.    I  have  chosen  the 
checksum  because  of  its simplicity  and  ease  of 
implementation.

In  implementing  the checksum two choices  must  be 
made:  (1) The block size over which the checksum is 
to be taken;  (2) The number of bits to be allocated 
to  the  checksum.   The most convenient block  size 
appears  to  be that associated  with  one  physical 
record  on disk;  i.e.,  a disk sector of 128 bytes.  
Having  chosen the first parameter we find that  the 
largest  value the checksum could take on occurs  if 
the ASCII rubout character (@DEL = 07FH) is repeated 
128 times.  Since 07FH is equivalent to 127 decimal, 
the worst case checksum would be:

          SUM = 128 * 127 = 16256

This value falls between 2^15 and 2^16.  Thus, a 16-
bit  checksum  would insure a unique  sum  for  each 
unique  data  block.   I am using the term  "unique" 
rather loosely here.   Two data blocks consisting of 
the same characters but in different order are   not  
considered unique, by this definition.

At  least  one popular "serial I/O" card  employs  a 
UART  who's  output is fixed at 7  data  bits.   The 
Cromemco   TU-ART  employs  the  Texas   Instruments 
TMS5501  device to support serial I/O.   The  serial 
output of this device is fixed at 7 data bits with a 
parity  bit of zero.   Thus,  while it would be most 
efficient  to  transfer the 16-bit checksum  as  two 
eight-bit  characters,  this approach would  exclude 
systems  employing  the  TU-ART  card  to  drive  an 
acoustic  coupler.   For this reason,  an ASCII  HEX 
encoding  of   the  checksum  was  employed.    This 
results  in the 16-bit value being broken into  four 
"nibbles" of 4 bits each.   The ASCII representation 
of  each  nibble ranges from ASCII 0 through  9  and 
ASCII  A through F.   There remains the question  of 
ordering  the  output  value;  i.e.,  what  sequence 
should  be  used in  transferring  the  nibbles.   I 
somewhat  arbitrarily  chose  the  most  significant 
nibble first and least significant nibble last.

We  now  have  a  protocol where  each  data  block, 
including   the  header  block,   has   a   checksum 
associated   with   it.    As  each   character   is 
transferred,  both  the TX and RX systems accumulate 
individual checksums.   The TX system transfers  its 
final  value  to the RX,  who tests it for  equality 
with its own value.  If the values agree, an @ACK is 
returned,  otherwise a @NAK is returned and the data 
block is retransmitted.   How many times should reTX 
be  allowed to occur on the same data  block  before 
canceling  (@CAN)  the transfer?   I  have  somewhat 
arbitrarily  chosen the value of  5.   Remember,  it 
takes  quite a bit of time to repeat a data block  5 
times.   Five  repeats plus the original at 300 BAUD 
requires approximately:

          retry time = 6*(128+4)/30 Sec. = 26.4 Sec.

Also  remember we are not dealing with "crud"  on  a 
disk  (which uses 10 retries) but with noise on  the 
line.   If  the line noise,  or perhaps some  system 
problem,  causes  a reTX in excess of 5 times on the 
same data block,  brother, you have a problem!  Note 
further  that  many more than 5 reTXs'  are  allowed 
provided no more than 5 occur on a given data block.

While  we  seem to have solved  the  data  integrity 
question  on  a data block basis we still need  some 
way of assuring ourselves that each and every  block 
was  received  properly and that some  reTXed  block 
didn't get recorded twice by mistake.   One approach 
is  to include a block or frame count as part of the 
block transfer.   Since the files transferred  might 
be  quite  large,  a  16-bit block  count  might  be 
needed.  Given the 7 data bit limit mentioned above, 
this  would  require an additional 4 characters  per 
block.   I chose a different approach which does not 
add  to the size of the data block.   I  have  found 
that  if  a cumulative total of reTXs' is   kept  by 
both  TX and RX systems,  then the equality of these 
values  virtually  assures the  transfer  was  error 
free.  Thus, the TX systems sends his retry count to 
the  RX  system as a part of the End of TeXt  (@ETX) 
record.   This  record immediately follows the  last 
<data.blk>  record.   If the counts  agree,  the  RX 
system  sends @ACK.   Else,  a @NAK is  sent.   Both 
systems  then  display on their respective  consoles 
that   the   transfer  was  either   successful   or 
unsuccessful along with the total number of reTXs'.

We now have a protocol that looks something like the 
following:

-->     @SOH FILENAMETYP SUM
<--     @ACK
-->     AAAAAAAAAAAAAAAA SUM
<--     @ACK
-->     BBBBBBBBBBBBBBBB SUM
...
...
-->     JJJJJJJJJJJJJJJJ SUM
<--     @NAK                (RETRANSMISSION REQUEST)
-->     JJJJJJJJJJJJJJJJ SUM
<--     @ACK
-->     KKKKKKKKKKKKKKKK SUM
<--     @ACK
...
...
-->     ZZZZZZZZZZZZZZZZ SUM
<--     @ACK
-->     @ETX CNT
<--     @ACK

The "SUM" associated with each data block represents 
the  four ASCII HEX characters associated  with  the 
checksum.   The "CNT" at the end represents a single 
character    value    interpreted   as   a    binary 
retransmission count value.  Thus, it represents the 
count  modulo 128 since the number of data  bits  in 
the protocol is set to 7 data bits.


     VARIABLE BLOCK SIZE AND DATA PARITY CHECK


The  above protocol is about as far as we can go  if 
limited  to  7 data bits and  no  parity.   However, 
since  most  UARTS/USARTS provide for both  software 
control of the number of data bits (5  thru  8)  and 
additional  control  over parity selection (even  or 
odd)  coupled with parity  enable/disable,  valuable 
additions can be made to the protocol.

Lets  first  consider variable block  size.   If  we 
limit the block size to one sector (128  characters) 
then  we  must  access and write the  disk  every  4 
seconds (approx.) at 300 BAUD.   The read/write head 
on most drives unloads within this interval.   Thus, 
the head is being loaded each time a write operation 
is performed.  This takes on the order of 35 Msec or 
about  one character time at 300 BAUD (33.3 Msec per 
character).   In addition, the proper sector must be 
found  - assuming the head is already positioned  at 
the  appropriate track.   Since it takes 166.6  Msec 
for one rotation of the disk,  the average "latency" 
is one half that value; i.e., 83.3 Msec.  Thus, each 
time we write the disk costs us, on average,

          write time = 83.3 + 35 Msec = 118.3 Msec.

This  is  approximately 4 character  times  at  1200 
BAUD.   The  worst case time would be  approximately 
211.6 Msec or approximately 6 character times at 300 
BAUD (includes 10 Msec track stepping time).   These 
times  apply  to the Shugart 800 drive.   The  times 
should  be fairly representative of all floppy  disk 
drives.

Given  the above statistics,  it seems desirable  to 
increase  the  block  size and  thereby  reduce  the 
number of times a disk write operation is performed.  
In arriving at an optimum block size (if one exists) 
we must consider the impact of increased block  size 
on   both  buffer  memory  size  and  time  lost  in 
retransmitting  a larger data block.  I have no firm 
number  in mind but since CP/M allocates disk  space 
in 8 sector blocks,  a value of 1024 = 8 * 128 seems 
a  good  starting point.   This calls for  a  16-bit 
block  size  value which can be sent  as  two  8-bit 
bytes interpreted as binary values rather than ASCII 
characters.   To  be  consistent with  the  checksum 
ordering  the  most significant byte is  transmitted 
first.

The  next  protocol  enhancement  to  be  introduced 
provides for a parity error test.   If a data parity 
error  is found,  there is no need to  continue  the 
block  transfer.    Instead,  the  block  should  be 
immediately retransmitted.  This further facilitates 
the   introduction  of  larger  block   sizes.    To 
accommodate the retransmission request due to parity 
error,  two  additions  to our protocol are  needed.  
First,  we  must add a resync (@SYN) request to  our 
<ack.form>.   In response to the receipt of an  @SYN 
from  the RX device,  the TX device will discontinue 
the block transfer and begin a retransmission of the 
same    block.     Second,    to    assure    proper 
synchronization, each data block should begin with a 
distinguishing character.  I have selected the ASCII  
Record Separator (@RS) for this task.   Thus, if the 
RX device detects an @RS following his  transmission 
of  an  @SYN,  he  knows  the  block  retransmission 
request  has been received by the TX device and that 
this is the beginning of that block.  

Finally,  it  is desirable to be able to identify  a 
block with more or less characters than specified by 
the  block count.   This can be done by inserting  a 
special  character between the end of data  and  the 
beginning  of  the checksum.   I have  selected  the 
ASCII Unit Separator (@US) for this task.   If there 
is such a disagreement,  an @SYN is immediately sent 
by the RX to the TX causing a retransmission.   This 
completes  the protocol specification and leaves  us 
with a typical data block that looks something like,

-->  @RS N XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX @US SUM
<--  @ACK

Where N denotes the block count and,  as before, SUM 
denotes the checksum.

I have given this protocol the name "MCALL-C", which 
stands  for  Micro proto"CALL" - Clear.   The  clear 
means that the data is not encoded,  as is the  case 
for the PCNET protocol.  In PCNET protocol, the data 
is  encoded  in  a radix 41 code  rather  than  pure 
ASCII.   This encoding allows binary information  to 
be  transferred  while  using  only  41  "printable" 
characters to encode the data.






The  complete MCALL-C definition both in BACKUS-NAUR 
form  and  in a more graphic form (section  (3))  is 
shown  next.    The definition is from the point  of 
view of the originator or (TX) system.







        ***********************************

(1) DATA TRANSMITTED
    (@XXX SIGNIFIES AN ASCII CONTROL CHAR)

<FILE>  ::= <F.HDR> <F.TEX>
<F.HDR> ::= @SOH <HEADER> @US <CHKSUM>
<HEADER>::= <8 CHAR FILENAME> <3 CHAR FILETYPE>
<CHKSUM>::= <16 BIT CHECKSUM ENCODED IN ASCII HEX
             MS-NIBBLE FIRST, LS-NIBBLE LAST>
<F.TEX> ::= <TEXT> @ETX <ERRTTL>
<TEXT>  ::= <BLOCK> | <BLOCK> <TEXT>
<BLOCK> ::= @RS <CHRCNT> <STRING> @US <CHKSUM>
<CHRCNT>::= <NUMBER (LESS ONE)  OF CHARACTERS IN
             <STRING>>
<STRING>::=  <PRINTABLE  ASCII CHAR STRING  OF  FILE              
DATA>     
<ERRTTL>::= <TOTAL ERROR COUNT MOD 128>

(2) DATA RECEIVED (HANDSHAKING PROTOCOL)

<ACK.FORM>::= <@ACK> | <@NAK> | <@SYN> | <@CAN>
<@ACK>  ::= @ACK       (SUCCESSFUL TRANSFER OF DATA)
<@NAK>  ::= @NAK       (RETRANSMISSION REQUEST)
<@SYN>  ::= @SYN       (RESYNC REQUEST)
<@CAN>  ::= @CAN       (ABORT TRANSMISSION)

<HDR.ACK>::= <F.HDR> <ACK.FORM>
<BLK.ACK>::= <BLOCK> <ACK.FORM>
<EOF.ACK>::= @ETX <ERRTTL> <ACK.FORM>
              (FILE CLOSED ACK)

(3) SAMPLE FILE TRANSMISSION

-->     @SOH FILENAMETYP @US SUM    (HEADER BLOCK)
<--     @ACK
-->     @RS N AAAAA...AAAAA @US SUM (FIRST DATA
                                     BLOCK)
<--     @ACK
-->     @RS N BBBBB...BBBBB @US SUM (SECOND DATA
                                     BLOCK)
<--     @ACK
.....
.....
.....
-->     @RS N VVVVV...VVVVV @US SUM
<--     @NAK                        (RETRANSMISSION
                                     REQ)
-->     @RS N VVVVV...VVVVV @US SUM
<--     @ACK
.....
.....
.....
-->     @RS N YYYYY...YYYYY @US SUM
<--     @ACK
-->     @RS N ZZZZZ...ZZZZZ @US SUM
<--     @ACK
-->     @ETX M                      (END OF FILE)
<--     @ACK

        ***********************************

Having specified the protocol,  we must now  resolve 
the  problem  presented  by the existence  of  UARTS 
whose  number of data bits is limited to  seven  and 
whose  operation does not support parity  generation 
and testing.  The best approach might be to have two 
similar but different protocols.  One to accommodate 
the  TMS5501 and another to take advantage of the  8 
data bits plus parity.   Lets call the 7-bit version 
MCALL-C  and the 8-bit version,  MCALL-BC.   The "B" 
related  to  the  Big  data  block  size.   The  two 
protocols are identical except in the way the  block 
size and the checksum are represented and the use of 
parity  testing  in  one but   not  the  other.   By 
limiting  the differences to these three parameters, 
both  protocols  can  be accommodated  by  the  same 
program.   A  "flag"  could be set  in  response  to 
operator  input to specify which processing path was 
selected.  

For  MCALL-C  we  define  the  block  size  and  the 
checksum as follows:

<CHARCNT> ::= <NUMBER (LESS ONE) OF CHARACTERS IN
               <STRING> IN THE RANGE 0 TO 127>
<CHKSUM>  ::= <16-BIT CHECKSUM ENCODED IN ASCII HEX 
               WITH MS-NIBBLE FIRST>

For  MCALL-BC  we  define these  two  parameters  as 
follows:

<CHARCNT> ::= <NUMBER (LESS ONE) OF CHARACTERS IN 
               <STRING> IN THE RANGE 0 TO 65535 WITH
               MS-BYTE FIRST>
<CHKSUM>  ::= <16 BIT CHECKSUM WITH MS-BYTE FIRST>

As  to  the effectiveness of the  protocol,  I  have 
implemented  the  MCALL-C  protocol  as  part  of  a 
program I have written called "MCALL".   The program 
fixes the UART data format at 7 data bits with  even 
parity,   although   no  parity  test  is  currently 
performed.   This  protocol  has been  tested  on  a 
variety of I/O cards for  the S-100 BUS and includes 
the  Cromemco  TU-ART.   I  find the  protocol  very 
effective  in file transfers and have never  had  an 
unsuccessful  transfer  under normal  circumstances.  
By  normal I mean under both good and  foul  weather 
conditions  with total reTX counts ranging up to  10 
or  more  per message.   I generally get  error-free 
performance even when I tap on the telephone handset 
with  a  pencil to  introduce  noise.  Occasionally, 
however, using the "bang approach" I have caused the 
system  to  "bomb" or record the same  block  twice.  
However,  the operator is alerted to the latter case 
via  an "unsuccessful file transfer" message at  the 
end.   This  is where the comparison of reTX  counts 
pays off.

The current version of MCALL supports only  MCALL-C.  
I  hope  to add MCALL-BC in the future,  along  with 
other protocols and program  enhancements.   Further 
information  relating  to MCALL can be  obtained  by 
contacting:


               MICRO-CALL SERVICES
               9655-M Homestead Court
               Laurel, MD  20810
               (301) 776-5253