Extended Bios Function Calls (28_Feb_84)

	Copyright 1984
	Morrow Designs, Inc.
	San Leandro, Ca.


Function Summary
----------------

Func0	Read from System Memory

Func1	Write to system memory

Func2	Read ramdaty and Apif

Func3	Read system mtabs

Func4	Read drvtbl and all DPH

Func5	Read dpb_table and all DPB

Func6	Read character table

Func7	Read virtual drive message

Func8	Read free space

Func9	Format a Track

Func10	Initialize the CTC

Func11	Inject Ims Sting into the Free Space

Func12	Enable/Disable centronics interrupts

Func13	Enable/Disable disk [read after write] / [read before write]

Func14	Execute in system bank

Func15	Verify track, destructive

Func16	Verify track, non-destructive

Func17	Modify contents of CFlag with the E register

Func18	Read the Rom ID Block

.paŠFunction Description:



Func0 - Read from System Memory
-------------------------------
	DE -> Destination (in the tpa)
	HL -> Source (in the system bank)
	BC -> Number of bytes to move


Func1 - Write to system memory
------------------------------
	DE -> Destination (in the system bank)
	HL -> Source (in the tpa)
	BC -> Number of bytes to move


Func2 - Read ramdaty and APIF
-----------------------------
	DE -> Destination (in the tpa)


Func3 - Read system mtabs
-------------------------
	DE-> Destination (in the tpa)


Func4 - Read drvtbl and all DPH
-------------------------------
	DE -> Destination (in the tpa)


Func5 - Read dpb_table and all DPB
----------------------------------
	DE -> Destination (in the tpa)


Func6 - Read character table
----------------------------
	DE -> Destination (in the tpa)


Func7 - Read virtual drive message
----------------------------------
	DE -> Destination (in the tpa)


Func8 - Read Free space
-----------------------
	DE -> Destination (in the tpa)

.paŠFunc9 - Format a Track
----------------------
	DE -> Pointer to an MTab
	IX -> Pointer to user APIF Area followed by a sector
	      table with the sectors in reverse order.


Func10 - Initialize the CTC
---------------------------
	---- No Arguments


Func11 - Inject Ims Sting into the Free Space
---------------------------------------------
	DE -> Pointer to Ims String (first byte of the string is its length).


Func12 - Enable/Disable centronics interrupts
---------------------------------------------
	E  -> Switch (0=disable)


Func13 - Enable/Disable disk [read after write] / [read before write]
---------------------------------------------------------------------
	E  -> Switch	Read after Write  - 0=disable, 1=enable
			Read before Write - 0=disable, 2=enable


Func14 - execute in system bank
-------------------------------
	HL -> Execution Address (in system bank)


Func15 - Verify track, destructive
----------------------------------


Func16 - Verify track, non-destructive
--------------------------------------


Func17 - Modify contents of CFlag with the E register
-----------------------------------------------------
	E -> New value of CFlag
	D -> Old Contents of CFlag


Func18	Read the Rom ID Block
-----------------------------
	DE -> Destination (in the tpa)


.paŠSample Access Routine (28_Feb_84)

	A large number of the extended bios routines (0, 2 through 8 and 18)
move data structures from the system bank to the tpa bank. Typically, these
structures are moved into the tpa for modification and then put back into the
system bank. The following three routines can greatly simplify this task.

;----------------------------------------------------------------------
; GETBUF - Move system memory into the local buffer (4_Jan_84)
;-------------------------------------------------------------
;	1) This routine forces the destination to be the local buffer, calls
;	   the cold start (extended bios functions) entry point, and then saves
;	   the registers after swapping hl and de.
;	2) Enter with Accm equal to the extended bios function desired
;
GetBuf:	ld	de,LocBuf	;DE:= Pointer to Local Buffer
	call	DoCold		;Move System Memory into the local buffer

	ld	(saveBC),bc	;Save the returned registers
	ex	de,hl		;HL:= Pointer to first xlt
	ld	(saveDE),de
	ld	(saveHL),hl
	ret			;Return

;----------------------------------------------------------------------
; PUTBUF - Put the Local Buffer into System Memory (4_Jan_84)
;------------------------------------------------------------
;	1) This is the inverse of GetBuf; It replaces the system's memory
;	   with the contents of the local buffer.
;	2) GetBuf MUST be called before entering this routine.
;
PutBuf:	ld	a,1		;Function_1:= Write to system memory
	ld	bc,(SaveBC)
	ld	de,(SaveDE)
	ld	hl,(SaveHL)	;Restore the Returned Registers
	call	DoCold		;Write the Mtabs back into system memory
	ret

;----------------------------------------------------------------------
; DOCOLD - Call the Bios Cold Boot Entry Point (4_Jan_84)
;--------------------------------------------------------
;	1) The Cold Boot Entry point to the bios (1st entry in the bios
;	   jump table) is located by looking at locations 1 & 2 which
;	   point to the warm boot address (the desired address + 3).
;
DoCold:	push	hl		;Save the HL Register Pair
	ld	hl,(1)		;HL:= Warm Boot Address
	ld	l,0		;HL:= Cold Boot Address
	ex	(sp),hl		;Restore the HL Register Pair
	ret			;Goto The Cold Boot entry

SaveBC:	dw	0		;Save location for the BC register pair
SaveDE:	dw	0		; "      "      "   "  DE    "      "
SaveHL:	dw	0		; "      "      "   "  HL    "      "
LocBuf:	ds	100h,0		;Local BufferŠ