Subject:   Project status report

From:     Bob Groppo

Date:     Sept. 20, 1982


                    PROJECTS COMPLETED

 New tech test     				
  a) This test is for placement of technicians and is currently
     in use

 CMI M10 and M16 Review
  a) written review is available

 MOS customer service rackmount [Grayco]
  a) MOS 1.4 fixed problem (system still not returned to
     Grayco for reasons I don't understand)

 MOS customer service table tops (Compumetrics)
   a) written report is available

 Decision 1 line filter 
   a) Corcom 3EP1 spec'd - this requires new wiring of cabinet
      and retesting to FCC specs
 
 MOS 1.4 for marketing on M16
 
 MOS Masters and update
   a) intergrated into production

 CMI Restore under MOS 
   a) Load constants resets the STEP line 
 
MPZ80 EPROMs for CMI M16 Drives (fix bugs)
   a) restore FFFFh tracks
   b) Load Constants includes step reset
   c) Image map matches actual map when in monitor
   d) Monitor now enables the EN INT bit on Mult I/O

 Advanced Micro Digital switch settings 
   a) preliminary release as Apnote 3


 Universal cooling
   a) appears to require a minimum of 90 CFM given
      a 10 degree rasie from ambient and 300 watt power
      disappation

 8" HDC/DMA conversion kits
   a) PLL adjustment for the HDC/DMA manual appendix
   b) preliminary documentation available (needs artwork)
 
.paŠMULTI/O clock problem
   a) MOS 1.4 solved this problem with the Mult I/O although
      a hardware reason for why the fix works is not apparent.
      My suspicions are the 2 volt supply we apply to the CMOS
      clock.

 Cablinç / Jumperinç Decision systemó foò standaòd printeró  
    a) prelimnary release as apnote 5

 6 Meg HDCA 
    a) the state machine needs work to support this-
       merely swapping clocks does not work reliably.

 Change rt3@mult and ramtest 3 
    a) will be on the new test diskettes (E.3)
      (input 03 changed to a NOP in the beginning)
 
 C Itoh evaluation
    a) written report available
   
 Miniscribe buffered seek evaluation 
    a) written report available

 Qume 8" drive evaluation
    a) written report will soon be available
    b) one 8 inch full size consistantly ate diskettes
    c) slimline 8 inch ate one Dysan diskette and no other
       diskettes yet although still under test

 HDCA Bad spot mapping
    a) verified new BAD program functional
    b) errors reported from vendors need to be documented yet
       in the appropriate manuals
.paŠ               PROJECTS STILL IN PROGRESS

 E.3 Review 
   (awaiting new release from software )

 MPZ80 Rev 3 CPU 
  a) awaiting 82S153 parts from SIG (equations completed)
  b) substantial artwork changes to fix current bugs
     NMI, ERROR, pSYNC driver etc.
  c) new clock circuitry (possibly Zilog)
  d) 8 Mhz spec coming from Zilog

 Big switcher
  a) preliminary tests - first switcher smoked
     but am now awaiting new supplies with newer specs

 FCC - Tests Required
  a) Micro Decision System checkout with various serial cables
  b) Decision 1 checkout with new filter and serial cables

 256K RAM board 
  a) first 4 boards assembled - waiting for correct delay lines
     these boards will need debugging and checkout/burnin
  b) trace cuts and jumpers need documentation
  c) evaluate RAM chips (packages and speeds)
     qualified so far: T.I., Hitatchi and Mitsubishi
  d) parity option checkout
  e) documentation


 G & G Engineering
  a) Visit location to find what their problems are
     with the HD/DMA systems and HDCA systems

 Centronics to daisy converter
  a) Software drivers are specified
  b) Board pinout is established and will be protoyped
     when parts become available
  c) awaiting connectors from T & B Ansley
  d) provided above is acceptable, layout the board

 Change uDecision seek test for random read/write
  a) all done except for an assembly language random routine

 220V Micro Decision Supply
  a) Stancor stepdown transformer
     1) Mounting documentation
     2) electrical connection documentation
     3) European plug issue needs resolution

 Tech training sessions (course outline & materials)
   a) preliminary outline for MPZ80 and HDC/DMA completed
.paŠ








               PROJECTS NOT IN PROGRESS





 Motherboard tests (MPZ80 EPROM)
    a) Current EPROM needs to check interrupts, daisy port and 
       clock

 PAL and EPROM programming solutions for production
    a) parts need to be programmed without master proms
       (ideally through an automated proceedure using a
       computer and serial port to down load from diskette)

 Morrow Transformer specs
    a) all power transformers and supplies need
       checking / specs / schematics

 MULT I/O Battery Backup

 Ken's printer  -jumpered for 9600 baud operation

 DJ/DMA Test procedures checkout

 MOS does not stop on I/O errors during inits

 MOS UPM erase problem 
   a) this happens after erasing 13 files from UPM

 MOS Drive validation
   a) needs to use the badmap from FORMATMW

 Production board testing
   a) testing multiple boards with one bus
      1) requires roms pals and proms
   b) complete test documentation
      1) disk tests
      2) memory tests
      3) interrupt tests

.paŠ         PROJECTS  BEGINNING WITHIN NEXT TWO WEEKS

 Qume 5" drive evaluation
    Scheduled test of 20 slimline double sided
    Scheduled long term test of 2 evaluation units

 Cartridge disk evaluation
    Extensive checkout of 5 inch 5 meg removable media
    
 Miniscribe 1006 evaluation
    Extensive checkout of two drives (fire sale)

.paŠ            ONGOING DOCUMENTATION PROJECTS

All Manuals 
   Theory of operations for each board (2 weeks per manual)
 
Manuals needing technical update:
   HDCA Rev 4 (disk format and error description)
   HD/DMA     (Load constants, interrupts  and drive select
               PLL adjustments in appendix)
   DJ/DMA     (technical input, PLL check in appendix)
   DJ2D/B     (re-write)
   I/O        (rewrite with I/O charts)
   256K Memory (manual to be written, technical input)
   DISCUS Installation

Applications Notes
     Release of Ap notes 2 - 5

Miscellaneous Documentation
    Board Parts lists (substitution list)
    Written test proceedures for production
    Bipolar Prom cross reference chart