Morrow Mt-70 Terminal Firmware Documentation (20_Dec_84)

	Copyright 1984
	Morrow Designs, Inc.
	San Leandro, Ca.


General:

	The Morrow Mt-70 terminal consists of a video display unit and a
detachable keyboard interconnected by a coiled cord. Both the VDU and the
keyboard have their own processors.

	The processor in the keyboard (an 8048) takes care of scanning,
debouncing and encoding key presses. The keyboard also processes commands from
the VDU. These commands include turning on and off key clicks, caps lock, auto
repeat and keyboard application mode. The keyboard can also be commanded to
send its ID code. All information to and from the keyboard flows serially
through the interconnecting coiled cord by way of a special protocol.
	The 8048 processor in the keyboard uses its own internal ram. Program
code is carried in a 2732 rom. The keyboard uses NO interrupts.

	The VDU is responsible for taking characters from the keyboard and
sending them to the host system; Additionally, the VDU is responsible for
taking characters from the host system. Characters from the host system can
be displayed, can be sent to the keyboard (eg turn on/off key clicks) or can
be used to control the display (eq Erase the current line).
	Characters from the keyboard are initially placed in a small circular
buffer in page zero. Then they are translated (if necessary) and placed in
another, larger (1 page), circular buffer. From this second buffer they are
sent to the host.
	Characters from the host system are fed into a large (1k) buffer. From
this buffer they are routed to the display, to the keyboard, or to the display
control routines (Control Character Processing or Escape Sequence Processing).
	The 6512 processor in the VDU has 2k available for general purpose ram
and 2k each for the character and attribute rams. Program code for the VDU is
kept in a 2732 rom.
.pa

; Terminal Escape Character Sequences (20_Dec_84)
;------------------------------------------------

20         ---				30  0      Alignment Check
21  ! @-P  Print Graphics Char		31  1      ---
22  " 0-7  Set Cursor Type		32  2      ---
23  #      Display Version		33  3      ---
24  $      Set Graphics Mode		34  4      ---
25  %      Clear Graphics Mode		35  5      ---
26  &      ---				36  6      Dump Current Line to Host
27  '      ---				37  7      ---

28  (      Set Dim			38  8      ---
29  )      Set Bright			39  9      ---
2A  *      Clear Screen			3A  :      ---
2B  +      Clear Screen			3B  ;      ---
2C  ,      ---				3C  <      ---
2D  -      ---				3D  = x y  Set Cursor
2E  .      ---				3E  >      ---
2F  /      ---				3F  ?      Read Cursor


40  @ 0-1  Disable/Enable Screen Saver	50  P      ---
41  A      ---				51  Q      Insert Character
42  B      ---				52  R      Delete Line
43  C      ---				53  S      ---
44  D      ---				54  T      Erase to End of Line
45  E      Insert Line			55  U      Set Monitor Mode
46  F      ---				56  V      ---
47  G 0-7  Set Attribute		57  W      Delete Character

48  H      ---				58  X      Clear Monitor Mode
49  I      Back Tab			59  Y      Erase to End of Screen
4A  J 0-1  Disable/Enable Keyclick	5A  Z      ---
4B  K 0-1  Normal/Inverse Screen	5B  [      Set Applications Keypad
4C  L      ---				5C  \      ---
4D  M      ---				5D  ]      Clear Applications Keypad
4E  N      ---				5E  ^      ---
4F  O      ---				5F  _      ---
.pa

; Terminal Control Character Functions (7_Nov_84)
;------------------------------------------------

00  @      ---				10  P      ---
01  A      ---				11  Q      ---
02  B      ---				12  R      ---
03  C      ---				13  S      ---
04  D      ---				14  T      ---
05  E      ---				15  U      ---
06  F      ---				16  V      ---
07  G      Bell				17  W      ---

08  H      Cursor Left (BackSpace)	18  X      ---
09  I      Tab				19  Y      ---
0A  J      Cursor Down (Line Feed)	1A  Z      Clear Screen & Home Cursor
0B  K      Cursor Up			1B  [      Escape
0C  L      Cursor Right			1C  \      ---
0D  M      Carriage Return		1D  ]      ---
0E  N      ---				1E  ^      Home Cursor
0F  O      ---				1F  _      Carriage Return Line Feed


; Character Set Translations
;---------------------------

0 - U.S.
1 - U.K.
2 - French
3 - German
4 - Spanish
5 - Danish/Norwegian
6 - Finnish/Swedish
7 - Italian