To install MITE on the Sanyo 1000 with SMARTMODEM

   1. Set switches inside SMARTMODEM front panel as follows:

	1 - down (unless no parameter changes are expected)
	2 - up
	3 - down
	4 - up
	5 - up (if auto answer desired)
	6 - up
	7 - up (if normal residential phone line)
	8 - doesn't matter

   2. Build RS-232 cable as follows:

	2 ----- 2
	3 ----- 3
	4 ----- 4
	5 ----- 5
	6 ----- 8	NOTE: lines 6 and 8 are flipped
	7 ----- 7
	8 ----- 6
       20 ----- 20

   3. Connect either end to SMARTMODEM, other end to Sanyo

   4. Set baud rate to 1200, as described in Sanyo manual.
      MITE will select between 300 and 1200 under software
      control. Help from a technician may be required to
      perform this step.

   5. Copy MITE/S.COM to your own diskette, to avoid accidental
      loss of the master copy.

   6. Read through entire MITE manual. If possible have a copy
      of MITE running on a system in front of you.	

   7. Your macro string index characters have been installed as
      the characters 0 through 9, respectively.

   8. Note that the DTR auto-hangup feature causes problems with
      dynamically changing parameters, as the 8251 drops DTR every
      time you go to change certain of the parameters. If you do
      not plan to change things once you are logged in (and do not
      plan to transfer binary data files, which automatically does
      parameters changes), then switch 1 can be left UP, which will 
      allow DTR controlled hangup to work. In any case, you can
      always make the Smartmodem hangup by typing three plusses
      followed by the command AT H0 (see Smartmodem manual). NOTE:
      Switch 1 must be UP for BYE.COM to function normally (which
      includes binary file transfers with XMODEM).