TASM USER'S MANUAL


      TASM - A Table Driven Cross Assembler for the MSDOS* Environment





                           Thomas N. Anderson
                     Speech Technology Incorporated
                837 Front Street South, Issaquah, WA   98027


                             March, 1992
                             Version 2.9

[Speech Technology Incorporated  manufactures electronic devices  to aid  the
visually impaired employing digital speech synthesis technology.]


TASM software is Copyright (C)  1985-1992 by Speech Technology  Incorporated.
All rights reserved.

This document is Copyright (C)  1985-1992 by Speech Technology  Incorporated.
All rights reserved.  Permission is granted to copy this document and related
software except  for  the source  code.    The source  code,  distributed  to
registered users, may be copied for the sole use of the registered user.




 * MSDOS is a trademark of Microsoft Corporation.


TASM - Table Driven Assembler Version 2.9                              Page 2

TABLE OF CONTENTS

SECTION                                             PAGE
______________________________________________________________________
INTRODUCTION                                           4
INVOCATION                                             5
 File Names                                            5
 Option: a - Assembly Control                          6
 Option: b - Binary Object Format                      7
 Option: c - Contiguous Block Output                   7
 Option: d - Define a Macro                            7
 Option: e - Expand Source                             7
 Option: f - Fill Memory                               7
 Option: g - Object File Format                        7
 Option: h - Hex Object Code Table                     7
 Option: i - Ignore Case in Labels                     8
 Option: l - Label Table                               8
 Option: m - MOS Technology Object Format              8
 Option: o - Set Number of Bytes per Object Record     8
 Option: p - Page Listing File                         8
 Option: q - Disable Listing File                      8
 Option: r - Set Read Buffer Size                      8
 Option: s - Enable Symbol File Generation             9
 Option: t - Table Name                                9
 Option: x - Enable Extended Instruction Set          10
 Option: y - Enable Assembly Timing                   10
ENVIRONMENT VARIABLES                                 11
 TASMTABS                                             11
 TASMOPTS                                             11
EXIT CODES                                            11
SOURCE FILE FORMAT                                    12
EXPRESSIONS                                           13
 Labels                                               13
 Numeric Constants                                    13
 Character Constants                                  14
 String Constants                                     14
 Location Counter Symbol                              14
 Operators                                            15
ASSEMBLER DIRECTIVES                                  17
 ADDINSTR                                             17
 AVSYM                                                17
 BLOCK                                                17
 BSEG/CSEG/DSEG/NSEG/XSEG                             17
 BYTE                                                 17
 CHK                                                  18
 CODES/NOCODES                                        18
 DB                                                   18
 DW                                                   18
 DEFINE                                               18
 DEFCONT                                              19
 EJECT                                                19
 ELSE                                                 20
 END                                                  20
 ENDIF                                                20
 EQU                                                  20
 EXPORT                                               21

TASM - Table Driven Assembler Version 2.9                              Page 3

 IFDEF                                                21
 IFNDEF                                               21
 IF                                                   22
 INCLUDE                                              22
 LIST/NOLIST                                          22
 LOCALLABELCHAR                                       22
 LSFIRST/MSFIRST                                      22
 ORG                                                  22
 PAGE/NOPAGE                                          23
 SET                                                  23
 SYM/AVSYM                                            23
 TEXT                                                 24
 TITLE                                                25
 WORD                                                 26
OBJECT FILE FORMATS                                   27
 Intel Hex Object Format                              27
 MOS Technology Hex Object Format                     28
 Motorola Hex Object Format                           28
 Binary Object Format                                 28
LISTING FILE FORMAT                                   30
PROM PROGRAMMING                                      31
ERROR MESSAGES                                        32
BUGS AND LIMITATIONS                                  35

APPENDIX A - ORDERING INFORMATION                     36

TASM - Table Driven Assembler Version 2.9                              Page 4

INTRODUCTION


TASM is a table driven cross assembler for the MS-DOS environment.   Assembly
source code, written in the appropriate dialect (generally very close to  the
manufacturers assembly  language),  can  be  assembled  with  TASM,  and  the
resulting object code  transferred to  the target  microprocessor system  via
PROM or other mechanisms.

The current microprocessor families supported by TASM are:

        6502                       8048
        6800/6801/68HC11           8051
        6805                       8080/8085
        TMS32010/TMS320C25         Z80
        TMS7000

The user  so  inclined  may  build  tables  for  other  microprocessors.  The
descriptions of the various existing tables and instructions on building  new
tables are not in this document but can be found in the TASMTABS.DOC file  on
the TASM distribution disk.

TASM characteristics include:

  1.  Powerful expression parsing (17 operators).
  2.  Supports a subset of the 'C' preprocessor commands.
  3.  Macro capability (through use of DEFINE directive).
  4.  Multiple statements per line.
  5.  Four object file formats:
          Intel hex, MOS Technology hex, Motorola hex, binary.
  6.  Absolute code generation only.
  7.  Source code available (in C).
  8.  Uniform syntax  across  versions  for  different  target machines.
  9.  Features in support of PROM programming (preset memory,
          contiguous block).
  10. Supports extended instructions for many of the supported
          microprocessor families.
  11. Tables read at run time; single TASM executable for all table versions.
  12. Symbol table export for inclusion in subsequent assemblies.
  13. Symbol table export file compatible with the Avocet 8051
          simulator (.SYM format).

SHAREWARE

TASM is distributed  as shareware.    TASM is  not public domain.   The  TASM
distribution files may be freely copied (excluding the source code files) and
freely used for the purpose of evaluating the suitability of TASM for a given
purpose.   Use  of  TASM  beyond  a  reasonable  evaluation  period  requires
registration.   Prolonged use without registration is unethical.


TASM - Table Driven Assembler Version 2.9                              Page 5

INVOCATION

TASM can be invoked as follows  (optional fields shown in brackets,  symbolic
fields in italics):

    tasm -pn [-option_flag ...] src_file
                           [obj_file [lst_file [exp_file [sym_file]]]]

    Where  option_flag can be one or more of the following:

        -table        Specify version (table = table designation)
        -ttable       Table (alternate form of above)
        -aamask       Assembly control (optional error checking)
        -b            Produce object in binary (.COM) format
        -c            Object file written as a contiguous block
        -dmacro       Define a macro (or just a macro label)
        -e            Show source lines after macro expansion
        -ffillbyte    Fill entire memory space with fillbyte (hex)
        -gobjtype     Object file (0=Intel, 1=MOS Tech, 2=Motorola, 3=binary)
        -h            Produce hex table of the assembled code (in list file)
        -i            Ignore case for labels
        -l[al]        Produce a label table in the listing
        -m            Produce object in MOS Technology format
        -oobytes      Bytes per object record (for hex obj formats)
        -p[lines]     Page the listing file (lines per page. default=60)
        -q            Quiet, disable the listing file
        -rkb          Set read buffer size in Kbytes (default 2 Kbytes)
        -s            Write a symbol table file
        -x[xmask]     Enable extended instruction set (if any)
        -y            Time the assembly

The file parameters are defined as follows:

src_file  Source file name
obj_file  Object code file name
lst_file  Listing file name
exp_file  Symbol export file (only if the EXPORT directive is used).
sym_file  Symbol table file
              (only if the "-s" option or the SYM/AVSYM directives are used).

The source  file  must be  specified.   If  not,  some usage  information  is
displayed.  Default file names for all the other files are generated if  they
are not explicitly  provided.  The  filename is formed  by taking the  source
filename and changing the extension to one of the following:

Extension           File type
________________________________________________________
.OBJ                Object file
.LST                Listing file
.EXP                Symbol export file
.SYM                Symbol table  file

TASM has  no built-in  instruction set  tables.   Instruction set  definition
files are read at run time.  TASM determines which table to use based on  the
'-table' field shown  above.  For  example, to  assemble the code  in a  file
called source.asm, one would enter:

TASM - Table Driven Assembler Version 2.9                              Page 6

        tasm -48   source.asm            for an 8048 assembly
        tasm -65   source.asm            for a  6502 assembly
        tasm -51   source.asm            for an 8051 assembly.
        tasm -85   source.asm            for an 8085 assembly.
        tasm -80   source.asm            for a  Z80  assembly.
        tasm -05   source.asm            for a  6805 assembly.
        tasm -68   source.asm            for a  6800/6801/68HC11 assembly.
        tasm -70   source.asm            for a  TMS7000  assembly.
        tasm -3210 source.asm            for a  TMS32010 assembly.
        tasm -3225 source.asm            for a  TMS320C25 assembly.

The file name that the  tables are read from is  formed by taking the  digits
specified after the '-' and appending it to 'TASM' then appending the  '.TAB'
extension.  Thus, the '-48' flag would cause  the tables to be read from  the
file 'TASM48.TAB'.

It is possible to designate  tables by non numeric  part numbers if the  '-t'
flag is used.  For  example, if a user built  a table called TASMF8.TAB  then
TASM could be invoked as follows:

        tasm -tf8 source.asm

Each option flag must be  preceded by a dash.   Options need not precede  the
file names, however.  The various options are described below:

a  -  Assembly  Control.  TASM  can  provide  additional  error  checking  by
specifying the '-a' option at the time of execution.  If the '-a' is provided
without a digit following, then all the available error checking is done.  If
a digit follows, then it is used as  a mask to determine the error checks  to
be made.  The bits of the mask are defined as follows:

Bit    Option Flag   Description
___________________________________________________________________________
0      -a1           Check for apparent illegal use of indirection
1      -a2           Check for unused data in the arguments
2      -a4           Check for duplicate labels
3      -a8           Check for non-unary operators at start of expression.
4      -a10          Check for 8051 AJMP/ACALL branches off current 2K page.

Combinations of the above bits  can also be used.   For example, '-a5'  would
enable the checking for illegal indirection and duplicate labels.

Illegal indirection applies to micros that use parenthesis around an argument
to indicate indirection.  Since  it is always legal to  put an extra pair  of
parenthesis around  any  expression  (as  far as  the  expression  parser  is
concerned), the user may think that  he/she is indicating indirection for  an
instruction that has no  indirection and TASM would  not complain.   Enabling
this checking will  result in an  error message (warning)  whenever an  outer
pair of parenthesis is used and the instruction set definition table does not
explicitly indicate that to be a valid form of addressing.

Unused data in  arguments applies to  cases where  a single byte  of data  is
needed from an  argument, but  the argument contains  more than  one byte  of
data.  If  a full  sixteen bit address  is used  in a  'Load Immediate'  type
instruction that needs  only a  single byte,  for example,  an error  message
would be generated.  Here is an example (6502 code):

TASM - Table Driven Assembler Version 2.9                              Page 7

0001   1234                    .org $1234
tasm: Unused data in MS byte of argument.  Line 0002 in test.asm
0002   1234 A9 34       start  lda  #start

To make the above checks occur whenever  you do an assembly, add a line  like
this to your AUTOEXEC.BAT file:

        SET TASMOPTS=-a

b  -  Binary Object Format. This option causes the object file to be  written
in binary  - one  byte for  each byte  of code/data.   Note  that no  address
information is included in  the object file in  this format.  The  contiguous
block (-c) output mode is forced when  this option is invoked.  This flag  is
equivalent to '-g3'.

c - Contiguous Block Output. If this  option is specified, then all bytes  in
the range from the  lowest used byte  to the highest will  be defined in  the
object file.  Normally, with the default Intel Hex object format enabled,  if
the Program Counter  (PC) jumps  forward because  of an  .ORG directive,  the
bytes skipped over will not have any value assigned them in the object  file.
With this option enabled, no output to  the object file occurs until the  end
of the assembly at  which time the whole  block is written.   This is  useful
when using TASM to  generate code that will  be put into a  PROM so that  all
locations will have a known value.  This option is often used in  conjunction
with the -f option to ensure all unused bytes will have a known value.

d - Define  a Macro.  Macros are  defined on  the command  line generally  to
control the assembly of various IFDEF's that are  in the source  file.   This
is a convenient way to generate various versions of object code from a single
source file.

e - Expand Source. Normally TASM shows lines in the listing file just as they
are in the source file.  If macros  are in use (via the DEFINE directive)  it
is sometimes desirable to see the source lines after expansion.  Use the '-e'
flag to accomplish this.

f   -   Fill   Memory.   This   option   causes the  memory image  that  TASM
maintains to be initialized to the value specified by the two hex  characters
immediately following the 'f'.  TASM maintains a memory image that is a  full
64K bytes in size (even if the  target processor cannot  utilize that  memory
space).  Invocation of this option introduces a delay at start up of up to  2
seconds (time required to initialize all 64K bytes).

g -  Object File  Format. TASM  can generate  object code  in four  different
formats as indicated below:

        -g0    for Intel hex (default)
        -g1    for MOS Technology hex (same as -m)
        -g2    for Motorola hex
        -g3    for binary (same as -b)

The '-m' and '-b' flags may also be used, as indicated above.

See the section on OBJECT FILE FORMATS for descriptions of each of the above.



TASM - Table Driven Assembler Version 2.9                              Page 8

h - Hex Object  Code Table. This option  causes a hex  table of the  produced
object code to  appear in the  listing file.   Each line of  the table  shows
sixteen bytes of code.


i - Ignore Case in Labels.  TASM is normally case sensitive when dealing with
labels.  For  those that  prefer case  insensitivity, the  '-i' command  line
option can be employed.

l - Label Table.  This option causes  a label table to appear in the  listing
file.  Each  label is shown  with its corresponding  value. Macro labels  (as
established via the DEFINE directives) do not appear.

Two optional suffixes may follow the '-l' option:

        Suffix          Description
        _______________________________________________
        l               Use long form listing
        a               Show all labels (including local labels)

The suffix should immediately follow the '-l'.  Here are some examples:

        -l      to show non-local labels in the short form
        -la     to show all labels in the short form
        -ll     to show non-local labels in the long form
        -lal    to show all labels in the long form


m - MOS Technology Object  Format. This option causes  the object file to  be
written in  MOS Technology  hex  format rather  than  the default  Intel  hex
format.  See section on OBJECT FILE FORMATS for a description of the format.

o - Set Number of Bytes per Object Record.  When  generating  object code  in
either the MOS Technology format  or the Intel hex format,   a default of  24
(decimal) bytes of object are defined on each  record. This can be altered by
invoking the '-o' option  immediately followed by   two  hex digits  defining
the number of bytes per record desired. For example,  if 32 bytes per  record
are desired,  one might  invoke TASM as:

        TASM -48 -o20 source.asm

p - Page Listing  File. This option  causes the listing file  to have top  of
page headers and form  feeds inserted at  appropriate intervals (every  sixty
lines of output).  To override the default of sixty lines per page,  indicate
the desired number of lines per page as a decimal number immediatly following
the '-p'.  Here is an example:

        TASM -48 -p56 source.asm

q - Disable Listing File.  This option causes all output to the listing  file
to be  suppressed, unless a .LIST directive is encountered in the source file
(see LIST/NOLIST directives).

r - Set Read Buffer Size. This option overrides the default read buffer  size
of 2 Kbytes.  The first hexadecimal digit immediately after the 'r' is  taken
as the  number of  K  bytes to  allocate for  the  read buffer  (.e.g.  '-r8'

TASM - Table Driven Assembler Version 2.9                              Page 9

indicates an 8K byte buffer, '-rf' indicates  a 15K byte buffer).  Note  that
that read buffers are  taken from the  same memory pool  as labels and  macro
storage, and that additional read buffers are needed if "includes" are  used.
Thus, using 8K byte buffers may be suitable for most assemblies, but programs
with large numbers of symbols may not allow such a value.  Also, reducing the
buffer size  to 1  Kbyte can  increase the  memory pool  available for  label
storage, if such is needed.

s - Enable Symbol File Generation.    If this flag  is set, a symbol file  is
generated at the end of the assembly.  The format of the file is one line per
label, each label starts in the first  column and is followed by white  space
and then four hexadecimal digits representing the  value of the label.    The
following illustrates the format:

        label1         FFFE
        label2         FFFF
        label3         1000

The symbol  file name  can be  provided as  the fifth  file name  on the  the
command line, or the name will be generated from the source file name with  a
'.SYM' extension.  The symbol table file  can also be  generated by  invoking
the SYM directive.  The AVSYM directive also generates the symbol file but in
a different format (see section on ASSEMBLER DIRECTIVES).

t - Table Name.  As an alternative to specifying the instruction set table as
two decimal digits, the table indication may be preceeded by the '-t' option.
This is useful if the desired table name starts with a non-numeric.  Thus,  a
table for an F8 might be selected as:

        TASM -tf8 source.asm

TASM would expect to read the  instruction set definition tables from a  file
named TASMF8.TAB.

TASM - Table Driven Assembler Version 2.9                             Page 10


x - Enable Extended Instruction Set.  If a processor family has  instructions
that are valid for only  certain members, this option  can be used to  enable
those beyond the basic standard instruction set.  A hex digit may follow  the
'x' to indicate a  mask value used in  selecting the appropriate  instruction
set.  Bit 0 of the mask selects the basic instruction set, thus a '-x1' would
have  no  effect.    A  '-x3'  would  enable  the  basic  set  plus  whatever
instructions have bit  1 set in  their class mask.   A '-x'  without a  digit
following is equivalent to a '-xf' which sets all four of the mask bits.  The
following table indicates the current extended instruction sets available  in
the TASM tables:

Base   Base           Extension 1   Extension 2  Extension 3    Extension 4
Table  Family         (-x3)         (-x7)        (-x5)          (-x9)
_____________________________________________________________________________
48     8048           8041A                      8022           8021
65     6502           R65C02                     R65C00/21
05     6805           M146805 CMOS               HC05C4
80     Z80            HD64180       
68     6800           6801/6803     68HC11
51     8051                         
85     8080                         
3210   TMS32010                     
3225   TMS320C25                                 TMS320C26
70     TMS7000                      

The above  table does  not attempt  to show  the many  microprocessor  family
members that may apply under a given column.

See the TASMTABS.DOC on-line document for details on each specific table.

y - Enable Assembly Timing.  If  this option is enabled TASM will generate  a
statement of elapsed time and  assembled lines per second  at the end of  the
assembly.


TASM - Table Driven Assembler Version 2.9                             Page 11

ENVIRONMENT VARIABLES

The TASM  environment can  be customized  by using  the enviroment  variables
listed below:

TASMTABS.  This  variable  specifies  the  path  to  be  searched  for   TASM
instruction set definition tables.   If it is  not defined then the  table(s)
must exist in the current  working directory.  If it  was desired to put  the
instruction set definition  tables in a  directory called 'TASM'  on a  drive
called 'C:', the following statement would be appropriate in the AUTOEXEC.BAT
file:

        set TASMTABS=C:\TASM

TASMOPTS. This variable specifies  TASM command line options  that are to  be
invoked every time TASM is executed.  For example, if TASM is being used  for
8048 assemblies  with  binary  object  file  output  desired,  the  following
statement would be appropriate in the AUTOEXEC.BAT file:

        set TASMOPTS=-48 -b


EXIT CODES

When TASM terminates, it will return to DOS the following exit codes:

Exit Code      Meaning
___________________________________________________________
0              Normal completion, no assembly errors
1              Normal completion, with assembly errors
2              Abnormal completion, insufficient memory
3              Abnormal completion, file access error
4              Abnormal completion, general error


Exit codes 2 and above  will also be accompanied  by messages to the  console
concerning the error.


TASM - Table Driven Assembler Version 2.9                             Page 12

SOURCE FILE FORMAT

Statements in the  source file must  conform to a  format as follows  (except
for assembler  directive  statements  which are  described  in  a  subsequent
section):

        label  operation    operand       comment

All of  the  fields  are  optional,  under  appropriate  circumstances.    An
arbitrary amount of white space (space and tabs) can separate each field  (as
long as the maximum line length of 255 characters is not exceeded).  Each  of
the fields are described below:

Label Field. If the first character of the line is alphabetic, it is  assumed
to be the start of  a label.  Subsequent characters  are accepted as part  of
that label until a space, tab, or ':' is encountered.  The assembler  assigns
a value to the label corresponding  to the current location counter.   Labels
can be a maximum of 32 characters  long.  Labels can contain upper and  lower
case letters, digits, underscores, and  periods (the first character must  be
alphabetic).  Labels are  case sensitive - the  label 'START' is a  different
label from 'start' - unless the '-i' (ignore case) option is enabled.

Operation Field. The operation field  contains an instruction mnemonic  which
specifies the action  to be  carried out by  the target  processor when  this
instruction is executed.  The interpretation of each mnemonic is dependent on
the target microprocessor  (as indicated by  the selected TASM  table).   The
operation field may  begin in  any column except  the first.   The  operation
field is case insensitive.

Operand Field. The operand field specifies the data to be operated on by  the
instruction.  It  may include expressions  and/or special symbols  describing
the addressing mode  to be  used.  The  actual format  and interpretation  is
dependent on  the target  processor.   For a  description of  the format  for
currently supported  processors,  see  the  TASMTABS.DOC  file  on  the  TASM
distribution disk.

Comment Field.  The comment field always  begins with a semicolon.  The  rest
of the line from the semicolon to the end of the line is ignored by TASM, but
passed on to  the listing file  for annotation purposes.   The comment  field
must be the last field on a line,  but it may be the only field, starting  in
column one, if desired.

Multiple  Statement Lines.   If the backslash  character is encountered on  a
source line,   it  is  treated as  a  newline.   The  remainder of  the  line
following  the  backslash  will be processed as an independent line of source
code.  This allows one to put multiple statements  on a line.  This  facility
is not so useful of itself,   but when coupled with  the capability  of   the
DEFINE   directive,    powerful    multiple  statement    macros    can    be
constructed  (see  section  on ASSEMBLER DIRECTIVES).  Note that when   using
the  statement  separator,  the character  immediately  following  it  should
be considered the first character of a new  line,  and thus must either be  a
start of a label or  white space (not an instruction).  As the examples show,
a space is put between the backslash and the start of the next instruction.


Some  examples  of  valid  source  statements follow (6502 mnemonics shown):

TASM - Table Driven Assembler Version 2.9                             Page 13


label1   lda      byte1   ;get the first byte
         dec      byte1
         jne      label1
                  
;                 
label2            
         sta      byte2,X
         ;        a multiple statement line follows
         lda      byte1\ sta byte1+4\ lda byte2\ sta byte2+4



EXPRESSIONS

Expressions are  made  up of  various  syntactic elements  (tokens)  combined
according to  a set  of syntactical  rules.   The  tokens are  summarized  as
follows:

        1.  Labels
        2.  Constants
        3.  Location Counter Symbol
        4.  Operators
        5.  Parenthesis

Labels. Labels are strings of characters that have a numeric value associated
with them, generally representing an address.   Labels can contain upper  and
lower case letters, digits,  underscores, and periods.   The first  character
must be a  letter or the  local label prefix  (default '_'). The  value of  a
label is  limited  to  32  bit  precision.   Labels  can  contain  up  to  32
characters, all of which are significant (none are ignored when looking at  a
label's value, as in some assemblers).   Case is significant unless the  '-i'
command line option is invoked.

Local labels must  only be  unique within the  scope of  the current  module.
Modules are defined with the MODULE directive.  Here is an example:

               .MODULE xxx
               lda regx
               jne _skip
               dec
        _skip  rts
               
               .MODULE yyy
               lda regy
               jne _skip
               dec
        _skip  rts


In the above example, the _skip label is reused without harm.  As a  default,
local labels are not shown in the label table linting (resulting from the  '-
l' command line  option).   See also  sections on  MODULE and  LOCALLABELCHAR
directives.

Numeric Constants. Numeric constants must  always begin with a decimal  digit

TASM - Table Driven Assembler Version 2.9                             Page 14

(thus hexadecimal constants that  start with a letter  must be prefixed by  a
'0' unless the  '$' prefix is  used).  The  radix is determined  by a  letter
immediately following the digit string according to the following table:

       Radix          Suffix                   Prefix
       ______________________________________________________
       2              B or b                   %
       8              O or o                   @
       10             D or d (or nothing)      
       16             H or h                   $

Decimal is the default radix, so decimal constants need no suffix or prefix.

The following representations are equivalent:

       1234H          or     $1234
       100d           or     100
       177400O        or     @177400
       01011000b      or     %01011000

The prefixes  are provided  for  compatibility with  some other  source  code
formats but  introduce  a  problem of  ambiguity.    Both '%'  and  '$'  have
alternate uses  ('%' for  modulo,  '$' for  location  counter symbol).    The
ambiguity is  resolved  by examining  the  context.   The  '%'  character  is
interpreted as the modulo operator only if it is in a postion suitable for  a
binary operator. Similarly, if the first character following a '$' is a valid
hexadecimal digit, it is assumed to be a radix specifier and not the location
counter.

Character Constants. Character constants are single characters surrounded  by
single quotes  (following  quote  is  optional).   The  ASCII  value  of  the
character in the quotes is returned.  No escape provision exists to represent
non-printable characters within the quotes,  but this is not necessary  since
these can be just  as easily represented as  numeric constants (or using  the
TEXT directive which does allow escapes).

String Constants. String constants are  one or more characters surrounded  by
double quotes.  Note  that string constants are  not allowed in  expressions.
They are  only  allowable  following  the  TITLE,  BYTE  and  TEXT  assembler
directives. The quoted strings  may also contain escape  sequences to put  in
unprintable values.  The following escape sequences are supported:

        Escape
        Sequence       Description
        ___________________________________________________________
        \n             Line Feed
        \r             Carriage return
        \b             Backspace
        \t             Tab
        \f             Formfeed
        \\             Backslash
        \"             Quote
        \000           Octal value of character

Location  Counter  Symbol.   The  current value of the location counter  (PC)
can be  used in  expressions by  placing a  '$' in  the desired  place.   The

TASM - Table Driven Assembler Version 2.9                             Page 15

Location Counter Symbol is allowable anywhere  a numeric constant is.   (Note
that if the '$' is followed  by a decimal digit then it  is  taken to be  the
hexadecimal radix  indicator  instead  of the  Location  Counter  symbol,  as
mentioned above).    The '*'  may  also be  used  to represent  the  location
counter,  but  is  less   preferred  because  of   its  ambiguity  with   the
multiplicative operator.

Operators. Expressions  can  optionally  contain operators  to  perform  some
alterations or  calculations  on  particular  values.     The  operators  are
summarized as follows:

       Operator    Type            Description
       __________________________________________
       +           Additive        addition
       -                           subtraction
                                   
       *           Multiplicative  multiplication
       /                           division
       %                           modulo
       <<                          logical shift left
       >>                          logical shift right
                                   
       ~           Unary           bit inversion (one's complement)
       -                           unary negation
                                   
       =           Relational      equal
       ==                          equal
       !=                          not equal
       <                           less than
       >                           greater than
       <=                          less than or equal
       >=                          greater than or equal
                                   
       &           Binary          binary 'and'
       |                           binary 'or'
       ^                           binary 'exclusive or'

The syntax is much the same as in 'C' with the following notes:

1.  No operator precedence  is in effect.  Evaluation  is from left to  right
unless grouped by  parenthesis (see example below).

2.  All evaluations are done with 32 bit signed precision.

3.  Both '=' and '==' are allowable equality checkers.  This is allowed since
the syntax  does not  provide assignment  capability (as  '=' would  normally
imply).

The relational operators return a value of 1 if the relation is true and 0 if
it is false.  Thirtytwo bit signed arithmetic is used.

It is  always  a  good idea  to  explicitly  indicate the  desired  order  of
evaluation with  parenthesis,   especially  to   maintain  portability  since
TASM does  not  evaluate  expressions  in  the  same  manner  as  many  other
assemblers.   To  understand  how it  does  arrive    at   the    values  for
expressions, consider the following example:

TASM - Table Driven Assembler Version 2.9                             Page 16

        1 + 2*3 + 4

TASM would evaluate this as:

       (((1 + 2) * 3) + 4) = 13

Typical rules of precedence would cause the (2*3) to be evaluated first, such
as:

        1 + (2*3) + 4      = 11

To make  sure  you get  the  desired  order of  evaluation,  use  parenthesis
liberally.

Note that  TASM versions  earlier than  2.7.8 employed  a somewhat  different
method of evaluating expressions  (also without precedence) that  essentially
resulted in a right to left evaluation.

Here are some examples of valid expressions:

        (0f800H + tab)
        (label_2 >> 8)
        (label_3 << 8) & $f000
        $ + 4
        010010000100100b + 'a'
        (base + ((label_4 >> 5) & (mask << 2))

TASM - Table Driven Assembler Version 2.9                             Page 17

ASSEMBLER DIRECTIVES

Most of  the  assembler directives  have  a  format similar  to  the  machine
instruction format.    However,  instead of  specifying  operations  for  the
processor to carry out,  the directives cause the  assembler to perform  some
function related to  the assembly process.  TASM has two  types of  assembler
directives - those that mimic the 'C' preprocessor functions, and those  that
resemble the more traditional assembler  directive functions.  Each of  these
will be discussed.

The 'C' preprocessor  style directives are  invoked with a  '#' as the  first
character of the line followed by the appropriate directive (just as in 'C').
Thus, these directives cannot have a label preceding them (on the same line).
Note that in the examples directives are shown in upper case, however, either
upper or lower case is acceptable.

ADDINSTR. This directive can  be used to  define additional instructions  for
TASM to use in this assembly.  The format is:

[label]  .ADDINSTR inst args opcode nbytes modop class shift binor

The fields are  separated by  white space  just as  they would  appear in  an
instruction  definition  file.  See  the   TASMTABS.DOC  file  on  the   TASM
distribution disk for more detail.

AVSYM.  See SYM/AVSYM.

BLOCK. This directive causes the Instruction Pointer to advance the specified
number of bytes without assigning values to the skipped over locations.   The
format is:

        [label] .BLOCK        expr

Some valid examples are:

        word1   .BLOCK     2
        byte1   .block     1
        buffer  .block     80

BSEG/CSEG/DSEG/NSEG/XSEG. These  directives can  be invoked  to indicate  the
appropriate address space for  symbols and labels  defined in the  subsequent
code.   The  invocation  of these  directives  in  no way  affects  the  code
generated, only provides  more information in  the symbol table  file if  the
AVSYM directive is employed.   Segment control directives  such as these  are
generally supported  by assemblers  that  generate relocatable  object  code.
TASM does not generate  relocatable object code and  does not support a  link
phase, so these  directives have  no direct  effect on  the resulting  object
code. The segments are defined as follows:

        Directive       Segment Description
        _________________________________________________________
        BSEG            Bit  address
        CSEG            Code address
        DSEG            Data address (internal RAM)
        NSEG            Number or constant (EQU)
        XSEG            External data address (external RAM)

TASM - Table Driven Assembler Version 2.9                             Page 18

BYTE.  This directive allows a value assignment to the byte pointed to by the
current Instruction Pointer.  The format is:

        [label] .BYTE   expr [, expr ...]

Onlythe lower eight bits of expr are used.  Multiple bytes may be assigned by
separating them with  commas or  (for printable strings)  enclosed in  double
quotes. Here are some examples:


      label1   .BYTE     10010110B
               .byte     'a'
               .byte     0
               .byte     100010110b,'a',0
               .byte     "Hello", 10, 13, "World"


CHK.  This directive causes  a checksum to be  computed and deposited at  the
current location.    The  starting  point  of  the  checksum  calculation  is
indicated as an argument.  Here is the format:

        .CHK    starting_addr

Here is an example:


        start:  NOP
                LDA #1
                .CHK start


The checksum is calculated as the simple arithmetic sum of all bytes starting
at the start_add up to  but not including the  address of the CHK  directive.
The least significant byte is all that is used.

CODES/NOCODES. These directives can be used to alternately turn on or off the
generation of formatted listing output with line numbers, opcodes, data, etc.
With NOCODES  in  effect, the  source  lines are  sent  to the  listing  file
untouched.  This  is useful around  blocks of  comments that need  a full  80
columns of width for clarity.

DB.  This is alternate form of the BYTE directive.

DW.  This is alternate form of the WORD directive.

DEFINE. The DEFINE directive  is one of the  most powerful of the  directives
and allows string substitution with optional arguments (macros).  The  format
is as follows:

    #DEFINE  macro_label[(arg_list)]  [macro_definition]

    macro_label := string to be expanded when found in the source file.
                  
    arg_list    := optional argument list for variable substitution
                  
    macro_def   := string to replace the occurrences of macro_label in

TASM - Table Driven Assembler Version 2.9                             Page 19

                            the source file.

The simplest form of the DEFINE directive might look like this:

        #DEFINE         MLABEL

Notice that  no  substitutionary string  is  specified.   The  purpose  of  a
statement like this would typically be to  define a label for the purpose  of
controlling some subsequent conditional assembly (IFDEF or IFNDEF).

A more complicated example, performing  simple substitution, might look  like
this:

        #DEFINE         VAR1_LO         (VAR1 & 255)

This statement would cause all occurrences of  the  string  'VAR1_LO' in  the
source to be substituted with '(VAR1 & 255)'.

As   a   more   complicated   example,    using   the   argument    expansion
capability, consider this:

        #DEFINE         ADD(xx,yy)      clc\ lda xx\ adc yy\ sta xx

If the source file then contained a line like this:

        ADD(VARX,VARY)

It would be expanded to:

        clc\ lda VARX\ adc VARY\ sta VARX

The above  example shows  the use  of the  backslash ('\')  character   as  a
multiple   instruction    statement  delimiter.   This  approach  allows  the
definition of fairly  powerful,   multiple statement   macros.   The  example
shown generates 6502 instructions to add one memory location to another.

Some rules associated with the argument list:

1.  Use a maximum of 10 arguments.

2.  Each argument should be a maximum of 15 characters.

Note that macros can be defined on the TASM command line, also, with the '-d'
option flag.

DEFCONT. This directive can be used to  add to the last macro started with  a
DEFINE directive.   This  provides a  convenient way  to define  long  macros
without running off the edge of the page. The ADD macro shown above could  be
defined as follows:

        #DEFINE         ADD(xx,yy)     clc
        #DEFCONT                     \ lda xx
        #DEFCONT                     \ adc yy
        #DEFCONT                     \ sta xx

EJECT.   This   directive   can   be used  to force  a top  of form  and  the

TASM - Table Driven Assembler Version 2.9                             Page 20

generation of a page  header on the  list file.  It  has no   effect  if  the
paging mode is off (see PAGE/NOPAGE).  The format is:

        .EJECT

ELSE.  This directive  can optionally be  used with IFDEF,  IFNDEF and IF  to
delineate an alternate block of code to be assembled if the block immediately
following the IFDEF, IFNDEF or IF is not assembled.

Here are some examples of the use of IFDEF, IFNDEF,  IF,  ELSE,  and ENDIF:

        #IFDEF   label1
        lda      byte1
        sta      byte2
        #ENDIF   
                 
        #ifdef   label1
        lda      byte1
        #else    
        lda      byte2
        #endif   
                 
        #ifndef  label1
        lda      byte2
        #else    
        lda      byte1
        #endif   

        #if ($ >= 1000h)
        ; generate an invalid statement to cause an error
        ;  when we go over the 4K boundary.
         !!! PROM bounds exceeded.
        #endif

END.   This  directive should follow all  code/data generating statements  in
the source file.  It forces the last record to be written to the object file.
The format is:

        [label]       .END

ENDIF. This directive must  always follow an IFDEF,  IFNDEF, or IF  directive
and signifies the end of the conditional block.

EQU. This directive can be used to  assign values to labels.  The labels  can
then be used in expressions in place of the literal constant.  The format is:

        label   .EQU    expr

Here is an example:

        MASK   .EQU   0F0H
        ;             
               lda    IN_BYTE
               and    MASK
               sta    OUT_BYTE


TASM - Table Driven Assembler Version 2.9                             Page 21

An alternate form of 'EQU' is  '='.  The previous example is equivalent to:

        MASK    =   0F0H

or

        MASK    =0FOH
        MASK    =$FO

White space must exist after the label,  but none is required after the '='.

EXPORT. This directive can be used to define labels (symbols) that are to  be
written to the export symbol file.  The symbols are written as equates (using
the .EQU  directive)  so  that  the  resulting file  can  be  included  in  a
subsequent assembly.  This feature can help overcome some of the deficiencies
of TASM due to its lack of a relocating linker. The format is:

[label]  .EXPORT      label

The following example  illustrates the use  of the EXPORT  directive and  the
format of the resulting export file:

Source file:

        .EXPORT        read_byte
        .EXPORT        write_byte
        .EXPORT        open_file

Resulting export file:

read_byte      .EQU   $1243
write_byte     .EQU   $12AF
open_file      .EQU   $1301


IFDEF. This directive can be used to optionally assemble a block of code.  It
has the following form:

        #IFDEF  macro_label

When invoked, the list of macro labels (established via DEFINE directives) is
searched.  If the label is found, the following lines of code are  assembled.
If not found, the input file is skipped  until an ENDIF or ELSE directive  is
found.

Lines that are skipped over still appear in the listing file, but a '~'  will
appear immediately after the current PC and no object code will be  generated
(this is applicable to IFDEF, IFNDEF, and IF).

IFNDEF. This directive is the opposite of the IFDEF directive.  The block  of
code following is assembled only  if the specified macro_label is  undefined.
It has the following form:

        #IFNDEF  macro_label

When invoked, the list of macro labels (established via DEFINE directives) is

TASM - Table Driven Assembler Version 2.9                             Page 22

searched.   If the  label  is not  found, the  following  lines of  code  are
assembled.  If it is found, the input file is skipped until an ENDIF or  ELSE
directive is found.

IF.   This directive  can be  used to  optionally assemble  a block  of  code
dependent on the value of a given expression.  The format is as follows:

        #IF     expr

If the expression expr evaluates to non-zero, the following block of code  is
assembled (until an ENDIF or ELSE is encountered).

INCLUDE.  The INCLUDE directive reads  in and assembles the indicated  source
file.  INCLUDEs can  be nested up  to six levels.   This allows a  convenient
means to keep common definitions, declarations, or subroutines in files to be
included as needed.  The format is as follows:

        #INCLUDE        filename

The filename must be enclosed in double quotes.  Here are some examples:

        #INCLUDE       "macros.h"
        #include       "equates"
        #include       "subs.asm"

LIST/NOLIST.  These directives can be used to alternately turn the output  to
the list file on (LIST) or off (NOLIST).  The format is:

        .LIST
        .NOLIST

LOCALLABELCHAR. This directive can be used to override the default "_" as the
label prefix indicating a local label.  For example, to change the prefix  to
"?" do this:

        .LOCALLABELCHAR "?"

Be carefull to  use only  characters that  are not  operators for  expression
evaluation.  To do  so causes ambiguity for  the expression evaluator.   Some
safe characters are "?", "{", and "}".

LSFIRST/MSFIRST. These  directives  determine  the  byte  order  rule  to  be
employed for the WORD  directive.  The default  (whether correct or not)  for
all TASM  versions  is the  least  significant  byte first  (LSFIRST).    The
following illustrates its effect:

        0000  34 12    .word $1234
        0002           .msfirst
        0002  12 34    .word $1234
        0004           .lsfirst
        0004  34 12    .word $1234


ORG. This directive provides the means to set the Instruction Pointer (a.k.a.
Program Counter) to the desired value.  The format is:


TASM - Table Driven Assembler Version 2.9                             Page 23

        [label] .ORG    expr

The label is optional.  The Instruction pointer is assigned the value of  the
expression, expr.  For example, to  generate code starting at address  1000H,
the following could be done:

        start   .ORG    1000H

The expression  (expr)  may contain  references  to the  current  Instruction
Pointer, thus  allowing various  manipulations to  be done.  For example,  to
align the Instruction Pointer  on the next 256  byte boundary, the  following
could be done:

                .ORG  (($ + 0FFH) & 0FF00H)

ORG can also be used to reserve space without assigning values:

               .ORG    $+8

An alternate form of ORG  is '*=' or '$='.   Thus the following two  examples
are exactly equivalent to the previous example:

                *=*+8
                $=$+8

PAGE/NOPAGE.  These  directives can be  used to alternately  turn the  paging
mode on (PAGE) or  off (NOPAGE).  If  paging is in  effect, then every  sixty
lines of output will be  followed by a Top of  Form character and a two  line
header containing page number, filename, and the title.  The format is:

        .PAGE
        .NOPAGE

The number of lines per page can be set with the '-p' command line option.


SET. This directive allows the value of an existing label to be changed.  The
format is:

        label   .SET    expr

The use of the SET directive should be avoided since changing the value of  a
label can sometimes  cause phase  errors between  pass 1  and pass  2 of  the
assembly.

SYM/AVSYM. These directives can be  used to cause a  symbol table file to  be
generated.  The format is:

        .SYM    ["symbol_filename"]
        .AVSYM  ["symbol_filename"]


TASM - Table Driven Assembler Version 2.9                             Page 24

For example:

        .SYM       "symbol.map"
        .SYM       
        .AVSYM     "prog.sym"
        .AVSYM

The two  directives are  similar, but  result in  a different  format of  the
symbol table file.  The format of the  SYM file is one line per symbol,  each
symbol starts in the  first column and  is followed by  white space and  then
four hexadecimal digits representing the value of the symbol.  The  following
illustrates the format:

       label1         FFFE
       label2         FFFF
       label3         1000

The AVSYM is provided  to generate symbol tables  compatible with the  Avocet
8051 simulator.  The format is similar, but each line is prefixed by an  'AS'
and each symbol value is prefixed by a segment indicator:

        AS     start          C:1000
        AS     read_byte      C:1243
        AS     write_byte     C:1280
        AS     low_nib_mask   N:000F
        AS     buffer         X:0080

The segment  prefixes are  determined by  the most  recent segment  directive
invoked (see BSEG/CSEG/DSEG/NSEG/XSEG directives).

TEXT. This directive allows an ASCII string to be used to assign values to  a
sequence of  locations starting  at  the current  Instruction Pointer.    The
format is:

        [label] .TEXT   "string"

The ASCII value of each character in string is taken and assigned to the next
sequential location.  Some escape sequences are supported as follows:

        Escape
        Sequence       Description
        ___________________________________________________
        \n             Line Feed
        \r             Carriage return
        \b             Backspace
        \t             Tab
        \f             Formfeed
        \\             Backslash
        \"             Quote
        \000           Octal value of character

TASM - Table Driven Assembler Version 2.9                             Page 25


Here are some examples:

        message1   .TEXT   "Disk I/O error"
        message2   .text   "Enter file name "
                   .text   "abcdefg\n\r"
                   .text   "I said \"NO\""


TITLE.  This directive allows the user to define a title string that  appears
at the top of each page of the list file (assuming the PAGE mode is on).  The
format is:

                .TITLE  "string"

The string should not exceed 80 characters.  Here are some examples:

                .TITLE  "Controller version 1.1"
                .title  "This is the title of the assembly"
                .title  ""

TASM - Table Driven Assembler Version 2.9                             Page 26


WORD. This directive allows a value assignment to the next two bytes  pointed
to by the current Instruction Pointer.  The format is:

        [label] .WORD  expr

The least significant byte of expr is put at the current Instruction  Pointer
with the most significant  byte at the next  sequential location (unless  the
MSFIRST directive has been invoked).  Here are some examples:

        data_table     .WORD   (data_table + 1)
                       .word   $1234
                       .Word   (('x' - 'a')  << 2)
                       .Word   12, 55, 32


TASM - Table Driven Assembler Version 2.9                             Page 27

OBJECT FILE FORMATS

TASM supports four object file formats:

        1.  Intel Hex (default).
        2.  MOS Technology Hex.
        3.  Motorola Hex.
        4.  Binary

Each are described below:

Intel Hex Object Format.  This is the  default format.   This format is  line
oriented and uses  only printable  ASCII characters except  for the  carriage
return/line feed at the end of each line.  Each line in the file assumes  the
following format:

:NNAAAARRHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHCCTT

Where:

All fields marked 'hex' consist of two or four ASCII hexadecimal digits (0-9,
A-F).  A maximum of 24 data bytes will be represented on each line  (override
the 24 byte default with the '-o' command line option).

:      = Record Start Character
NN     = Byte Count (hex)
AAAA   = Address of first byte (hex)
RR     = Record Type (hex, 00 except for last record which is 01)
HH     = Data Bytes (hex)
CC     = Check Sum (hex)
TT     = Line Terminator (carriage return, line feed)

The last line of  the file will be  a record conforming  to the above  format
with a byte count of zero:

         :00000001FF

The checksum is defined as:

  sum = byte_count + addr_hi + addr_lo + record_type + (sum of data bytes)
  checksum =  ((-sum) & ffh)

TASM - Table Driven Assembler Version 2.9                             Page 28

MOS Technology Hex Object Format. This format is line oriented and uses  only
printable ASCII characters except  for the carriage  return/line feed at  the
end of each line.  Each line in the file assumes the following format:

;NNAAAAHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHCCCCTT

All fields marked 'hex' consist of two or four ASCII hexadecimal digits (0-9,
A-F).  A maximum of 24 data bytes will be represented on each line  (override
the 24 byte default with the '-o' command line option).

;      = Record Start Character
NN     = Byte Count (hex)
AAAA   = Address of first byte (hex)
HH     = Data Bytes (hex)
CCCC   = Check Sum (hex)
TT     = Line Terminator (carriage return, line feed)

The last line of the file will be a record with a byte count of zero (';00').

The checksum is defined as:

    sum  =  byte_count + address_hi + address_lo + record_type +
                (sum of all data bytes)
    checksum =  (sum & ffffh)


Motorola Hex  Object Format.  This  format is  line  oriented and  uses  only
printable ASCII characters except  for the carriage  return/line feed at  the
end of each line.  Each line in the file assumes the following format:

S1NNAAAAHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHCCCCTT

All fields marked 'hex' consist of two or four ASCII hexadecimal digits (0-9,
A-F).  A maximum of 24 data bytes will be represented on each line  (override
the 24 byte default with the '-o' command line option).

S1     = Record Start Prefix
NN     = Byte Count (hex) (data byte count + 3)
AAAA   = Address of first byte (hex)
HH     = Data Bytes (hex)
CC     = Check Sum (hex)
TT     = Line Terminator (carriage return, line feed)

The last  line of  the  file will  be a  record  with a  byte count  of  zero
('S903AAAACCTT'). The checksum is defined as:

    sum  =  byte_count + address_hi + address_lo + record_type +
            (sum of all data bytes)
    checksum =  (~sum & ffh)


Binary Object Format. This  file format has only  a binary representation  of
each data byte with no  address, checksum or format description,  whatsoever.
It is often a convenient format to use to pass the data to other programs  on
your PC (like a PROM programmer package) but because of the  non-printability
and lack of address information, it is not often used to transmit the code to

TASM - Table Driven Assembler Version 2.9                             Page 29

other systems.

Note that when this object format is  selected (-b option), the -c option  is
forced.  This is done so that no ambiguity arises as a result of the lack  of
address information in the file.  Without the -c option, discontinuous blocks
of object code would appear contiguous.


TASM - Table Driven Assembler Version 2.9                             Page 30

LISTING FILE FORMAT

Each line of  source code  generates one  (or more)  lines of  output in  the
listing file.  The fields of the output line are as follows:

1.  Current  source  file  line  number  (4 decimal digits).

2.  An optional '+'  appears if this is   an  'INCLUDE'   file. (One '+'  for
each level of INCLUDE invoked).

3.  Current Instruction Pointer (4 hex digits).  An optional '~' follows  the
Instruction Pointer if the line of source code is not being assembled because
of an IFDEF, IFNDEF, or IF directive.

4.  Resulting code/data generated from  this source line (two hex digits  per
byte, each byte separated by a space, up to six bytes per line).

5.  The source line exactly as it appears in the source file.

If   paging   is   enabled  (by either  the  '-p' option  flag or  the  .PAGE
directive) some additional  fields will be  inserted into the   listing  file
every 60 lines.  These fields are:

        1.  Top of Form (form feed).
        2.  Assembler identifier (e.g. "TASM 6502 Assembler").
        3.  Initial source file name.
        4.  Page number.
        5.  Title.

TASM - Table Driven Assembler Version 2.9                             Page 31

PROM PROGRAMMING

A wide variety of PROM programming equipment is available that can use object
code in  one or  more of  the formats  TASM supports.   Here  are some  notes
concerning the generation of code to be put in PROMs:

1.  PRESET  MEMORY.   It is often  desirable to  have all bytes  in the  PROM
programmed even if not explicitly assigned  a value in the source code  (e.g.
the bytes are skipped over with a .ORG statement).  This can be  accomplished
by using the  -c (contiguous  block) and the  -f (fill)  command line  option
flags.  The -c will  ensure that every byte from  the lowest byte assigned  a
value to the the  highest byte assigned  a value will be  in the object  file
with no gaps.   The  -f flag will  assign the  specified value  to all  bytes
before the assembly begins so that when the object file is written, all bytes
not assigned a  value in  the source code  will have  a known value.   As  an
example, the following command line will generate object code in the  default
Intel Hex format with all bytes not assigned a value in the source set to  EA
(hex, 6502 NOP):

                tasm -65 -c -fEA test.asm

2.  CONTIGUOUS BLOCKS.   To ensure that TASM  generates object code to  cover
the full address range of the target PROM, put a .ORG statement at the end of
the source file set to  the last address desired.   For example, to  generate
code to be put in a 2716 EPROM (2 Kbytes) from hex address $1000 to $17ff, do
something like this in the source file:

                         ;start of the file
                         .ORG    $1000
                         ;rest of the source code follows
 
                         <source code>
 
                         ;end of the source code
                         .ORG    $17ff
                         .BYTE   0
                         .END

Now, to  invoke TASM  to generate  the code  in the  binary format  with  all
unassigned bytes set to 00 (6502 BRK), do the following:

                tasm -65 -b -f00 test.asm

Note that -b forces the -c option.


TASM - Table Driven Assembler Version 2.9                             Page 32

ERROR MESSAGES


Error Message                             Description
______________________________________________________________________________
Binary operator where value expected.     Two  binary  operators  in  a   row
                                          indicate a missing value.

Cannot malloc for label storage           Insufficient memory  to store  more
                                          labels. See LIMITATIONS.

Duplicate label.                          Duplicate    label    checks    are
                                          optionally  enabled  by  the   '-a'
                                          option.

File name too short                       A file name on the command line  is
                                          fewer than  3 characters.  This  is
                                          done to  prevent a  garbled  option
                                          flag from being  taken as a  source
                                          file, which in  turn can result  in
                                          the source file taken as an  object
                                          file (which are truncated at start-
                                          up time).

Heap overflow on label definition.        TASM was unable to allocate  memory
                                          to store the label.

Invalid operand.  No indirection for this instruction.
                                          The first character  of an  operand
                                          was  a  left  parenthesis  for   an
                                          instruction    that    does     not
                                          explicitly  specify  that  as   the
                                          format.    Some   micros  use   the
                                          parenthesis  as  an  indicator   of
                                          indirection, but putting a layer of
                                          parenthesis around an expression is
                                          always a valid thing to do (as  far
                                          as  the  expression  evaluator   is
                                          concerned).  The test for this case
                                          is only done if  the -a4 option  is
                                          selected. See  section on  ASSEMBLY
                                          CONTROL.

Invalid token where value expected.       Two binary operators  in a row  are
                                          not allowed.

Label too long                            Labels are limited to 31 characters.

Label value misaligned                    The value  of  a label  appears  to
                                          have  a  different  value  on   the
                                          second pass then it was computed to
                                          have on the  first pass.   This  is
                                          generally   due   to   Zero    Page
                                          Addressing mode  problems with  the
                                          6502 version of TASM.  Labels  that
                                          are used in operands for statements

TASM - Table Driven Assembler Version 2.9                             Page 33

                                          that  could   utilize   Zero   Page
                                          addressing mode  should  always  be
                                          defined before used as an operand.

Label not found                           A label used  in an expression  was
                                          not  found  in  the  current  label
                                          table.

Label must pre-exist for SET.             The  SET  directive  can  only   be
                                          applied to an existing label.

Label table overflow                      To   many    labels    have    been
                                          encountered.

List file open error                      TASM  was  not  able  to  open  the
                                          specified list file.

Macro expansion too long.                 The expansion of  a macro  resulted
                                          in a line that exceeded the maximum
                                          length.

Maximum number of macros exceeded         To many macros (DEFINEs) have  been
                                          encountered.

No END directive before EOF               The source file did not have an END
                                          directive in it. This is not fatal,
                                          but may cause the last object  file
                                          record to be lost.

No  files  specified                      TASM was  invoked  with  no  source
                                          file specified.

No such label yet defined.                A SET directive was encountered for
                                          a label not yet defined.  The value
                                          of labels that are modified by  the
                                          SET directive must already exist.

No indirection for this instruction.      A parenthesis was found around  the
                                          operand  expression.     This   may
                                          indicate   an   attempt   to    use
                                          indirection     where     it     is
                                          inappropriate.

Non-unary operator at start of expression A binary operator (such as '*') was
                                          found  at  the   beginning  of   an
                                          expression.  Some micros use '*' as
                                          an indirection operator.  Since  it
                                          is also a  legititmate operator  in
                                          an expression,  some ambiguity  can
                                          arise.        If    a    particular
                                          instruction/addressing  mode   does
                                          not allow indirection, and a '*' is
                                          placed in front  of the  associated
                                          expression,  the   assembler   will
                                          assume this error.     See the  -a8
                                          option of ASSEMBLY CONTROL.

TASM - Table Driven Assembler Version 2.9                             Page 34

Object file open error                    TASM  was  not  able  to  open  the
                                          specified object file.

Range of argument exceeded                The value  of an  argument  exceeds
                                          the valid  range  for  the  current
                                          instruction and addressing mode.

Range of relative branch exceeded         A branch  instruction  exceeds  the
                                          maximum range.

Source file open error                    TASM  was  not  able  to  open  the
                                          specified source file.

Unrecognized directive                    A statement starting with a '.'  or
                                          '#' has  a  mnemonic  that  is  not
                                          defined as a directive.

Unrecognized  instruction                 A statement has an opcode  mnemonic
                                          that is not defined.

Unrecognized argument                     A statement has  an  operand format
                                          that is not defined.

Unknown token                             Unexpected  characters  were  found
                                          while parsing an expression.

Unused data in MS byte of argument.       An instruction  or  directive  used
                                          the least  significant byte  of  an
                                          argurment   and   left   the   most
                                          significant byte unused, but it was
                                          non-zero.

Unkown option Flag.                       Invalid  option   flag   has   been
                                          specified  on  the  command   line.
                                          invoke TASM  with  nothing  on  the
                                          command line to see a list of valid
                                          options.


TASM - Table Driven Assembler Version 2.9                             Page 35

BUGS AND LIMITATIONS

Limitations and Specifications
                                           TASM                  TASMB
_____________________________________________________________________________
Maximum number of labels                   2000                  10000
Maximum length of labels                   32 characters
Maximum address space                      64 Kbytes (65536 bytes)
Maximum number of nested INCLUDES          4
Maximum length of TITLE string             79 characters
Maximum source line length                 255 characters
Maximum length after macro expansion       255 characters
Maximum length of expressions              255 characters
Maximum length of pathnames                79 characters
Maximum length of command line             127 characters
                                           
Maximum number of instructions (per table) 600                   1000
Maximum number of macros                   1000                  
Maximum number of macro arguments          10                    
Maximum length of macro argument           16 characters         
Heap size (for labels, macros, & buffers)  20000 bytes           60000
Memory requirements                        160K                  256K

Bugs

1.  The  8048 version of  TASM does not  check for use  of memory beyond  any
reasonable bounds (e.g.  an 8048 has a maximum address space of 4 Kbytes  but
TASM will let you pretend that you have 64 Kbytes).

2.  Expression  evaluation has  no operator  precedence in  effect which  can
make  for  unexpected results if not explicitly grouped with parenthesis.

3.  First page of  listing file will not show  a user defined title  (defined
via TITLE directive).

4.  TASM sometimes does not generate  error messages  for  improperly  formed
expressions.


TASM - Table Driven Assembler Version 2.9                             Page 36

APPENDIX A - ORDERING INFORMATION

TASM is distributed as shareware.   The shareware portion of the product  may
be freely copied and  used for evaluation  purposes.  Use  of TASM beyond  an
evaluation period of 90 days requires registration. Registered users  receive
the following benefits:

    1.  The recent version of TASM.
    2.  TASM source code (in C).
    3.  Bound TASM manual.
    4.  Telephone support.
    5.  Knowledge that they are supporting the development of useful
        but inexpensive software.

DESCRIPTION                                  UNIT PRICE    PRICE
___________________________________________________________________________

TASM Registration (TASM disk, manual, & source)  $40.00    _______

TASM Site Registration (for sites with multiple   90.00    _______
   users.  Includes same materials as above.)          

TASM User's Manual (included above)               10.00    _______

TASM update for registered users                  10.00    _______
   (latest disk (with source), and manual)             

Subtotal                                                   _______

Tax (Washington state residents add 8.2%)                  _______

Billing fee (for orders not accompanied by check) 10.00    _______

Foreign postage (outside North America) add $10.00         _______
  (Foreign orders must be in US funds drawn on a US bank)

TOTAL (post paid)                                          _______


Which processors are of primary interest to you?  __________________
(This is for our information only.  You will receive all current TASM tables).

Shipping Address:                                Send check or money order to:
                                                 Speech Technology Incorporated
______________________________________________   Software Division
                                                 837 Front Street South
______________________________________________   Issaquah, WA  98027   USA

______________________________________________