********************************************************************
	*                                                                  *
	*          INSTALLATION  INSTRUCTIONS FOR                          *
	*          THE XEBEC CORP. HARD DISK DRIVER                        *
	*          CP/M-80 (R)       S100 BUS HOST COMPUTER                *
	*                                                                  *
	********************************************************************
	               REVISION 2.0   FEBRUARY 28, 1983







	THE XEBEC HARD DISK DRIVER SOFTWARE PACKAGE CONSISTS OF FOUR
	FILES SUPPLIED ON THE DISTRIBUTION DISKETTE.  THESE ARE
	"HDINSTL.DOC", "HDFMT.ASM", "HDLINK.ASM", AND "HDDVR.ASM".
	
	HDINSTL.DOC (THIS FILE) IS ALL THE DOCUMENTATION NECESSARY
	FOR THE USER TO INSTALL THE DRIVER ON HIS S100 BUS SYSTEM.
	
	HDFMT.ASM IS A UTILITY PROGRAM WHICH ENABLES THE USER TO
	FORMAT THE HARD DISK AND INITIALIZE THE DIRECTORY AREA.
	
	THE FILES HDLINK.ASM AND HDDVR.ASM ARE THE FILES WHICH 
	ENABLE THE USER TO GENERATE THE HARD DISK DRIVER PROGRAM.
	
	THE DRIVER OPERATES BY LINKING ITSELF TO THE EXISTING FLOPPY
	DISK BIOS.  THIS IS ACCOMPLISHED BY FINDING THE FLOPPY BIOS
	JUMP TABLE AND PATCHING THE ENTRY POINTS FOR ALL DISK OPERATIONS.
	THE USER SHOULD ONLY RUN "HDBOOT" ONCE PER COLD BOOT OF 
	THE SYSTEM, DUE TO THE NATURE OF THE PATCHING PROCESS.
	
	THE ADVANTAGE OF THIS DRIVER OVER THE CONVENTIONAL
	TYPE OF DRIVER IS THAT THE USER IS NOT REQUIRED TO CREATE
	A CUSTOM BIOS TO GET HIS HARD DISK SUBSYSTEM RUNNING.
	BY SIMPLY EDITING A FEW VARIABLES INTO THE SOURCE
	FILES AND ASSEMBLING THEM, THE DRIVER IS READY TO OPERATE
	ON THE USER'S SPECIFIC SYSTEM.
	
        FOLLOWING ARE THE STEPS NECESSARY TO CREATE A DRIVER
	TAILORED TO THE USER'S SYSTEM.
	
	1.  FOR A SINGLE HARD DISK SUBSYSTEM, A 1K BYTE BLOCK OF 
            MEMORY MUST BE CREATED ABOVE CP/M FOR THE DRIVER PROGRAM.
            FOR A TWO DRIVE SYSTEM ( C & D ), A 2K BYTE BLOCK OF
            MEMORY MUST BE CREATED ABOVE CP/M FOR THE DRIVER PROGRAM.
            THIS IS NORMALLY DONE BY A CP/M SYSGEN.




Š

        2.  EDIT THE DESIRED STARTING ADDRESS FO THE DRIVER
	    INTO THE FILE "HDLINK.ASM".  THIS WILL BE THE
	    BEGINNING ADDRESS OF THE BLOCK CREATED IN STEP 1.
            THE VARIABLE NAME IS "START".
 	
               A.  IF A TWO DRIVE SYSTEM ( C & D ) IS DESIRED,
                   REMOVE THE COMMENTS IN "HDLINK.ASM" LOCATED
                   BETWEEN THE DOUBLE ROWS OF '$' NEAR THE END.

	3.  EDIT THE FOLLOWING VARIABLES INTO THE FILE "HDDVR.ASM":
	       
	       A. DESIRED STARTING ADDRESS OF THE DRIVER (THIS MUST
	          BE THE SAME AS THE ADDRESS IN "HDLINK.ASM").THE 
                  VARIABLE NAME IS "START".

	       B. THE HOST ADAPTOR BASE ADDRESS.  THE VARIABLE NAME
	          IN THE FILE IS "BASE".  THE FACTORY STANDARD
	          IS 80H...IF A DIFFERENT BASE ADDRESS IS DESIRED
	          THE ADDRESS SWITCHES ON THE HOST ADAPTOR AND THIS 
	          EQUATE WILL NEED TO BE CHANGED.

		C. IF YOUR SYSTEM HAS A Z80 CPU, SETTING THE EQUATE
		   Z80 TO TRUE AND WILL ALLOW THE DRIVER TO USE THE 
                   Z80 BLOCK MOVE INSTRUCTIONS.
	
	       D. IF A TWO DRIVE SYSTEM ( C & D ) IS DESIRED,
                  REMOVE THE COMMENTS IN "HDDVR.ASM" IN FIVE PLACES
                  BETWEEN THE DOUBLE ROWS OF '$'.
                   
        4.  EDIT THE HOST ADAPTOR BASE ADDRESS INTO THE FILE
	    "HDFMT.ASM".  AGAIN, THE FACTORY STANDARD IS 80H.
             THE VARIABLE NAME IN THE FILE IS "BASE".

	5.  ASSEMBLE HDFMT, HDLINK, AND HDDVR USING THE CP/M "ASM" PROGRAM.
	
	6.  CREATE HDFMT.COM USING THE CP/M "LOAD" PROGRAM.
















Š	
	7.  TO CREATE THE "HDBOOT.COM", DO THE FOLLOWING:
	
	       A. INSURE THAT DDT.COM IS ON THE SAME DISKETTE
	          AS THE FILES "HDLINK.HEX" AND "HDDVR.HEX".
	
	       B. TYPE:
	                 DDT HDLINK.HEX
	       
	       C. WHEN DDT RETURNS WITH THE - PROMPT, TYPE:
	
	                 IHDDVR.HEX
	                 RXXXX
	       
		  WHERE XXXX IS DETERMINED BY THE FORMULA:
		
		  XXXX=FC00H - DESIRED STARTING ADDRESS (H) + 800H
	
		  EXAMPLE:

		         STARTING ADDRESS F800

                         XXXX=FC00H - F800H + 800H
		
		         XXXX=0C00H


	       D. TYPE CTRL-C TO RETURN TO THE CP/M CONSOLE
	          COMMAND PROCESSOR.
	
	       E. TYPE:
	                 SAVE 8 HDBOOT.COM
	
	          YOU NOW HAVE THE DRIVER PROGRAM UNDER THE NAME "HDBOOT.COM"
	
	8.  FORMAT THE HARD DISK USING THE UTILITY PROGRAM "HDFMT".
	
	9.  WHEN THE HARD DISK HAS BEEN SUCESSFULLY FORMATTED, YOU
	    ARE READY TO INSTALL THE DRIVER.
	
	10. TYPE:
	           HDBOOT
	
	    THIS WILL INSTALL THE DRIVER FOR THIS SESSION.
	    EACH TIME YOU COLD BOOT THE SYSTEM, YOU WILL
	    NEED TO RUN THE "HDBOOT" PROGRAM.  REMEMBER,
	    ONLY DO THIS ONCE PER COLD BOOT.



            (R)   CP/M IS A REGISTERED TRADEMARK OF DIGITAL RESEARCH.